## Slide 1: Compressive Structured Light for Recovering Inhomogeneous Participating Media
Jinwei Gu, Shree Nayar, Eitan Grinspun
Peter Belhumeur, and Ravi Ramamoorthi
Columbia University

## Slide 2: Structured Light Methods
Image
Plane
One common assumption:
  Each pixel receives light from a single surface point.
Camera
Projector
0101001…
0101001…
Opaque Surface

## Slide 3
Inhomogeneous Participating Media
Volume densities rather than boundary surfaces.
Efficiency in acquisition is critical, especially for time-varying participating media.
Drifting Smoke of Incense
(532fps Camera)‏
Mixing a Pink Drink with Water
(1000fps Camera)‏
Video clips are from http://www.lucidmovement.com

## Slide 4: Related Work
Laser Sheet Scanning
[Hawkins, et al., 05][Deusch, et al., 01]
Laser Line Interpolation
[Fuchs, et al. 07]
Structured light for opaque objects immersed in a participating medium
Multi-view volume reconstruction
  “Flame sheet” from 2 views
  Tomographic reconstruction from 8~360 views
[Narasimhan et al., 05]
[Hasinoff et al., 03]
[Ihrke et al., 04, 06]
[Trifonov et al., 06]
Single view and controllable light

## Slide 5
Compressive Structured Light
Projector
x
y
z
Participating
Medium
Camera
I(y, z)‏
Target low density media and assume single scattering
Assume volume density, gradients are sparse
Each pixel is a line integral measurement of volume density

## Slide 6
Under single scattering and orthographic projection,
Image Formation
Projector
Camera Pixel
Voxel
z
x
y
x
b
a
b = aT x
assume no attenuation,
(See paper for derivation)
[Hawkins et al., 05]
[Fuchs et al., 07]

## Slide 7
Temporal Coding
Projector
x
y
z
Participating
Medium
Camera
I(y, z)‏
Time 1
x
=
b1
X
a1
b1
a1

## Slide 8
Temporal Coding
Projector
x
y
z
Participating
Medium
Camera
I(y, z)‏
x
=
b2
X
a2
b2
a2
Time 2

## Slide 9
Temporal Coding
Projector
x
y
z
Participating
Medium
Camera
I(y, z)‏
x
=
b3
X
a3
b3
a3
Time 3

## Slide 10
Temporal Coding
=
X
b
A
Efficient acquisition requires: m < n
An under-determined linear system, which can be solved according to certain prior knowledge of x.
Coded Light Pattern
m×n
Measurements
m×1
Volume Density
n×1

## Slide 11: Solving Underdetermined System Ax = b
Least Square (LS):
Nonnegative Least Square (NLS):
For underdetermined system, they are equivalent to
Minimum Norm Least Square

## Slide 12: Solving Underdetermined System Ax = b
Least Square (LS):
Nonnegative Least Square (NLS):
Volume density of smoke
[Hawkins et al. 05]
Least Square
(NRMSE=0.330)‏
Nonnegative Least Square
(NRMSE=0.177)‏

## Slide 13: Solving Underdetermined System Ax = b
Use the sparsity of the signal for reconstruction
The sparsity of natural images has extensively been used before in computer vision
  Total-variation noise removal
  Sparse coding and compression
  …
Recent renaissance of sparse signal reconstruction
  Sparse MRI
  Image sparse representation
  Light transport
  …
[Rudin et al., 92]
[Lustig et al., 07]
[Olshausen et al., 95]
[Simoncelli et al., 97]
[Peers et al., 08]
[Mairal et al., 08]
Compressive Sensing

## Slide 14: Compressive Sensing: A Brief Introduction
Sparsity / Compressibility:
  Signals can be represented as a few non-zero coefficients in an appropriately-chosen basis, e.g., wavelet, gradient, PCA.
[Candes et al., 06][Donoho, 06]…
Original Image
N2 pixels
Wavelet Representation
K significantly non-zero coeffs
K < < N2

## Slide 15: Compressive Sensing: A Brief Introduction
Sparsity / Compressibility:
  Signals can be represented as a few non-zero coefficients in an appropriately-chosen basis, e.g., wavelet, gradient, PCA.
For sparse signals, acquire measurements (condensed representations of the signals) with random projections.
[Candes et al., 06][Donoho, 06]…
=
X
Measurement Ensemble
m×n, where m<n
Measurements
m×1
Signal
n×1
b
A

## Slide 16: Compressive Sensing: A Brief Introduction
Sparsity / Compressibility:
  Signals can be represented as a few non-zero coefficients in an appropriately-chosen basis, e.g., wavelet, gradient, PCA.
For sparse signals, acquire measurements (condensed representations of the signals) with random projections.
Reconstruct signals via L1-norm optimization:
  Theoretical guarantees of accuracy, even with noise
[Candes et al., 06][Donoho, 06]…

## Slide 17: Compressive Sensing: A Brief Introduction
L-1 norm is known to give sparse solution.
  An example: x = [x1, x2]
  Sparse solutions should be points on the two axes.
  Suppose we only have one measurement: a1x1+a2x2=b
x1
x2
a1x1+ a2x2=b
x1
x2
a1x1+ a2x2=b
L-1 Norm
L-2 Norm
Sparse Solution
Non-sparse Solution
More information about compressive sensing can be found at
http://www.dsp.ece.rice.edu/cs/

## Slide 18: Reconstruction via Compressive Sensing
CS-Value:
CS-Gradient:
CS-Both:

## Slide 19: Reconstruction via Compressive Sensing
Least Square
(NRMSE=0.330)‏
Nonnegative Least Square
(NRMSE=0.177)‏
CS-Value
(NRMSE=0.026)‏
CS-Gradient
(NRMSE=0.007)‏
CS-Both
(NRMSE=0.001)‏

## Slide 20: More 1D Results
Least Square
(NRMSE=0.272)‏
Nonnegative Least Square
(NRMSE=0.076)‏
CS-Value
(NRMSE=0.052)‏
CS-Gradient
(NRMSE=0.014)‏
CS-Both
(NRMSE=0.005)‏

## Slide 21: More 1D Results
Least Square
(NRMSE=0.266)‏
Nonnegative Least Square
(NRMSE=0.146)‏
CS-Value
(NRMSE=0.053)‏
CS-Gradient
(NRMSE=0.024)‏
CS-Both
(NRMSE=0.021)‏

## Slide 22: Simulation
Ground truth
  128×128×128 voxels
  For voxels inside the mesh, the density is linear to the distance from the voxel to the center of the mesh.
  For voxels outside of the mesh, the density is 0.
Slices of the volume
Volume (128×128×128)‏

## Slide 23: Simulation
Temporal coding
  32 binary light patterns and 32 corresponding measured images
  The 128 vertical stripes are assigned 0/1 randomly with prob. of 0.5
32 Measured Images (128×128)‏
32 Light Patterns (128×128)‏

## Slide 24: Simulation Results
Least Square
Nonnegative
Least Square
CS-Value
CS-Gradient
CS-Both
1/16
1/8
1/4
1/2
1

## Slide 25: Simulation Results
Least Square
Nonnegative
Least Square
CS-Value
CS-Gradient
CS-Both
1/16
1/8
1/4
1/2
1

## Slide 26: Experimental Setup
Projector: DLP, 1024x768, 360 fps
Camera: Dragonfly Express 8bit, 320x140 at 360 fps
24 measurements per time instance, and thus recover dynamic volumes up to 360/24 = 15 fps.
Projector
Camera
Milk Drops

## Slide 27: Static Volume: A 3D Point Cloud Face
Photograph
Measurements
(24 images of size 128x180)‏
A 3D point cloud of a face etched in a glass cube
Reconstructed Volume
(128x128x180)‏

## Slide 28: Milk Dissolving: One Instance at time
Photograph
Milk drops dissolving in a water tank.
Measurements (24 images of size 128x250)‏
Reconstructed Volume (128x128x250)‏

## Slide 29
Milk Dissolving: Time-varying Volume
Video (15fps)‏
Reconstructed Volume
(128x128x250)‏
Milk drops dissolving in a water tank.

## Slide 30
Milk Dissolving: Time-varying Volume
Video (15fps)‏
Reconstructed Volume
(128x128x250)‏
Milk drops dissolving in a water tank.

## Slide 31: Discussion & Future Work
Iterative algorithm to correct for attenuation
No Attenuation Correction
With Attenuation Correction
Spatial Coding of Compressive Structured Light
  Reconstruction from a single high resolution image
  High requirement of calibration
Multiple Scattering
Compressive Sensing for acquisition in other domains (Peers et al: Compressive Light Transport Sensing)‏

## Slide 32: Acknowledgement
Tim Hawkins: measured smoke volume data.
Sujit Kuthirummal, Neeraj Kumar, Dhruv Mahajan, Bo Sun, Gurunandan Krishnan for useful discussion.
Anonymous reviewers for valuable comments.
NSF, Sloan Fellowship, ONR for funding support.

## Slide 33: Thank you!
The End.

## Slide 35
Under single scattering and orthographic projection, we have
Image Formation Model
Projector
Camera Pixel
Voxel
z
x
y
Attenuation
Scattering
Attenuation

## Slide 36
Image Formation Model
Projector
Camera Pixel
Voxel
z
x
y
With negligible attenuation, we have:
Constant from all y,z
Attenuation
Scattering
Attenuation
[Hawkins et al., 05]
[Fuchs et al., 07]

## Slide 37
Thus,
Image Formation Model
Projector
Camera Pixel
Voxel
z
x
y
With negligible attenuation, we have:
x
b
a

## Slide 38
Thus,
Image Formation Model
Projector
Camera Pixel
Voxel
z
x
y
With negligible attenuation, we have:
x
b
a
b = aT x

## Slide 39: Simulation: 1D Case
Smoke volume data
  120 volumes measured at different times.
  Each volume is of size 240×240×62.
[Hawkins, et al., 05]

## Slide 40: Experiment 1: Two-plane Volume
Photograph
Two glass planes covered with powder.
  The letters “EC” are drawn on one plane and “CV” on the other plane by removing the powder.
Measurements (24 images)‏

## Slide 41: Experiment 1: Two-plane Volume
No Attenuation Correction
Two glass planes covered with powder.
  The letters “EC” are drawn on one plane and “CV” on the other plane by removing the powder.
With Attenuation Correction
Reconstructed Volume (128x128x180)‏

## Slide 42: Experiment 1: Two-plane Volume
No Attenuation Correction
Two glass planes covered with powder.
  The letters “EC” are drawn on one plane and “CV” on the other plane by removing the powder.
With Attenuation Correction
Reconstructed Volume (128x128x180)‏

## Slide 43: Iterative Attenuation Correction
1. Assume no attenuation, solve for
2. Compute the attenuated light for each row
3. Solve the linear equations for
,
where
L(x,y)‏
Projector
I(y,z)‏
Camera

## Slide 44: Iterative Attenuation Correction
Ground truth
Iteration 1
Iteration 2
Iteration 3
0.00
0.04
0.10
Iterations
Error
Reconstruction Error
0.06
0.08
0.02