\section{Examples}

\label{sec:examples}

In the following examples, we often omit the message body and the

corresponding \header{Content-Length} and \header{Content-Type} headers

for brevity.

\subsection{Registration}

\label{sec:examples:registration}

Bob registers on start-up.  The message flow is shown in Figure \ref{fig:register}.

\txtpsfigsize{!}{!}{register}{SIP Registration Example}

F1 REGISTER Bob -$>$ Registrar

\begin{verbatim}

REGISTER sip:registrar.biloxi.com

Via: SIP/2.0/UDP 10.4.1.4:5060

To: Bob <sip:bob@biloxi.com>

From: Bob <sip:bob@biloxi.com>;tag=456248

Call-ID: 843817637684230@phone21.boxesbybob.com

CSeq: 1826 REGISTER

Contact: <sip:bob@10.4.1.4>

Expires: 7200

Contact-Length: 0

\end{verbatim}

The registration expires after two hours.  The registrar responds with a 200 OK:

F2 200 OK Registrar -$>$ Bob

\begin{verbatim}

SIP/2.0 200 OK

Via: SIP/2.0/UDP 10.4.1.4:5060

To: Bob <sip:bob@biloxi.com>

From: Bob <sip:bob@biloxi.com>;tag=456248

Call-ID: 843817637684230@phone21.boxesbybob.com

CSeq: 1826 REGISTER

Contact: <sip:bob@10.4.1.4>

Expires: 7200

Contact-Length: 0

\end{verbatim}

\subsection{Session Setup}

\label{sec:examples:session-setup}

This example contains the full details of the example session setup in Section~\ref{sec:overview-of-operations}.  The message flow is shown in Figure \ref{fig:trapezoid}.

F1 INVITE Alice -$>$ atlanta.com proxy

\begin{verbatim}

INVITE sip:bob@biloxi.com SIP/2.0

Via: SIP/2.0/UDP 10.1.3.3:5060

To: Bob <sip:bob@biloxi.com>

From: Alice <sip:alice@atlanta.com>;tag=1928301774

Call-ID: a84b4c76e66710@10.1.3.3

CSeq: 314159 INVITE

Contact: <sip:alice@10.1.3.3>

Content-Type: application/sdp

Contact-Length: 142

(Alice's SDP not shown)

\end{verbatim}

F2 100 Trying atlanta.com proxy -$>$ Alice

\begin{verbatim}

SIP/2.0 100 Trying

Via: SIP/2.0/UDP 10.1.3.3:5060

To: Bob <sip:bob@biloxi.com>

From: Alice <sip:alice@atlanta.com>;tag=1928301774

Call-ID: a84b4c76e66710@10.1.3.3

CSeq: 314159 INVITE

Contact-Length: 0

\end{verbatim}

F3 INVITE atlanta.com proxy -$>$ biloxi.com proxy

\begin{verbatim}

INVITE sip:bob@biloxi.com SIP/2.0

Via: SIP/2.0/UDP 10.1.1.1:5060;branch=77ef4c2312983.1

Via: SIP/2.0/UDP 10.1.3.3:5060

To: Bob <sip:bob@biloxi.com>

From: Alice <sip:alice@atlanta.com>;tag=1928301774

Call-ID: a84b4c76e66710@10.1.3.3

CSeq: 314159 INVITE

Contact: <sip:alice@10.1.3.3>

Content-Type: application/sdp

Contact-Length: 142

(Alice's SDP not shown)

\end{verbatim}

F4 100 Trying biloxi.com proxy -$>$ atlanta.com proxy

\begin{verbatim}

SIP/2.0 100 Trying

Via: SIP/2.0/UDP 10.1.1.1:5060;branch=77ef4c2312983.1

Via: SIP/2.0/UDP 10.1.3.3:5060

To: Bob <sip:bob@biloxi.com>

From: Alice <sip:alice@atlanta.com>;tag=1928301774

Call-ID: a84b4c76e66710@10.1.3.3

CSeq: 314159 INVITE

Contact-Length: 0

\end{verbatim}

F5 INVITE biloxi.com proxy -$>$ Bob

\begin{verbatim}

INVITE sip:bob@10.4.1.4 SIP/2.0

Via: SIP/2.0/UDP 10.2.1.1:5060;branch=4b43c2ff8.1

Via: SIP/2.0/UDP 10.1.1.1:5060;branch=77ef4c2312983.1

Via: SIP/2.0/UDP 10.1.3.3:5060

To: Bob <sip:bob@biloxi.com>

From: Alice <sip:alice@atlanta.com>;tag=1928301774

Call-ID: a84b4c76e66710@10.1.3.3

CSeq: 314159 INVITE

Contact: <sip:alice@10.1.3.3>

Content-Type: application/sdp

Contact-Length: 142

(Alice's SDP not shown)

\end{verbatim}

F6 180 Ringing Bob -$>$ biloxi.com proxy

\begin{verbatim}

SIP/2.0 180 Ringing

Via: SIP/2.0/UDP 10.2.1.1:5060;branch=4b43c2ff8.1

Via: SIP/2.0/UDP 10.1.1.1:5060;branch=77ef4c2312983.1

Via: SIP/2.0/UDP 10.1.3.3:5060

To: Bob <sip:bob@biloxi.com>;tag=a6c85cf

From: Alice <sip:alice@atlanta.com>;tag=1928301774

Call-ID: a84b4c76e66710@10.1.3.3

CSeq: 314159 INVITE

Contact-Length: 0

\end{verbatim}

F7 180 Ringing biloxi.com proxy -$>$ atlanta.com proxy

\begin{verbatim}

SIP/2.0 180 Ringing

Via: SIP/2.0/UDP 10.1.1.1:5060;branch=77ef4c2312983.1

Via: SIP/2.0/UDP 10.1.3.3:5060

To: Bob <sip:bob@biloxi.com>;tag=a6c85cf

From: Alice <sip:alice@atlanta.com>;tag=1928301774

Call-ID: a84b4c76e66710@10.1.3.3

CSeq: 314159 INVITE

Contact-Length: 0

\end{verbatim}

F8 180 Ringing atlanta.com proxy -$>$ Alice

\begin{verbatim}

SIP/2.0 180 Ringing

Via: SIP/2.0/UDP 10.1.3.3:5060

To: Bob <sip:bob@biloxi.com>;tag=a6c85cf

From: Alice <sip:alice@atlanta.com>;tag=1928301774

Call-ID: a84b4c76e66710@10.1.3.3

CSeq: 314159 INVITE

Contact-Length: 0

\end{verbatim}

F9 200 OK Bob -$>$ biloxi.com proxy

\begin{verbatim}

SIP/2.0 200 OK

Via: SIP/2.0/UDP 10.2.1.1:5060;branch=4b43c2ff8.1

Via: SIP/2.0/UDP 10.1.1.1:5060;branch=77ef4c2312983.1

Via: SIP/2.0/UDP 10.1.3.3:5060

To: Bob <sip:bob@biloxi.com>;tag=a6c85cf

From: Alice <sip:alice@atlanta.com>;tag=1928301774

Call-ID: a84b4c76e66710@10.1.3.3

CSeq: 314159 INVITE

Contact: <sip:bob@10.4.1.4>

Content-Type: application/sdp

Contact-Length: 131

(Bob's SDP not shown)

\end{verbatim}

F10 200 OK biloxi.com proxy -$>$ atlanta.com proxy

\begin{verbatim}

SIP/2.0 200 OK

Via: SIP/2.0/UDP 10.1.1.1:5060;branch=77ef4c2312983.1

Via: SIP/2.0/UDP 10.1.3.3:5060

To: Bob <sip:bob@biloxi.com>;tag=a6c85cf

From: Alice <sip:alice@atlanta.com>;tag=1928301774

Call-ID: a84b4c76e66710@10.1.3.3

CSeq: 314159 INVITE

Contact: <sip:bob@10.4.1.4>

Content-Type: application/sdp

Contact-Length: 131

(Bob's SDP not shown)

\end{verbatim}

F11 200 OK atlanta.com proxy -$>$ Alice

\begin{verbatim}

SIP/2.0 200 OK

Via: SIP/2.0/UDP 10.1.3.3:5060

To: Bob <sip:bob@biloxi.com>;tag=a6c85cf

From: Alice <sip:alice@atlanta.com>;tag=1928301774

Call-ID: a84b4c76e66710@10.1.3.3

CSeq: 314159 INVITE

Contact: <sip:bob@10.4.1.4>

Content-Type: application/sdp

Contact-Length: 131

(Bob's SDP not shown)

\end{verbatim}

F12 ACK Alice -$>$ Bob

\begin{verbatim}

ACK sip:bob@10.4.1.4 SIP/2.0

Via: SIP/2.0/UDP 10.1.3.3:5060

To: Bob <sip:bob@biloxi.com>;tag=a6c85cf

From: Alice <sip:alice@atlanta.com>;tag=1928301774

Call-ID: a84b4c76e66710@10.1.3.3

CSeq: 314159 ACK

Contact-Length: 0

\end{verbatim}

The media session between Alice and Bob is now established.

Bob hangs up first.  Note that Bob's SIP phone maintains its own \header{CSeq} numbering space, which, in this example, begins with 231.  Also not that since Bob is making the request, the \header{To} and \header{From} URLs and tags have been swapped.

F13 BYE Bob -$>$ Alice

\begin{verbatim}

BYE sip:alice@10.1.3.3 SIP/2.0

Via: SIP/2.0/UDP 10.4.1.4:5060

From: Bob <sip:bob@biloxi.com>;tag=a6c85cf

To: Alice <sip:alice@atlanta.com>;tag=1928301774

Call-ID: a84b4c76e66710@10.1.3.3

CSeq: 231 BYE

Contact-Length: 0

\end{verbatim}

F14 200 OK Alice -$>$ Bob

\begin{verbatim}

SIP/2.0 200 OK

Via: SIP/2.0/UDP 10.4.1.4:5060

From: Bob <sip:bob@biloxi.com>;tag=a6c85cf

To: Alice <sip:alice@atlanta.com>;tag=1928301774

Call-ID: a84b4c76e66710@10.1.3.3

CSeq: 231 BYE

Contact-Length: 0

\end{verbatim}

The SIP Call Flows document \cite{draft-ietf-sip-call-flows} contains further examples of SIP messages.