\section{Querying for Capabilities}

\label{sec:query-for-capabilities}

The SIP method {\OPTIONS} allows a client to query another client or server as to its capabilities.  This allows a client to discover information about the methods, content types, extensions, codecs etc. supported without actually "ringing" the other party. For example, before a client inserts a \header{Require} header field into an {\INVITE} listing an option that it is not certain the destination UAS supports, the client can query the destination UAS with an {\OPTIONS} to see if this option is returned in a \header{Supported} header field.

The target of the {\OPTIONS} request is identified by the \header{Request-URI}, which could identify another User Agent or a SIP Server.  Alternatively, a server receiving an {\OPTIONS} request with a \header{Max-Forwards} header value of 0 {\MAY} respond to the request regardless of the \header{Request-URI}.

\motivation{This behavior is common with HTTP/1.1.}

An {\OPTIONS} request sent as part of an established dialog does not have any impact on the dialog.

\subsection{Construction of OPTIONS Request}

\label{sec:query-for-capabilities:request}

An {\OPTIONS} request is constructed using the standard rules for a SIP request as discussed Section~\ref{sec:general:gen}.

A \header{Contact} header field {\MAY} be present in an {\OPTIONS}.

# \motivation{OPEN ISSUE \#197: What is the semantic of this \header{Contact}}

An \header{Accept} header field {\SHOULD} be included to indicate the type of message body the UAC wishes to receive in the response.

Example {\OPTIONS} request:

\begin{verbatim}

# OPTIONS sip:carol@chicago.com SIP/2.0

Via: SIP/2.0/UDP 10.1.1.1:5060;branch=23411513a6

# Via: SIP/2.0/UDP 10.1.3.3:5060

To: <sip:carol@chicago.com>

# From: Alice <sip:alice@atlanta.com>;tag=1928301774

Call-ID: a84b4c76e66710@10.1.3.3

CSeq: 63104 OPTIONS

Contact: <sip:alice@10.1.3.3>

Accept: application/sdp

Contact-Length: 0

\end{verbatim}

\subsection{Processing of OPTIONS Request}

\label{sec:query-for-capabilities:response}

The response to an {\OPTIONS} is constructed using the standard rules for a SIP response as discussed in Section~\ref{sec:general:serv-resp}.  The response code chosen is the same that would have been chosen had the request been an {\INVITE}.  That is, a 200 (OK) would be returned if the UAS is ready to accept a call, a 486 (Busy Here) would be returned if the UAS is busy, etc.  This allows an {\OPTIONS} request to be used to determine the basic state of a UAS, which can be an indication of whether the UAC will accept an {\INVITE} request.

Note that this use of {\OPTIONS} has limitations due the differences in proxy handling of {\OPTIONS} and {\INVITE} requests. While a forked {\INVITE} can result in multiple 200 OK responses being returned, a forked {\OPTIONS} will only result in a single 200 OK response, since it is treated by proxies using the non-{\INVITE} handling.  See Section~\ref{sec:initiateuac} for the normative details.

\header{Allow}, \header{Accept}, \header{Accept-Encoding}, \header{Accept-Language}, and \header{Supported} header fields {\SHOULD} be present in a 200 OK response to an {\OPTIONS} request.

# A \header{Contact} header field {\MAY} be present in a 200 OK response.

# A \header{Warning} header field {\MAY} be present.

A message body {\MAY} be sent, the type of which is determined by the \header{Accept} header in the {\OPTIONS} request.

Example {\OPTIONS} response (corresponding to the request in Section~\ref{sec:query-for-capabilities:request}):

\begin{verbatim}

# SIP/2.0 200 OK

# Via: SIP/2.0/UDP 10.1.1.1:5060;branch=23411513a6

# Via: SIP/2.0/UDP 10.1.3.3:5060

To: <sip:carol@chicago.com>;tag=93810874

# From: Alice <sip:alice@atlanta.com>;tag=1928301774

Call-ID: a84b4c76e66710@10.1.3.3

CSeq: 63104 OPTIONS

Contact: <sip:carol@10.3.6.6>

Allow: INVITE, ACK, CANCEL, OPTIONS, BYE

Accept: application/sdp

Accept-Encoding: gzip

Accept-Language: en

Supported: foo

Content-Type: application/sdp

Contact-Length: 274

v=0

o=carol 28908764872 28908764872 IN IP4 10.3.6.6

s=-

t=0 0

c=IN IP4 10.3.6.6

m=audio 0 RTP/AVP 0 1 3 99

a=rtpmap:0 PCMU/8000

a=rtpmap:1 1016/8000

a=rtpmap:3 GSM/8000

a=rtpmap:99 SX7300/8000

m=video 0 RTP/AVP 31 34

a=rtpmap:31 H261/90000

a=rtpmap:34 H263/90000

\end{verbatim}

# Comments

This statement is not further supported in the text.  There should be something that says how this information is returned

Do we want to say explicitly that OPTIONs may be sent prior to any INVITE?

Bug \#197 about contents of this Contact header.

Also Bug \#197.