## Slide 1: VoIP intro
Henning Schulzrinne

## Slide 2: Name confusion
Commonly used interchangeably:
  Voice-over-IP (VoIP) – but includes video
  Internet telephony – but may not run over Internet
  IP telephony (IPtel)
Also: VoP (any of ATM, IP, MPLS)
Some reserve Internet telephony for transmission across the (public) Internet
Transmission of telephone services over IP-based packet switched networks
Also includes video and other media, not just voice

## Slide 3: A bit of history
1876 invention of telephone
1915 first transcontinental telephone (NY–SF)
1920’s first automatic switches
1956 TAT-1 transatlantic cable (35 lines)
1962 digital transmission (T1)
1965 1ESS analog switch
1974 Internet packet voice (2.4 kb/s LPC)
1977 4ESS digital switch
1980s Signaling System #7 (out-of-band)
1990s Advanced Intelligent Network (AIN)
1992 Mbone packet audio (RTP)
1996 early commercial VoIP implementations (Vocaltec); PC-to-PC calling

## Slide 4: System model
to.com
SIP trapezoid
outbound proxy
a@foo.com: 128.59.16.1
registrar
signaling
media

## Slide 5: Functions needed
Signaling
  Find destination user (vs. host)
    Using registration (“binding”)
  Negotiate media and their parameters
  Authenticate caller
  Implement services and policies
    Call vs. media services
Media
  Deliver media streams
    Right order, right codec, right timing
    Provide QoS feedback

## Slide 6: AVVID Architecture - Open Packet Telephony
The World Is Now Global— All Apps Must Travel Time and Distance
Applications
Call Processing
Infrastructure
Clients
IP SoftPhone
PSTN gateways
Analog phone support
DSP farms
IP
Network
PSTN
Directory
Call
Processing
Cisco Unity
Voice Mail, UMS
Intelligent Contact Manager
IP IVR, IP AA Apps Engine
Voice Portal
ICM
Collaboration
Video
GK
Brian Gracely, Cisco, 2001

## Slide 7: PBX features
call waiting/multiple calls | RFC 3261
hold | RFC 3264
transfer | RFC 3515/Replaces
conference | RFC 3261/callee caps
message waiting | message summary package
call forward | RFC 3261
call park | RFC 3515/Replaces
call pickup | Replaces
do not disturb | RFC 3261
call coverage | RFC 3261
from Rohan Mahy’s VON Fall 2003 talk
simultaneous ringing | RFC 3261
basic shared lines | dialog/reg. package
barge-in | Join
“Take” | Replaces
Shared-line “privacy” | dialog package
divert to admin | RFC 3261
intercom | URI convention
auto attendant | RFC 3261/2833
attendant console | dialog package
night service | RFC 3261
centrex-style features
boss/admin features
attendant features

## Slide 8: Legacy (PSTN) issues
Map between E.164 numbers and URLs
Locate PSTN gateways
PSTN services
  Shared lines & key systems
  Early media (pre-pick up)
  Emergency calling
  Dumb end systems (elevator phones)