## Slide 1: Overview of IEEE 802.11 and 802.16 MAC Layer
September 25, 2009
SungHoon Seo
hoon@cs.columbia.edu

## Slide 2: Standard History
IEEE 802.11 WLAN
802.11 – 1/2Mbps, 2.4GHz
802.11a – 54Mbps, 5GHz
802.11b – 11Mbps, 2.4GHz
802.11g – 54Mbps, 2.4GHz
802.11n – higher throughput improvement using MIMO
802.11e – QoS enhancement
802.11i – enhanced security
802.11f – Inter-Access Point Protocol
802.11k – radio resource measurement enhancement
IEEE 802.16 WMAN
802.16-2001 – fixed BWA, 10-63GHz
802.16e-2005 – Mobile Broadband Wireless Access system
802.16m – advanced air interface with data rate of 100Mbps mobile and 1Gbps fixed

## Slide 3: Selected MAC Features
MAC addressing
Network entry
Connection management
QoS
Management messages
MAC header
Mobility management and handover
Power management

## Slide 4: (1) MAC Addressing
802.11
Station (STA)
  Maintains only one permanent address
    48-bit MAC address
Access Point (AP)
  BSSID (Basic Service Set IDentification)
    MAC address of WLAN interface at AP
  SSID (Service Set IDentification)
    Human readable ASCII character (1~32 octets)
802.16m
Mobile Station (MS)
  Permanent address
    Unique 48-bit address
  Temporary address
    Station identifier during network entry (within cell)
    A flow identifier that uniquely identifies the management and transport connection with the MS

## Slide 5: (2) Network Entry
802.11
Scanning
  Active/passive probe
Association
  Acquire AID
Authentication
  Pre/post authentication
802.16m
Synchronization with BS by acquiring preambles
Acquiring the required information (e.g., BS and service provider identifier)
  for initial network entry and cell selection
Ranging
Authentication and registration
Service-flow setup

## Slide 6: (3) Connection Management
802.11
CSMA/CA
  DCF: Contention based connection establishment
  PCF are optional
Tree types of messages
  DATA message
    User data
  Management message
    Probe, association, authentication, etc
  Control message
    ACK, PS-POLL, etc
802.16m
Connections identified by
  Combination of the station identifier and the flow identifier
Two types of connections
  Management connection
    To carry MAC mgmt msg
    Bidirectional
    Reserved for unicast
  Transport connection
    To carry user data including upper layer signaling
    Fragmentation & augmentation
    Unidirectional
    Established with a unique flow identifier

## Slide 7: (4) Quality of Service
802.11
EDCA (Enhanced Distributed Channel Access)
  Admission control in 802.11e
Different CW assignment based on the service type
  BE (best effort)
  BK (background)
  VI (video)
  VO (voice)
802.16m
Assigns a unidirectional flow of packets
  With specific QoS requirements with a service flow
  MS and BS negotiate the possible QoS parameter during service-flow set up
Type of service
  UGS (unsolicited grant service)
    CBR traffic, such as VoIP
    Fixed size tx opportunities at regular time interval
  rtPS (real-time polling service)
    VBR traffic, such as MPEG video
  nrtPS (non-rt polling service)
    Delay-tolerant data service w/ minimum data rate, such as FTP
  BE (best effort)
    No BW reservation

## Slide 8: (5) MAC Management Messages
802.11
ARQ
  Trigger retransmission
  For every un-acked and timeout frame
  When the media is highly congested, it’s the burden of radio spectral capacity
802.16m
Support fast and reliable transmission of MAC mgmt message
  Using HARQ is under consideration
  Only unsuccessful fragments are retransmitted

## Slide 9: (6) MAC Header
802.11
30 Bytes MAC header
  Frame control (2B)
  Duration/ID (2B)
  Address 1, 2, 3 (each 6B)
  Sequence control (2B)
  Address 4 (2B)
802.16m
Efficient MAC header
  for small payload applications
Fewer fields
  Extended header indicator
  Flow identifier
  Payload length
Shorter size
  Only TWO bytes

## Slide 10: (7) Mobility Management and Handover
802.11
Original standard does not support the handover
  Inter-Access Point Protocol
  802.11f – withdrawn 2006
  Now working on 802.11kradio resource management and 802.11rfast roaming
Supporting MAC layer handover
  To mainly reduce scanning delay for neighbor AP discovery
802.16m
MS-assisted handover and
Network-controlled handover
  MS executes handover as directed by BS
  using HO control command
Handover procedure
  HO initialization
  HO preparation
  HO execution

## Slide 11: (8) Power Management
802.11
PSM (power saving mode)
  Listening to BEACON frame at every listen interval
  Listen interval = unit of beacon period (default 100 msec)
  Listen interval is fixed when a STA performs association with an AP
Channel limitation
  A STA can listen to signaling on the only one channel at a time
  Other channel cannot be listen without channel switching
802.16m
SLEEP mode
  Sleep mode req/res with MAC management messages
  Sleep cycle = units of frame or sub-frames = sleep window + listen window
  Dynamically adjusting the duration of sleep and listening windows
IDLE mode
  MS becomes periodically available for DL broadcast-traffic, e.g. paging wo/ registering with the network

## Slide 12: Our Goal
To design efficient MAC protocol of mobile WiMAX
  At SERVER side
    Maximize the number of VoIP call at the same time
  At CLIENT side
    Minimize service disruption
    Maximize the energy efficiency
  INTERWORKING
    Support seamless connectivity between heterogeneous networks, i.e., WLAN and cellular networks