## Slide 1: A Session Initiation Protocol (SIP) Load Control Event Package draft-shen-soc-load-control-event-package-00.txt
Charles Shen† and Henning Schulzrinne, Columbia University
Arata Koike, NTT
IETF Interim Meeting, December 2010
† Now with AT&T

## Slide 2: Main updates
  Addressed comments from the mailing list by
    Bruno Chatras
    Janet Gunn
    Volker Hilt
    Geoff Hunt
    Timothy Moran
    Eric Noel
    Parthasarathi R
  Full diff available at http://tools.ietf.org/rfcdiff?url1=http://tools.ietf.org/id/draft-shen-sipping-load-control-event-package-03.txt&url2=http://www.ietf.org/id/draft-shen-soc-load-control-event-package-00.txt

## Slide 3: 1. Filter value computation
  Section 4.2
  Clarified that filter value computation is based on algorithms out-of-scope of this document. The values do not have to be static, depending on the specific algorithm.
  The wording in the example operation scenario in Section 4.3 is adjusted accordingly

## Slide 4: 2. RPH header
  Section 4.4
  Mentioned RPH header in the revised texts:
  "A simple policy is to reject excessive requests with 500 responses as if they were obeying the rate, except that the SIP server should honor the Resource-Priority header field as defined in RFC4412 [RFC4412] in order to preserve more high-priority requests."

## Slide 5: 3. Logical combination AND / OR
Section 6.3.1
Clarified further on whether the sub-elements should be interpreted as "AND/OR" combination within the Call-Identity element.
Allows the call identity to be specified by multiple fields of a SIP request simultaneously, e.g., both the From and the To header fields

## Slide 6: 4. Action for filtering
Section 6.4
Clarified actions for filtering. added
"In static load filter configuration scenarios, using the <rate> sub-element is RECOMMENDED because it is hard to enforce the percentage rate or window-based control when the incoming load from upstream or the reactions from downstream are uncertain."
Changed the default action for non-acceptable requests from "Drop" to "Reject" in order to curb retransmission.

## Slide 7: 5. Security considerations
Section 9
Revised texts now state that:
“all load control notification MUST be authenticated and authorized before being accepted.”

## Slide 8: Open Issue: mandatory default schema
Initially brought up by Bruno in 2009
Background
  This I-D defines a SIP Event with its associated XML schema. The I-D does not preclude additional schemas to be used. When a more sophisticated schema is used in specific environments, the SIP event mechanisms defined in this draft can still be applicable, only the schema need to be different (e.g., ETSI-specific schema ETSI ES 283 034 in NGN).
Problem description
  The argument is that when using an alternative schema (e.g., ETSI-specific schema ETSI ES 283 034 in NGN), the respective SIP entities do not have to support the schema in this I-D. However, the current version mandates the support for the schema in this I-D in order to facilitate interoperability.

## Slide 9: Open Issue: mandatory default schema
Possible solutions
Retain the current I-D's statement. If necessary, create separate I-D for alternative schema (e.g., ETSI-specific schema ETSI ES 283 034 in NGN) which is mandatory for that I-D. The other I-D may refer to this I-D for contents that are in common. In the case both I-Ds become RFCs, a product may be declared as RFC-A compliant or RFC-B compliant.
2. Change the wording in the current version, making the schema in this I-D default but removing its mandatory support requirement.
3. Split the current I-D into two documents. One about the common contents on the mechanism, the second about the schema itself. Alternative schemas can be defined in other separate I-Ds. In this case, decision still needs to made about whether any one schema needs to be mandatory.

## Slide 10: Open Issue: document status
Shall this I-D be accepted as a WG item, in particular, as the base document for the third deliverable in the WG charter:
  “3. A specification for a SIP load filtering mechanism.”?

## Slide 11: Backup Slides
Backup slides:
Mechanism overview

## Slide 12: Problem Statement
SIP overload feedback control is reactive
  typically affects traffic already admitted & treat it equally
Where applicable, it is desirable to leverage known overload contexts (e.g., time and scope)
  Complement feedback control
  Push control closer to the source
  Specify selected parties to be controlled
  Setting up control in advance

## Slide 13: Solution
SIP event package for load control
  Subscribe and Notify-based mechanism, instantiation of SIP event framework RFC3265
Definition of load control XML document
  Condition
    Call Identity: source/destination, SIP or Tel URI(s)
    Validity: time period to activate control
    Method: e.g., INVITE
  Actions
    E.g., accepting a target controlled rate

## Slide 14: Example
Service Provider B
Hotline Callee
212-555-1234
9am-10am,
2009-1-1
Service Provider A
Enterprise Network B
Enterprise Network A
Filter Spec
ID: To: +1-212-555-1234
Time: 9am-10am 2009-1-1
Act: accept rate= Nmax
Filter Spec
ID: To: +1-212-555-1234
Time: 9am-10am 2009-1-1
Act: accept rate=NSPA
Filter Spec
ID: To: +1-212-555-1234
Time: 9am-10am 2009-1-1
Act: accept rate=NEPA
Filter Spec
ID: To: +1-212-555-1234
Time: 9am-10am 2009-1-1
Act: accept rate=NSPB
Notes: SIP Event SUBSCRIBE and NOTIFY mechanisms