## Slide 1: Vision: Policy-Driven Distributed and Collaborative Demand Response in Multi-Domain Commercial Buildings
Archan Misra (Telcordia)
and
Henning Schulzrinne (Columbia University)
Notes: 1

## Slide 2: Commercial & residential building energy usage

## Slide 3: Demand Response in Commercial Buildings & Campuses
Need to move beyond centralized control of limited “high-load” devices to
  Accommodate different policy domains & administrative hierarchies
    financial incentives need to be local
    avoid annoying users with inflexible policies
      e.g., important lab experiments or “need dishes for dinner”
  Automated incorporation of devices in the DR paradigm
    load management
    convenience & comfort (room temperature, boot time) vs. cost
  Flexible, pricing-based DR (instead of simple peak load control)
  Delegate down objectives and trade-offs (costs), not commands
    and provide feedback to device and user

## Slide 4: Three Models for Demand Adaptation
Centralized
DRACHMA
Decentralized
administrator-driven adaptation
hierarchical
owner/user policy-driven adaptation
device-centric adaptation

## Slide 5: Hierarchies of control
Corporate HQ
(“be green”, “save 10% of energy budget”)
Branch office 1
R&D department
Gym
Branch office 2
Accounting
Refrigeration
lab
office Dr. Doe
real-estate manager
(many tenants)

## Slide 6: DR For Commercial Buildings: The Problem Space
Feature | Residential | Commercial | Campus
Typical DER Resources | PVs, CHP | PVs, CHP, micro-turbine | PVs, micro-turbine, capacitor banks
Major loads | HVAC, lighting, fridge, pool, washing machine, dishwasher | HVAC, lighting, office equipment, IT servers, refrigeration | HVAC, lighting, elevators, lab equipment, IT servers
# of DR Loads | O(10) | O(100) | O(1000)
Major Distinguishing Issues |  | Multiple operational domains (different organizations/companies) distributed DR; High device heterogeneity | Potentially multiple operational domains (univ. departments); differentiated priority among domains to DER resources

## Slide 7: DRACHMA: The Hierarchical DR Model
Master DR Orchestrator (potentially in EMS)
Distribution Grid/ Utility
Grid Price Signal (t, t+T)
MicroTurbine
Battery Storage
Weather IT
Information
Wind/Sun
Forecast Data
Hierarchical DR Orchestrator
Hierarchical DR Orchestrator
Device
Production
Profile
Storage Parameters
(e.g., E(t), discharge
rate)
In-Building Price Signal (t, t+T)
Aggregatedd Demand Signal(t, t+T)/
Willingness to Pay (t, t+T)
Hierarchical DR Orchestrator (+ Policy)
Hierarchical DR Orchestrator (+ Policy)
Load Device (HVAC)
Load Device
(Server)
Device
Profile
LCO

## Slide 8: Generation variation

## Slide 9: Challenge 1: Device and Domain Autoconfiguration

## Slide 10: Challenge 2: Distributed DR Adaptation
Modified Time-Horizon Optimization
Make Framework work without explicitly knowing demand functions (distributed operation)
Incorporate Consumption Constraints (6 Different Load Types)
Factor in underflow/overflow constraints on storage
Key Challenges in Building This Distributed Adaptation Framework
Three key technical components
  Stochastic Optimization: Express the uncertainty in renewable production & demand as stochastic variables.
  Optimal Control: Derive key price-inflexion points for the next few minutes to hours.
  Distributed Utility Maximization: Set prices to maximize utility & make the algorithms implementable in a practical building environment
Maximize user comfort—utility functions
Minimize Energy Price
Conventional Instantaneous Optimization

## Slide 11: Challenge 3: Expressing Composite Load/Adaptation Models
Today - BACnet
DRACHMA
Future
Load Control Object (LCO): generic mechanism for
Transmission of load shed signals (scheduled, current)
Notification of compliance to load shed signals
hierarchical DR controllers to signal the aggregate demand and DR capabilities of sub-trees of heterogeneous devices
capture the price vs. consumption characteristics and constraints of a collection of heterogeneous devices

## Slide 12: Challenge 4: Automate actions
GW
SECE
B2BUA
PUBLISH
PIDF-LO
SUB/NOT
PIDF-LO, RPID,
others
monitor energy
usage
geocoding
travel time
next appt.
control appliances
update SNs, SMS, email
call state
Alice  a@b.com,
+1 212 555 1234
edit scripts
RFID

## Slide 13: Conclusion
Need to decentralize control  reflect local organization
Automate:
  local and global objectives  local behavior
  avoid manual actions  input from external data sources