## Slide 1: NetServ – Software-defined networking end-to-end
Henning Schulzrinne & IRT Lab
Columbia University

## Slide 2: Usage transition
Limited personal communication
Content-based
Personalized content and computation
email
static information retrieval (ftp  web)
phone
large-scale distribution of popular content (entertainment video)
social networks
context-based information
millions of tiny apps
3 core applications

## Slide 3: From fixed-function to APIs everywhere
customizable apps
user-controlled
upgradeable
APIs
fixed-function
vendor controlled
NetServ

## Slide 4: NetServ: Key ideas & requirements
Common programming environment across platforms
  Java
Scalable network-based services
  from handling each packet to exporting measurement APIs
From link layer to applications
Isolation & protection
Available to vendors, network operators & users
Automated and distributed management of functionality

## Slide 5: NetServ end-to-end
server
OpenFlow switches
BSC

## Slide 6: NetServ motivation
Old world
  (computation, storage)  forwarding
1990s: active networking
  mainly IP-level & per-packet
Exploring new opportunities
  providing additional services in the current Internet  NetServ
  CDNs and content-centric networks
  MIBs  “intelligent” network management
  virtualized networks
  denial-of-service attack prevention
  QoS monitoring

## Slide 7: Enabler 1: merging of server & router
10+ interfaces
0 GB disk
1 low-end processor
1 interface
TB disk
1-32 multi-core processors

## Slide 8: Enabler 2: Software: from floppy to autonomous

## Slide 9: The grand vision
NetServ everywhere
  Common service API on router, PC, set-top box, ...
  Storage and computation on network nodes
  Enabling platform for NGI
Internet is a multi-user computer
  Code modules run anywhere
  Secure and extensible
  Active networking redux!

## Slide 10: Not-so-grand initial focus
Activate the network (edge)
  Eyeball ISPs sell router resources to content publishers
  Content publishers install servers and packet processors on edge routers
Economic incentives
  New revenue source for ISPs
  Alternative to CDN for content publishers

## Slide 11: In-router & side-car
PIC
PE
PIC
storage & computation
multiple computation
& storage providers
data center or
POP
RE
10GigE
“side car”
storage & computation

## Slide 12: NetServ operations
also: flow level (1st packet) operations

## Slide 13: Different from active networks?
Active networks
  Packet contains executable code or pre-installed capsules
    Can modify router states and behavior
    Mostly stateless
  Not successful
    Per-packet processing too expensive
    Security concerns
    No compelling killer app to warrant such a big shift
  Notable work: ANTS, Janos, Switchware
NetServ
  Virtualized services on current, passive networks
    Service invocation is signaling driven, not packet driven
    Some flows & packets, not all of them
    Emphasis on storage
  Service modules are stand-alone, addressable entities
    Separate from packet forwarding plane
    Extensible plug-in architecture

## Slide 14: Deployment scenarios
Three actors
  Content publisher (e.g. youtube.com)
  Service provider (e.g. ISP)
  End user
Model 1: Publisher-initiated deployment
  Publisher rents router space from providers (or end users)
Model 2: Provider-initiated deployment
  Publisher writes NetServ module
  Provider sees lots of traffic, fetches and installs module
  Predetermined module location (similar to robots.txt)
Model 3: User-initiated deployment
  User installs NetServ module to own home router or PC
  or on willing routers along the data path

## Slide 15: How about GENI?
GENI = global-scale test bed for networking research
  parallel experiments in VMs
 initially, long-term, “heavy” services
NetServ tutorials at GEC 9, 11

## Slide 16: NetServ node architecture
NetServ packet transport
Virtual execution
environment
Building block layer
Virtual execution
environment
Building block layer
Virtual execution
environment
Building block layer
Service modules
Service modules
Service modules
NetServ controller
Module download
Module install
Signaling message
to install module
Signaling message
forwarded to next hop
Data packets processed
by service modules

## Slide 17: NetServ current prototype
NSLP
daemon
GIST
daemon
NetServ
Controller
Linux kernel
Transport layer
Service
Container
Service
Container
Service
Container
OSGi
OSGi
OSGi
Packet
processing
modules
Server
modules
OSGi control sockets
Client-
Server
data
packets
Forwarded
data packets
Signaling
packets
iptables
command
Netfilter
NFQUEUE #2
NFQUEUE #1
Raw
socket
UNIX
socket
NetServ Control
Protocol (TCP)

## Slide 18
NFQUEUE
Linux kernel
Building block layer
Library modules
System modules
Wrappers for native
functions
Packet processing
application module 1
Server
application
module 1
Command from NetServ controller
JVM
Client-server data packets
dispatcher.addPktProcessor(this);
Forwarded data
packets
Packet dispatcher
…
Servlet API
Xuggler
XML-RPC
…
…
Packet processing
application module 2
OSGi
libnetfilter_queue

## Slide 19: Background: What’s OSGi?
“Dynamic module system for Java”
  originally for set top boxes
Why OSGi? Why not just JAR files?
  More than just JAR files; much richer encapsulation, metadata in manifest
  Automatic dependency resolution
  Version management
  Provides systems services (logging, configuration, user authentication, device access, …)
  ~ Debian's apt-get or Apple's App Store methods of installation

## Slide 20: OSGi
Architecture
  Bundles: JAR files with manifest
  Services: Connects bundles
  Services Registry: Management of services
  Modules: Import/export interfaces for bundles
Possible to “wrap” existing Java apps and JARs
  Add additional manifest info to create OSGi bundle
  E.g.: Jetty web server now ships with OSGi manifest; now extensively used with OSGi containers and custom bundles
  For NetServ, we created a OSGi bundle for the Muffin HTTP proxy server
Image credit: Wikipedia

## Slide 21: OSGi
Many core frameworks
  Eclipse Equinox, Apache Felix, Knoplerfish
Real-world examples
  Eclipse IDE uses OSGi for plugin architecture
Mostly finds use in enterprise applications needing plug-in functionality
  IBM Websphere, SpringSource (now VMWare) dm server, Red Hat's Jboss, …

## Slide 22: Signaling

## Slide 23: Signaling
How to get code (pointers) into nodes?
Modalities:
  everywhere within a certain scope
  nodes matching characteristics (“all base stations”)
  along data path
can’t be manually installed

## Slide 24: NSIS-based on-path signaling
N1
N3
N2
NetServ repository
Signaling message is sent towards the destination rather than to a specific router

## Slide 25: NSIS architecture
Signaling application-specific functions
(packet filter, NAT setting, etc)
NSLP for QoS
NSLP for
NAT/firewall
GIST
(General Internet Signaling Transport)
Transport layer security
UDP
TCP
SCTP
DCCP
IP layer security
IP
NetServ NSLP
NTLP
GIST
API
NSLP
Control
plane for
signaling:
NSIS

## Slide 26: NSIS Signaling

## Slide 27: Design of NetServ Protocol 2
Only NSIS nodes with a running NetServ NSLP will process the protocol messages
Other nodes forward the packets transparently

## Slide 28: GIST and NetServ Protocol
NetServ Protocol runs on top of GIST
GIST provides hop by hop node discovery, peer association and message transport

## Slide 30: How does code get into nodes?
All nodes in (enterprise) network
gossip

## Slide 31: NetServ + OpenFlow

## Slide 32: Performance evaluation
Java packet processing overhead:
Overhead significant, but not prohibitive
Handles typical edge router traffic on modest PC hardware

## Slide 33: NetServ data path
Currently: Linux kernel
  Pass packets to user-level service container processes
  Use Netfilter queues
  Flexible – can modify, add, delete, store packets
  Problem:
  Slow Performances compared to hardware routers

## Slide 34: What is OpenFlow?
PC
Hardware Layer
Software Layer
Flow Table
MAC
src
MAC
dst
IP
Src
IP
Dst
TCP
sport
TCP
dport
Action
OpenFlow Firmware
*
*
5.6.7.8
*
*
*
port 1
port 4
port 3
port 2
port 1
1.2.3.4
5.6.7.8
PKT
Controller
OpenFlow Switch
IP dst: 5.6.7.8
OF
Protocol
PKT
1st packet
routing
following packets
routing

## Slide 35: What is OpenFlow?
OpenFlow = API for switches
Control how packets are forwarded
  not packet transformation
Operations implemented on (cheap) packet switch
  smaller or no control processor
  omits routing (BGP & OSPF), spanning tree, firewall, QoS, …
  move control functionality to general-purpose server(s)
Typically, centralized control
but: NetServ enables distributed control

## Slide 36: OpenFlow integration
Openflow controller as a NetServ service module
  Runs inside the OSGi Service Container
  Modified version of the Beacon OF Controller (Java)
  Listens for signaling commands through JSON-RPC (sent by NetServ Controller or external services)
  Sends commands to OF-enabled hardware (OpenFlow protocol)

## Slide 37: OpenFlow operation
OpenFlow Switch
subseq. pkts
dst: 10.0.0.1
Flow Table
MAC
src
MAC
dst
IP
src
IP
dst
TCP
sport
TCP
dport
Action
*
*
10.0.0.1
*
*
*
Output
port 1
OpenFlow
Controller
OpenFlow
Protocol
FlowMod
PacketIn
1st pkts
dst: 10.0.0.1
PKT
(4)
(1)
(5)
(3)
(2)
10.0.0.1
PKT
PKT
PKT
Notes: 1° Packet that must go to 10.0.0.1 arrives to the switch, but no flowtable entries matches it, so it goes to the OFC
The OFC decides the forwarding port for this packet according to the routing algorithm, and the packet arrives to the destination host
At the same time it writes a flowmod inside the flowtable, saying that this flow must be outputted to port 1
Following packets arrive to the switch, and they match a flowtable entry, so they are routed in hardware

## Slide 38
Data
OF Protocol
JSON-RPC
Processing Unit
(PU)
OF Switch
Other networks
OF Controller
NetServ SETUP packet arrives
Processing module installed
Add_filter
1° Packet arrives
Packet_IN
Flow Mod
Packet_IN
Flow Mod
Packet
processing time
1° Packet gets routed
Following Packets path
Packet processing
time
NetServ
Controller
Flow Mod
1
3
2
4
5
Notes: Proactive GIST filter
Processing module installed and add filter data structure inside OF controller
Packet header is matched to the services filtering rules inside the OFC, and if match, the packet is forwarder to the PU
The output packet is sent to the OFC another time, for the regular routing
Subsequent packets are forwarded in hardware

## Slide 39: NetServ/OpenFlow prototype
Flow Table
MAC
src
MAC
dst
IP
Src
IP
Dst
UDP
sport
UDP
dport
Action
OpenFlow Switch
2222
*
*
*
*
*
port 1
port 2
3333
2222
1.2.3.4
5.6.7.8
dd:ee:ff
aa:bb:cc
port 2
NetServ Host
NetServ Controller
OSGi Container
OpenFlow Controller
UDPEcho
service
port 3
port 1
Forwarded to next hop
Signaling packet:
Install UDPEcho service.
Filter UDP
Port 2222
      Linux Kernel
OF Protocol
Filter Added
PKT
Host 2
5.6.7.8
Host 1
1.2.3.4
JSON
RPC

## Slide 40
OpenFlow Switch
PKT
1st packet
Dst: 10.0.0.1
Subsequent packets
Dst: 10.0.0.1
Flow Table
MAC
src
MAC
dst
IP
src
IP
dst
UDP
sport
UDP
dport
Action
2222
*
10.0.0.1
*
33:44
11:22
Output
port 2
OpenFlow Controller
OSGi
NetServ
Controller
NetServ Node
Packet
Processing
Module
Linux kernel
SETUP signaling message
2222
*
10.0.0.1
*
55:66
33:44
Output
port 1
Port 1
Port 2
PKT
PKT
PKT
(1)
(5)
(3)
(4)
(8)
(2)
(6)
(9)
(7)
10.0.0.1
Notes: Gist proactive filter (non è visualizzato,c’è solo nell’altra figura.)
NSIS signaling packet arrives. Netserv controller sends a JSON-RPC command to install a filter inside OFC. In addition it also install the packet processing service
1° Packet arrives to the switch, but no flowtable entries matches it, so it goes to the OFC. The OFC matches the flow with its netserv modules filters and forward the packet to the processing service. In addition the OFC adds a flow entry to the flow table
The processed packet go from the PU to the switch, and the switch asks another time to the controller what to do. The packet is forwarded using normal routing algorithm to the destination. Another flow entry is added to the flow table.
Following packets match both the flow entries, so they are forwarded in hardware

## Slide 41: DoS experiment on GENI
Autonomic network management
  Self protecting from a SIP DoS attack (similar to NetServ Overload demo)
  Use of IP flow-based IDS (netmonitor service)
  Use of rate limiter (throttle service)

## Slide 42: DoS experiment on GENI
Victim Server
Attack Sources
Attack Sources
Attack Sources
DoS Attack
NetServ NS2
DoS Attack
OpenFlow-enabled NerServ Nodes (PUs)
NAME + OFC
PU1
PU2
PU3
NetServ NS3
OpenFlow
Controller
OSGi
NetServ
Controller
NetServ Node
NAME
OpenFlow Switch
Net
monitor
OSGi
NetServ
Controller
NetServ Node
Net
monitor
OSGi
NetServ
Controller
NetServ Node
Net
monitor
OSGi
NetServ
Controller
NetServ Node
Throttle
Throttle
OSGi
NetServ
Controller
NetServ Node (NS1)
Linux Kernel
DoS Attack
SIP messages
Replicated packets
SIP messages NS1 node OF switch
OF switch SIP server
        PU1 (replicating)

## Slide 43: DoS experiment on GENI
Victim Server
Attack Sources
Attack Sources
Attack Sources
DoS Attack
NetServ NS2
DoS Attack
OpenFlow-enabled NerServ Nodes (PUs)
NAME + OFC
PU1
PU2
PU3
NetServ NS3
OpenFlow
Controller
OSGi
NetServ
Controller
NetServ Node
NAME
OpenFlow Switch
Net
monitor
OSGi
NetServ
Controller
NetServ Node
Net
monitor
OSGi
NetServ
Controller
NetServ Node
Net
monitor
OSGi
NetServ
Controller
NetServ Node
Throttle
Throttle
OSGi
NetServ
Controller
NetServ Node (NS1)
Linux Kernel
DoS Attack
SIP messages
Replicated packets
Attack arrives
Net monitor NAME (attack detected) Throttle @ NS1

## Slide 44: DoS experiment on GENI
Victim Server
Attack Sources
Attack Sources
Attack Sources
DoS Attack
NetServ NS2
DoS Attack
OpenFlow-enabled NerServ Nodes (PUs)
NAME + OFC
PU1
PU2
PU3
NetServ NS3
OpenFlow
Controller
OSGi
NetServ
Controller
NetServ Node
NAME
OpenFlow Switch
Net
monitor
OSGi
NetServ
Controller
NetServ Node
Net
monitor
OSGi
NetServ
Controller
NetServ Node
Net
monitor
OSGi
NetServ
Controller
NetServ Node
Throttle
Throttle
OSGi
NetServ
Controller
NetServ Node (NS1)
Linux Kernel
DoS Attack
Throttle
Throttle
SIP messages
Replicated packets
Attack increases
NAME (to prevent PU1 overload) Net monitor@PU2-PU3
NAME Throttle@NS2-NS3

## Slide 45: OF Controller for the NetServ/OpenFlow Node
Handle multiple Processing Units (WIP)
  Control NetServ nodes attached to an OF switch as PUs (no OFC runs inside of it)
  Parallel packet processing
  Splitting packet flow through several PUs
OpenFlow-enabled NerServ Nodes (PUs)
NetServ
OpenFlow Controller
PU1
PU2
PU3
OpenFlow Switch
OpenFlow Switch
Other networks
Other networks
Flow Split method:
Not possible with the current OFPv1.1 (will be with v1.2)
Current implementation replicate the flow to all PUs. Every PU drops unwanted packets (using netfilter u32 matching module)

## Slide 46
OpenFlow Controller
OSGi
NetServ
Controller
NetServ Node
NetServ
Controller
NetServ
Controller
NetServ Node
NetServ
Controller
NetServ Node
Signaling packets
OpenFlow Switch
First packet of a flow
Subsequent packets
NetServ Node
Packet
Processing
Module
OSGi
Packet
Processing
Module
OSGi
Packet
Processing
Module
OSGi

## Slide 47: Future improvements Processing optimized architecture
Victim Server
Attack Sources
Attack Sources
Attack Sources
DoS Attack
NetServ NS2
DoS Attack
OpenFlow-enabled NerServ Nodes (PUs)
NAME + OFC
PU1
PU2
PU3
NetServ NS3
OpenFlow
Controller
OSGi
NetServ
Controller
NetServ Node
NAME
OpenFlow Switch
Flow
based
IDS
OSGi
NetServ
Controller
NetServ Node
Flow
based
IDS
OSGi
NetServ
Controller
NetServ Node
Flow
based
IDS
OSGi
NetServ
Controller
NetServ Node
DPI
OpenFlow Switch
DPI
OSGi
NetServ
Controller
NetServ Node (NS1)
Linux Kernel
Packets inspected by DPI module deployed in NS1
Packets inspected by PU3
DoS Attack
Packets forwarded only by NS1 and VLAN tagged

## Slide 48: NetServ applications

## Slide 49: Application: ActiveCDN

## Slide 50: Application: Media relay
Standard media relay
  Required due to NAT
  Out-of-path
  Inefficient and Costly
NetServ media relay
  Closer to users
  Improved call quality
  Reduced cost for ITSP

## Slide 51: Application: Keep-alive responder
NAT Keep-alive responder off
  UA behind NAT must send keep-alive messages
  Major bottleneck for SIP server
NAT Keep-alive responder on
  Module responds on behalf of SIP server
  No traffic to server

## Slide 52: Application: Overload control
NetServ Module
Controlled by SIP server
Throttles incoming traffic
Randomized traffic rejection
SIP Server
Installs NetServ module on demand
Controls all NetServ modules
Real-time feedback to modules

## Slide 53: ActiveCDN

## Slide 54: Content Distribution Networks
Distributes content requests from user
  To (hopefully) nearest node in a system of nodes that can serve the content
Preferred method for content providers to host content
  Content provider can build/maintain its own CDN
  More likely: use an ASP’s CDN and host content there
Content requests are re-routed to the nearest server

## Slide 55: CDN Providers and Research
  CDN service providers
    Established players: Akamai, Edgecast, Amazon CloudFront
    New entrants: service providers (AT&T), web hosting companies (The Planet)
    Self-hosting: YouTube (used Limelight CDN before Google acquisition)
    Commoditized services…
Pageviews/minute handled by Akamai

## Slide 56: What do CDNs do today?
Very good at:
  Monitoring network traffic, latency, etc.
    Proprietary systems, maybe tie-up with network service providers
    In 2009: Akamai was sending 5 million traceroute messages on the Internet every 5 minutes to measure latency
  Achieving economies of scale through deploying large, homogenous nodes …
  … at strategic locations around the world
    K-median and Facility Location problems: well studied
  Detecting closest CDN nodes for incoming request
  Re-directing user to that node
    Through name-based redirection (DNS): Akamai, most others
    Message-based redirection (HTTP redirect): Youtube

## Slide 57: ActiveCDN and NetServ
Allow content providers to dynamically deploy in-network CDN nodes
  “flow through caching”
Determine optimal placement of nodes dynamically
Deploy custom functionality
  user demographics
  user QoE
 aggregate node capabilities across wide variety of operators
   need broker functionality (future work)

## Slide 58
End user
NetServ
router
NetServ
router
Regular
router
Regular
router
Content
provider
(1) User requests http://youtube.com/getvideo?id=foo
(2) YouTube sends video file
(4) NetServ-enabled routers download the module
(3) YouTube sends on-path signal to deploy ActiveCDN module
(5) NetServ routers notify that the module is active
(6) Another user requests http://youtube.com/getvideo?id=foo
(7) YouTube redirects user to nearest NetServ node running ActiveCDN
(8) User requests http://netserv1.verizon.com/youtube/foo.flv
(9) NetServ router relays the video content, while fetching the file and caching it
N
N

## Slide 59: ActiveCDN Demo – watermarking
Content
server
User 1
N
NetServ node
User 2
Content
server
User 1
N
NetServ node
Content
server
User 1
Watermark
Step 1
Step 2
Step 3
Screen 1
Screen 2
Screen 3
User 1 downloads and watches video content from provider
Content server sends on-path signal to install ActiveCDN module into NetServ router
User 2’s request gets redirected to NetServ router, which serves processed video

## Slide 60: ActiveCDN screenshots
NetServ router:
Installation of module
Stream/download content
Process content
Serve to end user
Client browser
First request: served by content server
Second request: redirected to NetServ node
Third request: processed/cached content

## Slide 61: Some background info
Watermarking
  Done using Xuggler: Java library with native hooks into FFMPEG, LAME audio library, etc.
Weather information
  Using XML feed from weather.gov, which takes latitude/longitude info and returns weather information
  Use Java’s XML library and Xpath to get relevant data from feed
  MaxMind GeoIP library which is great for public IP geo-location,
    For GEC9: all IP addresses in demo use private Ips
    Used a “translation table” to map private IPs to real latitude/longitude

## Slide 62: ActiveCDN Demo – module migration
Screen 2:
NetServ nodes popping up
In the eastern region
Screen 3:
Web traffic generated from eastern PlanetLab nodes
Screen 2:
(Flickering) NetServ nodes migrating to the wild west!
Screen 1:
Web traffic generated from western PlanetLab nodes
Step 1
Step 2
Tell:
PlanetLab nodes run scripts fetching small files from the web server
ActiveCDN modules with short TTL keep getting installed and removed
PlanetLab scripts are choreographed to make modules migrate westward!
Idea: that dynamic traffic patterns can be efficiently handled by ActiveCDN

## Slide 63: Content-Centric Networking
Concept: we are moving away from host-centric networking towards content-centric networking
Most prominent work: CCNx from Xerox PARC
Idea: issue Interest packets, get Data responses, content routing handled in network

## Slide 64: CCNxServ: Services in CCNx
CCNx is great for static content
  But how about dynamic services?
CCNxServ: services for CCNx
  Runs on top of “pure” CCNx stack
    As opposed to related work (SCN, SoCCeR) that modifies CCNx stack
  Uses dynamic loading (OSGi/NetServ) in combination with CCNx naming scheme
  Service modules retrieved through CCNx

## Slide 65: Services in CCNx
CCNx
NetServ
Receives service request
Signals netserv-controller
Installs NetServ
module
Service module invoked
1
3
4
5
Returns processed content
6
Fetches content and services
2
Content goes to CCNx space
7

## Slide 66: Services in CCNx - II
(Top) ccngetfile getting the CCNx content with service specified, and saving to local folder.
(Right) VLC player playing the resulting video. Note the weather watermark at the bottom right.

## Slide 67: Conclusion

## Slide 68: Ongoing & future work
NetServ on other devices:
  commercial router (JUNOS)
  home router
  WiMAX base station
Authorization for packet access using RPKI
Create standard APIs for service modules that wants to interact with the data path
  either the linux kernel or an OF switch
Extend NetServ signaling syntax in order to expose OF switch features
Utilize NetFPGA card as hardware processing unit
Internet multicast using NetServ

## Slide 69: Conclusion
Universal programmability
  across protocol stack
  across user type
  across modality (read, modify, serve)
  across intensity – from “every packet” to flow or management-only
Integrated approach
  protection & isolation
  software installation & versioning
  http://www.cs.columbia.edu/irt/project/netserv/

## Slide 70: Columbia University NetServ team
Salman Baset
Roberto Francescangeli (signaling)
Jan Janak (software engineering assistance)
Michael Kester (measurements)
Eric Liu (measurements)
Jae Woo Lee (architect, infrastructure)
Emanuele Maccherani (OpenFlow)
Wonsang Song
Suman Srinivasan (applications, CDNs, CCNx)
Henning Schulzrinne (PI)