## Slide 1: Will the Last Phone User Please Turn Off the Dial Tone?
        Henning Schulzrinne (Columbia University)

## Slide 2: Overview
The PSTN is dying
  *1876 ✞2018?
… but real-time communications continues
Issues:
  numbering
  public policy issues
    911 & location
Open Internet as enabler of competitive VoIP

## Slide 3: The fall of the PSTN empire
mobile replacement
SIP trunking
VoLTE
IMS
VoIP over DSL
2011
2015
2018
2020+
more text
less voice

## Slide 4: Four separate components
?

## Slide 5: Real-time: voice  non-voice
1950—2005: real-time ≡voice
Now: real-time = web interaction + text + voice
Displacement:
  teenage 2-hour chat  Facebook, IM
  coordination & transaction calls  web
    schedule appointments, travel agency, airline, …
  business calls  messaging
  “I’m heading home”  Google Latitude

## Slide 6: Time of transition
Old | New
IPv4 | IPv6
circuit-switched voice | VoIP + text
separate mobile voice & data | LTE + LTE-VoIP
911, 112 | NG911, NG112
digital cable (QAM) | IPTV
analog & digital radio | Pandora, Internet radio, satellite radio
credit cards, keys | NFC
end system, peers | client-server v2 aka cloud
all the energy into transition  little new technology

## Slide 7: Telecom revenue

## Slide 8: Cell ownership, 2004-2011
4/28/2011
8
Mobile Phone Trends
Chart: 
| Fall 2004 | Winter 2005 | Spring 2006 | Fall 2007 | Winter 2008 | Spring 2008 | Summer 2008 | Winter 2008 | Spring 2009 | Fall 2009 | Winter 2010 | Spring 2010 | Fall 2010 | Winter 2010
 | 0.65 | 0.66 | 0.73 | 0.78 | 0.77 | 0.78 | 0.82 | 0.84 | 0.85 | 0.84 | 0.8 | 0.82 | 0.85 | 0.82

## Slide 9: Cell ownership vs. other devices
4/28/2011
9
Mobile Phone Trends

## Slide 10: Mobile-only households and demographics (CDC data)
4/28/2011
10
Mobile Phone Trends
High Wireless Substitution:
Young adults (esp. those ages 24-29)
Renters
Low income (poverty line or below)
Latino/Hispanic

## Slide 11: Household spending on telecom
 new services must displace old services
Notes: Bernstein Research
Source: Bureau of Economic Analysis

## Slide 12: Wireless + Internet replace voice

## Slide 13: Telephone Social Policies
Universal service (Lifeline, high cost, …) | Necessary to function (call doctor, call school, …)
Basic service price regulation | Ensure widespread availability
911 | Report emergencies for self and others
Power backup | Ensure emergency communications
Outage reporting | Ensure reliability
Lawful intercept (CALEA) | Phone as tool for criminals
Disability access (ringers, HAC) | Ensure participation in society
CPNI | Phone as private medium

## Slide 14: Now: the Internet
Universal service | USF reform? (Connect America Fund)
Price | Unregulated, competition?
911 | NG911
Power backup | Cell phones? Responsibility moves to household (UPS)
Outage reporting | FCC Part 4 NPRM multiple access modes
Lawful intercept (CALEA) | Encryption?
Disability access | Twenty-First Century Communications and Video Accessibility Act of 2010?
CPNI | Uncertain privacy rights

## Slide 15: It’s just a number
Number | Type | Problem
201 555 1212 | E.164 | same-geographic different dial plans (1/no 1, area code or not) text may or may not work
#250, #77, *677 | voice short code | mobile only, but not all no SMS
12345 | SMS short code | SMS only country unclear
211, 311, 411, 911 | N11 codes | Distinct call routing mechanism Mostly voice-only May not work for VoIP
800, 855, 866, 877, 888 | toll free | not toll free for cell phone may not work internationally
900 | premium | voice only unpredictable cost

## Slide 16: Numbers
Administered in blocks by NANPA
  funded by carriers: $5.9M/year
Separate processes for each number type
  Regular E.164 numbers by 1k blocks
Complicated LNP and porting technology
  often takes several phone calls to provider
  takes, at best, several hours
  limited wireline ⇔ wireless porting
  limited wireline out-of-area porting

## Slide 17: Numbers vs. DNS
 | Phone # | DNS
Country-specific | mostly | optional
# of devices / name | 1 (except Google Voice) | any
# names /device | 1 for mobile | any
ownership | carrier, but portability unclear (800#) | property, with trademark restrictions
porting | complex, often manual wireline-to-wireless may not work | about one hour (DNS cache)
delegation | companies (number range) | anybody
identity information | wireline, billing name only | WHOIS data (spotty)
Notes: http://www.nanpa.com/reports/faq.html#g1

## Slide 18: Future numbers
Should numbers become personal property?
  separate service & number
  simplify number portability
Divorce device & number
  any-to-any, dynamic mapping
Separate user identity & number

## Slide 19: Cost issues
Chart: Monthly expenditure
| Phone | Dial-up Internet | Broadband | Cell phone
Monthly | 39 | 23 | 41 | 4.5
VoIP: $8-$25/month
Notes: FCC Report #1
http://www.census.gov/compendia/statab/2011/tables/11s1147.pdf

## Slide 20: The curse of fixed costs
Subscribers decrease  fewer subscribers for same fixed costs
But: switching equipment is written off

## Slide 21: Available access speeds
20 Mb/s
10 Mb/s
5 Mb/s
2 Mb/s
1 Mb/s
10%
60%
90%
97%
100%
avg. sustained
throughput
of households
marginal VOIP

## Slide 22: Legacy applications
“Dry” copper loop
Alarm systems
   transition to cellular (can’t cut wire)
ATMs  wireless, DSL

## Slide 23: 911
Transition to NG911 underway
Main issues:
  Indoor location for wireless
    location accuracy of 50/150m not sufficient
    need apartment-level accuracy, including floor
    Civic (Apt. 9C, 5 W Glebe), not geo
  Avoid protracted transition
    maintain two infrastructures for decade+?
  National infrastructure LoST hierarchy

## Slide 24: COLR (Carrier of Last Resort)
Must offer service in covered area
No direct equivalent for IP
 USF

## Slide 25: A layered model for regulation Service layers, not technology
TCP / IP
Applications
Enhanced
Services
Unregulated
Basic Service
Regulated
1980
Applications
ISPs
Dial Up
Notes: Another way of looking at this.
Examples of title II regulations: interconnection, universal service, access charges, privacy, filing, disabled access, interoperability, disclosure, CALEA, and anti-discrimination requirements.
When the FCC says that the Internet is unregulated, this is largely what it is talking about. You, as ISPs, are not certified by the FCC. You do not have your rates approved by the FCC. And you have no obligations like interconnection or universal service.
I might note that the Telecom Act of 1996 introduced a new legal term: Information service providers. This means essentially the same thing as “Enhanced Service Providers.”
The layers are fully separate.
They are provisioned by separate service providers.
I can point to the the different equipment. Different equipment services the different layers.
And of course, the different layers represent separate (though dependent) markets.

## Slide 26: Voice, transport and access
Apps
IP
Voice
Transport
Apps
IP
Voice
Transport
Voice
Transport
Basic
Enhanced
1880s-1980s
1980s-2000s
Now - future
Notes: Bob Cannon

## Slide 27: Evolution of competition
Assumption: competition desirable and efficient
Theodore Vail AT&T
CLEC
ILEC
ILEC
ILEC/CMRS
CATV
OTT
VoIP
1876
1930
1984
1996
2003
2010-
transport
voice
CLEC
OTT
VoIP

## Slide 28: 2 Internet futures
content and applications
fiber or copper loop
(“Homes with tails”)
IP
Google
Chatroulette
Level 3
RCN
content production (*)
content distribution
CDN
broadband access
local infrastructure
regional and national backbone
vs.
AT&T
Comcast/NBC (*)
Verizon
Notes: see old MCI functional separation

## Slide 29: Scenario 1: max. competition
applications
(Netflix, Pandora, your blog)
OS
(Windows Server, Linux, MacOS)
data centers
(Equinix, Amazon, …)
wide area network
(Qwest, Sprint, VZ, TeliaSonera, NTT, DTAG, Level 3, AT&T)
web browser
(Firefox, IE, Chrome, …)
OS
(Windows, Android, MacOS)
system platform
(Intel, ARM, …)
ISP
(competing)
fiber, radio
(regulated monopoly)
conduit
(public)
content & application providers
consumers

## Slide 30: Scenario 2: vertically integrated
classical Internet
(web)
interactive multimedia (IMS)
video
(live, VOD)
incumbent operator (e.g., AT&T, Verizon)
cable company (sometimes)
100 Mb/s to consumer
4 Mb/s
small operators
Google
Internet

## Slide 31: Eyeball ISPs: 2001 vs. 2010
Notes: AT&T: http://www.everythingdsl.com/att/: 7.8 M; http://www.att.com/Investor/Financial/Earning_Info/docs/Supp_IB_4Q10.xls: 14.3M
Comcast: http://files.shareholder.com/downloads/CMCSA/1209582425x0x441905/918e0cf1-4a90-4575-9535-0c51452950da/Comcast_Q4Trending_2.15.11.pdf: 16.988
TW: http://phx.corporate-ir.net/External.File?item=UGFyZW50SUQ9NzkxMTJ8Q2hpbGRJRD0tMXxUeXBlPTM=&t=1: 9.469 + 0.349 = 9.803M
VZ: http://investor.verizon.com/financial/annual/2010/mda03_02.html: 8.392 BB + 4.082 FiOS = 12.474M
Windstream: http://www.snl.com/Cache/10782778.pdf?O=3&IID=4121400&OSID=9&FID=10782778 = 1.3M
Charter: http://phx.corporate-ir.net/External.File?item=UGFyZW50SUQ9ODM2ODl8Q2hpbGRJRD0tMXxUeXBlPTM=&t=1 = 3.24M
Qwest: http://investor.qwest.com/download/4Q.2010.Q.Profile.FINAL.pdf = 2.9 M
Cablevision: http://phx.corporate-ir.net/External.File?item=UGFyZW50SUQ9ODE3NjZ8Q2hpbGRJRD0tMXxUeXBlPTM=&t=1 = 2.892M
CenturyLink: http://phx.corporate-ir.net/External.File?item=UGFyZW50SUQ9NDEzODgyfENoaWxkSUQ9NDI1MjcxfFR5cGU9MQ==&t=1 = 2.394M
Mediacom: 838,000

## Slide 32: What is network neutrality?
“The principle advocates no restrictions by Internet service providers and governments on content, sites, platforms, the kinds of equipment that may be attached, and the modes of communication.” (Wikipedia)
2005 FCC statement:
  “access the lawful Internet content of their choice.
  run applications and use services of their choice, subject to the needs of law enforcement.
  connect their choice of legal devices that do not harm the network.
  competition among network providers, application and service providers, and content providers.”
= Any lawful content, any lawful application, any lawful device, any provider

## Slide 33: Two views
Open Internet advocates
Free market advocates
no prioritization
flat rates
all networks
no real problem
allow any business arrangement
“it’s my network”
use anti-monopoly laws if needed

## Slide 34: Why?
Civic considerations
  freedom to read (passive)
  freedom to discuss & create (active)
Economic opportunity
  edge economy >> telecom economy
    Telecom revenue (US): $330B
    Content, etc. not that large, however
      Google: $8.44B
    others that depend on ability to provide services
  content, application, service providers
Technical motivation
  avoid network fragmentation
  reduce work-around complexity

## Slide 35: How to be non-neutral
deep packet inspection
block Skype
block transport protocol
block UDP & TCP ports
insert TCP RST
block IP addresses
QoS discrimination
application
transport
network
all affect
VoIP

## Slide 36: Are these neutrality issues?
Redirect DNS NXDOMAIN to ISP web site
Content translation
  e.g., reduce image resolution for cellular data
Blocking transport protocols other than UDP + TCP
Prohibit web servers
Reset DSCP (ToS bits)
Not allow IPv6
3GPP: only make non-BE available to carrier

## Slide 37: Some high-profile cases
Madison River (2005)
  DSL provider blocked SIP ports
  fined $15,000 by FCC
Comcast (late 2007)
  insert TCP RST into BitTorrent traffic
  later overturned on appeal in DC Circuit Court
RCN (2009): P2P
Various mobile operators
Comcast vs. Level 3 (2010, in dispute)
  Level-3
Notes: http://hraunfoss.fcc.gov/edocs_public/attachmatch/DA-05-543A1.pdf
http://www.zeropaid.com/news/88573/comcast-prevails-in-bittorrent-throttling-case/

## Slide 38: Network neutrality & freedom of speech
Applies only to U.S. government, not private entities
  Example: soap box in city park vs. mall
  private vs. public universities
Freedom to speak + no forced speech
  demise of “fairness doctrine” (2011 final)
1st amendment: Congress shall make no law abridging the freedom of speech

## Slide 39: Network transparency
RFC 1958: “Architectural Principles of the Internet”
However, in very general terms, the community believes that the goal is connectivity, the tool is the Internet Protocol, and the intelligence is end to end rather than hidden in the network.
RFC 2275: “Internet Transparency”
  NATs, firewalls, ALGs, relays, proxies, split DNS
RFC 3724: “The Rise of the Middle and the Future of End-to-End: Reflections on the Evolution of the Internet Architecture”
RFC 4924: “Reflections on Internet Transparency”
  A network that does not filter or transform the data that it carries may be said to be "transparent" or "oblivious" to the content of packets. Networks that provide oblivious transport enable the deployment of new services without requiring changes to the core. It is this flexibility that is perhaps both the Internet's most essential characteristic as well as one of the most important contributors to its success.

## Slide 40: Network transparency and neutrality
neutral
transparent
QoS discrimination
pay for priority
block protocol features

## Slide 41: Means, motive and opportunity
Political motivation
  suppress undesirable opinion
    e.g., union web site, abortion SMS
Economic advantage
  prevent competition in related services
    e.g., VoIP or over-the-top VoD
  leverage pricing power
    OTT content provider has to offer service to everyone
  market segmentation
    consumer vs. business customers
Non-tariff barriers
  e.g., special (undocumented) APIs
Notes: http://en.wikipedia.org/wiki/Means,_motive,_and_opportunity

## Slide 42: Open Internet FCC history
2004: “four freedoms” (Powell)
2005: Internet policy statement (Martin)
9/2009: Genachowski speech
  non-discrimination, transparency
12/2009/: NPRM
9/2010: PN
12/2010: Open Internet rules
10,000+ short comments, hundreds of long comments
Notes: http://www.openinternet.gov/
http://www.openinternet.gov/read-speech.html

## Slide 43: Who is covered?
Broadband Internet Access Service = A mass-market retail service by wire or radio that provides the capability to transmit data to and receive data from all or substantially all Internet endpoints, including any capabilities that are incidental to and enable the operation of the communications service, but excluding dial-up Internet access service. This term also encompasses any service that the Commission finds to be providing a functional equivalent of the service described in the previous sentence, or that is used to evade the protections set forth in this Part.
excludes
dial-up
coffee shops, bookstores, airlines (premise operators)
“edge providers”: CDNs, search engines, …

## Slide 44: Principles
Transparency. Fixed and mobile broadband providers must disclose the network management practices, performance characteristics, and terms and conditions of their broadband services;
No blocking. Fixed broadband providers may not block lawful content, applications, services, or non-harmful devices; mobile broadband providers may not block lawful websites, or block applications that compete with their voice or video telephony services
No unreasonable discrimination. Fixed broadband providers may not unreasonably discriminate in transmitting lawful network traffic.

## Slide 45: FCC Open Internet order
 | Wired | Wireless
Disclosure | yes | yes
Non-blocking | every protocol | “web”, “VoIP”
Non-discrimination | reasonable network management | “monitor”

## Slide 46: FCC Open Internet order
CFR text: 1 page
Main content: 85 pages
  with 500 footnotes
Regulatory Flexibility Analysis
5 commissioner statements: 60 pages

## Slide 47: Some corner cases
Parental protection
  user (paying subscriber…) choice
KosherNet
Spam
  would only affect IP-level blocking
DOS
  classified as unwanted traffic
Notes: http://www.koshernet.com/

## Slide 48: 47 CFR 8
§ 8.1 Purpose.
  The purpose of this Part is to preserve the Internet as an open platform enabling consumer choice, freedom of expression, end-user control, competition, and the freedom to innovate without permission.
§ 8.3 Transparency.
  A person engaged in the provision of broadband Internet access service shall publicly disclose accurate information regarding the network management practices, performance, and commercial terms of its broadband Internet access services sufficient for consumers to make informed choices regarding use of such services and for content, application, service, and device providers to develop, market, and maintain Internet offerings.

## Slide 49: Disclosure (Transparency) – Network Practices
Congestion management: congestion management practices; types of traffic; purposes; practices’ effects on end users’ experience; criteria used in practices, such as indicators of congestion that trigger a practice, and the typical frequency of congestion; usage limits and the consequences of exceeding them; and references to engineering standards, where appropriate.
Application-Specific Behavior
Device Attachment Rules
Security

## Slide 50: Disclosure (Transparency) – Performance
Service description: A general description of the service, including the service technology, expected and actual access speed and latency, and the suitability of the service for real-time applications.
Impact of specialized services: If applicable, what specialized services, if any, are offered to end users, and whether and how any specialized services may affect the last-mile capacity available for, and the performance of, broadband Internet access service.

## Slide 51: Disclosure (Transparency) – Commercial Terms
Pricing: For example, monthly prices, usage-based fees, and fees for early termination or additional network services.
Privacy Policies: For example, whether network management practices entail inspection of network traffic, and whether traffic information is stored, provided to third parties, or used by the carrier for non-network management purposes.
Redress Options: Practices for resolving end-user and edge provider complaints and questions.

## Slide 52: Conclusion
Multi-pronged attack on PSTN
  transition to mobile for consumers
  cable VoIP
  less voice, more text
  Ethernet phones + IP PBX + SIP trunking for business
Separate PSTN vs. copper infrastructure
Challenges mostly in retaining PSTN policy goals
  reliability, affordability, accessibility, ubiquity