## Slide 1
SECE: Sense Everything, Control Everything
Prototype Sensor and Actuator
I
R
T
Internet Real Time Lab
Presented by Hyunwoo Nam

## Slide 2
I
R
T
Internet Real Time Lab
Presence Server
GW
SECE
B2BUA
PUBLISH
PIDF-LO
SUB/NOT ..
monitor energy
usage
Geocoding
travel time
control appliances
update SNs, SMS, email
call state
Alice  a@b.com,
+1 212 555 1234
edit scripts
RFID
The big picture
“SECE allows non-technical users to create service that combine Communication,
Calendaring, Location and Device in the physical world. ”
“Prototype sensor/actuator for devices that are not IP-capable”

## Slide 3
I
R
T
Internet Real Time Lab
The Arduino
Microcontroller: ATmega328
Operating voltage: 5v
Flash memory: 32KB
SRAM: 2KB
EEPROM: 1KB
• $21
• Programming Environment
(C language) or AVR-Studio
• Easy to start with
• Phidgets, X10, Zigbee available
• Huge community
• Software development on
Mac OS-X and Windows
• How to connect to the Internet?
“ Arduino Ethernet shield (stackable) ”
TCP/IP stack built in

## Slide 4
I
R
T
Internet Real Time Lab
Appliances controlled by Arduino
Arduino
X10 PLC Controller
X10 Lamp Module
RJ11 Cable
X10 power line signal
USB/Serial
Arduino IDE
“ Control Lamp using Arduino ”

## Slide 5
I
R
T
Internet Real Time Lab
Appliances controlled by Arduino (continue)
“ Control IR Electronics ”
-SAMSUNG:
TV, AUDIO..
-LG:
TV, PROJECTOR..
SECE users
The Internet
Arduino
IR LED
IR Electronics
SECE server
LG
- TV_ON:0x8A75F20D
- TV_OFF:0x5A63B203
SAMSUNG
- AUDIO_ON:0x8A75F20D
AUDIO_OFF:0x5A63B203
..
IR standard table
0x8A75F20D
0x8A75F20D

## Slide 6
I
R
T
Internet Real Time Lab
Communication with SECE server
DHCP
DNS
Get IP address
Get SECE server IP
address using Hostname
TCP/IP
Webscoket handshake via HTTP
User login
POST /lamp?v=100 HTTP/1.1
Auth.token
Send X10 Signal
LAMP
ARDUINO
SECE SERVER
SECE USER
OAuth Token
Turn on lamp
Update DNS
Turn on Arduino
&& Button pressed
Stored in EEPROM
JSON Format

## Slide 7
I
R
T
Internet Real Time Lab
Conclusion
• Implemented a set of Arduino libraries for SECE project
• Can control Arduino from SECE server over the Internet
• Can control other commercial modules (Phidgets/X10/Infrared) via Arduino
• Can communicate with Zigbee modules for location tracking system
• Implement OAuth communication between Arduino and SECE server
• Discover individual sensors from Arduino - figuring out what types of sensors are connected to a particular Arduino and naming
them • Setup permissions for individual sensors
- public, private, shared within a group, etc..
Achievements
Future works