## Slide 1: Cheaper, Faster, Safer: Research and Public Policy for the Internet
Henning Schulzrinne
FCC & Columbia University
Any opinions are those of the author and do not necessarily reflect the views or policies
of Columbia University or the FCC.
with slides by Julie Knapp, Walter Johnston, Karen Peltz-Strauss, and others

## Slide 2: Overview
Telecom regulation (in the US)
Regulation as technology enabler
Case studies:
  Open Internet
  Spectrum
  Network measurements
  Access for people with disabilities
  PSTN transition
Challenges for research

## Slide 3: Laws & regulation as technology enabler
Classical regulatory goals
  market failures
  consumer protection (e.g., bill shock, robocalls)
  safety (e.g., RF limits)
  universal availability (geography, income, disability)
Spreading technology
  make mandatory  scale, ecosystems
  new uses

## Slide 4: Examples
Part 15 (“unlicensed”)
  since 1938
  major revision 1989
    higher frequencies
    unintentional, incidental, intentional
    authorized devices
   WiFi
GPS in cell phones
  E911 rules
   location-based services
Notes: http://papers.ssrn.com/sol3/papers.cfm?abstract_id=1120465

## Slide 5: Examples
Closed captioning
  initially, for Deaf and Hard of Hearing
  migrated to
    airports
    doctor’s offices
    sports bars
  enables text-based retrieval

## Slide 6: The US hierarchy of laws
Constitution
Commerce clause
Law
Telecom Act 1934 & 1996
47 CFR
Narrative
reasonable network management
Section 8: To regulate Commerce with foreign Nations, and among the several States, and with the Indian Tribes (1787)
SEC. 706. ADVANCED TELECOMMUNICATIONS INCENTIVES. (a) IN GENERAL- The Commission … shall encourage the deployment on a reasonable and timely basis of advanced telecommunications capability to all Americans (including, in particular, elementary and secondary schools and classrooms) by utilizing, in a manner consistent with the public interest, convenience, and necessity, …, or other regulating methods that remove barriers to infrastructure investment.

## Slide 7: Example: CFR 47
§ 15.5 General conditions of operation.
(a) Persons operating intentional or unintentional radiators shall not be deemed to have any vested or recognizable right to continued use of any given frequency by virtue of prior registration or certification of equipment, or, for power line carrier systems, on the basis of prior notification of use pursuant to §90.35(g) of this chapter.
(b) Operation of an intentional, unintentional, or incidental radiator is subject to the conditions that no harmful interference is caused and that interference must be accepted that may be caused by the operation of an authorized radio station, by another intentional or unintentional radiator, by industrial, scientific and medical (ISM) equipment, or by an incidental radiator.

## Slide 8: Selected 47 CFR
Part | Content
4 | Disruptions to Communications
5 | Experimental Radio Service
6 | Access to Telecommunications Service, Telecommunications Equipment and Customer Premises Equipment by Persons with Disabilities
9 | Interconnected Voice over Internet Protocol Services
15 | Radio Frequency Devices
20 | Commercial Mobile Radio Services (= cellular)
68 | Connection of Terminal Equipment to the Telephone Network
79 | Closed Captioning and Video Description of Video Programming
97 | Amateur Radio Services

## Slide 9: Telecom regulation
Local, state and federal
  local: CATV franchise agreements
  state: Public Utility Commission
    responsible for all utilities – gas, water, electricity, telephone
  federal: FCC, FTC (privacy), DOJ (monopoly)
Elsewhere: gov’t PTT  competition
  vs. US: regulated private monopolies
Based on 1934 Telecommunications Act
Amended in 1996
Divides the world into
  Title I: Telecommunications Services
  Title II: Broadcast Services
  Title III: Cable Services
  Title V: Obscenity and Violence

## Slide 10: Process
NOI
NPRM
R&O
Notice of Inquiry
Notice of Proposed Rule Making
Report & Order
comments & ex parte

## Slide 11: FCC
Independent federal agency
About 2,000 employees
Chairman (D)
4 Commissioners (2 D, 2 R)
Consumer and Governmental Affairs
Enforcement
International
Media
Public Safety & Homeland Security
Wireless Telecommunications
Wireline Competition

## Slide 12: Open Internet

## Slide 13: Two views
Open Internet advocates
Free market advocates
no prioritization
flat rates
all networks
no real problem
allow any business arrangement
“it’s my network”
use anti-monopoly laws if needed

## Slide 14: Why?
Civic considerations
  freedom to read (passive)
  freedom to discuss & create (active)
Economic opportunity
  edge economy >> telecom economy
    Telecom revenue (US): $330B
    Content, etc. not that large, however
      Google: $8.44B
    others that depend on ability to provide services
  content, application, service providers
Technical motivation
  avoid network fragmentation
  reduce work-around complexity

## Slide 15: How to be non-neutral
deep packet inspection
block Skype
block transport protocol
block ports
insert RST
block IP addresses
QoS discrimination
application
transport
network

## Slide 16: Some high-profile cases
Madison River (2005)
  DSL provider blocked SIP ports
  fined $15,000 by FCC
Comcast (late 2007)
  insert TCP RST into BitTorrent traffic
  later overturned on appeal in DC Circuit Court
RCN (2009): P2P
Various mobile operators
Comcast vs. Level 3 (2010, in dispute)
  Level-3
Notes: http://hraunfoss.fcc.gov/edocs_public/attachmatch/DA-05-543A1.pdf
http://www.zeropaid.com/news/88573/comcast-prevails-in-bittorrent-throttling-case/

## Slide 17: Which Internet are you connected to?
multicast
QoS
IPv6
IPv4
PIA
IPv4
DHCP
IPv4
NAT
port 80 + 25

## Slide 18: Cisco’s traffic prediction
Ambient video = nannycams, petcams, home security cams, and other persistent video streams
Notes: http://www.cisco.com/en/US/solutions/collateral/ns341/ns525/ns537/ns705/ns827/white_paper_c11-481360_ns827_Networking_Solutions_White_Paper.html

## Slide 19: Bandwidth costs
Amazon EC2
  $50 - $120/TB out, $0/TB in
CDN (Internet radio)
  $600/TB (2007)
  $10-30/TB (Q1 2012 – CDNpricing.com)
NetFlix (7 GB DVD)
  postage $0.70 round-trip  $100/TB
FedEx – 2 lb disk
  5 business days: $6.55
  Standard overnight: $43.68
  Barracuda disk: $91 - $116/TB
Notes: FedEx and EC2 prices as of 09/15/09
CDN: http://www.mindbranch.com/listing/product/R678-29.html
http://www.cdnpricing.com/

## Slide 20: The value of bits
Technologist: A bit is a bit is a bit
Economist: Some bits are more valuable than other bits
  e.g., $(email) >> $(video)
Application | Volume | Cost per unit | Cost / MB | Cost / TB
Voice (13 kb/s GSM) | 97.5 kB/minute | 10c | $1.02 | $1M
Mobile data | 5 GB | $40 | $0.008 | $8,000
MMS (pictures) | < 300 KB, avg. 50 kB | 25c | $5.00 | $5M
SMS | 160 B | 10c | $625 | $625M
Notes: T-Mobile 2010
AT&T data
http://www.nowsms.com/discus/messages/12/8500.html

## Slide 21: Principles
Transparency. Fixed and mobile broadband providers must disclose the network management practices, performance characteristics, and terms and conditions of their broadband services;
No blocking. Fixed broadband providers may not block lawful content, applications, services, or non-harmful devices; mobile broadband providers may not block lawful websites, or block applications that compete with their voice or video telephony services
No unreasonable discrimination. Fixed broadband providers may not unreasonably discriminate in transmitting lawful network traffic.

## Slide 22: Spectrum

## Slide 23: Overview
What’s the problem?
How much data & spectrum is there?
Can we make better use of it?
  Better technology
  General-purpose technology
  Better sharing in time and space

## Slide 24: You’ve heard the statistics…
Mobile phone subscriptions now top the number of people - - 328 million subscriptions
90% of us keep our mobile device within arms length 24 hours a day, 7 days a week
Smartphone sales have eclipsed PC sales
Mobile broadband is being adopted faster than any computing platform in history
A typical smartphone places 24 times as much demand on spectrum as an old feature phone
Tablets demand 120 times as much
Multiple experts expect that mobile demand for spectrum will increase more than 35x in the next few years (3,500%)
24/7
24X
120X

## Slide 25: Monthly fixed consumption
top 1% 
  49.7% of upstream traffic
  25% of downstream traffic
North America | Mean | Median | Mean : Median
Upstream | 4.5 GB | 600 MB | 7.33
Downstream | 18.6 GB | 6.0 GB | 3.06
Aggregate | 23.0 GB | 7.0 GB | 3.28
Europe | Mean | Median | Mean : Median
Upstream | 8.2 GB | 1.2 GB | 6.87
Downstream | 31.3 GB | 12.7 GB | 2.47
Aggregate | 39.6 GB | 14.7 GB | 2.69
Notes: Sandvine, Global Internet Phenomena Report Spring 2011

## Slide 26: Spectral efficiency
b/s/Hz: modulation, FEC, MIMO, …
but also total spectral efficiency
  guard bands
  restrictions on adjacent channel usage
  “high power, high tower”  small cells  higher b/s/Hz
data efficiency
  e.g., H.264 is twice as good as MPEG-2/ATSC
  and maybe H.265 twice as good as H.264
distribution efficiency
  unicast vs. multicast
protocol efficiency
  avoid polling  need server mode
mode efficiency
  caching
  side loading
  pre-loading

## Slide 27: A 2016 thought experiment
2016: 71% of (consumer) bandwidth is video
Average monthly TV consumption (US): 154 hours
Netflix: 1 GB/hour (SD) … 2.3 GB/hour (HD)
   300 GB/month/person
  more if people in household watch different content
 0.9 Mb/s (averaged over 24 hours)
Cisco VINI: 150 MB/month  2.7 GB/month
LTE: need 600 kHz/user (typical 1.5 b/s/Hz)
   500 MHz per cell sector  about 800 users/cell sector

## Slide 28: What can we do?
end system caching
better audio & video codecs
efficient apps
spectral efficiency (LTE-A)
directional antennas
general purpose spectrum
dense cells
white spaces & sharing
IP multicast
WiFi offload
small cells = better spectral efficiency + more re-use
LTE: 1.5 b/s/Hz
GSM: 0.1 b/s/Hz

## Slide 29: From beachfront spectrum to brownfield spectrum

## Slide 30: From empty back yard to time share condo

## Slide 31
cellular = about 500 MHz in total

## Slide 32: Unlicensed & lightly-licensed bands (US)
UHF (476-700 MHz) – incentive auctions (licensed) + some unlicensed
2.4 GHz (73 MHz) – 802.11b/g
3.6 GHz (100 MHz) – for backhaul & WISPs
4.9 GHz (50 MHz) – public safety
5.8 GHz (400 MHz) – 802.11 a/n
  much less crowded than 2.4 GHz
  supported by many laptops, few smartphones

## Slide 33: 2.4 vs. 5.8 GHz

## Slide 34: 5.8 GHz expansion: sharing with incumbents
50 mW
Indoor Use Only
250 mW
1 W
5150
5250
5350
5725
5825
Frequency (MHz)
250 mW
5470
Existing
Existing
Existing
New
Device detects radar
and moves to an unoccupied channel
DFS
DFS

## Slide 35: Freeing spectrum: incentive auctions
Incentive auctions will share auction proceeds with the current occupant to motivate voluntary relocation of incumbents
  Otherwise, no incentive for current occupant to give back spectrum
  Stations keep current channel numbers
    via DTV map
TV
TV
TV
TV
BB
BB
Without Realignment:
Reduced Broadband Bandwidth
TV
TV
BB
Adjacent Channel
Interference
With Realignment: Accommodates Increased Broadband Bandwidth
TV
TV
Adjacent Channel
Interference

## Slide 36: Small cell alternatives
Femto cells
  use existing spectrum
  need additional equipment
WiFi off-load
  use existing residential equipment
  5G networks = heterogeneous networks?
Distributed antenna systems
Femto-cells
Cellular
Distributed Antenna Systems
Signals are distributed throughout the
Building via amplifiers/antennas

## Slide 37: TV white spaces
2
4
5
7
9
3
6
8
10
Non-
Broadcast
spectrum
Non-
Broadcast
spectrum
New York City
Full Power
TV Stations
Philadelphia
Full Power
TV Stations
Low
Power TV
White
Space
White
Space
White
Space
White
Space
Etc.
Etc.
TV channels are “allotted” to cities to serve the local area
Other licensed and unlicensed services are also in TV bands
“White Spaces” are the channels that are “unused” at any given location by licensed devices
Low
Power TV
Only for illustrative purposes
Wireless
Microphones
Wireless
Microphones

## Slide 38: TVWS Spectrum Availability
38
Available spectrum varies by location
In rural areas many channels are available
In big cities only a few channels may be available at some locations
Examples of availability in UHF channels 21 – 51 (Illustrative):
21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51
21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51
New York
Washington, DC
Full Service DTV Station
Low Power TV Station
Channel Open/ Adjacent to TV
Channel Open/ Not Adjacent to TV
In less dense areas many channels are available.
For example: Wilmington, NC: 25 channels = 150 MHz
Harrisburg, PA: 19 channels = 114 MHz
Notes: 38

## Slide 39: TV White Spaces
Final rules adopted Sept. 2010:
  New spectrum for unlicensed
  Based on geolocation & data base of protected services
  Also allows for spectrum sensing with rigorous review & authorization process
Services protected in the data base:
  TV digital and analog Class A, low power, translator & booster stations
  Broadcast auxiliary (wireless mikes)
  Cable head-ends and TV translators
  Land mobile
  Sites with significant wireless microphone use
39
Mode 1: Portable device obtains
location/channels from fixed device
Mode 2: Portable device uses its own geolocation/data base access capability
Data Base
Notes: 39

## Slide 40: Benefits of TV White Space
Prime spectrum
  Great propagation & coverage
  High amounts in much of the USA
  Close to spectrum used by commercial wireless services  potential synergy
New IEEE 802.22™ standard:
  Broadband wireless access over a large area up to 100 km
  Up to 29 Mb/s per TV channel
  Can increase data rate through use of multiple channels
WiFi & TVWS complementary:
  Wi-Fi has greater bandwidth but usage density is increasing
Notes: 40

## Slide 41: New options to reduce traffic
Download video content during off-hours
  or defer software updates until WiFi is available
Peer-to-peer distribution of popular content
IP multicast (1-to-many) of live content
Make apps less chatty

## Slide 42: Spectrum Outlook
No single solution:
  reduce spectrum usage
    caching & better modulation
  re-use spectrum
  re-cycle old spectrum

## Slide 43: Measurements

## Slide 44: Measurement History
FCC has an evolved schema in place to acquire and analyze data on legacy PSTN
  Broadband networks and the Internet have not been general focus of these study efforts
More recent and evolving broadband interest
  Section 706 of Telecommunications Act, 1996, required annual report on availability of advanced telecommunications services to all Americans
    Resulted in information on deployment of broadband technology but not its performance
  FCC’s National Broadband Plan – March 2010
    Proposed performance measurements of broadband services delivered to consumer household
    Work plan evolved from recommendations of National Broadband Plan

## Slide 45: Broadband Measurement Study
First effort for Commission
Sought high level of voluntary participation from stakeholders
  ISPs, academia, others
Interactions shaped initial study
Broadband measurement still work in progress

## Slide 46: What Was Done
Enlisted cooperation of 13 ISPs covering 86% of US Population
Enlisted cooperation of vendors, trade groups, universities and consumer groups
Agreement reached on what to measure and how to measure it
Enrolled 9,000 consumers as participants
  6,800 (7,782) active during (2012) report period
  A total of 9,000 active over the data collection period
Issued report August 2011 and July 2012

## Slide 47: What Was Released
Measuring Broadband America Report
  Main Section describing conclusions and major results
  Technical Appendix describing tests and survey methodology
Spreadsheet providing standard statistical measures of all tests for all ISPs and speed tiers measured
March data set (report period) with 4B data elements from over 100M tests
  Data set presented as used with anomalies removed
  Documentation provided on how data set was processed
Data set from February thru June
  All data, as recorded
Geocoded data on test points recently released
Information available at http://www.fcc.gov/measuring-broadband-america

## Slide 48: What Was Measured
Sustained Download | Burst Download
Sustained Upload | Burst Upload
Web Browsing Download | UDP Latency
UDP Packet Loss | Video Streaming Measure
VoIP Measure | DNS Resolution
DNS Failures | ICMP Latency
ICMP Packet Loss | Latency Under Load
Total Bytes Downloaded | Total Bytes Uploaded

## Slide 49: MBA architecture

## Slide 50: Advertised vs. actual

## Slide 51: Latency by technology

## Slide 52: Data usage

## Slide 53: Cable/Telco Tussle
Some Cable companies advertise burst speed
  Quota based technique providing temporary speed increase of < 15 seconds
    Also affected by other household activity
  Can’t be applied generally to DSL where sync rate often limiting factor
  Marginal value to fiber where each subscriber has potentially available 37 Mb/s to 75 Mb/s provisioned bandwidth
Compromise to measure both burst and sustained speed
Burst speed does have some potential to improve browsing, gaming and like applications

## Slide 54: Reliability
Packet loss rate < 1%
Correlation between peak periods and packet loss
  Higher loss during peak hours
Most companies during peak experience < .4% packet loss
Worst case seen during March .8%
Data from other periods may have numbers in excess of 1% (Georgia Tech)
1% packet loss often cited as video threshold

## Slide 55: Web Page Downloading Canary in the Coal Mine?
Performance seems to top out after 10 Mbps
Many possible explanations
  Latency, server loading, household platform limitations, etc.
However, discussions with Georgia Tech indicate that they have seen similar performance issues
Discussion with Ofcom and others suggest that globally, full benefits of higher line rates not being realized AT PRESENT
Higher ISP speed may challenge industry to examine performance bottlenecks
More data needed

## Slide 56: Unknowns
Report measured ISP performance and not end to end
In-home contributions unknown but being looked at elsewhere (France)
Contributions of other network elements not correlated

## Slide 57: Broadband adoption
Eighth Broadband Progress Report, August 2012

## Slide 58: Access to broadband
Eighth Broadband Progress Report, August 2012

## Slide 59: Competition (US)
if lucky, incumbent LEC + cable company
  DSL: cheaper, but low speed
    mean: 2.5 – 3.5 Mb/s
  FTTH (FiOS): 21M households
    10-100 Mb/s
  Cable: > $50/month, higher speeds
    8-50 Mb/s
often, high switching costs ($200 early termination fee)
  or tied to bundles (TV, mobile)
can’t easily predict whether problem would be different
Notes: http://s.ftthcouncil.org/files/RVA.FTTH_.Apr09.060109.pdf

## Slide 60: FTTH

## Slide 61: State of competition (US)
FCC: Internet Access Services Status as of December 31, 2009
Notes: http://www.fcc.gov/Daily_Releases/Daily_Business/2010/db1208/DOC-303405A1.pdf: Internet Access Services: Status as of December 31, 2009

## Slide 62: International comparison: fixed
3rd International Broadband Data Report (IBDR), August 2012

## Slide 63: International comparison: mobile
3rd International Broadband Data Report (IBDR), August 2012

## Slide 64: Accessibility

## Slide 65: Access to Telecommunications and Technology Means:
Jobs
Education
Information
Recreation
Marketplace
Transportation
Independence
Privacy

## Slide 69: Improved Relay Services
Video Relay (2000) – first E.164 IP-based multimedia system
  initially H.323, transitioning to SIP
Speech-to-Speech (2000)
Spanish Relay (2000)
Internet Relay (2001)
Access to audiotext (IVR) systems
Typing speed – 60 wpm
Captioned Telephone (2003)

## Slide 70: Turn of Century: Many Gaps in Laws
No coverage of Internet-based communication services or video programming
No mandates for video description
Limited captioning capability on television devices (screens up to 13 inches)
No specific protections for deaf-blind population
No guarantee of emergency access or accessible user interfaces on video devices for people who are blind or visually impaired

## Slide 71: Twenty-First Century Communications and Video Accessibility Act Public Law 111-260; Public Law 111-25
Need for the Legislation: Disability protections enacted by Congress and implemented by the FCC had not kept up with emerging technologies
    Prior focus was on telecommunications
    Prior laws applied to legacy technologies
CVAA addresses accessibility challenges of 21st century technologies

## Slide 72: Market Forces: Past failures to Achieve access
  Each disability market is too small
  Lower incomes mean less purchasing power
  Need for adaptive equipment discourages purchases
Government steps in where market has failed
Addresses accessibility needs to promote innovation and not overly burden industry: Goal is to incorporate access at design stages
Accessibility achieves access for all – goes beyond disability community

## Slide 73: Title II – Video Description
Required for:
  4 national broadcast networks in top 25 markets
  Top 5 cable channels
Amount of programming: 4 hours of prime time or children’s programming per week
FCC must conduct additional inquires on availability, benefits, uses, and costs: 1 year after rule phase-in
CVAA authorizes expansion to 7 hours of video description per week and eventually all market areas

## Slide 74: FCC Implementation of CVAA
Creation of Advisory Committees (directed by CVAA to achieve consumer-industry balance)
    Emergency Access Advisory Committee
    Video Programming Accessibility Advisory Committee
Adoption of Rules
Creation of Accessibility Clearinghouse:
  http://apps.fcc.gov/accessibilityclearinghouse/
Biennial Reports to Congress
Handling of Complaints

## Slide 75: RESEARCH

## Slide 76: How can researchers participate?
Write relevant papers
  what’s technologically possible?
  what are real-world problems?
  economic + technology analysis
Submit filings for the record
  during comment periods
Ex-parte visits
Presentations to educate FCC staff

## Slide 77: Conclusion
Regulator as critical part of technology eco system
  technology enabler
  manager of the “common”
  consumer protection
  maintain or enhance competition
  deal with market failures
Challenges
  outdated laws
  technology transition: waiting for last one to turn off lights…