## Slide 1: OTT and the future of the PSTN
Henning Schulzrinne
FCC

## Slide 2: PSTN: The good & the ugly
The good | The ugly
Global Connectivity (across devices and providers) | Minimalist service
High reliability (engineering, power) | Limited quality (4 kHz)
Ease of use | Hard to control reachability (ring at 2 am)
Emergency usage | Operator trunks!
Universal access (HAC, TTY, VRS) | No universal text & video
Mostly private (protected content & CPNI) | Limited authentication Security more legal than technical (“trust us, we’re a carrier”)
Relatively cheap (c/minute) | Relatively expensive ($/MB)

## Slide 3: The OTT to “traditional” spectrum
Non-interconnected VoIP
Not interconnected
Interconnected VoIP
911
CALEA
QoS-enabled VoIP
“specialized service”
e.g., MVPD service
USF
Bidirectional connectivity to E.164 numbers
Facilities-based VoIP
[technical possibility]
QoS as commercial service
Can reach any telephone number
often, logical, not physical separation (“service flow”)
Video relay service
Multimedia for Deaf & HoH
Can reach any E.164 number via relay
Traditional Analog/TDM POTS
needs no explanation
user-initiated resource reservation
(RSVP, NSIS, DOCSIS 3)

## Slide 4: What are key attributes?
Universality
  reachability  global numbering & interconnection
  media  HD audio, video, text
  availability  universal service regardless of
    geography
    income
    disability
  affordability  service competition + affordable standalone broadband
Public safety
  citizen-to-authority: emergency services (911)
  authority-to-citizen: alerting
  law enforcement
  survivable (facilities redundancy, power outages)
Quality
  media (voice + …) quality
  assured identity
  assured privacy (CPNI)
  accountable reliability

## Slide 5: What is less important?
Technology
  wired vs. wireless
    but: maintain quality if substitute rather than supplement
  packet vs. circuit
  “facilities-based” vs. “over-the-top”
    distinction may blur if QoS as a separable service
Economic organization
  “telecommunication carrier”
 | Signaling | Media
Analog | circuit (A) | circuit (A)
Digital | circuit (D) | circuit (D)
AIN | packet (SS7) | circuit (D)
VoIP | packet (SIP) | packet (RTP)

## Slide 6: OTT: access to broadband
Eighth Broadband Progress Report, August 2012

## Slide 7: Advertised vs. actual 2012
Measuring Broadband America, July 2012

## Slide 8: Significantly better than 2011
Measuring Broadband America, July 2012

## Slide 9: Latency by technology
Measuring Broadband America, July 2012

## Slide 10: Other QoS impairments
Packet loss
  VoIP: < 1-5% acceptable
  Video: loss  lower throughput
Home networks
“Buffer bloat” in gateways
  “don’t download that video, I’m on the phone!”
Reliability?
S. Sundaresan et al, Broadband Internet Performance: A View From the Gateway, ACM SIGCOMM 2011

## Slide 11: Broadband virtuous cycle
fixed broadband investment
cellular broadband (backhaul)
applications
(incl. OTT)
adoption
(relevance, value)
broadband availability
OI principles

## Slide 12: Open Internet Principles
Transparency. Fixed and mobile broadband providers must disclose the network management practices, performance characteristics, and terms and conditions of their broadband services;
No blocking. Fixed broadband providers may not block lawful content, applications, services, or non-harmful devices; mobile broadband providers may not block lawful websites, or block applications that compete with their voice or video telephony services
No unreasonable discrimination. Fixed broadband providers may not unreasonably discriminate in transmitting lawful network traffic.

## Slide 13: Going forward
Interconnected VoIP: done
  CALEA, USF, E911
  Part 4 outage reporting
In progress
  Intercarrier compensation: IP interconnection expectation + transition to bill-and-keep
  NG911, better location
  video relay services, CVAA
To do
  numbering & databases
  security model (robocalls, text spam, vishing)
  VoIP interconnection model
… , we expect all carriers to negotiate in good faith in response to requests for IP-to-IP interconnection for the exchange of voice traffic. The duty to negotiate in good faith has been a longstanding element of interconnection requirements under the Communications Act and does not depend upon the network technology underlying the interconnection,
whether TDM, IP, or otherwise. Moreover, we expect such good faith negotiations to result in interconnection arrangements between IP networks for the purpose of exchanging voice traffic.