## Slide 1: IP interconnect
Henning Schulzrinne
March 2012

## Slide 2: Overview
Layers & interconnection
What do we need to connect?
Architectures

## Slide 3: Protocol roles
RTP (+ RTCP)
  media (audio) transport
  same for audio & video
SIP
  session setup and control
  used in IMS and PacketCable, as well as by Vonage
    used by Skype for PSTN interconnect
  contains SDP (session description)
    negotiates codecs
  same for audio & video

## Slide 4: SIP message format
SDP
INVITE sip:bob@there.com SIP/2.0
Via: SIP/2.0/UDP here.com:5060
From: Alice <sip:alice@here.com>
To: Bob <tel:12024181544>
Call-ID: 1234@here.com
CSeq: 1 INVITE
Subject: just testing
Contact: sip:alice@pc.here.com
Content-Type: application/sdp
Content-Length: 147
v=0
o=alice 2890844526 2890844526 IN IP4 here.com
s=Session SDP
c=IN IP4 100.101.102.103
t=0 0
m=audio 49172 RTP/AVP 0
a=rtpmap:0 PCMU/8000
SIP/2.0 200 OK
Via: SIP/2.0/UDP here.com:5060
From: Alice <sip:alice@here.com>
To: Bob <tel:120241815144>
Call-ID: 1234@here.com
CSeq: 1 INVITE
Subject: just testing
Contact: sip:alice@pc.here.com
Content-Type: application/sdp
Content-Length: 134
v=0
o=bob 2890844527 2890844527 IN IP4 there.com
s=Session SDP
c=IN IP4 110.111.112.113
t=0 0
m=audio 3456 RTP/AVP 0
a=rtpmap:0 PCMU/8000
message body
header fields
request line
request
response

## Slide 5: Review: VoIP stack
PHY
(fiber)
MAC
(Ethernet)
L2.5
(MPLS)
L3
(IP)
UDP
SIP
RTP
codec
PHY
(fiber)
MAC
(Ethernet)
L2.5
(MPLS)
L3
(IP)
PHY
(fiber)
MAC
(Ethernet)
L2.5
(MPLS)
L3
(IP)
UDP
SIP
RTP
codec
PHY
(fiber)
MAC
(Ethernet)
L2.5
(MPLS)
L3
(IP)
UDP
SIP
RTP
codec
Comcast
Level3
IntelePeer
Xconnect

## Slide 6: Components & standards
E.164 phone number  IP address (+ carrier)
  ENUM: uses DNS
  new IETF effort (TERQ)
RTP exchange
  what codecs?
SIP exchange
  features and assumptions

## Slide 7: Physical architecture 1: Internet
Internet
no POI
no circuits
Vonage
69.59.253.143
E.164 -> IP
Comcast
66.179.53.44
AT&T
216.77.188.73
+1 202 418 1544
 voip.att.net

## Slide 8: Physical architecture 2: POIs
POIs
circuits or POPs
Vonage
69.59.253.143
E.164 -> IP
Comcast
66.179.53.44
AT&T
216.77.188.73
+1 202 418 1544
 voip.att.net
POI SF
POI Miami
MPLS circuit
or part of carrier network

## Slide 9: Carrier hotels
111 8th Avenue in Manhattan

## Slide 10: Big IXPs
Ashburn, VA
Atlanta
Boston
Chicago
Dallas
Kansas City
Los Angeles
New York
Palo Alto
San Jose
Seattle
Tampa
Vienna, VA

## Slide 11: The cost of transport
Cogent: 4.51 $/Mb/s/month (2010)  1.4 c / GB
Voice (G.711)
  64 kb/s nominal one-way
  200 kb/s with protocol headers, duplex
  = 0.0015 GB/min
  = 0.0021 c/min
Notes: http://www.telegeography.com/research-services/global-internet-geography/index.html
http://dslprime.com/dslprime/42-d/4148-costs-and-caps
http://seekingalpha.com/instablog/329338-kurt-b-feierabend/57157-cogent-communication-s-ever-falling-bandwidth-pricing: $4.51 Mb/s ->
1 Mb/s  324 GB/month
thus, $4.51 Mb/s  1.4 c / GB
voice call