## Slide 1: Machine-TO-MACHINE or the INTERNET of THINGS
Henning Schulzrinne
FCC & Columbia University
with slides from Harish Viswanathan, Alcatel-Lucent

## Slide 2: Overview
What is M2M precisely?
What is it good for?
A taxonomy
Technical challenges for M2M
Research examples: SECE and EnHANTS

## Slide 3: What is M2M?
Machine-to-machine:
  “Machine to machine (M2M) refers to technologies that allow both wireless and wired systems to communicate with other devices of the same ability.” (Wikipedia)
  sensors and actuators
    often within a control loop
    long history: telemetry, SCADA, industrial automation, building HVAC and security (e.g., BACnet)
    difference: IP-based protocols and/or Internet
  no direct human consumer or producer
  IoT  from custom communication to common stack
No single dominant application, but thousands of embedded applications
   need low cost to develop & deploy

## Slide 4: Key enablers
IoT
Cheap SOCs
Mature Internet protocols
Cellular connectivity
Unlicensed
Analytics
(“big data”)
Applications

## Slide 5: IoT = cheap microcontrollers + network interfaces
Raspberry PI ($35)
Gumstix (WiFi, BT): 58 mm, $199
Arduino Uno, €20

## Slide 6: Major market segments
fixed or wireless networking connectivity
to connect these devices and sensors to a central server and transmit
information about the objects
external hardware, sensors, and RFID, end point devices
to collect data and monitor status
service layer infrastructure and associated services
to address the common needs across multiple vertical domains
Application services and system integration
to seamlessly integrate the disparate M2M solution components
Harish Viswanathan, Alcatel-Lucent, 2012
Notes: | Presentation Title | Month 2010 | 6

## Slide 7: M2M is not…
does not always uses cellular networks
is not always energy-constrained
is not always cost-constrained
only uses puny microcontrollers
is not always run by large organizations
  many small & mid-sized providers
  usually embedded into other products

## Slide 9: A taxonomy of selected M2M applications
Application |  | Energy-constrained | Processor or memory constrained (= $) | Reliability | Unsupervised | Cellular, unlicensed?
Automotive | V2I, I2V |  |  |  |  | C
 | V2V |  |  | ✔ | ✔ | U
Agriculture | environmental sensors | ✔ | ✔ | ✔ | ✔ | C, U
Industrial | plant monitoring & control | ✔? | ✔? | ✔ | ? | C, U
Infrastructure | utility monitoring | - | ✔ | ✔ | ✔ | C, U?
 | traffic | - | ✔ | ✔ | ✔ | C, U?
Medical | physio | ✔ | ✔ | ✔ | ? | C, U

## Slide 10: Market size by vertical
2012 Application Services Revenue in $B
Source: Beecham Report, 2008

## Slide 11: Connections and revenue
Home
Energy
Tourism
Industry
Transportation
Environment
Healthcare
Security
Automotive
Signage
Notes: **

## Slide 12: M2M communication models
Source: OECD (2012), “Machine-to-Machine Communications: Connecting Billions of Devices”, OECD Digital Economy Papers, No. 192, OECD Publishing. http://dx.doi.org/10.1787/5k9gsh2gp043-en
dispersed | Smart grid, meter, city Remote monitoring | Car automation eHealth Logistics Portable consumer electronics
concentrated | smart home factory automation eHealth | on-site logistics
 | fixed | mobile

## Slide 13: M2M networking technologies
Source: OECD (2012), “Machine-to-Machine Communications: Connecting Billions of Devices”, OECD Digital Economy Papers, No. 192, OECD Publishing. http://dx.doi.org/10.1787/5k9gsh2gp043-en
dispersed | PSTN Broadband 2G/3G/4G Power line communications | 2G/3G/4G satellite
concentrated | wireless personal area networks wired networks indoor electrical wiring WiFi | WiFi WPAN
 | fixed | mobile

## Slide 14: M2M varies in communication needs
1/hour
1/minute
1/second
10/second
sensors
actuators
Notes: http://www.nytimes.com/2012/10/02/world/europe/device-sends-message-to-swiss-farmer-when-cow-is-in-heat.html?pagewanted=all

## Slide 15: Not just cellular or unlicensed

## Slide 16: Technical challenges
Transport
PHY & L2
Network
E.164 numbers
signaling load
authentication
radio diversity
Session, control
Application
HTTP,
CoAP,
SIP,
XMPP
IPv4,
IPv6
6LowPAN
ROLL
UDP
TCP
SCTP
802.15.4
802.11
GSM
LTE
IPv4 address exhaustion
security?
resource control
reliability
complexity (SCTP)
event notification (pub/sub)?
common abstractions?
firewalls & NATs
secure upgrades
software quality
XML
SensorML
Zigbee profile

## Slide 17: Network challenges
Unlicensed
  How do I attach and authenticate a device to a (home) network?
  Credentials?
Licensed
  Reliability  multiple simultaneous providers
  Mobility  different providers in different regions
  Charging  often low, intermittent usage, sometimes deferrable (“Whispernet”)
    From $50/device/month  < $1/month?
Authentication
  Which devices can be used by whom and how?
    “Any employee can monitor the room temperature in any public space, but only Facilities staff can change it”

## Slide 18: Signaling increases 30-50% faster than data
Control Plane
5 %
M2M peak (hourly) traffic
Cellular capacity
33 %
Data Plane
M2M traffic modeling shows disproportionately large signaling
< 1% of data plane capacity is consumed by M2M but more than 30% of signaling capacity is consumed
Isolate M2M traffic from regular traffic
Flexible scaling requirements because of bulk contracts
Signaling traffic management
Low Power, short payloads, bursty traffic
Low cost but also low performance requirements
In network monitoring
Harish Viswanathan, Alcatel-Lucent, 2012
Notes: **

## Slide 19: FCC TAC preliminary recommendations
R1: Additional M2M unlicensed band (1.2 – 1.4, 2.7 – 3.1 GHz)
R2: M2M service registration
R3: Numbering and addressing plan
  IPv4  IPv6
R4: M2M center-of-excellence at FCC
R5: Certification lite
R6: 2G sunset roadmap
  2G re-farming, security issues  LTE with IPv6
R7: Encourage 3G/4G module building

## Slide 20: Current unlicensed spectrum
+ TV white spaces (in 476-692 MHz range) – availability varies

## Slide 21: FCC actions for (M2M) spectrum
More than 300 MHz of additional spectrum in pipeline
Encourage unlicensed & lightly-licensed spectrum
  TV white spaces: geographical databases
  3.5 GHz & 4.9 GHz
  incentive auction guard bands as new unlicensed UHF spectrum (600 MHz)
Experimental licensing review

## Slide 22: Extreme M2M: self-powered devices
Leviton WSS0S - Remote Switch
EnHANT project (Columbia U.)
indoor lighting  10 kb/s

## Slide 23: Example: SECE (Sense Everything, Control Everything)
Web-based user interface
Rules in domain specific language
Interface to online services
Interface to communication devices
Sensor and actuator infrastructure

## Slide 24: SECE User Interface

## Slide 25: Infrastructure for Sensors and Actuators
Conventional Devices
USB (Phidgets)
Wireless (XBee)
Tiny (Arduino)
Communication
VoIP phone
Skype
Legacy (X10)

## Slide 26: Sensors and Actuators in IRT lab
What it really looks like
XBee door lock
Sensor and actuator testbed

## Slide 27: smobd: Subsystems & Interfaces on Linux

## Slide 28: Conclusion
M2M is not a single technology  technology enabler
Build on secret of Internet: simple protocol building blocks that can be combined
  accommodate wide
Address key infrastructure challenges:
  flexible network access
  in-field upgrades
  scalable security models