## Slide 1: Large-Scale Internet Measurements for data-driven public policy
Henning Schulzrinne
(+ Walter Johnston & James Miller)
FCC & Columbia University

## Slide 2: Overview
Why measure?
Results of FCC MBA 2011 and 2012
The challenge of mobile measurements
Baking measurements into the infrastructure

## Slide 3: Why measure?
Whole conferences on measurement
  often driven by lost-key method
Long history of IETF measurement work
  RFC 2330: 1998
  focused on specific metrics, not so much overall architecture
Performance measurements don’t work well
  Individual consumers:
    not statistically reliable (geek-heavy)
    no ground truth data
    confounding factors (e.g., home networks)
    data generally not published  hard to compare metrics
  Service providers:
    limited infrastructure  hard to scale

## Slide 4: FCC measurement history
FCC has acquired and analyze data on legacy PSTN
More recent and evolving broadband interest
  Section 706 of 1996 Telecommunications Act  annual report on availability of advanced telecommunications services to all Americans
    Resulted in information on deployment of broadband technology (“Form 477”)
    but not its performance
  FCC’s National Broadband Plan – March 2010
    Proposed performance measurements of broadband services delivered to consumer households
    Work plan evolved from recommendations of National Broadband Plan

## Slide 5: The role of network measurements
Measurement infrastructure
ISP diagnostics
“my Interwebs are just beach balls”
User diagnostics & validation
hard failures  soft failures
Public policy
BB evolution?
Informed consumer choice
Universal service

## Slide 6: Principles
The FCC Measuring Broadband America program is based on principles of openness, transparency and partnership with diverse stakeholders.
We are committed to:
  Ensuring that commonly accepted principles of scientific research, good engineering practices, and transparency guide the program;
  Encouraging collaboration of industry, academia and government;
  Publishing the comprehensive technical methodology used to collect the data, including the source code for the tests as open source;
  Releasing data used to produce each report coincident with the report’s release, and releasing all data for each collection cycle within one year of collection.

## Slide 7: Measurement architecture
Lucid
broadband Internet
access provider (ISP)
backbone
ISP
Measuring Broadband America 2011 & 2012
Measuring Broadband America future?
Notes: http://commons.wikimedia.org/wiki/File:Homenet.svg

## Slide 8: The MBA project - logistics
Enlisted cooperation:
  13 ISPs covering 86% of US population
  vendors, trade groups, universities and consumer groups
Reached agreement reached on what to measure and how to measure it
Enrolled roughly 9,000 consumers as participants
  6,800 (7,782) active during March 2011 (April 2012)
  A total of 9,000 active over the data collection period

## Slide 9: What was measured
Sustained Download | Burst Download
Sustained Upload | Burst Upload
Web Browsing Download | UDP Latency
UDP Packet Loss | Video Streaming Measure
VoIP Measure | DNS Resolution
DNS Failures | ICMP Latency
ICMP Packet Loss | Latency Under Load
Total Bytes Downloaded | Total Bytes Uploaded

## Slide 10: What was released
Measuring Broadband America reports
  Main section describing conclusions and major results
  Technical appendix describing tests and survey methodology
Spreadsheet providing standard statistical measures of all tests for all ISPs and speed tiers measured
Report period data set with 4B data elements from over 100M tests
  Data set presented as used with anomalies removed
  Documentation provided on how data set was processed
  All data, as recorded
Geocoded data on test points recently released
Information available at http://www.fcc.gov/measuring-broadband-america

## Slide 11: 2011: Most ISPs deliver close to advertised during peak hours

## Slide 12: 2012: You improve what you measure…

## Slide 13: Web page downloading

## Slide 14: The Internet is not a series of (fixed-width) tubes
Some cable companies advertise burst speed
  Quota based technique providing temporary speed increase of < 15 seconds
    Also affected by other household activity
  Can’t be applied generally to DSL where sync rate often limiting factor
  Marginal value to fiber where each subscriber has potentially available 37 Mb/s to 75 Mb/s provisioned bandwidth
   Links are no longer constant-size bit pipes
Measured both burst and sustained speed

## Slide 15: Broadband 2012
Deployment
  USF: Connect America Fund
Performance
  Measuring Broadband America
  mobile project announced
Significant progress:
  wider availability of 100 Mb/s
  fiber available to 46 million homes (FiOS, U-verse)
  community/non-traditional broadband (Chattanooga, Kansas City)
  LTE networks

## Slide 16: Mobile performance
Announced effort with 4 largest wireless providers
Options available
  structured drive testing  expensive
  semi-formal drive testing  snapshot, limited coverage
  passive measurements  privacy concerns, limited sampling
 Smartphone app + volunteers + existing infrastructure
Challenges:
  how to capture variation in time, space and device?
  how to ensure location privacy?
  impact of bandwidth usage for metered & capped plans?

## Slide 17: What can’t we measure?
Small providers
  may be more infrastructure- & engineering-challenged
Anchor institutions
Network reliability
  large-scale outages gathered by “Part 4” outage reporting, but not public
  small-scale outages?
Network features
  Who has access to DNSsec? IPv6? Which ports are being blocked?
Which country has the cheapest broadband?
  And why?
What drives consumer adoption of higher speeds & new applications?
  Speed  applications OR applications  speed?
Why does 1/3 of US not use the Internet?
  Relative importance of availability, affordability, relevance?

## Slide 18: LMAP proposed architecture
Host | Tier
2001:db8::1 | 10/2
2001:db8::2 | 25/5
measurement
clients
measurement
server
network parameter server
measurement
controller
data collector
e.g., UDP echo
What is my tier?
Start metrics 17 & 42!
measurement
samples

## Slide 19: Conclusion
Measurements: from sometime experiment and LAN to built-in capability
Good telecom policy needs good data
  not just counting lines
  PSTN transition to IP  there is no second network
Re-use measurement for three purposes:
  ISP diagnostics and planning
  Consumer diagnostics
  Public policy data gathering
Dear IETF: We need your help!

## Slide 20: BACKUP

## Slide 21: FCC
Independent federal agency
About 1,600 employees
Chairman (D)
4 Commissioners (2 D, 2 R)
Consumer and Governmental Affairs
Enforcement
International
Media
Public Safety & Homeland Security
Wireless Telecommunications
Wireline Competition

## Slide 22: Process
NOI
NPRM
R&O
Notice of Inquiry
Notice of Proposed Rule Making
Report & Order
comments & ex parte

## Slide 23: Performance varies
ISPs seem to impose network wide performance standards
However, there can be exceptions by speed tier

## Slide 24: 2011: some don’t

## Slide 25: Burst speed increase
Most impact of burst speed seen between 6 and 12 Mb/s
Note: This chart not in report and shows calculated difference between burst and sustained performance

## Slide 26: Latency by technology

## Slide 27: Data usage

## Slide 28: Reliability
Packet loss rate < 1%
Correlation between peak periods and packet loss
  Higher loss during peak hours
Most companies during peak experience < .4% packet loss
Worst case seen during March: .8%
Data from other periods may have numbers in excess of 1% (Georgia Tech)
1% packet loss often cited as video threshold

## Slide 29: Web page downloading: Canary in the Coal Mine?
Performance seems to top out after 10 Mb/s
Many possible explanations
  Latency, TCP issues, server loading, household platform limitations, …
However, discussions with Georgia Tech indicate that they have seen similar performance issues
Discussion with Ofcom and others suggest that globally, full benefits of higher line rates not being realized
Higher ISP speed may challenge industry to examine performance bottlenecks
More data needed

## Slide 30: International comparison: fixed
3rd International Broadband Data Report (IBDR), August 2012

## Slide 31: International comparison: mobile
3rd International Broadband Data Report (IBDR), August 2012

## Slide 32: 2012 Upload speeds

## Slide 33: 2012 peak period actual vs. advertised

## Slide 34: Advertised vs. actual

## Slide 35: Burst download vs. sustained download

## Slide 36: Web page loading time

## Slide 37: Cumulative distribution of download speeds

## Slide 38: CDF of sustained download speed

## Slide 39: Throughput predictability

## Slide 40: Actual download speeds: 2011 vs. 2012