## Slide 1: Investigating HVAC’s Effect on Barometer Readings indoors
Wonsang Song

## Slide 2: Measurement setting
Sensor
  Model: BOSCH BMP085
  Mode: ultra high resolution (RMS noise: 0.25 m)
  Sampling rate: 60 Hz
  One measurement: average of one minute

## Slide 3
Graph shows measured altitudes (blue) at different points on 7th floor in CEPSR building and pressures at sea level (red) posted in the NOAA site
Instead of location, weather seems to have a significant effect
  Actual altitude change during 34 minutes: -6.65 m
  Expected altitude change due to the weather: -4.42 m
  Pressure increases from 101.68 kPa to 101.88 kPa during 2 hours => rate of altitude change is -0.13 m/min
Chart: 11/5, 7th CEPSR
| office-721 | restroom | office-721 | restroom | office-721 | hallway-sw | hallway-sw | hallway-se | hallway-se | hallway-se | hallway-ne | hallway-ne | hallway-nw | hallway-nw | office-721
Measured Altitude | 64.19 | 63.63 | 63.14 | 62.44 | 62.34 | 61.82 | 61.73 | 60.99 | 60.77 | 60.59 | 59.84 | 59.51 | 58.9 | 58.76 | 57.54
Pressure at Sea Level | 101.68 | 101.79 | 101.88

## Slide 4
Same measurement but when pressure at sea level decreases
Altitude increases as pressure outside decreases
  Actual altitude change during 27 minutes: 2.23 m
  Expected altitude change due to the weather: 3.37 m
  Pressure decreases from 102.32 kPa to 102.14 kPa during 2 hours => rate of altitude change is +0.125 m/min
Chart: 11/6, 7th CEPSR
| office-721 | restroom | restroom | office-721 | hallway-sw | hallway-sw | hallway-se | hallway-se | hallway-ne | hallway-ne | hallway-nw | hallway-nw | restroom | office-721
Measured Altitude | 75.66 | 75.3 | 75.53 | 75.86 | 76.37 | 76.34 | 76.42 | 76.43 | 76.93 | 76.86 | 76.54 | 76.96 | 77.46 | 77.89
Pressure at Sea Level | 102.32 | 102.24 | 102.14

## Slide 5
Same measurement but at a different, higher location
Indoor altitude decreases as outside pressure increases
  Actual altitude change during 22 minutes: -3.60 m
  Expected altitude change due to the weather: -2.28 m
  Pressure increases from 100.73 kPa to 100.88 kPa during 2 hours => rate of altitude change is -0.10m/min
Chart: 11/8, 13th NWB
| hallway #1 | hallway #1 | hallway #1 | hallway #2 | hallway #2 | hallway #3 | hallway #3 | restroom | restroom | hallway #1 | staircase | staircase
Measured Altitude | 102.48 | 102.27 | 102.17 | 101.57 | 101.34 | 101.12 | 100.84 | 100.42 | 100.3 | 99.66 | 99.51 | 98.88
Pressure at Sea Level | 100.73 | 100.8 | 100.88

## Slide 6
Measurement at one location
Confirms that measured altitude changes as weather changes
  Actual altitude change during 30 minutes: -5.65 m
  Expected altitude change due to the weather: -5.4 m
  Pressure increases from 101.97kPa to 102.1 kPa during 1 hours => rate of altitude change is -0.18m/min
Chart: 11/9, 7th CEPSR
| cepsr-721 | cepsr-721 | cepsr-721 | cepsr-721 | cepsr-721 | cepsr-721 | cepsr-721 | cepsr-721 | cepsr-721 | cepsr-721 | cepsr-721 | cepsr-721 | cepsr-721 | cepsr-721 | cepsr-721
Measured Altitude | 59.16 | 58.89 | 58.98 | 58.67 | 58.34 | 57.86 | 57.26 | 56.5 | 56.25 | 55.96 | 55.21 | 54.73 | 54.27 | 54.11 | 53.51
Pressure at Sea Level | 101.97 | 102.1

## Slide 7: Discussion
We do not observe any significant changes in barometer readings at different points on the same floor
  We expected altitudes measured in restrooms would increase due to lower pressure, but they do not
Instead, measured altitude changes as time goes or as weather changes
However, we cannot conclude HVAC does not affect barometer readings
  We don’t know the status and intensity of HVAC of the buildings

## Slide 8: Related work
“The main errors in indoor measurements were caused by the different ventilation in different rooms in building. However, no drastic changes in the air pressure were noticed.”
- J. Parviainen, J. Kantola, and J. Collin, “Differential Barometry in Personal Navigation,” presented at the IEEE/ION Position Location and Navigation System (PLANS), 2008.
“Before ignition in the PPV experiment, the fan created uniform pressures at all three elevations of 21 Pa (0.003 PSI).”
- S. Kerber and W. Walton, “Effect of Positive Pressure Ventilation on a Room Fire,” U.S. Department of Commerce, NISTIR-7213, Mar. 2005.
= 1.74 m