## Slide 1: Finding 9-1-1 Callers in Tall Buildings
Wonsang Song, Jae Woo Lee, Byung Suk Lee, and Henning Schulzrinne
Columbia University

## Slide 2: Problem
Location is key in emergency calls
  To route calls to proper call center
  To pinpoint the caller on site
But indoor location is still a challenge
  GPS does not work indoors
  Vertical accuracy is very important indoors
  Barometers are not accurate in emergency situations because of PPV or HVAC

## Slide 3: Our approach
Use smartphone’s inertial sensors to trace people’s vertical movement
  Dead reckoning: calculate traveled distance or number of floors from sensor measurements
Augment sensor-based approach with minimum and practical infrastructure support
  Bluetooth beacons at building’s entrance provide initial location and other building information

## Slide 4: Evaluation
Errors when traveling 1-9 floors without stopping using elevator
Errors when traveling 9 floors making 1-4 stops using elevator
Landing counting errors in 50 trials of walking 4 floors on stairway
CDF of errors when traveling 2 floors (7.3m) using escalator