## Slide 1: Practical Economics of Networks
Henning Schulzrinne
FCC & Columbia University
SDP (Turin, Italy) - April 2013

## Slide 2: Overview
What questions do policy makers ask?
What data sources are available?
Access network issues
  capex & opex
  competition
The pitfalls of QoS
Open Internet principles in the US

## Slide 3: Policy questions

## Slide 4: Policy questions
Should content and service providers pay access networks for access?
How do content and service providers relate to CDNs, transit providers and access providers?
What are some of the pitfalls when talking about QoS in the context of network economics?
What real-world economic data sources are available to analyze network performance and pricing and what are some of their limitations?
How is interconnection handled in the non-IP world, e.g., for interconnecting voice (PSTN) networks?
What are some of the economics of building access networks?

## Slide 5: Why policy & regulators?
Market failure
  private monopoly
    e.g., pre-divestiture BOCs as local phone companies
  competitive market failures (e.g., duopoly, consumer rights)
     merger reviews (e.g., Comcast + NBC, AT&T + T-Mobile, T-Mobile + MetroPCS)
  social policy objectives (e.g., disability rights, universal access)
Law enforcement
  illegal conduct (consumer/subsidy fraud, misrepresentation, …)
  unsafe conduct (“no fence around antenna”)
Consumer education
  information asymmetry (e.g., “lemon laws”)
Economic development
  “public goods” (e.g., scientific research)

## Slide 6: Policy inputs
Policy
Law
(1934 & 1996 Act)
Prior actions (e.g., VoIP definition)
Court cases (Brand X, Comcast, …)
Economic analysis
(competition, investment, consumers)
Other impacts (social policy objectives, fraud risk, …)

## Slide 7: Telecom policy tool kit
gov’t monopoly
laissez faire
price-regulated utility
structural
separation
facilities-based competition + interconnection
anti-trust
network neutrality
unbundled network elements
gov’t grants
(USF)
high cost + low income
disability access
public safety
CALEA

## Slide 8: Telephone Social Policies
Universal service (Lifeline, high cost, …) | Necessary to function (call doctor, call school, …)
Basic service price regulation | Ensure widespread availability
911 | Report emergencies for self and others
Power backup | Ensure emergency communications
Outage reporting | Ensure reliability
Lawful intercept (CALEA) | Phone as tool for criminals
Disability access (ringers, HAC) | Ensure participation in society
CPNI | Phone as private medium

## Slide 9: Telecom regulation
Local, state and federal
  local: CATV franchise agreements
  state: Public Utility Commission
    responsible for all utilities – gas, water, electricity, telephone
  federal: FCC, FTC (privacy), DOJ (monopoly)
Elsewhere: gov’t PTT  competition
  vs. US: regulated private monopolies
Based on 1934 Telecommunications Act
Amended in 1996

## Slide 10: Before the Internet, Before the Phone… Common Carrier
Content
Common Carrier Trains
Right-of-way
Coal

## Slide 11: Communications Carriers
Characteristics:
  Carrier of third parties’ goods / Bailment
  Market power / infrastructure
  Vital economic Input: goods carried are important
Policy:
  Non-discrimination
  Just & reasonable rates
  Liability
    Not liable for what content is
    Liable for damage to content
  Benefit from sovereign
    Access to right of way
  Privacy / security
Importance and value of information – stocks, elections, agriculture.
Notes: In typical western dialectic – the literature struggles with an either / or. Either it is market power – or it is bailment.
Since each justification on its own is vulnerable to criticism – we oscillate between the two without a firm policy foundation for common carriage.
I would suggest rather that it is both / and. It is both market power and bailment. A truly competitive market is one where, if the bailor harms us, we can switch to another service – the bailor loses for the bailor’s negligence.
However, the bailor carrier remains in a power position in the market as a carrier and can easily put us in harms way. I think a little market power is amplified by the ability of the bailor to use that market power.
My take is that both of these are important to understanding the WHY of common carriage.
(Liability for damaged to goods while in care; But no liability for damaged caused by goods - Trains not liable for transporting Al Capone)
Telegraph
  Importance and Value of transmitted information – stocks, elections, agriculture. Importance to the economy and to the country well recognized.
  Access, reliability, non discrimination
  States
    Granted access to Right of Way
    Imposed Common Carrier Obligations
      Serve all customers without discrimination
      Transmit messages in order received
      Keep content of messages private
      Interconnection between networks
Telephone
  Precedent: telephone is just voice telegraph; therefore common carrier
  State and local authority
    Authorize Service and grant access to Rights of Way and eminent domain
    Impose Common Carriage Obligations
      Ban discrimination in line installations
      Rate regulation
      Interconnection
      Non Discrimination
Originally regulated by the US Interstate Commerce Commission
  Regulated all common carriers: Railroads, shipping, telegraph, telephone

## Slide 12: The US hierarchy of laws
Constitution
Commerce clause
Law
Telecom Act 1934 & 1996
47 CFR
Narrative
reasonable network management
Section 8: To regulate Commerce with foreign Nations, and among the several States, and with the Indian Tribes (1787)
SEC. 706. ADVANCED TELECOMMUNICATIONS INCENTIVES. (a) IN GENERAL- The Commission … shall encourage the deployment on a reasonable and timely basis of advanced telecommunications capability to all Americans (including, in particular, elementary and secondary schools and classrooms) by utilizing, in a manner consistent with the public interest, convenience, and necessity, …, or other regulating methods that remove barriers to infrastructure investment.

## Slide 13: Example: CFR 47
§ 15.5 General conditions of operation.
(a) Persons operating intentional or unintentional radiators shall not be deemed to have any vested or recognizable right to continued use of any given frequency by virtue of prior registration or certification of equipment, or, for power line carrier systems, on the basis of prior notification of use pursuant to §90.35(g) of this chapter.
(b) Operation of an intentional, unintentional, or incidental radiator is subject to the conditions that no harmful interference is caused and that interference must be accepted that may be caused by the operation of an authorized radio station, by another intentional or unintentional radiator, by industrial, scientific and medical (ISM) equipment, or by an incidental radiator.

## Slide 14: Process
NOI
NPRM
R&O
Notice of Inquiry
Notice of Proposed Rule Making
Report & Order
Petition for reconsideration
Federal court review
comments,
replies & ex parte
rarely

## Slide 15: FCC
Independent federal agency
About 1,600 employees
Chairman (D)
4 Commissioners (2 D, 2 R)
Consumer and Governmental Affairs
Enforcement
International
Media
Public Safety & Homeland Security
Wireless Telecommunications
Wireline Competition

## Slide 16: Open Internet Principles
Transparency. Fixed and mobile broadband providers must disclose the network management practices, performance characteristics, and terms and conditions of their broadband services;
No blocking. Fixed broadband providers may not block lawful content, applications, services, or non-harmful devices; mobile broadband providers may not block lawful websites, or block applications that compete with their voice or video telephony services
No unreasonable discrimination. Fixed broadband providers may not unreasonably discriminate in transmitting lawful network traffic.

## Slide 17: FCC Data - examples

## Slide 18: FCC data sets and reports of (Internet) interest
Measuring Broadband America (Internet performance measurements)
Broadband Progress Report (“706 report”)
  Broadband deployment data (“Form 477”)
International Broadband Data Report
Mobile Wireless Competition Report
Universal Service Monitoring Report (telephone service)
Telephone Subscribership in the United States
Report on Cable Industry Prices
Trends in Telephony Service
Not available:
  detailed price & subscription data
  outage and reliability information
Notes: http://www.fcc.gov/encyclopedia/trends-telephone-service

## Slide 19: What Was Measured
Sustained Download | Burst Download
Sustained Upload | Burst Upload
Web Browsing Download | UDP Latency
UDP Packet Loss | Video Streaming Measure
VoIP Measure | DNS Resolution
DNS Failures | ICMP Latency
ICMP Packet Loss | Latency Under Load
Total Bytes Downloaded | Total Bytes Uploaded

## Slide 20: Advertised vs. actual 2012

## Slide 21: Significantly better than 2011

## Slide 22: Access to broadband
Eighth Broadband Progress Report, August 2012

## Slide 23: State of competition (US)
FCC: Internet Access Services Status as of December 31, 2009
Notes: http://www.fcc.gov/Daily_Releases/Daily_Business/2010/db1208/DOC-303405A1.pdf: Internet Access Services: Status as of December 31, 2009

## Slide 24: Residential broadband penetration (US)

## Slide 25: International comparison: fixed
3rd International Broadband Data Report (IBDR), August 2012

## Slide 26: International data pricing - mobile
http://www.fcc.gov/document/international-broadband-data-report
3rd International Broadband Data Report (IBDR), August 2012

## Slide 27: International data pricing - mobile
http://www.fcc.gov/document/international-broadband-data-report

## Slide 28: The cost of networks

## Slide 29: Broadband virtuous cycle
fixed broadband
cellular broadband
applications
(e-learning, telemedicine, telework, …)
adoption
(relevance)
broadband availability

## Slide 30: Cost of bandwidth (2011)
Service | Speed (Mb/s) | Average price/month | $/Mb/s
DS1 (T1) | 1.54 | $450 | $292.20
DS3 | 45 | $5,000 | $111.11
Ethernet over Copper | 10 | $950 | $95.00
Fast Ethernet | 100 | $5,000 | $50.00
Metro Ethernet | 1000 | $25,000 | $25.00
Notes: http://www.shopforethernet.com/, September 2011

## Slide 31: The value of bits
Technologist: A bit is a bit is a bit
Economist: Some bits are more valuable than other bits
  e.g., $(email) >> $(video)
Application | Volume | Cost per unit | Cost / MB | Cost / TB
Voice (13 kb/s GSM) | 97.5 kB/minute | 10c | $1.02 | $1M
Mobile data | 5 GB | $40 | $0.008 | $8,000
MMS (pictures) | < 300 KB, avg. 50 kB | 25c | $5.00 | $5M
SMS | 160 B | 10c | $625 | $625M
Notes: T-Mobile 2010
AT&T data
http://www.nowsms.com/discus/messages/12/8500.html

## Slide 32: Broadband cost
70%
30%
e.g., CenturyLink: capital investment = 15% of revenues

## Slide 33: Maybe revisit?
Google
April 1, 2007

## Slide 34: Fiber deployment
wastewater pipe
(3-5 km/week)

## Slide 35: Broadband network cost - FTTP
Category | Details | Outside plant
FTTP in existing right-of-way | All underground, not including drops or electronics | $1,200…$1,300 per passing
 | 40% aerial, 60% underground, not including drops or electronics | $1,000…$1,100 per passing
FTTP drops | Range of distances and complexity | $300…$700 per connected home
Crown Fibre Holdings (Govt. of New Zealand); provided by CTC

## Slide 36: Broadband network cost – Fiber middle mile
Category | Details | Outside plant | Source
aerial, new attachment | Northeastern city municipal utility; 96% aerial, 4% underground; 87.6 miles | $30,000/mile | Public utility (actual cost)
aerial overlash | Major metropolitan area (U.S. east coast) | $15,000/mile | 
buried | Mixed suburban/urban locations and pot/bore construction | $89,000/mile | Washington, D.C.-area BTOP project (actual cost)
Data provided by CTC

## Slide 37: Middle mile cost example
CTC, 2009 (“Brief Engineering Assessment: Efficiencies available through simultaneous construction and co-location of communications conduit and fiber”)

## Slide 38: Broadband network cost – TV white spaces
Rural Appalachian community
3,000-passing service area
30% taking service
$2.4 million capital cost for all towers and electronics
  site, user, and backhaul
$800/passed
CTC design study for Garrett County, Maryland

## Slide 39: Concluding remarks

## Slide 40: Common fallacies in economic analysis
Assume perfect competition
  or ability to have multiple access providers
  or zero switching costs
Assume QoS = ATM or phone circuit
  rather than per-packet choice
Assume QoS for voice >> data
  TCP: 5% packet loss  500 kb/s max.
  Marginal cost difference between 80% and 100%-loaded network
Assume variable bandwidth demand
  Human-driven, with a bit of video quality adaptation
Ignore real-world profitability of entities
  non-existing profits shuffled to other parties
differentiated goods
Notes: Sandvine http://www.sandvine.com/downloads/documents/2010%20Global%20Internet%20Phenomena%20Report.pdfhttp://upload.wikimedia.org/wikipedia/commons/9/94/StochasticQueueingQueueLength.png

## Slide 41: Things policy makers might like to know…
Why is wireless/wireline broadband in my country more expensive or cheaper than in country X?
How can I ensure continued investment in network infrastructure?
What drives new network applications?
What is the impact of metered broadband?
  Will there be only one speed tier?
What is keeping 20-30% from adopting broadband?
Are there economic incentives to make networks more secure?

## Slide 42: Mobile data pricing

## Slide 43: Differentiation – classical models
Speed differentiation
  Residential broadband model
  European LTE plans (usually combined with volume)
  = rough division into non-video (web, email) & video customers
Volume metering
  Mobile model
  = rough division into video & non-video customers
  harder to visualize – discourages experimentation
  room for surprise
    mid-month cut-off
    bill shock
Commonly combined

## Slide 44: Differentiation – new models
Application restrictions
  “business” vs. personal use
  e.g., restrict tethering
  Open Internet concerns
Priority-based pricing
Content provider pays
  “like 800 numbers”
  potential for confusion? Which links are “free” and which aren’t?
  transaction costs – how to collect from millions of content providers?
  revenue potential?

## Slide 45: Example: vodafone.de
Plan | Speed | Volume
€ 17.99 | ≤ 3.6 Mb/s | 1 GB
€ 26.99 | ≤ 21.6 Mb/s | 3 GB
€ 35.99 | ≤ 42.2 Mb/s | 6 GB
€ 44.99 | ≤ 50.0 Mb/s | 10 GB
http://shop.vodafone.de/Shop/internet/mobile-internet-flat/
“unlimited” at 64 kb/s

## Slide 46: What about consumers?
Predictability – no “bill shock”
  “When did I download 1 GB and why?”
  What about teenagers?
Allow for a simple mental model
  Can users predict direct usage costs for activities?
  Do they want to know that the YouTube cat video costs $1.45?
  How close is day/night model to optimal model?
Minimize mental load
  Anticipating consequences
    It’s April 15 – am I going to run out by April 30? Or leave bytes on the table?
    Byte budgeting?
Perception of fairness
  Airline pricing?
  Why should I pay for my provider’s bugs?
Allow comparison between plans and providers
  Should I switch providers given my usage profile?
Notes: http://deborahstrickland.sys-con.com/node/1803559/mobile

## Slide 47: WiFi off-load
Cisco Visual Networking Index: Global Mobile Data Traffic Forecast 2012-2017
Notes: http://www.cisco.com/en/US/solutions/collateral/ns341/ns525/ns537/ns705/ns827/white_paper_c11-520862.html

## Slide 48: The 1% are becoming less dominant

## Slide 49: ARPU across providers
Provider | ARPU (month), US-based | Net income (1Q2013)
Verizon | $146.80* | $1.95B
AT&T | $65.20 | 
Google | $2.38 | $3.35B
Facebook | $0.74 | $64M
Netflix | $11.65 | $8M
Pandora (mobile) | $3.87 | $2.2M
*VZ is ARPA (per account)
Notes: http://www22.verizon.com/investor/news_verizon_reports_strong_revenue_and_customer_growth_for_verizon_wireless_and_fios_services_in_4q_2012.htm
http://www.fool.com/investing/general/2012/08/27/how-much-is-a-user-worth.aspx
http://www.forbes.com/sites/georgeanders/2012/07/26/facebook-ratio/
http://money.cnn.com/2012/05/16/technology/facebook-arpu/index.htm

## Slide 50: Demand shifting
time-flexible
time-rigid
software
updates
video
(sideloading)
email
voice & video call
navigation
augmented
reality
search
IM
web
(FB, news)
transactions
app store

## Slide 51: Advertising and two-sided markets
eCPM: $3.50 for PC, $0.75 for mobile
one click cost $0.84 on average (PPC)
one hour of higher-quality video: 1 GB = $10
  mobile: 10 MB / minute
 one minute commercial costs user $0.10
thus, plausible two-sided market for clicking on video ads
YouTube: Gangnam Style generated $0.0065 per play
  video is 4.2 minutes long  cost is $0.43
not so much for supporting video content
Notes: http://seekingalpha.com/article/717551-online-advertising-and-the-small-screen-problem
http://www.hochmanconsultants.com/articles/je-hochman-benchmark.shtml
http://www.theblaze.com/stories/2013/01/23/gangnam-style-video-earns-8-million-in-ad-revenue-on-youtube/

## Slide 52: Application usage
http://ciscovni.com/data_meter/
deferable
scalable
unclear which fraction is WiFi vs. cellular

## Slide 53: SINE: automated policy
Goal: make hetnets user-friendly
  primarily, $0 WiFi vs. $10/GB cellular
  but can accommodate variable cellular pricing
Policy engine:
  for each application, express value and delay tolerance
    “best network available, keep to $N/hour”
    “delay for N minutes”  email
    “user confirmation if cost > $X”
  willing to pay more as delay increases
    eventually, may pay for software download
Need better sideloading support for apps
  video queue, maps
Mapping database for predictive demand shifting
  “reaching WiFi in one hour”

## Slide 54: Conclusion
Economics of networks – more than micro economics
  = longer-term congestion control
    demand shifting in time (and space)
    realistic expectations for gain
    video already largely WiFi
  = price differentiation
Needs to take consumer behavior into account
  do users want to constantly watch the meter?
  realistic expectation of take-up – is 10% improvement worth the hassle as the smartphone novelty wears off?
  can we automate this?
Public policy concerns
  transparency
  non-discrimination
  effects on competition – carrier-carrier & vertical