## Slide 1: Transitioning the PSTN to IP
        Henning Schulzrinne

## Slide 2: The retirement of the circuit-switched network
What is happening and why does it matter?
What are the technical challenges we need to address?
  reliability & quality
  public safety (“911”, “112”)
  numbering & trustable identifiers
  universal service
  service stagnation  beyond voice?
  copper loops  competition, legacy services
It’s technical + economics + policy
US-centric, but similar elsewhere

## Slide 3: FCC’s Technology Transition Policy Task Force
  The Task Force’s work will be guided by the insight that, technological changes do not alter the FCC’s core mission, including protecting consumers, ensuring public safety, enhancing universal service, and preserving competition.
  The Task Force will conduct a data-driven review and provide recommendations to modernize the Commission’s policies in a process that encourages continued investment and innovation in these new technologies, empowers and protects consumers, promotes competition, and ensures network resiliency and reliability.

## Slide 4: The three transitions
From |  | to | motivation | issues
Copper |  | fiber | capacity maintenance cost | competition (“unbundled network elements”)
Wired |  | wireless | mobility cost in rural areas | capacity quality
Circuits |  | packets (IP) | flexibility cost per bit | line power
VoIP, VoLTE

## Slide 5: When?
TDM
switching
(core)
VoIP
access
fixed 4G
2013
no single transition date!
numbering
E.164
human-visible
hidden
“wireless network is 99% wired”

## Slide 6: The transition of the PSTN
User behavior changes
  more text, less voice
  video conferencing for personal & business use (telepresence)
  landline  mobile
  OTT VoIP (for international calls)
Core network technology changes
  IMS
  SIP trunking
Access and end system changes
  large PBX all VoIP
  voice as app
  WebRTC

## Slide 7: Landline  mobile

## Slide 8: Interstate switched access minutes

## Slide 9: Available access speeds
100 Mb/s+
20 Mb/s
5 Mb/s
2 Mb/s
1 Mb/s
18%
80%
95%
97%
100%
avg. sustained
throughput
of households
marginal VOIP
10 Gb/s
common now – future capability
1 Gb/s
10 Mb/s
99% by 2023?

## Slide 10: Access transitions (US)
Chart: 
| FTTH + HFC | FTTN + HFC | DSL | Satellite
Technology | 20 | 60 | 15 | 5
fiber
4G
copper
coax
unlicensed
wireless
⊕
networks go hybrid:
last 500-3000 ft

## Slide 11: Copper loops
DSL loop lengths
high-speed DSL
Copper loops  large-scale data competition (“unbundled network elements”)

## Slide 12: Cost vs. distance
Notes: http://www.mcleanbrown.com/pdf_docs/mandb_091709.pdf

## Slide 13: Lines are disappearing, but maintenance costs are constant
$2.72
per-line monthly
maintenance
cost
$17.57
voice revenue/line: $50
dis
voice only
(DSL: 20 M)
Chart: 
| 2007.0 | 2008.0 | 2009.0 | 2010.0 | 2011.0 | 2012.0 | 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0 | 2018.0 | 2019.0 | 2020.0
Residential | 93.89 | 80.52 | 71.6 | 63.05 | 54.3 | 46.16 | 38.59 | 31.89 | 26.04 | 21.03 | 16.8 | 13.24 | 10.32 | 7.77
Business | 54.43 | 54.27 | 49.72 | 45.57 | 43.15 | 40.32 | 37.12 | 33.84 | 30.5 | 27.24 | 24.07 | 21.03 | 18.14 | 15.21
JSI Capital Advisors projection
Notes: See http://jsicapitaladvisors.com/the-ilec-advisor/2011/10/20/communications-industry-forecast-2011-2020-ilec-and-clec-acc.html
See also NRRI Report 12-12, Oct. 2012

## Slide 14: Switches are ageing
1979
Nortel DMS-100
http://www.phworld.org/switch/ntess.htm

## Slide 15: PSTN: The good & the ugly
The good | The ugly
Global Connectivity (across devices and providers) | Minimalist service
High reliability (engineering, power) | Limited quality (4 kHz)
Ease of use | Hard to control reachability (ring at 2 am)
Emergency usage | Operator trunks!
Universal access (HAC, TTY, VRS) | No universal text & video
Mostly private (protected content & CPNI) | Limited authentication Security more legal than technical (“trust us, we’re a carrier”)
Relatively cheap (c/minute) | Relatively expensive ($/MB)

## Slide 16: What are some of the “keeper” attributes?
Universality
  reachability  global numbering & interconnection
  media  HD audio, video, text
  availability  universal service regardless of
    geography
    income
    disability
  affordability  service competition + affordable standalone broadband
Public safety
  citizen-to-authority: emergency services (911)
  authority-to-citizen: alerting
  law enforcement
  survivable (facilities redundancy, power outages)
Quality
  media (voice + …) quality
  assured identity: telephone numbers
  assured privacy (CPNI)
  accountable reliability
initial list – not exhaustive

## Slide 17: Universal service
Eligible Telecommunications Carriers
Carrier of Last Resort (COLR)
Universal Service Fund
For the purpose of regulating interstate and foreign commerce in communication by wire and radio so as to make available, so far as possible, to all the people of the United States, without discrimination on the basis of race, color, religion, national origin, or sex, a rapid, efficient, Nation-wide, and world-wide wire and radio communication service with adequate facilities at reasonable charges, for the purpose of the national defense, for the purpose of promoting safety of life and property through the use of wire and radio communications, … (47 USC § 151, 1934)
One Policy, One System, Universal Service
T. Vail
(1907)

## Slide 18: Long-term wireline architectures
SIP + RTP
SIP + RTP
SIP + RTP
or SS7 + TDM
SIP trunking
or residential
VoIP
analog loop
gateway
(class-5 replacement)

## Slide 19: Why not already?
Large part of corporate PBX already VoIP – why not everywhere?
Possible reasons – speculative:
  voice not seen as major profit center
  “good enough” – little service innovation
  switches paid for
  CPE upgrades needed to get new features (HD voice, video, advanced call features)

## Slide 20: Numbers: Disappearance of the old constraints

## Slide 21: The number is part of the problem
Geographically assigned (“area codes”)
  except for VoIP and cellular (US)
Separate numbering for SMS, voice, wireless, …
Only traditional carriers can obtain numbers
Complex local number portability
  limited wireless  wireline porting (“wire centers”)’
Service tied to number  makes 3rd party services difficult

## Slide 22: It’s just a number
Number | Type | Problem
201 555 1212 | E.164 | same-geographic different dial plans (1/no 1, area code or not) text may or may not work
#250, #77, *677 | voice short code | mobile only, but not all no SMS
12345 | SMS short code | SMS only country unclear
211, 311, 411, 911 | N11 codes | Distinct call routing mechanism Mostly voice-only May not work for VoIP or VRS
800, 855, 866, 877, 888 | toll free | not toll free for cell phone may not work internationally
900 | premium | voice only unpredictable cost

## Slide 23: Communication identifiers
Property | URL owned | URL provider | E.164 | Service-specific
Example | alice@smith.name sip:alice@smith.name | alice@gmail.com sip:alice@ilec.com | +1 202 555 1010 | www.facebook.com/alice.example
Protocol-independent | no | no | yes | yes
Multimedia | yes | yes | maybe (VRS) | maybe
Portable | yes | no | somewhat | no
Groups | yes | yes | bridge number | not generally
Trademark issues | yes | unlikely | unlikely | possible
Privacy | Depends on name chosen (pseudonym) | Depends on naming scheme | mostly | Depends on provider “real name” policy
Notes: http://findmyfacebookid.com

## Slide 24: Numbers vs. DNS & IP addresses
 | Phone # | DNS | IP address
Role | identifier + locator | identifier | locator (+ identifier)
Country-specific | mostly | optional | no
# of devices / name | 1 (except Google Voice) | any | 1 (interface)
# names /device | 1 for mobile | any | any
controlled by | carrier, but portability unclear (800#) and geo. limited | any entity, with trademark restrictions | any entity (ISP, organization)
who can obtain? | geographically-constrained, currently carrier only | varies (e.g., .edu & .mil, vs. .de) | enterprise, carrier
porting | complex, often manual; wireless-to-wireline may not work | about one hour (DNS cache) | if entity has been assigned PIAs
delegation | companies (number range) | anybody | subnets
identity information | carrier (OCN), billing name only  LERG, LIDB | WHOIS data (unverified) | RPKI, whois
Notes: http://www.nanpa.com/reports/faq.html#g1

## Slide 25: Number usage
FCC 12-46

## Slide 26: Phone numbers for machines?
212 555 1212
< 2010
500 123 4567
533, 544
now: one 5XX code a year…
(8M numbers)
see Tom McGarry, Neustar
500 123 4567
(and geographic numbers)
10 billion available
5 mio.
64 mio.
12% of adults
311,000
Notes: http://blog.neustar.biz/neustar-insights/telephone-numbers-are-for-people-not-machines/
http://www.parking.org/media/overview-of-the-us-parking-industry.aspx
http://www.statisticbrain.com/e-reader-statistics/
http://www.ite.org/reportcard/TechnicalReport.pdf

## Slide 27: Future numbers
Should numbers be treated as names?
  see “Identifier-Locator split”
  “multi-homing”
Should numbers have a geographic component?
  Is this part of a region’s cultural identity?

## Slide 28: Caller ID spoofing
Easily available on (SIP) trunks – can be legitimate
Used for vishing, robocalling, swatting, anonymity breaking, …
Caller ID Act of 2009: Prohibit any person or entity from transmitting misleading or inaccurate caller ID information with the intent to defraud, cause harm, or wrongfully obtain anything of value.
Also: phantom traffic rules

## Slide 29: Robocalling
“pink carriers”

## Slide 30: Security (trustworthiness)
Practically, mostly about identity, not content
Old model: “trust us, we’re the phone company”
Need cryptographically-verifiable information
  Is the caller authorized to use this number?
    not necessarily “ownership”
  Has the caller ID name been verified?
    cf. TLS

## Slide 31: Who assures identity?
Web:
  plain-text  rely on DNS, path integrity
    requires on-path intercept
  X.509 certificate: email ownership
    no attributes
  EV (“green”) certificate
PSTN
  caller ID
  display name: CNAM database, based on caller ID
Notes: http://www.cnamcallerid.com
https://www.opencnam.com
Truth in Caller ID Act of 2009

## Slide 32: Strawman “Public” PSTN database
Now: LIDB & CNAM, LERG, LARG, CSARG, NNAG, SRDB, SMS/800 (toll free), do-not-call, …
Future:
carrier code or SIP URLs
type of service (800, …)
owner
public key
…
1 202 555 1234
extensible set of fields
multiple interfaces (legacy emulation)
multiple providers
DB
HTTPS

## Slide 33: VoIP interconnection, public safety, universal access

## Slide 34: VoIP Interconnection
“VoIP interconnection” ≠ IP peering
Are there technical stumbling blocks?
  SIP features?
  Media codecs & conversion?
Separation application layer & transport
$0.001 / minute for IP transport ($0.10/GB)  location not relevant
Cisco
Notes: http://www.cisco.com/en/US/prod/collateral/routers/ps9343/data_sheet_c78-491738.html

## Slide 35: Public Safety (NG911 & NG112)
Transition to NG911 & NG112 underway
  NGxxx = all-IP (SIP + RTP) emergency calling
Key issues:
  Indoor location for wireless
    location accuracy of 50/150m may not be sufficient
    need apartment-level accuracy, including floor
    Civic (Apt. 9C, 5 W Glebe), not geo
  Cost, scaling and transition
Notes: Pictures: http://www.ksapco.net/psaps

## Slide 36: More than point-to-point voice
VoIP = Voice + Video + Vords (text)
   Real-time communication as base-level service?
Accommodate new media codecs (e.g., AMR)
See also “advanced communication systems” in U.S. Communications and Video Accessibility Act (CVAA)
Just point-to-point? or multipoint?
Services beyond call forwarding  web API model
  e.g., for robocall prevention

## Slide 37: Reliability
5 nines  5 minutes/year unavailable
How do we measure reliability & QoS?
  E.g., FCC Measuring Broadband America project?
   IETF LMAP
Can we improve power robustness?
  Circuit-switched: -48V @ 20-50 mA (~ 1 W)
  e.g., DOCSIS modem consumes ~7W (idle)
  Li-Ion battery = 2.5 Wh/$  3$/hour of standby time
Can we simplify multihoming to make new PSTN more reliable than old?
  e.g., cable + 4G

## Slide 38: Conclusion
Three simultaneous technology transitions:
  copper  fiber, wired  wireless, circuit  packet
But no cut-over date
Need to “grow up” quickly
  no more second network for reporting & fixing things
  universal service  Internet access for everyone
  single network  suitable for demanding services
  life-and-safety network
The Internet – your life will depend on it…