## Slide 1: Dealing with the 3 Great transitions
Henning Schulzrinne

## Slide 2: Lots of questions…
The Internet as infrastructure
The three great transitions
PSTN goes IP
Spectrum, spectrum, spectrum

## Slide 3: The three transitions
From |  | to | motivation | issues
Copper |  | fiber | capacity maintenance cost | competition (“UNE”)
Wired |  | wireless | mobility cost in rural areas | capacity quality
Circuits |  | packets (IP) | flexibility cost per bit | line power

## Slide 4: The Internet as infrastructure

## Slide 5: The great infrastructure
Technical structures that support a society  “civil infrastructure”
  Large
  Constructed over generations
  Not often replaced as a whole system
  Continual refurbishment of components
  Interdependent components with well-defined interfaces
  High initial cost
water
energy
transportation

## Slide 6: The Internet as core civil infrastructure
Involved in all information exchange
  (in a few years)
Crucial to
  commerce
  governance
  coordination
  inter-personal communication
Assumed to just be there
  “plumbing”, “pipes”, …

## Slide 7: Interfaces: Energy
1904
1901
110/220V
Lots of other (niche) interfaces
Replaced in a few applications

## Slide 8: Other long-lived interfaces
Cigarette lighter
(1956)
1878
1993
fuel nozzle
1982
SQL
1974
1992

## Slide 9: Interfaces: Transportation
1435 mm
1830 (Stephenson)
1846 UK Gauge Act
12’
About 60% of world railroad mileage

## Slide 10: The Internet Protocol Hourglass
email WWW phone...
SMTP HTTP RTP...
TCP UDP…
IP
ethernet PPP…
CSMA async sonet...
copper fiber radio...
small number of long-term stable interfaces
S. Deering

## Slide 11: Some Internet economics

## Slide 12: Bandwidth costs
Amazon EC2
  $50 - $120/TB out, $0/TB in
CDN (Internet radio)
  $600/TB (2007)
  $10-30/TB (Q1 2012 – CDNpricing.com)
NetFlix (7 GB DVD)
  postage $0.70 round-trip  $100/TB
FedEx – 2 lb disk
  5 business days: $6.55
  Standard overnight: $43.68
  Barracuda disk: $91 - $116/TB
Notes: FedEx and EC2 prices as of 09/15/09
CDN: http://www.mindbranch.com/listing/product/R678-29.html
http://www.cdnpricing.com/

## Slide 13: Internet transit costs
$ per Mb/s
per month

## Slide 14: The value of bits
Technologist: A bit is a bit is a bit
Economist: Some bits are more valuable than other bits
  e.g., $(email) >> $(video)
Application | Volume | Cost per unit | Cost / MB | Cost / TB
Voice (13 kb/s GSM) | 97.5 kB/minute | 10c | $1.02 | $1M
Mobile data | 5 GB | $40 | $0.008 | $8,000
MMS (pictures) | < 300 KB, avg. 50 kB | 25c | $5.00 | $5M
SMS | 160 B | 10c | $625 | $625M
Notes: T-Mobile 2010
AT&T data
http://www.nowsms.com/discus/messages/12/8500.html

## Slide 15: US broadband competition
DSL + cable
cable + fiber

## Slide 16: Broadband cost
70%
30%

## Slide 17: Maybe revisit?
Google
April 1, 2007

## Slide 18: Communication models – ca. 1980
TV (& radio)
broadcast
CATV
Telephone service
(voice, modem data, fax)
one-to-one
largely conduit
largely distributors

## Slide 19: Internet economic models - now
content and applications
fiber or copper loop
(“Homes with tails”)
IP
Google
Chatroulette
Level 3
RCN
content production (*)
content distribution
CDN
broadband access
local infrastructure
regional and national backbone
vs.
AT&T
Comcast/NBC (*)
Verizon
Notes: see old MCI functional separation

## Slide 20: Internet economic challenges
Specialization vs. vertical integration
Economies of scale  small number of competitors
  access networks (2)
  search engines (2)
  social networks (2)
Differentiated services (& prices)  1 Mb/s costs the same as 1 Gb/s
Who is (and can be) incented to invest in services and infrastructure?
Who gets to capture the value of bits?
  content/service provider vs. consumer surplus vs. provider profit

## Slide 21: The phone system is going IP

## Slide 22: Lines are disappearing, but maintenance costs are constant
NRRI Report 12-12, Oct. 2012
$2.72
per-line monthly
maintenance
cost
$14.89
voice revenue/line: $50

## Slide 23: Real-time: voice  non-voice
1950—2005: real-time ≡voice
Now: real-time = web interaction + text + voice
Displacement:
  teenage 2-hour chat  Facebook, IM
  coordination & transaction calls  web
    schedule appointments, travel agency, airline, …
  business calls  messaging
  “I’m heading home”  Google Latitude

## Slide 24: Copper loops
DSL loop lengths
high-speed DSL
Copper loops  large-scale data competition (“unbundled network elements”)

## Slide 25: Switches are ageing
1979
Nortel DMS-100
http://www.phworld.org/switch/ntess.htm

## Slide 26: Not the first PSTN technology transition
communication = data (“transmission”) + control (“signaling”)
invented 1888
deployed 1900s
1965
1894
Notes: http://www.corp.att.com/history/milestone_1965.html

## Slide 27: Evolution of VoIP
“amazing – the phone rings”
“does it do
call transfer?”
“How can I make it stop ringing?”
1996-2000
2000-2003
2004-2005
catching up
with the digital PBX
long-distance calling,
ca. 1930
going beyond
the black phone
2006-
“Can it really replace the phone system?”
replacing the
global phone system

## Slide 28: FCC transition goals
  The Task Force’s work will be guided by the insight that, technological changes do not alter the FCC’s core mission, including protecting consumers, ensuring public safety, enhancing universal service, and preserving competition.
  “The Task Force will conduct a data-driven review and provide recommendations to modernize the Commission’s policies in a process that encourages continued investment and innovation in these new technologies, empowers and protects consumers, promotes competition, and ensures network resiliency and reliability.”

## Slide 29: PSTN: The good & the ugly
The good | The ugly
Global Connectivity (across devices and providers) | Minimalist service
High reliability (engineering, power) | Limited quality (4 kHz)
Ease of use | Hard to control reachability (ring at 2 am)
Emergency usage | Operator trunks!
Universal access (HAC, TTY, VRS) | No universal text & video
Mostly private (protected content & CPNI) | Limited authentication Security more legal than technical (“trust us, we’re a carrier”)
Relatively cheap (c/minute) | Relatively expensive ($/MB)

## Slide 30: What are key attributes?
Universality
  reachability  global numbering & interconnection
  media  HD audio, video, text
  availability  universal service regardless of
    geography
    income
    disability
  affordability  service competition + affordable standalone broadband
Public safety
  citizen-to-authority: emergency services (911)
  authority-to-citizen: alerting
  law enforcement
  survivable (facilities redundancy, power outages)
Quality
  media (voice + …) quality
  assured identity: telephone numbers
  assured privacy (CPNI)
  accountable reliability

## Slide 31: Public Safety (NG911 & NG112)
Transition to NG911 & NG112 underway
  NGxxx = all-IP (SIP + RTP) emergency calling
Key issues:
  Indoor location for wireless
    location accuracy of 50/150m may not be sufficient
    need apartment-level accuracy, including floor
    Civic (Apt. 9C, 5 W Glebe), not geo
  Cost, scaling and transition
Notes: Pictures: http://www.ksapco.net/psaps

## Slide 32: Reliability
How do we measure reliability & QoS?
  E.g., FCC Measuring Broadband America project?
Can we improve power robustness?
  Circuit-switched: -48V @ 20-50 mA (~ 1 W)
  e.g., DOCSIS modem consumes ~7W (idle)
  Li-Ion battery = 2.5 Wh/$  3$/hour of standby time
  USB-powered devices  universal portable battery
Can we simplify multihoming to make new PSTN more reliable than old?
  e.g., cable + 4G

## Slide 33: Universal service
Eligible Telecommunications Carriers
Carrier of Last Resort (COLR)
Universal Service Fund
For the purpose of regulating interstate and foreign commerce in communication by wire and radio so as to make available, so far as possible, to all the people of the United States, without discrimination on the basis of race, color, religion, national origin, or sex, a rapid, efficient, Nation-wide, and world-wide wire and radio communication service with adequate facilities at reasonable charges, for the purpose of the national defense, for the purpose of promoting safety of life and property through the use of wire and radio communications, … (47 USC § 151, 1934)
One Policy, One System, Universal Service
T. Vail
(1907)

## Slide 34: It’s just a number
Number | Type | Problem
201 555 1212 | E.164 | same-geographic different dial plans (1/no 1, area code or not) text may or may not work
#250, #77, *677 | voice short code | mobile only, but not all no SMS
12345 | SMS short code | SMS only country unclear
211, 311, 411, 911 | N11 codes | Distinct call routing mechanism Mostly voice-only May not work for VoIP or VRS
800, 855, 866, 877, 888 | toll free | not toll free for cell phone may not work internationally
900 | premium | voice only unpredictable cost

## Slide 35: Numbers
Administered in blocks by NANPA
  funded by carriers: $5.9M/year
Separate processes for each number type
  Regular E.164 numbers by 1k blocks
Complicated LNP and porting technology
  often takes several phone calls to provider
  takes, at best, several hours
  limited wireline ⇔ wireless porting
  limited wireline out-of-area porting

## Slide 36: Numbers vs. DNS & IP addresses
 | Phone # | DNS | IP address
Role | identifier + locator | identifier | locator (+ identifier)
Country-specific | mostly | optional | no
# of devices / name | 1 (except Google Voice) | any | 1 (interface)
# names /device | 1 for mobile | any | any
ownership | carrier, but portability unclear (800#) | property, with trademark restrictions | ISP
who can obtain? | geographically-constrained, carrier only | varies (e.g., .edu & .mil, vs. .de) | enterprise, carrier
porting | complex, often manual; wireline-to-wireless may not work | about one hour (DNS cache) | if entity owns addresses
delegation | companies (number range) | anybody | subnets
identity information | wireline, billing name only | WHOIS data (spotty) | RPKI, whois
Notes: http://www.nanpa.com/reports/faq.html#g1

## Slide 37: Phone numbers for machines?
212 555 1212
< 2010
500 123 4567
533, 544
now: one 5XX code a year…
(8M numbers)
see Tom McGarry, Neustar
500 123 4567
Notes: http://blog.neustar.biz/neustar-insights/telephone-numbers-are-for-people-not-machines/

## Slide 38: Future numbers
Should numbers be treated as names?
  see “Identifier-Locator split” in Internet architecture
Should numbers have a geographic component?
  Is this part of a state’s cultural identity?

## Slide 39: More number questions…
Should numbers become personal property?
  Separate service from number
  Simplify number portability
  Can you put a 212 number in your will?
Divorce device from number
  any-to-any, dynamic mapping
Separate user identity & number

## Slide 40: Security (trustworthiness)
Practically, mostly about identity, not content
Old model: “trust us, we’re the phone company”
New reality: spoofed numbers & non-carrier entities
  both domestic and international
   SMS and voice spam
Need cryptographically-verifiable information
  Is the caller authorized to use this number?
  Has the caller ID name been verified?
    cf. TLS

## Slide 41: Who assures identity?
Web:
  plain-text  rely on DNS, path integrity
    requires on-path intercept
  X.509 certificate: email ownership
    no attributes
  EV (“green”) certificate
PSTN
  caller ID
  display name: CNAM database, based on caller ID
Notes: http://www.cnamcallerid.com
https://www.opencnam.com
Truth in Caller ID Act of 2009

## Slide 42: Caller ID spoofing
Caller ID Act of 2009: Prohibit any person or entity for transmitting misleading or inaccurate caller ID information with the intent to defraud, cause harm, or wrongfully obtain anything of value.

## Slide 43: Caller identification
name unimportant
bank ✔
credit card office ✔
known caller
previous calls
sent her emails
can you recommend student X?
name unimportant
IEEE ✔
known university ✔
what’s your SSN?

## Slide 44: Attribute validation
For unknown callers, care about attributes, not name
SIP address-of-record (AOR)  attributes
  employment (bank, registered 501c3)
  membership (professional)
  age (e.g., for mail order of restricted items)
  geographic location
Privacy
   selective disclosure
  no need to disclose identity

## Slide 45: Attribute Validation Service
Attribute Validation Server (AVS): Issuer
e.g., members.ieee.org
Caller: Principal
Alice
Student member in ieee.org
tel:+12345678
Callee: Relying Party
Bob
Accepts calls from members in ieee.org;
does not know Alice’s phone number
sips:bob@example.com
2. Makes a call with the ARID and part of access code
HTTP over TLS
SIP over TLS
3. Establishes the validity of the
ARID with access code and retrieves selected attributes e.g., Alice’s role
{Alice’s username, credentials, user ID, role}
1. Requests an ARID,
selecting attributes to disclose
Attribute Reference ID
(ARID)
e.g.,
https://members.ieee.org/arid/4163
c78e9b8d1ad58eb3f4b5344a4c0d5a
35a023
45

## Slide 46: “Public” PSTN databases
Now: LIDB & CNAM, LERG, LARG, CSARG, NNAG, SRDB, SMS/800 (toll free), do-not-call, …
Future:
carrier code or SIP URL
type of service (800, …)
owner
public key
…
1 202 555 1234
extensible set of fields

## Slide 47: VoIP Interconnection
“IP-IP interconnection”  don’t confuse with IP peering
Are there technical stumbling blocks?
  SIP features?
    IMS vs. non-IMS?
  Media codecs & conversion?
Separation application layer & transport
$0.000048 / minute for IP transport ($0.10/GB)

## Slide 48: More than voice
VoIP = Voice + Video + Vowels (text)
 Real-time communication as base-level service?
Accommodate new media codecs (e.g., AMR)
See also CVAA “advanced communication systems”
Point-to-point? or multipoint?

## Slide 49: Spectrum

## Slide 50
cellular = about 500 MHz in total

## Slide 51: From beachfront spectrum to brownfield spectrum
no interference!
guard bands!

## Slide 52: From empty back yard to time share condo
high tower, high power

## Slide 53: Spectral efficiency
b/s/Hz: modulation, FEC, MIMO, …
but also total spectral efficiency
  guard bands
  restrictions on adjacent channel usage
  “high power, high tower”  small cells  higher b/s/Hz
data efficiency
  e.g., H.264 is twice as good as MPEG-2/ATSC
  and maybe H.265 twice as good as H.264
distribution efficiency
  unicast vs. multicast
protocol efficiency
  avoid polling  need server mode
mode efficiency
  caching
  side loading
  pre-loading

## Slide 54: What can we do?
end system caching
better audio & video codecs
efficient apps
spectral efficiency (LTE-A)
directional antennas
general purpose spectrum
dense cells
white spaces & sharing
IP multicast
WiFi offload
small cells = better spectral efficiency + more re-use
LTE: 1.5 b/s/Hz
GSM: 0.1 b/s/Hz

## Slide 55: Unlicensed & lightly-licensed bands (US)
UHF (476-700 MHz) – incentive auctions (licensed) + some unlicensed
2.4 GHz (73 MHz) – 802.11b/g
3.6 GHz (100 MHz) – for backhaul & WISPs
4.9 GHz (50 MHz) – public safety
5.8 GHz (400 MHz) – 802.11 a/n
  much less crowded than 2.4 GHz
  supported by many laptops, few smartphones

## Slide 56: 2.4 vs. 5.8 GHz

## Slide 57: Freeing spectrum: incentive auctions
Incentive auctions will share auction proceeds with the current occupant to motivate voluntary relocation of incumbents
  Otherwise, no incentive for current occupant to give back spectrum
  Stations keep current channel numbers
    via DTV map
TV
TV
TV
TV
BB
BB
Without Realignment:
Reduced Broadband Bandwidth
TV
TV
BB
Adjacent Channel
Interference
With Realignment: Accommodates Increased Broadband Bandwidth
TV
TV
Adjacent Channel
Interference

## Slide 58: Small cell alternatives
Femto cells
  use existing spectrum
  need additional equipment
WiFi off-load
  use existing residential equipment
  5G networks = heterogeneous networks?
Distributed antenna systems
Femto-cells
Cellular
Distributed Antenna Systems
Signals are distributed throughout the
Building via amplifiers/antennas

## Slide 59: TV white spaces
2
4
5
7
9
3
6
8
10
Non-
Broadcast
spectrum
Non-
Broadcast
spectrum
New York City
Full Power
TV Stations
Philadelphia
Full Power
TV Stations
Low
Power TV
White
Space
White
Space
White
Space
White
Space
Etc.
Etc.
TV channels are “allotted” to cities to serve the local area
Other licensed and unlicensed services are also in TV bands
“White Spaces” are the channels that are “unused” at any given location by licensed devices
Low
Power TV
Only for illustrative purposes
Wireless
Microphones
Wireless
Microphones

## Slide 60: Spectrum Outlook
No single solution:
  reduce spectrum usage
    caching & better modulation
  re-use spectrum
  re-cycle old spectrum

## Slide 61: Conclusion

## Slide 62: My 2023 predictions
Still largely the same transmission technology
  fiber, OFDM
Still largely the same protocols
Similar applications
  but scaled up & integrated
Lots of boring new applications
  electric meter reading! finding parking spots!
Fewer cords (last mile & last foot)
Increasing complexity  serious security challenges

## Slide 63: Conclusion
Networks are too important to be left to (just) engineers
  but there are technology niches…
Key Internet problems are combinations of
  economic: who pays and gets paid?
  legal: who gets to do what?
  legacy: who doesn’t want to go away?
  political: who can make others do things they don’t like?