## Slide 1: Can the Internet survive the next 40 years?
Henning Schulzrinne

## Slide 2: Lots of questions…
What are the key attributes of the Internet that led to its success?
Can the Internet be made secure? (next time…)
What are the economic challenges for the Internet?
How can we ensure an open Internet for all?
What happens when old-style networks are being replaced?
What are the key challenges for the mobile Internet?
 engineering, economics & public policy

## Slide 3: The Internet as infrastructure

## Slide 4: The great infrastructure
Technical structures that support a society  “civil infrastructure”
  Large
  Constructed over generations
  Not often replaced as a whole system
  Continual refurbishment of components
  Interdependent components with well-defined interfaces
  High initial cost
water
energy
transportation

## Slide 5: The Internet as core civil infrastructure
Involved in all information exchange
  (in a few years)
Crucial to
  commerce
  governance
  coordination
  inter-personal communication
Assumed to just be there
  “plumbing”, “pipes”, …

## Slide 6: Interfaces: Energy
1904
1901
110/220V
Lots of other (niche) interfaces
Replaced in a few applications

## Slide 7: Other long-lived interfaces
Cigarette lighter
(1956)
1878
1993
fuel nozzle
1982
SQL
1974
1992

## Slide 8: Interfaces: Paper-based information
1798, 1922 (DIN)

## Slide 9: Interfaces: Transportation
1435 mm
1830 (Stephenson)
1846 UK Gauge Act
12’
About 60% of world railroad mileage

## Slide 10: The Internet Protocol Hourglass
email WWW phone...
SMTP HTTP RTP...
TCP UDP…
IP
ethernet PPP…
CSMA async sonet...
copper fiber radio...
small number of long-term stable interfaces
S. Deering

## Slide 11: Networking is getting into middle years
 | idea | current
IP | 1969, 1980? | 1981(RFC 791)
TCP | 1974 (RFC 675) | 1981(RFC 793)
telnet | 1969 (RFC15) | 1983 (RFC 854)
ftp | 1971 (RFC 114) | 1985 (RFC 959)
http | 1996 (RFC 1945) | 1999 (RFC 2616)
Notes: http://www.cs.utexas.edu/users/chris/think/ARPANET/Telnet/Telnet.shtml

## Slide 12: Which Internet are you connected to?
multicast
QoS
IPv6
IPv4
PIA
IPv4
DHCP
IPv4
NAT
port 80 + 25

## Slide 13: Some Internet economics

## Slide 14: Bandwidth costs
Amazon EC2
  $50 - $120/TB out, $0/TB in
CDN (Internet radio)
  $600/TB (2007)
  $10-30/TB (Q1 2012 – CDNpricing.com)
NetFlix (7 GB DVD)
  postage $0.70 round-trip  $100/TB
FedEx – 2 lb disk
  5 business days: $6.55
  Standard overnight: $43.68
  Barracuda disk: $91 - $116/TB
Notes: FedEx and EC2 prices as of 09/15/09
CDN: http://www.mindbranch.com/listing/product/R678-29.html
http://www.cdnpricing.com/

## Slide 15: Internet transit costs
$ per Mb/s
per month

## Slide 16: The value of bits
Technologist: A bit is a bit is a bit
Economist: Some bits are more valuable than other bits
  e.g., $(email) >> $(video)
Application | Volume | Cost per unit | Cost / MB | Cost / TB
Voice (13 kb/s GSM) | 97.5 kB/minute | 10c | $1.02 | $1M
Mobile data | 5 GB | $40 | $0.008 | $8,000
MMS (pictures) | < 300 KB, avg. 50 kB | 25c | $5.00 | $5M
SMS | 160 B | 10c | $625 | $625M
Notes: T-Mobile 2010
AT&T data
http://www.nowsms.com/discus/messages/12/8500.html

## Slide 17: US broadband competition
DSL + cable
cable + fiber

## Slide 18: Broadband cost
70%
30%

## Slide 19: Maybe revisit?
Google
April 1, 2007

## Slide 20: Fiber deployment
wastewater pipe
(3-5 km/week)

## Slide 21: Open Internet Principles
Transparency. Fixed and mobile broadband providers must disclose the network management practices, performance characteristics, and terms and conditions of their broadband services;
No blocking. Fixed broadband providers may not block lawful content, applications, services, or non-harmful devices; mobile broadband providers may not block lawful websites, or block applications that compete with their voice or video telephony services
No unreasonable discrimination. Fixed broadband providers may not unreasonably discriminate in transmitting lawful network traffic.

## Slide 22: Communication models – ca. 1980
TV (& radio)
broadcast
CATV
Telephone service
(voice, modem data, fax)
one-to-one
largely conduit
largely distributors

## Slide 23: Internet economic models - now
content and applications
fiber or copper loop
(“Homes with tails”)
IP
Google
Chatroulette
Level 3
RCN
content production (*)
content distribution
CDN
broadband access
local infrastructure
regional and national backbone
vs.
AT&T
Comcast/NBC (*)
Verizon
Notes: see old MCI functional separation

## Slide 24: Internet economic challenges
Specialization vs. vertical integration
Economies of scale  small number of competitors
  access networks (2)
  search engines (2)
  social networks (2)
Differentiated services (& prices)  1 Mb/s costs the same as 1 Gb/s
Who is (and can be) incented to invest in services and infrastructure?
Who gets to capture the value of bits?
  content/service provider vs. consumer surplus vs. provider profit

## Slide 25: Spectrum

## Slide 26
cellular = about 500 MHz in total

## Slide 27: From beachfront spectrum to brownfield spectrum
no interference!
guard bands!

## Slide 28: From empty back yard to time share condo
high tower, high power

## Slide 29: Spectral efficiency
b/s/Hz: modulation, FEC, MIMO, …
but also total spectral efficiency
  guard bands
  restrictions on adjacent channel usage
  “high power, high tower”  small cells  higher b/s/Hz
data efficiency
  e.g., H.264 is twice as good as MPEG-2/ATSC
  and maybe H.265 twice as good as H.264
distribution efficiency
  unicast vs. multicast
protocol efficiency
  avoid polling  need server mode
mode efficiency
  caching
  side loading
  pre-loading

## Slide 30: What can we do?
end system caching
better audio & video codecs
efficient apps
spectral efficiency (LTE-A)
directional antennas
general purpose spectrum
dense cells
white spaces & sharing
IP multicast
WiFi offload
small cells = better spectral efficiency + more re-use
LTE: 1.5 b/s/Hz
GSM: 0.1 b/s/Hz

## Slide 31: Unlicensed & lightly-licensed bands (US)
UHF (476-700 MHz) – incentive auctions (licensed) + some unlicensed
2.4 GHz (73 MHz) – 802.11b/g
3.6 GHz (100 MHz) – for backhaul & WISPs
4.9 GHz (50 MHz) – public safety
5.8 GHz (400 MHz) – 802.11 a/n
  much less crowded than 2.4 GHz
  supported by many laptops, few smartphones

## Slide 32: 2.4 vs. 5.8 GHz

## Slide 33: Freeing spectrum: incentive auctions
Incentive auctions will share auction proceeds with the current occupant to motivate voluntary relocation of incumbents
  Otherwise, no incentive for current occupant to give back spectrum
  Stations keep current channel numbers
    via DTV map
TV
TV
TV
TV
BB
BB
Without Realignment:
Reduced Broadband Bandwidth
TV
TV
BB
Adjacent Channel
Interference
With Realignment: Accommodates Increased Broadband Bandwidth
TV
TV
Adjacent Channel
Interference

## Slide 34: Small cell alternatives
Femto cells
  use existing spectrum
  need additional equipment
WiFi off-load
  use existing residential equipment
  5G networks = heterogeneous networks?
Distributed antenna systems
Femto-cells
Cellular
Distributed Antenna Systems
Signals are distributed throughout the
Building via amplifiers/antennas

## Slide 35: TV white spaces
2
4
5
7
9
3
6
8
10
Non-
Broadcast
spectrum
Non-
Broadcast
spectrum
New York City
Full Power
TV Stations
Philadelphia
Full Power
TV Stations
Low
Power TV
White
Space
White
Space
White
Space
White
Space
Etc.
Etc.
TV channels are “allotted” to cities to serve the local area
Other licensed and unlicensed services are also in TV bands
“White Spaces” are the channels that are “unused” at any given location by licensed devices
Low
Power TV
Only for illustrative purposes
Wireless
Microphones
Wireless
Microphones

## Slide 36: Spectrum Outlook
No single solution:
  reduce spectrum usage
    caching & better modulation
  re-use spectrum
  re-cycle old spectrum

## Slide 37: The phone system is going IP

## Slide 38: The three transitions
From |  | to | motivation | issues
Copper |  | fiber | capacity maintenance cost | competition (“UNE”)
Wired |  | wireless | mobility cost in rural areas | capacity quality
Circuits |  | packets (IP) | flexibility cost per bit | line power

## Slide 39: Copper loops
DSL loop lengths
high-speed DSL
Copper loops  large-scale data competition (“unbundled network elements”)

## Slide 40: Lines are disappearing, but maintenance costs are constant
NRRI Report 12-12, Oct. 2012
$2.72
per-line monthly
maintenance
cost
$14.89
voice revenue/line: $50

## Slide 41: Switches are ageing
1979
Nortel DMS-100
http://www.phworld.org/switch/ntess.htm

## Slide 42: Not the first PSTN technology transition
communication = data (“transmission”) + control (“signaling”)
invented 1888
deployed 1900s
1965
1894
Notes: http://www.corp.att.com/history/milestone_1965.html

## Slide 43: Evolution of VoIP
“amazing – the phone rings”
“does it do
call transfer?”
“How can I make it stop ringing?”
1996-2000
2000-2003
2004-2005
catching up
with the digital PBX
long-distance calling,
ca. 1930
going beyond
the black phone
2006-
“Can it really replace the phone system?”
replacing the
global phone system

## Slide 44: PSTN: The good & the ugly
The good | The ugly
Global Connectivity (across devices and providers) | Minimalist service
High reliability (engineering, power) | Limited quality (4 kHz)
Ease of use | Hard to control reachability (ring at 2 am)
Emergency usage | Operator trunks!
Universal access (HAC, TTY, VRS) | No universal text & video
Mostly private (protected content & CPNI) | Limited authentication Security more legal than technical (“trust us, we’re a carrier”)
Relatively cheap (c/minute) | Relatively expensive ($/MB)

## Slide 45: What are key attributes?
Universality
  reachability  global numbering & interconnection
  media  HD audio, video, text
  availability  universal service regardless of
    geography
    income
    disability
  affordability  service competition + affordable standalone broadband
Public safety
  citizen-to-authority: emergency services (911)
  authority-to-citizen: alerting
  law enforcement
  survivable (facilities redundancy, power outages)
Quality
  media (voice + …) quality
  assured identity: telephone numbers
  assured privacy (CPNI)
  accountable reliability

## Slide 46: Public Safety (NG911 & NG112)
Transition to NG911 & NG112 underway
  NGxxx = all-IP (SIP + RTP) emergency calling
Key issues:
  Indoor location for wireless
    location accuracy of 50/150m may not be sufficient
    need apartment-level accuracy, including floor
    Civic (Apt. 9C, 5 W Glebe), not geo
  Cost, scaling and transition
Notes: Pictures: http://www.ksapco.net/psaps

## Slide 47: Reliability
How do we measure reliability & QoS?
  E.g., FCC Measuring Broadband America project?
Can we improve power robustness?
  Circuit-switched: -48V @ 20-50 mA (~ 1 W)
  e.g., DOCSIS modem consumes ~7W (idle)
  Li-Ion battery = 2.5 Wh/$  3$/hour of standby time
Can we simplify multihoming to make new PSTN more reliable than old?
  e.g., cable + 4G

## Slide 48: Universal service
Eligible Telecommunications Carriers
Carrier of Last Resort (COLR)
Universal Service Fund
For the purpose of regulating interstate and foreign commerce in communication by wire and radio so as to make available, so far as possible, to all the people of the United States, without discrimination on the basis of race, color, religion, national origin, or sex, a rapid, efficient, Nation-wide, and world-wide wire and radio communication service with adequate facilities at reasonable charges, for the purpose of the national defense, for the purpose of promoting safety of life and property through the use of wire and radio communications, … (47 USC § 151, 1934)
One Policy, One System, Universal Service
T. Vail
(1907)

## Slide 49: FCC transition goals
  The Task Force’s work will be guided by the insight that, technological changes do not alter the FCC’s core mission, including protecting consumers, ensuring public safety, enhancing universal service, and preserving competition.
  “The Task Force will conduct a data-driven review and provide recommendations to modernize the Commission’s policies in a process that encourages continued investment and innovation in these new technologies, empowers and protects consumers, promotes competition, and ensures network resiliency and reliability.”

## Slide 50: Policy + technology

## Slide 51: Policy  technology
Part 15 (“unlicensed”)
  since 1938
  major revision 1989
    higher frequencies
    unintentional, incidental, intentional
    authorized devices
   WiFi
GPS in cell phones
  E911 rules
   location-based services
Notes: http://papers.ssrn.com/sol3/papers.cfm?abstract_id=1120465

## Slide 52: Policy  technology
Closed captioning
  initially, for Deaf and Hard of Hearing
  migrated to
    airports
    doctor’s offices
    sports bars
  enables text-based retrieval

## Slide 53: Policy inputs
Policy
Law
(1934 & 1996 Act)
Prior actions (e.g., VoIP definition)
Court cases (Brand X, Comcast, …)
Economic analysis
(competition, investment, consumers)
Other impacts (social policy objectives, fraud risk, …)

## Slide 54: Telecom policy tool kit
gov’t monopoly
laissez faire
price-regulated utility
structural
separation
facilities-based competition + interconnection
anti-trust
network neutrality
unbundled network elements
gov’t grants
(USF)
high cost + low income
disability access
public safety
CALEA

## Slide 55: Example: CFR 47
§ 15.5 General conditions of operation.
(a) Persons operating intentional or unintentional radiators shall not be deemed to have any vested or recognizable right to continued use of any given frequency by virtue of prior registration or certification of equipment, or, for power line carrier systems, on the basis of prior notification of use pursuant to §90.35(g) of this chapter.
(b) Operation of an intentional, unintentional, or incidental radiator is subject to the conditions that no harmful interference is caused and that interference must be accepted that may be caused by the operation of an authorized radio station, by another intentional or unintentional radiator, by industrial, scientific and medical (ISM) equipment, or by an incidental radiator.

## Slide 56: Process
NOI
NPRM
R&O
Notice of Inquiry
Notice of Proposed Rule Making
Report & Order
Petition for reconsideration
Federal court review
comments,
replies & ex parte
rarely

## Slide 57: FCC
Independent federal agency
About 1,600 employees
Chairman (D)
4 Commissioners (2 D, 2 R)
Consumer and Governmental Affairs
Enforcement
International
Media
Public Safety & Homeland Security
Wireless Telecommunications
Wireline Competition

## Slide 58: Policy  technology
Future opportunities:
  indoor location
  Video relay service = first multimedia phone-number-based interoperable real-time communication solution
  dynamic spectrum access (“TV white spaces”, 3.5 GHz band)

## Slide 59: Conclusion

## Slide 60: My 2023 predictions
Still largely the same transmission technology
  fiber, OFDM
Still largely the same protocols
Similar applications
  but scaled up & integrated
Lots of boring new applications
  electric meter reading! finding parking spots!
Fewer cords (last mile & last foot)
Increasing complexity  serious security challenges

## Slide 61: Conclusion
Networks are too important to be left to (just) engineers
  but there are technology niches…
Key Internet problems are combinations of
  economic: who pays and gets paid?
  legal: who gets to do what?
  legacy: who doesn’t want to go away?
  political: who can make others do things they don’t like?