## Slide 1: Source identity (origin authentication)
Henning Schulzrinne
August 2013
draft-peterson-secure-origin-ps-01
+ mailing list discussion

## Slide 2: Overview
Phone numbers will be with us for 10++ years
Their lack of validation is the main cause of phone-related criminality and nuisance
Related to domain name validation, but significant differences
  each country code has one (regulatory) root
Validate that originator of call is authorized to use From number
Earlier attempts have failed
The problem is well-scoped
  competing ideas are generally compatible
Known unknowns

## Slide 3: Two modes of caller ID spoofing
Impersonation
spoof target number
  personal or 800 number
Helpful for
  vishing
  stolen credit card validation
  retrieving voicemail messages
  SWATting
  disconnect utilities
  unwanted pizza deliveries
  retrieving display name (CNAM)
Anonymization
pick more-or-less random number
  including unassigned numbers
Helpful for
  robocalling
  intercarrier compensation fraud
  TDOS

## Slide 4: Robocalling
“pink carriers”

## Slide 5: Caller ID spoofing
Easily available on (SIP) trunks
US Caller ID Act of 2009: Prohibit any person or entity from transmitting misleading or inaccurate caller ID information with the intent to defraud, cause harm, or wrongfully obtain anything of value.
Also: FCC phantom traffic rules

## Slide 6: Legitimate caller ID spoofing
Doctor’s office
  call from personal physician cell phone should show doctor’s office number
Call center
  airline outbound contract call center should show airline main number, not call center
Multiple devices, one number
  provide single call-back number (e.g., Google Voice) from all devices
anonymity is distinct problem (caller ID suppression)

## Slide 7: Requirements
E.164 number source authenticity
  E.164 taken loosely (N11, P-ANI, non-reachable numbers, …)
  assume that numbers can be canonicalized for signing
    seems to work for VM, CDRs, SS7 translation, …
Complete solution (but not necessarily one mechanism)
  number assignment to validation
  validate caller ID
  later?: extended caller information
Functionality
  must work without human intervention at caller or callee
  minimal changes to SIP
  must survive SBCs
  must allow partial authorized & revocable delegation
    doctor’s office
    third-party call center for airline
  must allow number portability among carriers (that sign)

## Slide 8: Requirements
Privacy
  e.g., third parties cannot discover what numbers the callee has dialed recently
Efficiency
  will need a mode that causes minimal expansion of SIP headers (= suitable for UDP)
  e.g., caching of certs or public keys
Simplicity
  minimize overall complexity
  incremental deployment

## Slide 9: Not in scope
Validate other identifiers (e.g., sip:alice@example.com)
  might or might not translate (assignment hierarchy)
Validate textual caller ID (“CNAM”)
  anybody can call themselves “CARD HOLDER SVC”
Cross-national
  calls from +234 codes are not a major problem (right now)
Content (media) protection or integrity
   SRTP
Most man-in-the-middle signaling attacks
  e.g., evil proxy retargets call to grandma into selling Medicare supplements
  content (media) protection or integrity

## Slide 10: P-Asserted-Identity (RFC 3325)
RFC 3325 assumptions:
  originating end systems cannot alter SIP headers (or intermediate entities can be trusted to remove PAI headers)
  trusted chain of providers
P-Asserted-Identity: "Cullen Jennings" <sip:fluffy@cisco.com>
P-Asserted-Identity: tel:+14085264000

## Slide 11: RFC 4474 (SIP Identity)
INVITE sip:bob@biloxi.example.org SIP/2.0
Via: SIP/2.0/TLS pc33.atlanta.example.com;branch=z9hG4bKnashds8
To: Bob <sip:bob@biloxi.example.org>
From: Alice <sip:alice@atlanta.example.com>;tag=1928
Call-ID: a84b4c76e66710
CSeq: 314159 INVITE
Max-Forwards: 70
Date: Thu, 21 Feb 2002 13:02:03 GMT
Contact: <sip:alice@pc33.atlanta.example.com>
Identity: “KVhPKbfU/pryhVn9Yc6U=“
Identity-Info: <https://atlanta.example.com/atl.cer>;alg=rsa-sha1
Content-Type: application/sdp
Content-Length: 147
v=0
o=UserA 2890844526 2890844526 IN IP4 pc33.atlanta.example.com
s=Session SDP
…
changed by
SBC
SBC may change
domains

## Slide 12: Problems with RFC 4474
see rosenberg-sip-rfc4474-concerns
Cannot identify assignee of telephone number
Intermediate entity re-signs request
B2BUAs re-originate call request
  replace everything except method, From & To (if lucky)

## Slide 13: VIPR concerns
Uses PSTN for reachability validation
  “own” number  proof of previous PSTN call (start/stop time, …)
First call via PSTN
  doesn’t deal with robocalls
  “A domain can only call a specific number over SIP, if it had previously called that exact same number over the PSTN.”
Single, worldwide P2P network
  deployment challenging
Allows impersonator to find out who called specific number
draft-jennings-vipr-overview

## Slide 14: Changes in environment
Old (pre-2000) | new
Small number of carriers serving customers with fixed number pools (residential, inbound) | carriers that provide services to non-carriers (e.g., Google Voice, VRS) voice service providers (via APIs)
Carriers either larger or rural  trusted | “Pink” carriers (robocalls = lots of minutes)
Carriers with deep engineering skills | Telecom engineers fired or retired
Call routing determined by physical transport (MF or SS7) | logical routing via SIP proxies
Domestic calls stay within the country | call from NJ to NY may visit Berlin
#’s only for certificated carriers (~ 1000) | interconnected VoIP providers (trial)
1000 block assignment | individual numbers?
Geographic assignment (LATA, area code) | no direct relationship to geography (800#, mobile, VoIP, M2M, …)

## Slide 15: What makes solutions harder than in 2002?
Mostly E.164 numbers, not domain-based SIP URIs
Failure of public ENUM  no central database
B2BUA deployment
   SDP rewritten for most calls
Stickiness of infrastructure
  SS7 will be with us, unchanged, for decade+
Lots of non-SIP interconnection
  for both technical and non-technical reasons
  note: regulators typically encourage VoIP interconnection

## Slide 16: Changes: opportunities
Mobile, programmable devices
  IP connectivity
  allows (some) end system validation
IP-enabled PBX & SIP trunking
PKI developments, e.g., DANE

## Slide 17: Basic architecture
SS7
cert or public key
rendezvous mechanism
signs number
after normalization
validate
validate
validate
local carrier
LD carrier
may tunnel
as UUI

## Slide 18: Options
Number validation
Public key only (e.g., DNS)
public
private
X.509 cert
single certifier (per CC)
multiple certifiers per CC
single cert store (hierarchy)
any cert anywhere
separate delivery (URL)
single “CDN”
number-based access (no URL)
almost all of these could interoperate in single system

## Slide 19: Certificate models
Integrated with assignment
  assignment of number includes certificate: “public key X is authorized to use number N”
  issued by number assignment authority, possibly with delegation chain
    allocation entity  carrier  end user
separate proof of ownership
  similar to web domain validation
  e.g., Google voice validation by automated call back
    “Enter the number you heard”
  SIP OPTIONS message response?

## Slide 20: Delegation options
Official holder of number block interacts with registry
  “My customer TheDoctorIsOut can use 212-555-1234 out of my number block”
  requires database interaction
X.509 certificate delegation chain
  reveals relationship of carriers and customers

## Slide 21: Known unknowns
Who will sign first, by choice or mandate?
  large carriers (“get rid of robocall complaints”)
  legitimate outbound call centers (“I want my snow day alert to be received”)
  high-value users (“I want to prevent identity theft”)
  smartphone end users
Who will validate first?
  carriers concerned about intercarrier compensation fraud
  carriers sick of customer complaint calls
  new entrants looking for differentiator (“switch and no more robocalls!”)

## Slide 22: Incremental deployment
signed?
should be signed?
known caller?
validates?
N
N
N
Y
N
Y
Y
Y
N
Y

## Slide 23: Conclusion
Number spoofing is root of (almost) all phone evil
Number spoofing may accelerate decay of PSTN
Centralized number assignment makes problem tractable
Solution approaches based on different assumptions
  who is willing to do what & when?
All in for one approach or multiple solutions?
  reduce risk by multiple approaches?
  cost to central entities vs. cost to signers & validators
  or increase confusion, cost and non-adoption?