## Slide 1: Standard Interfaces: Prerequisite for Key Global Infrastructures
Henning Schulzrinne
FCC/Columbia University
06/2013

## Slide 2: The great infrastructure
Technical structures that support a society  “civil infrastructure”
  Large
  Constructed over generations
  Not often replaced as a whole system
  Continual refurbishment of components
  Interdependent components with well-defined interfaces
  High initial cost
water
energy
transportation

## Slide 3: The Internet as core civil infrastructure
Involved in all information exchange
  (in a few years)
Crucial to
  commerce
  governance
  coordination
  inter-personal communication
Assumed to just be there
  “plumbing”, “pipes”, …

## Slide 4: Interfaces: Energy
1904
1901
110/220V
Lots of other (niche) interfaces
Replaced in a few applications

## Slide 5: Interfaces: Paper-based information
1798, 1922 (DIN 476)
ISO 216 (1975)

## Slide 6: Interfaces: Transportation
1435 mm
4’ 8.5”
1830 (Stephenson)
1846 UK Gauge Act
1864 Transcontinental Railroad
1886 US standard
12’
About 60% of world railroad mileage

## Slide 7: Interfaces: Phone system
1970s
1949
Modular: 1975-
RJ11
4 kHz spectrum
48 V off-hook
275 mV audio
or 8 kHz digital

## Slide 8: Interfaces: fire hydrants
1904 John E. Hurst fire (Baltimore)
  destroyed 1,500 buildings
Reinforcements from DC, Philadelphia, NYC, …
but: fire hoses did not fit hydrants
  600 different versions
National standard 1905

## Slide 9: Other long-lived interfaces
Cigarette lighter
(1956)
1878
1993
fuel nozzle
1982
SQL
1974
1992
1841 (Whitworth)
Notes: http://en.wikipedia.org/wiki/Screw#Thread_standards

## Slide 10: What makes interfaces permanent?
Widely distributed, uncoordinated participants
Capital-intensive
  depreciated over 5+ years
  see Y2K problem
Allocation of cost vs. savings
  ISP saves money, end user pays
Hard to have multiple at once
  “natural monopoly”

## Slide 11: Extrapolating from history
IP now “the” data interface
Unclear that any packet-based system can be
  ≥ 10 times cheaper
  ≥ 10 times more functionality
  ≥ 10 times more secure
Replacing phone system due to generality, not performance
  IP offers general channel
 We’re stuck with IPv4/IPv6
  except for niche applications (car networks, BlueTooth, USB, …)

## Slide 12: Role of standards
Widespread use of technology requires standards
  railroad gauges, nuts & bolts, Morse code, phone system
    industrial age = interchangeable parts
Particularly for network technology
  many mid-size actors
  “network effect” = utility increases with number of users
    e.g., cars have inverse network effects
    chess game vs. email and word processor
  DECnet, SNA, ARCnet ⇒ Ethernet, IP
  “hypermedia” ⇒ HTML, HTTP

## Slide 13: The Internet Protocol Hourglass (S. Deering)
email WWW phone...
SMTP HTTP RTP...
TCP UDP…
IP
ethernet PPP…
CSMA async sonet...
copper fiber radio...

## Slide 14: Standards
Tanenbaum: “The nice thing about standards is that you have so many to choose from.”
VHS + Beta
Ethernet + Tokenring
ATM + IP
!
component technologies

## Slide 15: The standards route

## Slide 16: Standards as barrier to entry
Theodore Vail & E. J. Hall: AT&T standards for interconnection
  state regulators enforced
  company-wide standardization
China: LTE TDD, WiFi security, …
Nevertheless, in a number of sectors, concern has grown that China has pursued the development of unique national standards as the basis for its technical requirements, despite the existence of well- established international standards. Reliance on national standards could serve as a means of protecting domestic companies from competing foreign standards and technologies. The sectors affected include: automobiles, automotive parts, telecommunications equipment, wireless local area networks (see the "WAPI" section below), radio frequency identification technology, audio and video coding, fertilizers, food products, and consumer products, such as cosmetics. These China-specific standards, which sometimes appear to lack a particular technical or scientific basis, could create significant barriers to entry into China’s markets, because of the high cost of producing products that comply with the China-specific standards.
Notes: http://www.ustr.gov/sites/default/files/uploads/reports/2009/NTE/asset_upload_file868_15464.pdf

## Slide 17: Winner-take-all vs. winner-take-some
Complete substitute vs. overlapping
  Beta vs. VHS & Blue-ray vs. HD-DVD
  XM and Sirius
  Image file formats: JPEG for photographic images (lossy), GIF for rendered images (lossless)
Cost of adopting multiple standards
  e.g., low cost for image and video file rendering
  perfect format conversion?
Need for interoperation
  unknown destination
  e.g., Powerpoint vs. Apple Keynote
  but: flash memory mostly used locally
  role of DRM in restricting content mobility
Kemmerer/Liu/Smith, CACM 5/2013

## Slide 18: Flash memory

## Slide 19: Digital image formats

## Slide 20: FCC & standards
Carterfone decision (1968)
Part 68 rules
FCC Computer Inquiries
1983-1988: avoid direct standards setting
1983: approved T1 industry committee
  voluntary consensus standard
1988: declines to define digital standard
“safe harbor”
Notes: http://www.arussell.org/papers/2006Vol5Prt1_13.pdf
http://www.cybertelecom.org/library/hushaphone.htm
http://arstechnica.com/tech-policy/news/2008/06/carterfone-40-years.ars

## Slide 21: Example: GSM
Analog standards national
  no roaming, no economies of scale
1982: Groupe Spécial Mobile in CEPT
1987: 15 representatives from 13 European countries
1989: GSM migrates to ETSI
1990: Phase I spec
1992: first SMS
80% of global market

## Slide 22: GSM vs. multi-standard: consequences
GSM advantages
roaming: “native” or swapping SIM cards
interchangeable handsets
  earlier pre-pay market?
earlier SMS development
  vs. in-network-only messaging
lead in developing 3G as follow-on
US
Qualcomm?

## Slide 23: Example: OI
Standard Practices. The conformity or lack of conformity of a practice with best practices and technical standards adopted by open, broadly representative, and independent Internet engineering, governance initiatives, or standards-setting organizations is another factor to be considered in evaluating reasonableness. Recognizing the important role of such groups is consistent with Congress’s intent that our rules in the Internet area should not “fetter[]” the free market with unnecessary regulation, and is consistent with broadband providers’ historic reliance on such groups. We make clear, however, that we are not delegating authority to interpret or implement our rules to outside bodies.
Broadband providers’ practices historically have relied on the efforts of such groups, which follow open processes conducive to broad participation. See, e.g., William Lehr et al. Comments at 24; Comcast Comments at 53–59; FTTH Comments at 12; Internet Society (ISOC) Comments at 1–2; OIC Comments at 50–52; Comcast Reply at 5–7. Moreover, Internet community governance groups develop and encourage widespread implementation of best practices, supporting an environment that facilitates innovation. See supra Part II.A (discussing the benefits of edge providers having access to a uniform service interface, consisting of a core set of Internet standards and conventions); CDT Comments at 43–44.

## Slide 24: Telecom standards
Telecommunications and networking always focus of standardization
  1865: International Telegraph Union (ITU)
  1956: International Telephone and Telegraph Consultative Committee (CCITT)
First Internet RFC in 1969
First IETF meeting 1986

## Slide 25: Telecom standards
Application-specific
Data representation
Transport
Network
L2.5
MAC layer, RAN
Physical
Application protocols

## Slide 26: Standards: technology translator
Similar in some ways to text books
“accepted technology”
  lower/known risks (“vetted”)
  infrastructure (“eco system”)
    libraries, test tools, text books, certification, …
  reduce cost of picking among roughly equal choices
  sometimes reduce IPR risks (“patent pool”, RAND)
requires expertise and broader training
  many CS standards don’t have either
    example: HTTP/1.0, HTML 1.0, 802.11 WEP
Reasonable and Non Discriminatory Licensing

## Slide 27: Types of Standards
Mandatory vs. voluntary
  Allowed to use vs. likely to sell
  Example: health & safety standards UL listing for electrical appliances, fire codes
Types of standards
  performance standards
    “must survive fire for 30 minutes”
  interoperability standards
  system profiles
    “use option A, C and M”

## Slide 28: OMB circular A-119 (1998)
(1) Common and repeated use of rules, conditions, guidelines or characteristics for products or related processes and production methods, and related management systems practices.
(2) The definition of terms; classification of components; delineation of procedures; specification of dimensions, materials, performance, designs, or operations; measurement of quality and quantity in describing materials, processes, products, systems, services, or practices; test methods and sampling procedures; or descriptions of fit and measurements of size or strength.
Notes: http://www.whitehouse.gov/omb/circulars_a119

## Slide 29: OMB A-119: Performance vs. prescriptive
"Performance standard” … requirements in terms of required results with criteria for verifying compliance but without stating the methods for achieving required results.
A performance standard may define the functional requirements for the item, operational requirements, and/or interface and interchangeability characteristics.
juxtaposition to a prescriptive standard which may specify design requirements, such as materials to be used, how a requirement is to be achieved, or how an item is to be fabricated or constructed.

## Slide 30: OMB A-119: Voluntary Consensus Standard
"Voluntary consensus standards bodies" are domestic or international organizations which plan, develop, establish, or coordinate voluntary consensus standards using agreed-upon procedures.
Openness
Balance of interest
Due process
An appeals process
Consensus (“general agreement, but not necessarily unanimity”)

## Slide 31: Not all standards are equal
Can I access the standard document?
… for free?
What about preliminary drafts?
Who can contribute to the design of the standard?
  only one company or organization
  dues-paying members
  anybody
Do I have to pay to build a product based on the standard?
  patent licensing

## Slide 32: Open (and other) standards
proprietary standard (“de-facto standard”)
  controlled by single company
  may not be formally documented  reverse engineering
  e.g., Microsoft Word (.doc)
industry standard
  industry consortium (“XYZ Forum”)
open standard
  process requirements
  possibly free access
  well-defined patent policy
proprietary standards may be submitted for open standardization (e.g., ECMAscript, Java)
Notes: http://www.ansi.org/news_publications/other_documents/other_doc.aspx?menuid=7#Definition

## Slide 33: Open standards
consensus by a group or “consensus body” that includes representatives from materially affected and interested parties;
broad-based public review and comment on draft standards;
consideration of and response to comments submitted by voting members of the relevant consensus body as well as by the public;
incorporation of approved changes into a draft standard; and
availability of an appeal by any participant alleging that due process principles were not respected during the standards-development process.
2005 ANSI IPRPC Critical Issue Paper

## Slide 34: Standards and IPR
Standards are attractors of patent issues
  patent trolls (“non-practicing entities”)
  incumbents
Four steps to fortune:
  Get proprietary technology into standard (secretly)
  file patent & claim IPR
  sue every implementer
  ka-ching!
See Rambus case
Notes: http://www.idownloadblog.com/2011/07/17/patent-troll-2/
http://en.wikipedia.org/wiki/Rambus

## Slide 35: IPR licensing for standards
Royalty Free (RF)
  e.g., W3C
  only applies to working group members
Reasonable and non-discriminatory licensing (RAND)
  e.g., one possible IETF approach
  reasonable fees
    one-time fee
    unit fee (e.g., 20c/unit for H.264 video codec)
    percentage of retail price
  available on an equal basis to everybody
  hard to define “reasonable”
Mutual non-aggression licenses
  “don’t sue us and we won’t sue you”
  e.g., some Cisco licenses
Notes: http://www.w3.org/Consortium/Patent-Policy-20040205/
http://www.zdnet.com/blog/bott/a-closer-look-at-the-costs-and-fine-print-of-h264-licenses/2884?pg=2

## Slide 36: IPR
patent stacking: Taking out many patents for different aspects of a single innovation, thus forcing several royalty applications and payments
  one cell phone, 250,000 patents
standard-essential patents (SEPs): see Microsoft v. Motorola, 2013
Notes: http://www.mondaq.com/unitedstates/x/243154/Patent/Court+Determines+RAND+Rate+For+StandardEssential+Patents

## Slide 37: Patents
Tend to come in waves
  VoIP
  Smart phones

## Slide 38: Note Well
This summary is only meant to point you in the right direction, and doesn't have all the nuances. The IETF's IPR Policy is set forth in BCP 79; please read it carefully.
The brief summary:
By participating with the IETF, you agree to follow IETF processes.
If you are aware that a contribution of yours (something you write, say, or discuss in any IETF context) is covered by patents or patent applications, you need to disclose that fact.
You understand that meetings might be recorded, broadcast, and publicly archived.
For further information, talk to a chair, ask an Area Director, or review the following:
BCP 9 (on the Internet Standards Process)
BCP 25 (on the Working Group processes)
BCP 78 (on the IETF Trust)
BCP 79 (on Intellectual Property Rights in the IETF)

## Slide 39: Standards relationships
ITU
H.261 video
IETF
RTP, SIP
ITU
H.323
3GPP
cellular
NENA
9-1-1
SIP Forum
SIPConnect
system standards
protocol standards

## Slide 40: Internet Standardization
International Telecommunications Union (ITU)
      United Nations treaty organization
    Transmission standards (e.g., modem: V.90)
    Traditional telephone services, fax
IEEE
    anything electrical
    generally, link layer (IEEE 802.11)
Internet Engineering Task Force (IETF)
    Core: Internet Protocol, transport (TCP)
    Applications: email, HTTP, ftp, ssh, NFS, VoIP
    Not: HTML, XML, APIs

## Slide 41: W3C, OASIS, ATIS, ANSI, ISO
W3C
    HTML, XML, schema, SOAP, JavaScript APIs, semantic web, …
OASIS
    XML schema for specific applications
  Lots of other organizations: component vs. system engineering
ATIS, ANSI, ISO, …
  telecom standards
  operational standards

## Slide 42: ITU
Initially, national delegations
Members: state, sector, associate
  Membership fees (> 10,500 SFr)
Now, mostly industry groups doing work
Initially, mostly (international) telephone services
Now, transition from circuit-switched to packet-switched universe & lower network layers (optical)
Documents cost SFr, but can get three freebies for each email address

## Slide 43: Who makes the rules? - ITU
ITU = ITU-T (telecom standardization) + ITU-R (radio) + development
  http://www.itu.int
  14 study groups
  produce Recommendations:
    E: overall network operation, telephone service (E.164)
    G: transmission system and media, digital systems and networks (G.711, G.723)
    H: audiovisual and multimedia systems (H.323)
    I: integrated services digital network (I.210); includes ATM
    V: data communications over the telephone network (V.24)
    X: Data networks and open system communications (X.509)
    Y: Global information infrastructure and internet protocol aspects

## Slide 44: Example: IEEE balloting
IEEE-SA members only
Producers, users, general interest
  no group more than 50%
75% vote + 75% yes
30 to 60 days
Ballot comments: technical or editorial
Notes: http://standards.ieee.org/develop/balloting.html

## Slide 45: Example: IETF
Consensus mechanisms:
  the “working group hum”
  IESG DISCUSS: single DISCUSS holds up the document
    override with 2/3 yes votes
Notes: http://www.ietf.org/iesg/statement/discuss-criteria.html

## Slide 46: IETF
(based partially on slides by Lars Eggert, 2009/2010 and Scott Bradner, 2012)

## Slide 47: A quick overview of the IETF
The Internet Engineering Task Force is a loosely self-organized group of people who contribute to the engineering and evolution of Internet technologies. It is the principal body engaged in the development of new Internet standard specifications. RFC4677

## Slide 48: The IETF
Internet Engineering Task Force
formed in 1986
  evolved out of US ARPANET-related government activities
  Internet Configuration Control Board (ICCB) (1979) and Internet Activities Board (1983)
was not considered important for a long time - good!!
not “government approved” (US or other) - great!!
  although funding support from U.S. Government until 1997
people not companies
“We reject kings, presidents and voting. We believe in rough consensus and running code” Dave Clark (1992)

## Slide 49: The Internet Engineering Task Force – IETF
The IETF is an open, international community
  Network designers, operators, vendors and researchers
Goal: evolution of the Internet architecture and smooth operation of the Internet
Open to any interested individual
  “people, not companies”
Produces Internet standards (and other documents)
“We reject kings, presidents and voting. We believe in rough consensus and running code.”
Dave Clark (1992)

## Slide 50: The Role & Scope of the IETF
“Above the wire and below the application”
  IP, TCP, email, routing, IPsec, HTTP FTP, SSH, LDAP
  SIP, MobileIP, PPP, RADIUS, Kerberos secure email
  Streaming video & audio
  …
But wires are getting fuzzy
  MPLS, GMPLS, PWE3, VPN, ...
Hard to clearly define the IETF scope
  Constant exploration of the edges
“Since attendees must wear their name tags, they must also wear shirts or blouses. Pants or skirts are also highly recommended.”
RFC4677, The Tao of IETF: A Novice's Guide to the Internet Engineering Task Force

## Slide 51: IETF
Supposed to be engineering, i.e., translation of well-understood technology  standards
  make choices, ensure interoperability
  reality: often not so well defined
Most development work gets done in working groups (WGs)
  specific task, then dissolved (but may last 10 years…)
  typically, small clusters of authors, with large peanut gallery
  open mailing list discussion for specific problems
  interim meetings (1-2 days or phone calls) and IETF meetings (few hours)
  published as Internet Drafts (I-Ds)
    anybody can publish draft-somebody-my-new-protocol
    also official working group documents (draft-ietf-wg-*)
    versioned (e.g., draft-ietf-avt-rtp-10.txt)
    automatically disappear (expire) after 6 months

## Slide 52: IETF Meeting Attendance

## Slide 53: IETF by Numbers
1K-2K people at 3 meetings/year
  from ca. 40-50 different countries
  Many, many more on mailing lists
~120 Working Groups (WGs)
  ~2 WG chairs each
8 Areas with 15 Area Directors (ADs)
More than 6,300 RFCs published
  Internet Standards and informational documents
More than 50,000 Internet Draft revisions submitted
Chart: 
| US | CN | JP | SE | DE | FI | FR | KR | Others
Count | 388 | 101 | 92 | 92 | 69 | 46 | 40 | 35 | 221
Participants at IETF-75
Stockholm, July 2009
1084 total, 50 countries

## Slide 54: IETF 86 statistics

## Slide 55: Top-Level Organizational View
RFC Editor
IAOC
IAD
IESG
IASA
Areas

## Slide 56: ICANN
Internet Corporation for Assigned Names and Numbers
  manages IP address space (at top level)
  DNS top-level domains (TLD)
    ccTLD: country codes (.us, .uk, …)
    gTLDs (.com, .edu, .gov, .int, .mil, .net, and .org)
    uTLD (unsponsored): .biz, .info, .name, and .pro
    sTLD (sponsored): .aero, .coop, and .museum
  protocol constants
    port numbers, enterprise numbers, …
actual domains handled by registrars

## Slide 57: From protocol to RFC
Individual drafts
Working group drafts
Working group last call
repeat as needed
IETF last call
plus GenArea, security, …
IESG review
IANA actions
RFC publication

## Slide 58: Standards Track RFCs:
Best Current Practices (BCP)
  policies or procedures (best way we know how)
2-stage standards track (changed Oct 2011 - RFC 6410)
  Proposed Standard (PS)
  good idea, no known problems
  Internet Standard (STD)
  PS + stable + “benefit to Internet community”
  multiple interoperable implementations to prove document clarity
  note: interoperability not conformance

## Slide 59: Top-Level IESG & WG Structure
IETF is structured into Areas
  Each with Area Directors (ADs)
Areas are structured into Working Groups (WGs)
  Each with WG Chairs
Internet Engineering Steering Group (IESG) = all ADs
  Approves all Internet Standards
  Manages technical work
  Starts/ends WGs
  Assigns WG Chairs
General Area
J. Arkko
O&M Area
R. Bonica
B. Claise
Security Area
F. Farrell S. Turner
Internet Area R. Droms
B. Haberman
Routing Area
S. Bryant
A. Farrell
RAI Area
G. Camarillo R. Sparks
Applications Area
P. Resnick B. Leiba
Transport Area
W. Eddy M. Stiemerling
Internet Engineering Steering Group (IESG)
15 Area Directors
WG
WG
WG
WG
WG
WG
WG
WG
WG
WG
WG
WG
WG
WG
WG
WG
WG
WG
WG
WG
WG

## Slide 60: IETF WGs with regulatory impact
Regulatory issue | Area or WGs
Emergency calling | ECRIT, GEOPRIV
Emergency alerting | ATOCA
Universal service/intercarrier compensation | RAI
VoIP (numbering, caller ID spoofing) | TERQ, STIR
PSTN transition | RAI
Accessibility, video relay services | RAI
White spaces, spectrum | PAWS
Cybersecurity | DNSEXT
Competition | IPv6, MIF
Open Internet (network neutrality) | MPLS, DiffServ, email operations
Network measurement | IPPM

## Slide 61: Most Active IETF Participants

## Slide 62: IETF Documents – Two Types
Internet Draft (ID)
Active working documents
Not finalized! Not stable!
Anyone can submit
  draft-yourname-...
Only some IDs are WG documents!
  draft-ietf-wgname-...
Request for Comment (RFC)
Archival publications
  Never change once published
Not all RFCs are standards!
  Standards track:
    Proposed Standard
    Draft Standard
    Full Standard
  Other types:
    Informational
    Experimental
    Best-Current-Practice (BCP)

## Slide 63: IETF Document Format
English if the official language of the IETF; ASCII is the mailing list and document format
Various tools exits (xml2rfc, etc.)
Constant discussion of alternate formats
  IETF seen as “behind the times”
  (Almost) no drawings
  But no consensus on alternative
Note that the current format is still readable after 40+ years…

## Slide 64: IETF Organization – Areas
8 Areas to structure the technical work:
  Applications (APP)
  Transport Services (TSV)
  Security (SEC)
  Routing (RTG)
  Operations & Management (O&M)
  Real-Time Applications and Infrastructure (RAI)
  Internet (INT)
  General (GEN)

## Slide 65: IETF Organization – ADs
Area Directors (ADs)
  Each Area has 2, except for the General Area
ADs are responsible for:
  Setting direction in their Area
  Managing process in their Area
    Starting and closing Working Groups (WGs)
    Approving the scope of technical work
  Reviewing Working Group documents

## Slide 66: IETF Organization – IESG
Internet Engineering Steering Group (IESG)
  Formed by all 15 ADs
The IESG is the process management and RFC approval body
  Approves all WG creations
  Provides technical review
  Approves publication of IETF documents
  Reviews and comments on non-IETF submissions

## Slide 67: IETF Organization – IAB
Internet Architecture Board (IAB)
IAB provides overall architectural advice & oversight
  Provides “oversight” of IETF standards process
  Deals with IETF external liaisons to other SDOs
  Sponsors the Internet Research Task Force (IRTF)
  Write documents stating the IAB’s technical opinion
  Community & IESG review
  Participate in WG discussions

## Slide 68: IETF Organization – IRTF
Internet Engineering Research Task Force (IRTF)
Focused on long-term research problems in Internet
ASRG | Anti-spam
CFRG | Crypto forum
DTNRG | Delay-tolerant networking
HIPRG | Host identity
ICCRG | Internet congestion control
MOBOPTS | IP mobility optimizations
NMRG | Network management
P2PRG | Peer-to-peer
RRG | Routing
SAMRG | Scalable adaptive multicast
TMRG | Transport modeling
VNRG | Virtual networks

## Slide 69: IETF Organization – WGs
Where the IETF get its work done; belong to one Area
  Discussions on mailing list + meetings focused on key issues (ideally)
WG is focused by charter agreed between WG Chairs and ADs
  Restrictive charters with milestones – WGs close when their work is done
  No defined membership, just participants
“Rough consensus and running code”
  No formal voting - cannot define constituency
  Consensus does not require unanimity; disputes resolved by discussion

## Slide 70: IETF WGs
O&M Area
Security Area
Internet Area
Routing Area
RAI Area
Applications Area
Internet Research Task Force
A. Falk
Transport Area
6renum
adslmib
armd
bmwg
dime
dnsop
eman
grow
ipfix
mboned
netconf
netmod
opsawg
opsec
radext
v6ops
abfab
dane
dkim
emu
hokey
ipsecme
kitten
krb
msec
nea
oauth
pkix
tls
6lowpan
6man
ancp
autoconf
csi
dhc
dna
dnsext
hip
homenet
l2tpext
lisp
lwig
mext
mif
mip4
multimob
netext
ntp
pcp
pppext
savi
shim6
softwire
tictoc
trill
bfd
ccamp
forces
idr
isis
karp
l2vpn
l3vpn
manet
mpls
ospf
pce
pim
pwe3
roll
sidr
vrrp
atoca
avtcore, ext
bliss
clue
codec
dispatch
drinks
ecrit
enum
geopriv
mediactrl
mmusic
p2psip
payload
rtcweb
simple
sipclf
sipcore
siprec
soc
speechsc
speermint
splices
vipr
xcon
xmpp
xrblock
core
eai
ftpext2
httpbis
hybi
iri
marf
paws
precis
sieve
urnbis
vcarddev
websec
yam
alto
behave
cdni
conex
dccp
decade
fecframe
ippm
ledbat
mptcp
nfsv4
pcn
rmt
rohc
storm
tcpm
asrg
cfrg
dtnrg
hiprg
iccrg
mobopts
nmrg
p2prg
rrg
samrg
tmrg
vnrg
…bis = second (revision)

## Slide 71: RFC 5405 (UDP Guidelines)
Document was in individual and WG process for 481 days, and in IESG/RFC Editor process for 148 days, 629 days in total.
This is 1 years and 8 months.

## Slide 72: draft-cheshire-dnsext-multicastdns (Bonjour)
Document was in individual process for 2610 days, and in IESG/RFC Editor process for 262 days, 2872 days in total.
This is 7 years and 10 months. (And it’s not published yet…)

## Slide 73: The role of 3GPP
GSM, GPRS, W-CDMA, UMTS, EDGE, HSPA and LTE are all [RAN] Technologies specified by 3GPP
Core network and Systems architecture evolution have kept pace
Backward compatibility is a key element of each new 3GPP Release
73
The 3GPP Organizational Partners are Regional and National Standards Bodies;
Companies participate through their membership of one of these 6 Partners

## Slide 74: 3GPP Membership
74
371 Organisations (September 2010)

## Slide 75: Where the work is done
Chart: 
| Asia | Europe Middle East & Africa | North America
 | 4517 | 4689 | 2006
Meeting Delegates* by region (June 2010):
* Participants in TSG and WG meetings over the last year
Plenary meetings every 3 months, approve specifications and the Freezing of 3GPP Releases
The 50th TSG Plenary will be in Istanbul in December 2010

## Slide 76: Spanning the Generations...
GSM 1G
Analog technology. 1980s.
GSM 2G
Digital Technology - 1990s. New services such as SMS and low-rate data. IS-95 CDMA, GSM.
3G ITU’s IMT-2000
required 144 kb/s mobile, 384 kb/s
pedestrian, 2 Mb/s indoors;
CDMA2000 1X/EVDO, WiMAX,
and UMTS-HSPA.
4G ITU’s IMT-Advanced
operate in up to 40 MHz radio
channels and with very high
spectral efficiency. No technology meets requirements today.
IEEE 802.16m and LTE Advanced being designed to meet requirements.
3GPP Specified Radio Interfaces
  2G radio: GSM, GPRS, EDGE
  3G radio: WCDMA, HSPA, LTE
  4G radio: LTE Advanced
3GPP Core Network
  2G/3G: GSM core network
  3G/4G: Evolved Packet Core (EPC)
3GPP Service Layer
  GSM services
  IP Multimedia Subsystem (IMS)
  Multimedia Telephony (MMTEL)
  Support of Messaging and other OMA functionality
  Emergency services and public warning
  Etc.
Text adapted from 3G Americas White Paper, September 2010

## Slide 77: Building on Releases
Release 10 LTE-Advanced meeting the requirements set by ITU’s IMT-Advanced project.
Also includes quad-carrier operation for HSPA+.
Release 99: Enhancements to GSM data (EDGE). Majority of deployments today are based on Release 99. Provides support for GSM/EDGE/GPRS/WCDMA radio-access networks.
Release 4: Multimedia messaging support. First steps toward using IP transport in the core network.
Release 5: HSDPA. First phase of Internet Protocol Multimedia Subsystem (IMS). Full ability to use IP-based transport instead of just Asynchronous Transfer Mode (ATM) in the core network.
Release 6: HSUPA. Enhanced multimedia support through Multimedia Broadcast/Multicast Services (MBMS). Performance specifications for advanced receivers. Wireless Local Area Network (WLAN) integration option. IMS enhancements. Initial VoIP capability.
Release 7: Evolved EDGE. Specifies HSPA+, higher order modulation and MIMO. Performance enhancements, improved spectral efficiency, increased capacity, and better resistance to interference. Continuous Packet Connectivity (CPC) enables efficient “always-on” service and enhanced uplink UL VoIP capacity, as well as reductions in call set-up delay for Push-to-Talk Over Cellular (PoC). Radio enhancements to HSPA include 64 Quadrature Amplitude Modulation (QAM) in the downlink DL and 16 QAM in the uplink. Also includes optimization of MBMS capabilities through the multicast/broadcast, single-frequency network (MBSFN) function.
Release 8: HSPA Evolution, simultaneous use of MIMO and 64 QAM. Includes dual-carrier HSPA (DC-HSPA) wherein two WCDMA radio channels can be combined for a doubling of throughput performance. Specifies OFDMA-based 3GPP LTE.
Defines EPC.
Release 9: HSPA and LTE enhancements including HSPA dual-carrier operation in combination with MIMO, EPC enhancements, femtocell support, support for regulatory features such as emergency user-equipment positioning and Commercial Mobile Alert System (CMAS), and evolution of IMS architecture.
Text adapted from 3G Americas White Paper, September 2010

## Slide 78: Summary
No networks (and non-network interfaces) without standards
Different types of standards organizations
  component vs. system
  protocols vs. data formats
Important part of technology evolution
Interaction with IPR