## Slide 1: 5G: What can we learn from the previous four generations?
Henning Schulzrinne
Columbia University

## Slide 2: Design for 20 years

## Slide 3: Generational surprises
Generation | Expectation | Surprise
2G | better voice quality (“digital!”) | SMS
3G | WAP | web
4G | IMS | YouTube, WhatsApp
5G | IoT (low latency) | ?
underestimated cost and fixed-equivalence as drivers

## Slide 4: Lessons, in brief
Experience | Lessons
VoLTE, IMS | avoid complexity avoid entanglement plan intercarrier interfaces
Wi-Fi | don’t trust the RAN/AP
disaggregation of functions | clear & simple interfaces don’t assume trust between elements
app stores | keep it application-neutral
FTTH, backhaul cost | re-use backhaul where you can find it

## Slide 5: Complexity kills
IMS
Notes: http://voices.canonical.com/jussi.pakkanen/files/2012/01/synaptics-statemachine.png
http://upload.wikimedia.org/wikipedia/en/9/9c/TISPAN_IMS_Reference_Architecture.png

## Slide 6: Networks 1G through 4Gish
national carrier
one subscriber,
one phone,
one provider

## Slide 7: LTE – one carrier, plus roaming

## Slide 8: 5G – what exactly is a carrier?
LTE-U
802.11n
LTE
Level3
Cogent
Spectrum DB
Spectrum DB
40k towers each (US)

## Slide 9: 5G: Carriers as consumer brand
Outside
Inside

## Slide 10: What’s the simplest network?
AAA
HLR
(?)
IPv6 access
(any network)
DHCP
registrar
network characteristics (QoS)
IP address
AAA (incl. payment)
discovery
network
resources
one subscriber, multiple devices, multiple providers

## Slide 11: Where do we need mobility?
likely to have access provider diversity
  what is expected lifetime of IP address?
PMIP and MIP complex
  need to re-create application-layer security at L3
not really needed for HTTP video
  use mTCP?
  or HTTP restart?
maybe not even for real-time media
  registrar for new-call reachability
  application layer (SIP) mobility for mid-call hand-off?
or tunnels, tunnels everywhere?

## Slide 12: Make the network location-aware
2G/3G/4G are location-ignorant: “I only know your cell sector”
All mobile devices will be location-aware to the ~5 m
Some know where they will likely be in the near future
  public transit
  road navigation systems
   predict access and hand-off
All devices will have multiple radios
  use macro cell network to query for local access

## Slide 13: Simplify enrollment
enable access

## Slide 14: The law of new networks
“Any new network technology will be justified on (finally) providing QoS”
To succeed, they have to provide good-enough QoS for best effort
  at least with competition
The business model for QoS is difficult
  see bypass toll roads
QoS is usually not accessible to applications
  or not end-to-end

## Slide 15: IMS /VoLTE
IMS = It Mostly Speaks
VoLTE = Voice-Only Later than Expected

## Slide 16: Surge pricing – non-telecom
BI, 1/13/2015
Notes: Techcrunch

## Slide 17: Aggressive competitors compete on simplicity

## Slide 18: Capital investment
Company | Revenue | Capital expenditures | %
Comcast (US) [3Q14] | $11.04B | $1.644B | 14.9
Telekom (DE) [3Q14] | €15.6B | $2.58B | 16.5
Safaricom (KE) [H1FY15] | Ksh 79.34B | Ksh 12.37 | 15.5

## Slide 19: The value of bits
Technologist: A bit is a bit is a bit
Economist: Some bits are more valuable than other bits
  e.g., $/bit(email) >> $/bit(video)
  no-QoS bits dominate in volume
Application | Volume | Cost per unit | Cost / MB | Cost / TB
Cable video | 660 GB |  | $0.06 | $60
Voice (13 kb/s GSM) | 97.5 kB/minute | 10c | $1.02 | $1M
Mobile data | 5 GB | $40 | $0.008 | $8,000
MMS (pictures) | < 300 KB, avg. 50 kB | 25c | $5.00 | $5M
SMS | 160 B | 10c | $625 | $625M
Notes: T-Mobile 2010
AT&T data
http://www.nowsms.com/discus/messages/12/8500.html

## Slide 20: 5G prototype: Eduroam

## Slide 21: Growing-up lessons
Complexity kills
Play fair
CapEx is once, OpEx is forever
Know where you are
Share everything
Don’t trust strangers

## Slide 22: Backup

## Slide 23: LTE architecture
Notes: http://alcatel-lucent.com/enrich/v1i12007/article_c4a4.html

## Slide 24: Cell towers
Tower owner | Number of towers
Crown Castle | 39,739
American Tower | 40,000 (with VZW)
SBA Communications | 15,151
United Cellular Co. | 4,802
Verizon Wireless | 1,400
T-Mobile Towers | 1,003
Time Warner | 950
Mediacom Communications | 750
Charter Communications | 650
Diamond Communications | 637
Trillion Partners | 635
cost/tower: $150k
total US: 205k
Notes: http://www.statisticbrain.com/cell-phone-tower-statistics/
http://ir.sbasite.com/releasedetail.cfm?ReleaseID=908348

## Slide 25: Wireless market evolution