## Slide 1: Open internet
Henning Schulzrinne

## Slide 2: Open Internet/network neutrality
Conceptualized by Tim Wu (Columbia U.) and others
  general notion of non-discrimination (“neutrality”)
  details differ
Economic arguments
  foreclosure of new entrants
  vertical integration
Non-economic arguments
  participation, personal expression, …
Counter arguments
  free market interference
  disincents investment (uncertainty, implicit or explicit price regulation)
  lack of demonstrated harm
  anti-trust law as alternative
  1st amendment arguments (ISP as speaker)

## Slide 3: Common questions
Different charges for different types of content?
Block competing services (e.g., video or voice)?
Provide quality of service?
Block spam or denial-of-service traffic?
Prevent tethering except for a fee?
Usage-based charging ($/GB)?
Charge content providers?

## Slide 4: Some high-profile cases
Madison River (2005)
  DSL provider blocked SIP ports
  fined $15,000 by FCC
  based on Section 201 “just and reasonable”
Comcast (late 2007)
  insert TCP RST into BitTorrent traffic
  later overturned on appeal in DC Circuit Court
RCN (2009): P2P
Various mobile operators
Comcast vs. Level 3 (2010, in dispute) - interconnection
Comcast, Verizon, AT&T, … vs. Netflix
Notes: http://hraunfoss.fcc.gov/edocs_public/attachmatch/DA-05-543A1.pdf
http://www.zeropaid.com/news/88573/comcast-prevails-in-bittorrent-throttling-case/

## Slide 5: Background definitions
Telecommunications = the transmission, between and among points specified by the user, of information of the user's choosing, without change in the form or content of the information as sent and received. (47 U.S.C. § 153(43))
Telecommunications service = “the offering of telecommunications for a fee directly to the public, or to such classes of users as to be effectively available directly to the public, regardless of the facilities used." 47 USC § 153(46) (1999)
Information service = users of telecommunication services
cf. Basic vs. enhanced service (CI)
  Basic telecommunications: "the offering of a pure transmission capability over a communications path that is virtually transparent in terms of its interaction with customer supplied information.”
  Enhanced: everything else

## Slide 6: OI rules: definition
Broadband Internet access service. A mass-market retail service by wire or radio that provides the capability to transmit data to and receive data from all or substantially all Internet endpoints, including any capabilities that are incidental to and enable the operation of the communications service, but excluding dial-up Internet access service. This term also encompasses any service that the Commission finds to be providing a functional equivalent of the service described in the previous sentence, or that is used to evade the protections set forth in this Part.
Public Switched Network. The network that includes any common carrier switched network, whether by wire or radio, including local exchange carriers, interexchange carriers, and mobile service providers, that uses the North American Numbering Plan, or public IP addresses, in connection with the provision of switched services.

## Slide 7: Net neutrality is at the heart of a web of concerns
Direct linkages to anticompetitive behaviour, innovation and investment, privacy and data protection, consumer awareness, empowerment, and protection, and freedom of expression.
Indirect linkages to network and information security, broadband policy, Internet governance, and more.
J. Scott Marcus, 2015

## Slide 8: Technical Aspects: Quality of Experience (QoE)
Quality of Service (QoS) parameters and mechanisms are important to enable network operators to design, build and manage their networks, but they are not directly visible to end-users.
Crucial for end-users, however, is the quality that they personally during their use of a service.
These Quality of Experience (QoE) requirements are strongly dependent on the application. Some are sensitive to delay.
  E-Mail has little sensitivity to packet loss and delay.
  Real-time two-way Voice over Internet Protocol (VoIP) tends to be highly sensitive – delays greater than some 150 msec cause problems.
  Real-time two-way videoconferencing is similarly sensitive, and with greater bandwidth consumption.
  One-way video may or may not be sensitive, depending on user expectations for how quickly the stream starts (zapping time).
Delay-sensitive applications and mission critical services (police, fire, health, and transport) can benefit from managed Quality of Service (QoS).
J. Scott Marcus, 2015

## Slide 9: But QoS is more complicated…
Increased delay + usually, also loss (e.g., Wi-Fi or highly loaded link)  reduced TCP throughput
Thus, file transfer can be more QoS-sensitive than VoIP
  5% packet loss tolerable (with good codec) in VoIP
  5% kills TCP throughput  window size of ~1
More useful distinction:
  Some applications are more short-term QoS sensitive
  Reliability matters even for data applications (e.g., credit card reader)
N. Parvez, et al., “An Analytic Throughput Model for TCP NewReno”, 2010

## Slide 10: Economic background of network neutrality
At least three distinct strands of economic reasoning relates to differentiated quality of service in the Internet.
  Quality and price differentiation
  Economic foreclosure
  Two-sided (or multi-sided) markets
These interpretations are not necessarily incompatible, but they have different and possibly conflicting implications for public policy.
J. Scott Marcus, 2015

## Slide 11: Quality and price differentiation
Quality differentiation and price differentiation are well understood practices (cf. Hotelling (1929)).
In the absence of anticompetitive discrimination, differentiation generally benefits both producers and consumers.
BENIGN: We typically do not consider it problematic if an airline or rail service offers us a choice between first class and second class seats.
J. Scott Marcus, 2015

## Slide 12: Two-sided markets
The Internet can be thought of as a two-sided market, with network operators serving as a platform connecting providers of content (e.g. web sites) with consumers (cf. Tirole and Rochet (2004), and also Laffont, Marcus, Rey and Tirole (2003)).
RELATIVELY BENIGN: Under this view, some disputes are simply about how costs and profits should be divided between the network operators and the two (or more) sides of the market.
J. Scott Marcus, 2015

## Slide 13: Economic foreclosure
When a producer with market power in one market segment attempts to project that market power into upstream or downstream segments that would otherwise be competitive, that constitutes economic foreclosure.
PROBLEMATIC: Foreclosure harms consumers, and imposes an overall socio-economic deadweight loss on society. Foreclosure could be a concern in markets where effective market power (SMP) is given free rein.
J. Scott Marcus, 2015

## Slide 14: Differences between the US and the EU
The impending US regulatory approach responds to different circumstances than those relevant to Europe.
The overall US regulatory approach is partly a cause and partly a response to a very different marketplace.
Real consumer choice of an alternative broadband supplier in the US is limited to the point where the threat of consumers switching is no longer felt to constrain the behaviour of network operators.
The radical US deregulation of 2002-2005 left the US FCC with minimal ability to regulate broadband services; as a result, the US debate has been dominated by issues of legal sustainability rather than by policy goals.
J. Scott Marcus, 2015

## Slide 15: OI regulation: US
The FCC’s Report and Order of 12 March 2015 goes somewhat further than the 2010 Order.
  No Blocking: A person engaged in the provision of broadband Internet access service, insofar as such person is so engaged, shall not block lawful content, applications, services, or non-harmful devices, subject to reasonable network management.
  No throttling: A person engaged in the provision of broadband Internet access service, insofar as such person is so engaged, shall not impair or degrade lawful Internet traffic on the basis of Internet content, application, or service, or use of a non-harmful device, subject to reasonable network management.
  No paid prioritization: A person engaged in the provision of broadband Internet access service, insofar as such person is so engaged, shall not engage in paid prioritization. “Paid prioritization” refers to the management of a broadband provider’s network to directly or indirectly favor some traffic over other traffic …
J. Scott Marcus, 2015

## Slide 16: US OI rules: no blocking, no throttling
A person engaged in the provision of broadband Internet access service, …, shall not block lawful content, applications, services, or non-harmful devices, subject to reasonable network management.
A person engaged in the provision of broadband Internet access service, …, shall not impair or degrade lawful Internet traffic on the basis of Internet content, application, or service, or use of a non-harmful device, subject to reasonable network management.

## Slide 17: US OI rules: no paid prioritization
A person engaged in the provision of broadband Internet access service, …, shall not engage in paid prioritization.
“Paid prioritization” refers to the management of a broadband provider’s network to directly or indirectly favor some traffic over other traffic, including through use of techniques such as traffic shaping, prioritization, resource reservation, or other forms of preferential traffic management, either (a) in exchange for consideration (monetary or otherwise) from a third party, or (b) to benefit an affiliated entity.
The Commission may waive the ban on paid prioritization only if the petitioner demonstrates that the practice would provide some significant public interest benefit and would not harm the open nature of the Internet.

## Slide 18: US OI: general conduct rule
Any person engaged in the provision of broadband Internet access service, …, shall not unreasonably interfere with or unreasonably disadvantage (i) end users’ ability to select, access, and use broadband Internet access service or the lawful Internet content, applications, services, or devices of their choice, or (ii) edge providers’ ability to make lawful content, applications, services, or devices available to end users. Reasonable network management shall not be considered a violation of this rule.

## Slide 19: Open Internet/Network Neutrality evolution
specialized services
transparency
speed 
pricing
”no blocking”
non-discrimination
QoS
zero rating
FCC 2010

## Slide 20: EU BEREC NN (June 2016)
Based on EU Regulation 2015/2120
shall not block, slow down, alter, restrict, interfere with, degrade or discriminate between specific content, applications or services, or specific categories thereof, except as necessary, and only for as long as necessary
  but do not ban non- discriminatory data compression techniques which reduce the size of a data file without any modification of the content.
  E1: lawfulness of content, applications or services, or to public safety)
  E2: preserve the integrity and security of the network, of services provided via that network, and of the terminal equipment of end-users; (“This exception could be used as a basis for circumvention of the Regulation because security is a broad concept.”)
  prevent impending network congestion and mitigate the effects of exceptional or temporary network congestion, provided that equivalent categories of traffic are treated equally.

## Slide 21: Some OI references
Marcus (2014), “Network Neutrality Revisited: Challenges and responses in the EU and in the U.S.”, study for EU Parliament.
Marcus (2014), “The economic impact of Internet traffic growth on network operators”.
Marcus et al. (2011), “Network Neutrality”, study for EU Parliament.
Marcus (2010), “New Directions for U.S. Telecommunications Regulation? The Comcast decision and the ‘Third Way’”.
Rochet, Jean-Charles and Tirole, Jean (2004): “Two Sided Markets: An Overview”, March 2004, available at http://faculty.haas.berkeley.edu/hermalin/rochet_tirole.pdf
Jean-Jacques Laffont, Marcus, Patrick Rey, and Jean Tirole (2003), IDE-I, Toulouse, “Internet interconnection and the off-net-cost pricing principle”, RAND Journal of Economics, Vol. 34, No. 2, Summer 2003.
J. Scott Marcus, 2015