## Slide 1: Network technology review
Henning Schulzrinne
material drawn from various online sources, reports & author

## Slide 3: Dividing the problem

## Slide 4: The great infrastructure
Technical structures that support a society  “civil infrastructure”
  Large
  Constructed over generations
  Not often replaced as a whole system
  Continual refurbishment of components
  Interdependent components with well-defined interfaces
  High initial cost
water
energy
transportation
communication

## Slide 5: The Internet as core civil infrastructure

## Slide 6: Broadband, Internet, communications
Broadband (Internet)
dial-up
LMR

## Slide 7: Interdependencies with other lifelines
Trans
Power
Pipelines
Water
towers & antennas
outside plant
CO & DC
Telecom
shared
RoW
shared
poles
flooding
fuel
parts
recovery coordination
control

## Slide 8: Who runs communication systems and networks?
radio & TV stations
(1,784 TV, 15,470 radio)
cable companies
(“MVPD”)
communities (“muni networks”)
cellular providers (3-4)
wholesaler providers
(“carriers’ carrier”)
incumbent local exchange carriers
(“ILEC”)
satellite providers
private land mobile radio (public safety, transit, taxis, …)
competitive local exchange carriers
(“CLEC”)
rural local exchange carriers
(“RLEC”)
~1,000
# with ~90% marketshare
~12
~2

## Slide 9: European and US telecom operators

## Slide 10
Where does Europe stand compared to the rest of the world ? 3
3. A global transformation to a digital economy, fierce competition :
Gerard de Graaf European Commission

## Slide 11
Where does Europe stand compared to the rest of the world ? 1
A global transformation to a digital economy, fierce competition :
- fixed access to the internet
European Commission, OECD
Gerard de Graaf European Commission

## Slide 12: What do communications networks do that’s different?
Any-to-any: multiparty, coordination & cooperation, conflict
  less of a concern in (say) civil engineering
Economics: network effect, scale effects
Challenges:
  geographic distribution
  long-lived
  different industries participating

## Slide 13: What problems do networks solve?
Diversity in technologies
  wired vs. terrestrial wireless vs. satellite
  trade-off capacity vs. cost vs. distance
Variation in load
  intermittent demand  shared networks
  cannot design capacity for top 5 minutes of load
“Noise”
  electric noise
  radio interference
Human adversaries
  denial-of-service attacks
  information theft
  impersonation

## Slide 14: Network trade-offs
capacity per user
cost per user
* incremental cost assuming legacy networks;
“green field” cost is roughly the same

## Slide 15: A bit of (US) history
1895-1901: G. Marconi demonstrates wireless communications
1912: Titanic
Radio Act of 1912
  all radio stations licensed
  monitor distress channel (500 kHz)
Radio Act of 1927
  deal with AM (“medium wave”) chaos  licensing “in the public interest”

## Slide 16: Communications as a regulated industry
free-market economies, subject to government regulation
  “why” (and objections) later
telephony: federally regulated since 1910
broadcasting: 1927
telecommunications: 1934
  but dates back to Interstate Commerce Act of 1887 (railroads)
  cousins: railroads, electricity, air service, …
  specialized administrative agency for sector-specific regulation
    vs. general regulation (environmental, safety, employment, contracts, consumer protection, …)
Notes: Benjamin

## Slide 17: The Internet as core civil infrastructure
Involved in all information exchange
  (in a few years)
Crucial to
  commerce
  governance
  coordination
  inter-personal communication
Assumed to just be there
  “plumbing”, “pipes”, …

## Slide 18: Technology comes & goes, interfaces are forever
1904
1947
1908
1878
1993
fuel nozzle
1885?
1982
1974
1992
1956
1970s
Notes: http://www.cpcstech.com/usoc-universal-service-ordering-code-information.htm

## Slide 19: The two-layer model
content
apps & software
services
“Lower layers”
infrastructure
“the network”
copyright
universal service
disability access
investment
technology innovation
patents
resource scarcity
data privacy
location privacy
IP
data theft
disruption

## Slide 20: Layering
generality
functionality
email
any digital
communications
unreliable bits
over one link
secure, reliable, world-wide
L7
PHY (L1)

## Slide 21: The real model

## Slide 22: The Internet Protocol Hourglass
email WWW phone...
SMTP HTTP RTP...
TCP UDP…
IP
ethernet PPP…
CSMA async sonet...
copper fiber radio...
small number of long-term stable interfaces
S. Deering

## Slide 23: Why four (core) layers?
Layer | Colloquial name | Function
1 | PHY | photons & electrons  bits
2 | MAC | bits  packets on one technology
3 | L3 | packets end-to-end, on heterogeneous technologies, to interface
4 | L4 | unreliable  reliable host/interface  application
(5) | Presentation, data | application data structure encoding
7 | Application | Application behavior (email, web)

## Slide 24: History of the Internet: serialization
ad-hoc
binary
ASN.1
TLV
XML
JSON
CBOR
RFC822
HTTP/2.0

## Slide 25: Serialization: ASN.1
30 13 02 01 05 16 0e 41 6e 79 62 6f 64 79 20 74 68 65 72 65 3f
serialization = convert data structure into
(linear) byte stream
like C, without pointers…

## Slide 26: Serialization: RFC 822
Delivered-To: hgs10@lionmailmx.cc.columbia.edu
Received: by 10.140.158.132 with SMTP id e126csp131562qhe;
Thu, 28 Aug 2014 14:01:48 -0700 (PDT)
Return-Path: etickets@amtrak.com
Return-Path: etickets@amtrak.com
Received: from unknown (HELO etvswas01p) ([10.14.128.202])
by phlsmtprelay01.amtrak.com with ESMTP; 28 Aug 2014 16:55:42 -0400
Date: Thu, 28 Aug 2014 17:01:30 -0400 (EDT)
From: etickets@amtrak.com
To: HGS@cs.columbia.edu, HENNING.SCHULZRINNE@FCC.GOV
Message-ID: <633700356.JavaMail.TDDServerProd@amtrak.com>
Subject: Amtrak: eTicket and Receipt for Your 09/10/2014 Trip
MIME-Version: 1.0
Content-Type: multipart/mixed;
boundary="----=_Part.1409259690306”
MIME-Version: 1.0
Content-Type: multipart/mixed;

## Slide 27: Serialization: converting data structures into a byte stream
JSON
XML

## Slide 28: What makes a good serialization?
 | Binary | ASN.1 | RFC822 | TLV | XML | JSON | CBOR
Schema | informal | ✅ | ABNF | informal | XSD | in progress | ?
Compact | ✅ | ? | ❌ | ✅ | ❌ | 😐 | ✅
Secure | ✅? | ? | ❌(BO) | ✅ | ? | ✅ | ?
Fast (parsing) | ✅ | ❌ | ✅ | ✅ | ❌ | 😐 | ✅
Extensible | ❌ | ✅ | ✅ | ✅ | ✅ | ✅ | ✅
Self-describing | ❌ | ✅ (not ERs) | ✅ | ❌ | ✅ | ✅ | ❌
Security: loops (recursion), buffer overflows (length & pointers)

## Slide 29: The problems with layering
Doesn’t capture whole story
  control protocols
Information hiding
  inefficiency: more than needed
Information and implementation leakage
Ossification
Duplication
  “If you want it done right, you have to do it yourself”
Notes: Charles-Guillaume Étienne

## Slide 30: Internet architecture

## Slide 31: Internet traffic flows today
31
backbone (transit)
content
access network
(data center provider)
eyeball ISP
comm.
CDN
CDN
Level3
Cogent
Comcast
Google
Facebook
YouTube
Yahoo
Live
Baidu
Akamai
server farm
video
conferencing
content CDN
Netflix

## Slide 32: Network types
Access
  “last mile”
Regional or metro
  “metro fiber”, “metro Ethernet”
Wholesale
  connect points-of-presence across
  may also provide access to commercial buildings & data centers
Trans-oceanic
  often, owned separately (consortium), but integrated into wholesale networks

## Slide 33: A backbone network

## Slide 34: 1901 “data” backbone

## Slide 35: Submarine cable map
http://www.telegeography.com/
Notes: http://www.telegeography.com/

## Slide 36: It’s all spectrum - phone
Notes: http://www.voipsupply.com/images/voice_freq_range.jpg

## Slide 37: It’s all spectrum - wires
200 - 347 THz
1 GHz
10 MHz
copper
4 kHz

## Slide 38: It’s all spectrum - modem
Notes: http://hackadaycom.files.wordpress.com/2013/01/dial-up-handshake-infographic.png

## Slide 39: Fundamental limit to channel capacity
channel capacity
(bits/second)
bandwidth
(Hz)
signal-to-noise ratio
(typically, dB)
Shannon-Hartley limit

## Slide 40: Shannon examples
SNR (dB) = 10 log10 (S/N)
Telephone modem: SNR = 20 dB (1:100); frequency 4 kHz  4,000 log2 (101) = 26.63 kb/s
Noise can be larger than signal!
   negative SNR
Less noise  higher signal power
Only true for simple channel models
  “additive Gaussian white noise” (AWGN)
Spectral efficiency: bits per second per Hz
  often, around 1-2 b/s/Hz, but can be much higher

## Slide 41: It’s all spectrum - radio
typical cell channel:
5-20 MHz
FM radio: 100 kHz
TV: 5 or 6 MHz
AM radio: 9 or 10 kHz

## Slide 42: How is spectrum allocated?
ITU
AWS3 (2014): $2.65 MHz-Pop

## Slide 43: Spectrum sharing
How much politeness & fairness is required?
 LTE-U & LTE-LAA (license-assisted, listen-before-talk)
Notes: “Priority-Based Classification of Spectrum Access Models”, August 2013

## Slide 44: The value of spectrum
Spectrum auction prices vary dramatically:
  Germany June 2015: 0.23€ MHz per unit of population (pop)
    700, 900, 1500, 1800 MHz bands
  US February 2015: 2.71 US$/MHz/pop
    65 MHz:
      50 MHz paired in 1755-1780 & 2155-2180 MHz
      15 MHz unpaired in 1695-1710 MHz
Depends on
  timing – other auctions past and future
  competition (foreclosure, entry)
  encumbrances
  alternatives – densification
  availability in devices (bands)
Notes: http://telecoms.com/opinion/the-german-spectrum-auction-failure-to-negotiate/

## Slide 45: The economic value of spectrum
Valuing the use of spectrum in the EU, GSMA, June 2013

## Slide 46: Auctions have limitations
One-time estimate of value
  most spectrum is licensed indefinitely (US) or long-term (EU)
  technology may change value – up or down
    e.g., small cells, MIMO
  new neighbors may change value
  typical spectrum value:
May encourage speculation
  build-out requirements help (and common), but can be 3-10 years
Relies on small (3-4) number of carriers
  only subscription model
  how do you aggregate the value of 5.8 GHz spectrum?
Likely necessary where spectrum requires nationwide multi-$B investment

## Slide 47: Alternative models
Sharing by usage
  indoor vs. outdoor
  satellite vs. terrestrial (directional antennas!)
  multiple bands  rendezvous band  spectrum database
Unlicensed initially only home and enterprise
  and limited rural wireless ISPs (WISPs)
But CableWiFi and FON show other models
  cheap infrastructure
  existing high-capacity fiber/coax deployment (backhaul)
  emphasis on nomadic, not mobile, use
  emphasis on data, not voice  tolerate quality variability
  easily shareable among providers (just authentication)
 neutral spectrum provider
  cf. shared infrastructure models (Europe)

## Slide 48: Spectrum Databases
A wide range of solutions may be involved to enable dynamic spectrum sharing and should be considered in Spectrum DataBase (SDB) frameworks .
Unlicensed
Limits in Power Adequate
Local Sensing
Strong, detectable
signals
(e.g. DFS)
Sensing Networks
More Complex Detection, and better siting
Time Specific Exclusion
Database Driven
(e.g. SAS)
Fixed Exclusion
If Undetectable, or constantly on
Fixed Rules in Devices
Adjustable Rules in Database System
FCC TAC 2014

## Slide 49: 5G – what exactly is a carrier?
LTE-U
802.11n
LTE
Level3
Cogent
Spectrum DB
Spectrum DB
40k towers each (US)

## Slide 51: Commercial wireless spectrum (US)

## Slide 52: Spectrum for mobile services - EU

## Slide 53: But devices don’t support all spectrum

## Slide 54: LTE FDD bands
Notes: http://www.radio-electronics.com/info/cellulartelecomms/lte-long-term-evolution/lte-frequency-spectrum.php

## Slide 55: LTE TDD
Notes: http://www.radio-electronics.com/info/cellulartelecomms/lte-long-term-evolution/lte-frequency-spectrum.php

## Slide 56: Example: Verizon (US)
covers 308 M pop
roughly 112 M users
Notes: http://www.fiercewireless.com/special-reports/2015-how-much-lte-spectrum-do-verizon-att-t-mobile-and-sprint-have-and-wher

## Slide 57: Unlicensed & lightly-licensed bands (US)
UHF (476-700 MHz) – incentive auctions (licensed) + some unlicensed + TV white spaces
2.4 GHz (73 MHz) – 802.11b/g
3.550 GHz (150 MHz) – shared, database
3.6 GHz (100 MHz) – for backhaul & WISPs
4.9 GHz (50 MHz) – public safety
5.8 GHz (400 MHz) – 802.11 a/n

## Slide 58: 5.8 GHz Wi-Fi bands
Notes: http://www.radio-electronics.com/info/wireless/wi-fi/80211-channels-number-frequencies-bandwidth.php

## Slide 59: Existing spectrum
All spectrum below 6 GHz:
  allocated long ago
  holders have
    important public functions
    money (& lawyers)
    guns
    time ( committees)
    Congress
    and combinations
  need to be bought out even if they didn’t buy the spectrum (e.g., TV)

## Slide 60: Ideal spectrum
Unused or cheap
Available globally ( important for consumer goods & market size)
  preferably under similar licensing conditions
No noisy or sensitive neighbors
Propagates indoors through walls and glass
Not affected by rain or leaves outdoors
Wide bands (≥ 5 MHz, preferably 20 MHz+)
Is paired (uplink & downlink)
Can be processed with cheap electronics (Si, not GaAs)
Allows small antennas🦄🦄

## Slide 61: Spectrum roles
base-level coverage
urban capacity
indoor & capacity
directional
capacity
400 – 800 MHz
1 – 3 GHz
3-6 GHz
> 10 GHz
Digital dividend
TV incentive auction
AWS-3
3.5 GHz
mmWave NPRM

## Slide 62: Spectrum band trade-offs
Band | Antenna | Capacity (typical channel width) | In-building penetration | Rural
LF (below 400 MHz) | e.g., FM: 80 cm | 5-100 kHz per band | very good | very good
Low (400 MHz – 1 GHz) | small (1/4 λ = 7.5 cm) | 5-10 MHz | good | good
Mid-band (1 – 2.5 GHz) | small | 5-20 MHz | ok | ok
High-band (> 2.5 GHz) | small | 5-100 MHz | poor | poor
“1900 MHz takes somewhere between 2 to 4 times as many sites as 850 MHz”

## Slide 63: Attenuation by freqency

## Slide 64: 30-40GHz mmW – Spectrum Overview
64
Note: The Commission’s Fixed Microwave (Part 101) and Satellite Communications (Part 25) service rules govern most of US Mobile allocations shown above
Source : Samsung Communications Research Team

## Slide 65
vs.
“high tower, high power”
(TV, cellular downlink, radar transmitter)
cellular uplink
radar receiver
GPS receiver

## Slide 66: The filter problem
licensed band
user 2
licensed band
user 1
guard band
(wasted)
filter
(input or output)
Power imbalance:
cell downlink: 100 W ERP
cell uplink: 0.05 – 2 W
Notes: http://oem.bmj.com/content/61/9/769/T2.expansion.html

## Slide 67: TV white spaces (US)
First large-scale spectrum database
But limited use in the US
  number of channels
  power levels
  equipment
  available mostly in rural areas, not urban
Leonia, NJ
Amherst, MA

## Slide 68: Incentive auction
initial
clearing goal
reverse
auction
(TV stations)
forward
auction
(carriers)
TV station participated & got bid?
go off-air (6 MHz)
multiplex
VHF
repack
(39 months)
forward bids
insufficient 
reduce clearing goal
144 MHz
(May 2016)
descending clock auction
 reduce until clearing target met

## Slide 69: 600 MHz incentive auction
JP Morgan: $1.34/MHz/Pop
5 MHz uplink blocks
radio astronomy, medical monitoring
5 MHz downlink blocks
FirstNet
spectrum

## Slide 70: 3.5 GHz band
FSS: C Band (3.625–4.200)

## Slide 71: Federal Exclusion Zones

## Slide 72: User classes
Federal users
Fixed satellite users (FCC)
Priority licenses (PAL)
10 MHz channels in 3550-3650
General authorized use (GAL)
1
2
3
census tract
<= 70 MHz
3-year licenses
assigned via SAS
must not interfere

## Slide 73: 3.5 GHz
ESC: environmental sensing capability
allow commercial use in coastal and Great Lakes region
ESC senses radar signal  SAS  GAL devices cease operation or move to another channel

## Slide 74: TX Power Limits
Device | Geographic Area | Maximum Conducted Output Power (dBm/10 megahertz)** | Maximum EIRP (dBm/10 megahertz) | Maximum Conducted PSD (dBm/MHz)
End User Device | All | n/a | 23 | n/a
Category A CBSD | All | 24 | 30 | 14
Category B CBSD* | Non-Rural | 24 | 40 | 14
Category B CBSD* | Rural | 30 | 47 | 20

## Slide 75: Long-range networks
Wide-area Wireless Communication Challenges for the Internet of Things
Harpreet S. Dhillon, Howard sHuang, Harish Viswanathan
5G IOT  predictable geographic coverage, not (just) capacity

## Slide 76: Challenges for spectrum sharing
Enforcement!
  incumbents need to trust new entrants not to misbehave
    or to be swiftly extricated from the band
  as old as radio station identification (“You are listening to WNYC”)
  can’t rely on FCC field engineers with SUVs
 band user identification
  unalterable by (modestly sophisticated) user
  traceable to real ”servable” identity

## Slide 77: Challenges for spectrum sharing
Unlicensed ~2000
Unlicensed now
Unlicensed emerging
indoor home
indoor enterprise
campus
--> natural separation
secondary public SSID
re-use HFC/FTTH backhaul
LTE-U, LAA
what are the “kindergarten” rules?
only power rules (no listen-before-talk (CS) required)

## Slide 78: Spectrum outlook
Move from purpose-specific to generic spectrum
Spectrum rules tend to evolve (slowly)
  e.g., sharing conservative  liberal
Consider setting expectations for receivers (“no right to complain”)
  currently, implicit by original occupancy
Simple spectrum database models
  but increasingly dynamic data in space & time (e.g., mobile primary users)
  start with either licensed or generic “rendezvous” channel
  ask database for channels available across many bands (e.g., IETF PAWS)
Need for more constrained unlicensed bands?
  long range, low duty cycle networks – rendezvous, low-bandwidth IoT

## Slide 79: All networks are similar
time-division multiplexing
modulation
frequency division
medium = spectrum
packets
packets

## Slide 80: Reference architecture
L3 Router
SBC and
L3 Router
Set top box
command&control
Video
Cache
Users
Comm Complex
Transport Core
Regional Broadband
Network
Access Network
Video Complex
ISP
Interconnected Networks
Service Core
Internet
Peering
OTT
Other
Communications
Networks
Video Feeds
and 3rd Party
CDNs
Other Cores
Within the
Network
Interconnected Networks
Local Video
Feeds

## Slide 81: Local loop

## Slide 82: Physical architecture
Feeder Cables
  Carries traffic serving multiple endpoints form an “office” to a neighborhood (local convergence point, LCP, or serving area interface, SAI)
Distribution Cables
  Carry traffic for one or more households from LCP to the curb (network access point)
Drop Cables (above ground) or service wire (underground)
  Carry traffic from curb to dwelling unit
Depending upon the architecture
  Cables may be fiber, twisted pair or coax
  Local convergence point and/or network access point could host a patch panel, a DSLAM, an optical splitter, an Ethernet switch, or a fiber/coax interface.

## Slide 83: Broadband access
-48v

## Slide 84
Rendon Schneir, J., & Xiong, Y. A cost study of fixed broadband access networks for rural areas. Telecommunications Policy (2016), http://dx.doi.org/10.1016/j.telpol.2016.04.002i
Co-VSDL
FTTC
FTTRN
FTTdp
Street
FTTdp
Building
FTTH

## Slide 85: Bandwidths possible
Rendon Schneir, J., & Xiong, Y. A cost study of fixed broadband access networks for rural areas. Telecommunications Policy (2016), http://dx.doi.org/10.1016/j.telpol.2016.04.002i
distance = copper

## Slide 86: Logical architecture
Access network extends from Residential Gateway (RG) to Broadband Network Gateway (BNG)
Flow management between AN and RG depends upon the architecture
Flow management in the Ethernet Aggregation Network similar across architectures but may differ from how flows are managed between the AN and the RG
In Metro Network flows are typically distinguished by layer 3 QoS tags and/or separate VPNs
http://www.broadband-forum.org/technical/download/TR-101_Issue-2.pdf

## Slide 87: xDSL logical architecture
http://www.broadband-forum.org/technical/download/TR-101_Issue-2.pdf

## Slide 88: ADSL (ITU G.992.1)
ADSL spectral power repartition (PSTN)
FDD: Frequency Division Duplexing
 no interference between up and down
Frequency
POTS
300 Hz
3,4 kHz
22 kHz
133kHz
Upstream
Downstream
203 kHz
1.1 MHz
Power
DATA
POTS
300 Hz
3,4 kHz
22 kHz
133kHz
Upstream
Downstream
203 kHz
1.1 MHz
DATA
POTS
300 Hz
3.4 kHz
22 kHz
Upstream
Downstream
203 kHz
1.1 MHz
DATA

## Slide 89: Access: cable network
data, TV transmitted at different
frequencies over shared cable
distribution network
cable
modem
splitter
…
cable headend
CMTS
ISP
cable modem
termination system
HFC: hybrid fiber coax
  asymmetric: up to 30Mbps downstream transmission rate, 2 Mbps upstream transmission rate
network of cable, fiber attaches homes to ISP router
  homes share access network to cable headend
  unlike DSL, which has dedicated access to central office

## Slide 90: Simplified access network diagram
Jason Livingood (Comcast) FCC 2009
Notes: 90
http://www.broadband.gov/ws_fixed_bb.html

## Slide 91: DOCSIS 3.0 channel bonding
6 MHz
6 MHz
6 MHz
6 MHz
38 Mbps
38 Mbps
38 Mbps
38 Mbps
152 Mbps
Logical Channel Bonding Technology
DOCSIS 2.0 is limited to single channel’s capacity
DOCSIS 3.0 employs packet bonding across multiple channels
  Initially will bond 4 channels
  8 channel-capable silicon coming soon
  Upstream bonding in 2010
  Increased speeds 100Mbps+
Notes: 91

## Slide 92: Verizon’s FTTP architecture
ONT
Optical Network Terminal
OLT
Optical Line Terminal
Optical Couplers (WDM)
Voice & Data Downstream 1490 nm
Upstream 1310 nm
Voice, Data & Video 1490 nm, 1310 nm, 1550 nm
1x32
Optical Splitter
EDFA
Erbium Doped Fiber Amplifier
Video 1550 nm
Bandwidth & Services
Upstream
Downstream
Voice, Data & VOD at 622 Mbps
Voice & Data at 155 to 622 Mbps
Broadcast Video
1310 nm
1490 nm
1550 nm
Analog TV
Digital TV and HDTV
54 MHz
864 MHz
CENTRAL OFFICE
customer premise
Brian Whitton, Verizon
Notes: by Brian Whitton, Verizon Networks

## Slide 93: Communication satellites
Communication satellites, some properties, including: altitude above earth, round-trip delay time, number of satellites for global coverage.

## Slide 94: Geostationary satellites (1)
The principal satellite bands

## Slide 95: Geostationary satellites (2)
VSATs using a hub.
“bent pipe”

## Slide 96: HTS launches per year
Dedicated HTS | Hybrid Payload HTS | 
Thaicom 4 | Anik F2 | 
WildBlue 1 | AMC-15 | 
Spaceway 3 | AMC-16 | 
Ka-Sat | Ciel-2 | 
ViaSat-1 | Hylas 1 | 
Jupiter-1 | Arabsat 5C | 
Inmarsat 5F2 | YahSat 1B | 
Inmarsat 5F1 | Hylas 2 | 
Inmarsat 5F3 | Hispasat AG1 | 
NBN Co 1A | Express AM5 | 
GSAT-11 | Astra 2F | 
NBN Co 1B | Express AM6 | 
 | Amazonas 3 | 
 | Astra 2E | 
 | Thor 7 | 
 | Astra 2G | 
 | Jabiru-1 | 
David Hartshorn, 2014

## Slide 97: Low-Earth orbit satellites
The Iridium satellites form six necklaces around the earth.

## Slide 98: Exede beam map
http://www.wildbluetools.com/content/dealer/email/Beam_map-high-mid-low.html

## Slide 99: Satellite
Advantages
Near-universal geographic availability
  low incremental cost
    satellite terminal + installation
Resilient after natural disasters
  often used as backup
Disadvantages
Latency
  MBA 2014: RTT 671 ms
Temporary disruptions
  sun alignment
  rain fade
Capacity
  Viasat-1: 140 Gb/s (for 300,000 customers)
  usually, usage-capped

## Slide 100: Example: Exede satellite plans

## Slide 101: The cost of networks

## Slide 102: Broadband cost
70%
30%

## Slide 103: Rural broadband geo types
OECD: < 150 inhabitants/km2
EC rural broadband: < 100 / km2
EC combined: 50% of the population lives in rural grid cells. Rural grid cells exist outside urban clusters, whereas urban clusters are “clusters of contiguous grid cells of 1 km2 with a density of at least 300 inhabitants per km2 and a minimum population of 5000 [2014]
Finland: 18/km2
Tampere: 430/km2

## Slide 104: CAPEX and OPEX
CAPEX
  the cost of digging
  deployment of ducts
  the rollout of fiber (installation, fiber)
  manholes
OPEX
  7.5% for active elements
  1% for passive elements
  €0.8, €0.3, €1.1 and €0.8/month for the in-building, drop, distribution and feeder segments, respectively
Lifetimes

## Slide 105: CAPEX
per-home passed

## Slide 106: Investment per home connected

## Slide 107: Fiber deployment
wastewater pipe
(3-5 km/week)

## Slide 108: Broadband network cost - FTTP
Category | Details | Outside plant
FTTP in existing right-of-way | All underground, not including drops or electronics | $1,200…$1,300 per passing
 | 40% aerial, 60% underground, not including drops or electronics | $1,000…$1,100 per passing
FTTP drops | Range of distances and complexity | $300…$700 per connected home
Crown Fibre Holdings (Govt. of New Zealand); provided by CTC

## Slide 109: Broadband network cost – Fiber middle mile
Category | Details | Outside plant | Source
aerial, new attachment | Northeastern city municipal utility; 96% aerial, 4% underground; 87.6 miles | $30,000/mile | Public utility (actual cost)
aerial overlash | Major metropolitan area (U.S. east coast) | $15,000/mile | 
buried | Mixed suburban/urban locations and pot/bore construction | $89,000/mile | Washington, D.C.-area BTOP project (actual cost)
Data provided by CTC

## Slide 110: Middle mile cost example
CTC, 2009 (“Brief Engineering Assessment: Efficiencies available through simultaneous construction and co-location of communications conduit and fiber”)

## Slide 111: More fiber observations
Fiber middle-mile cost: $50-70k/mile
Fiber cost: 144 strands = $10k/mile, 48 strands = $4.7k/mile
Common characteristics:
  avoid active elements in network  power, maintenance  PON
  recently: avoid anything except fiber (including splitters)
    cf. wireless last mile approach
  fiber home run, even if PON (Google Fiber, Stockholm)
Fiber cost higher for buried, but cheaper if conduit or aerial
Recent FTTH:
  avoid indoor installation (cf. Verizon FiOS)
  one box in home (ONT + 802.11ac), not ONT + MoCa STB

## Slide 112: FTTH estimates
Bell Alliant in Western Canada has now passed over half a million homes with fiber home, the largest deployment in North America after Verizon. Their latest financial report showed capex of less than $500 per home passed.
Verizon reported costs fell below $700/home passed several years ago and headed to $600. Add the cost of actually installing a large fraction of those homes, and your cost per home passed by the network comes closer to $1,000.
Installing each home at Verizon added $500-600. Digging lawns and drilling holes into the homes is labor intensive.
Includes equipment whose price is rapidly dropping. Early Verizon gear cost $300-400/home, but today they are probably paying half that.
  Very large fiber builds in China are paying less than $100/home.

## Slide 113: FTTx cost vs. DSL
Alcatel-Lucent, 2013

## Slide 114: Capital investment
Company | Revenue | Capital expenditures | %
Comcast (US) [3Q14] | $11.04B | $1.644B | 14.9
Telekom (DE) [3Q14] | €15.6B | $2.58B | 16.5
Safaricom (KE) [H1FY15] | Ksh 79.34B | Ksh 12.37 | 15.5

## Slide 115: Engineering and business opportunities
Capital investment surprisingly small
Academic and industry research focuses on 15%, rather than 85%
Three likely models in different countries:
  public conduits (& fiber) + private Internet access
    community & electric utilities
  structurally-separated into transmission, interconnection & connect
  vertically integrated (monopoly & duopoly) provider

## Slide 116: Network competition models
single provider
(any technology)
cable
copper, fiber
shared copper, fiber
PHY
MAC
(Ethernet)
IP
regulated: pricing? behavior?
how many entrants? where?
poles & conduits
“bit stream”
margin squeeze

## Slide 117: Broadband competition challenges

## Slide 118: US cellular market

## Slide 119: The difficulty of competition
Static vs. dynamic (new entrants)
  existing, converging infrastructures
    coax cable + copper + wireless
Difficulties for new entrants (“overbuilder”)
  capital investment vs. amortized network
  legal barriers
  customer acquisition (“sticky” customers)
  incumbent pricing
Notes: https://aws.amazon.com/blogs/aws/aws-importexport-snowball-transfer-1-petabyte-per-week-using-amazon-owned-storage-appliances/

## Slide 120: Google Fiber

## Slide 121: Network costs
middle mile
backbone
last mile
CDN
yes, but mostly
electronics
DSL | no
HFC | homes/service node
fiber | no
cellular | densification
largely unaffected
by video
ISP-owned
vs. leased!
lack of IXPs in LDCs!

## Slide 122: Bandwidth costs
Amazon EC2
  $50 - $120/TB out, $0/TB in
CDN (Internet radio)
  $600/TB (2007)
  $7-20/TB (Q1 2014 – CDNpricing.com)
NetFlix (7 GB DVD)
  postage $0.70 round-trip  $100/TB
FedEx – 2 lb disk
  5 business days: $6.55
  Standard overnight: $43.68
  Barracuda disk: $91 - $116/TB
DVD-R (7 GB)
  $0.25/disk  $35/TB
Notes: FedEx and EC2 prices as of 09/15/09
CDN: http://www.mindbranch.com/listing/product/R678-29.html
http://www.cdnpricing.com/

## Slide 123: Transit prices
Chart: 
| 1998.0 | 1999.0 | 2000.0 | 2001.0 | 2002.0 | 2003.0 | 2004.0 | 2005.0 | 2006.0 | 2007.0 | 2008.0 | 2009.0 | 2010.0 | 2011.0 | 2012.0 | 2013.0 | 2014.0 | 2015.0
$/Mbps | 1200 | 800 | 675 | 400 | 200 | 120 | 90 | 75 | 50 | 25 | 12 | 9 | 5 | 3.25 | 2.34 | 1.57 | 0.94 | 0.63
http://drpeering.net/white-papers/Internet-Transit-Pricing-Historical-And-Projected.php

## Slide 124: cost recovery

## Slide 125: Consumer expenditures
“Americans spent $116 more a year on telephone services in 2011 than they did in 2007, according to the Labor Department, even as total household expenditures increased by just $67.
Meanwhile, spending on food away from home fell by $48, apparel spending declined by $141, and entertainment spending dropped by $126. The figures aren't adjusted for inflation.” (WSJ 2012)
Notes: Morgan Stanley, Macro Meets Micro: A Five- Year View of the Telecom Services Industry, July 2014.
http://online.wsj.com/articles/SB10000872396390444083304578018731890309450
http://www.bls.gov/opub/btn/archive/consumer-spending-in-2010-pdf.pdf

## Slide 126: Mobile ARPU – US vs. EU

## Slide 127: The value of bits
Technologist: A bit is a bit is a bit
Economist: Some bits are more valuable than other bits
  e.g., $(email) >> $(video)
Application | Volume | Cost per unit | Cost / MB | Cost / TB
Voice (13 kb/s GSM) | 97.5 kB/minute | 10c | $1.02 | $1M
Mobile data | 5 GB | $40 | $0.008 | $8,000
MMS (pictures) | < 300 KB, avg. 50 kB | 25c | $5.00 | $5M
SMS | 160 B | 10c | $625 | $625M
Notes: T-Mobile 2010
AT&T data
http://www.nowsms.com/discus/messages/12/8500.html

## Slide 128: The challenges of service differentiation
Method | Used by | Advantage | Drawbacks | Customer dislike estimate
Speed tiers | C, DSL | Differentiates basic usage modes | Less effective above 10 Mb/s | 😦
Usage-based charging (caps, metered) | M, (C, DSL), LD | heavy vs. light users encourages Wi-Fi use | complaints about meter accuracy adaptive applications (4G bill shock) pay for ads hard to predict | 😦😦😦
Application-based charging | M | Easier to predict Business model | Affects content competition barriers to entry | 😦😦😦
Differentiated privacy | AT&T, NetZero | Full functionality | Low-income users may not be attractive to advertisers | 😦 or 😦😦😦

## Slide 129: The challenges of service differentiation
Method | Used by | Advantage | Drawbacks | Customer dislike estimate
Priority | ? | Better experience for VoIP | Other experience must be bad  economy class in airline | ?
Time-of-day | LD, Sat | Approximates congestion Easy to understand | Not optimally efficient Possible bill shock | 😦😦
Congestion-based | ? | Encourages time shifting | Limited shift Unpredictability | 😦😦😦😦
The words you won't say on your deathbed are, "If only I had spent more time watching the bandwidth meter (or phone bill)."

## Slide 130: Cable TV vs. Internet
Bundle of all possible channels
   “skinny bundles” (few channels)
Lots of advocates of “fairness” for metering
Very few advocate scaling the monthly TV fee (Europe) or the cable TV fee by hours watched
  eminently feasible with STBs
  content tiers but not viewing tiers
“but cost of cable TV does not depend on viewers”
not really: content cost to MVPD is based on popularity