## Slide 1: A RiOT of opportunity: Integrating real-time data into the Internet of Things
Henning Schulzrinne
(+ Jan Janak & other CUCS IRT contributors)
RTC 2016

## Slide 2: Natural evolution

## Slide 4: Kids, don’t do this at home
Notes: https://twitter.com/internetofshit

## Slide 5
https://twitter.com/internetofshit

## Slide 6: Towel dispensers

## Slide 7: The IoT killer app
http://www.traptec.eu/

## Slide 8: Drones as part of the IoT
images
pollution
noise

## Slide 9: link.nyc & smart trash cans
GPRS or CDMA
GPS location service

## Slide 10: IoT is not exactly new

## Slide 11: But controlling light switches is still not the best use
Want to turn on the bedroom light? Sure, just pick up your smartphone, enter the unlock code, hit your home screen, find the Hue app, and flick the virtual switch. Suddenly, the smart home has turned a one-push task into a five-click endeavor, leaving Philips in the amusing position of launching a new product, Tap, to effectively replicate the wall switches we always had.
https://techcrunch.com/2014/12/04/the-problem-with-the-internet-of-things/

## Slide 12: Where does IoT make sense?
Probably
  home security
  residential & commercial locks
  home medical (recording)
  housekeeping (restroom supplies)
  outdoor lighting
  parking meters
  vending machines
Not so much
  light switches
  most household appliances
  clothing
  smoke detectors?
not cost-effective, not just useless

## Slide 13: Security

## Slide 14: IoT security confluence
IoT insecurity
supply chain
long-lived device
one-time purchase
mostly hardware expertise
millions of them
no liability
assembly of software
no UI
no BCP38

## Slide 16: DDOS via IoT
Krebs DDOS, 9/2016: 620 Gb/s, total of > 1.5 Tb/s
GRE, SYN, HTTP GET, POST
MiraiNet: “380k bots from telnet alone”
Enabled by UPnP  bypass NATs
xc3511 vizxv admin 888888 xmhdipc default 123456 54321 support
Notes: https://www.incapsula.com/blog/malware-analysis-mirai-ddos-botnet.html

## Slide 17: Mirai botnet
Chinese manufacturer, used by lots of OEMs
BusyBox Linux
Brute-force ssh and telnet
Web reset doesn’t change ssh or telnet

## Slide 18: Linux kernel lines of code
BusyBox:
177,650 SLOC

## Slide 19: You cannot hide
Hackers worldwide currently probe IoT devices for vulnerabilities after they have been connected to the internet for six minutes. Each hour these devices are tested for vulnerabilities - at least 800 times per hour - with an average of 400 login attempts occurring daily. On average, hackers try to access one IoT device every five minutes and a total of 66 per cent of their attempts end up being successful.
http://www.itproportal.com/news/the-average-iot-device-is-compromised-after-being-online-for-6-minutes/

## Slide 20: IoT DDOS economics
DDOS as externality
  device owners don’t care:
    barely slows down their Internet service
    device still functions normally
    don’t know victims, generally
  vendors don’t care (enough)
    not liable for damage (right now) – public nuisance?
    only marginally affects their business reputation
  ISP don’t care (much)
    individually, not much load – in lightly-loaded direction (outbound)
    hard to combat
    haven’t adopted BCP38 (egress address filtering)
Schneier
Oct. 2016
Cohan
Apr. 2013
Notes: https://www.schneier.com/blog/archives/2016/10/security_econom_1.html

## Slide 21: IoT lemons
“The Market for Lemons: Quality Uncertainty and the Market Mechanism” (Akerlof, 1970)
Information asymmetry
  purchaser cannot judge invisible qualities
  pays only average price
   above-average-quality goods not marketed
“defect four or more times and the problem is still occurring, the car may be deemed to be a lemon”  get purchase price back
  more than four patches?

## Slide 22: Fixes for externalities and lemons
Liability
  slow, one-by-one, uncertain standards of care
  what is “negligent”?
Certification
  voluntary or mandatory
Insurance liability
  homeowner’s insurance
Regulation
  adherence to minimum performance standards

## Slide 23: This is not that hard!
No factory-default passwords
  long-term, no human-setable passwords at all  client certs
No telnet, ssh, SNMP (typically)
Only configure from local subset
Automated, signed updates
Web interfaces use non-root accounts
Automated testing for XSS and SQL injection

## Slide 24: IoT good-citizen rules
Implement current best practices
  no plain-text data or commands
    low-power CPUs are no excuse – long-payback or infrequent crypto operations
  no default passwords
Do not assume that your (cellular) network is around in > 8 years
  short-range unlicensed bands more likely a safe harbor
Update yourself securely
Don’t trust random APs  PassPoint, 802.1x?
  matters mainly for DNS and denial-of-service
Go into fail-safe mode if no updates
Be nice to cellular network (signaling, white spaces, …)
  and maybe “kill switch” if misbehaving (or stolen!)
Don’t ask for special spectrum
  except maybe if you’re a health-and-safety device (but share nicely)
  or maybe low-bandwidth narrowband spectrum
FCC TAC recommendations +
Notes: http://www.sigfox.com/en/#!/technology

## Slide 25: Challenge: enrollment
Commercial buildings  enroll 1,000s of devices at once
Home  enroll one device at a time
  current model: one app per device (class)
  re-do if Wi-Fi password changes
  common options:
    QR code
    P2P Wi-Fi (Wi-Fi Direct)
  possibilities
    “hi, I’m a Philips light bulb – add me!” (PKI)

## Slide 26: How should we secure things?
Old model
New model
commissioner
device authorization
database
DIAMETER
create entries
“I want to join!”
802.1x
WPA2
(P, E)

## Slide 27: AllJoyn is doing something similar

## Slide 28: Privacy

## Slide 29
“Remember when, on the Internet, nobody knew who you were?”

## Slide 30: Privacy fears deter usage
Major Concerns Related to Online Privacy and Security Risks, Percent of Households with Internet Users, 2015
NTIA
May 2016
Notes: https://www.ntia.doc.gov/blog/2016/lack-trust-internet-privacy-and-security-may-deter-economic-and-other-online-activities

## Slide 31: Roughly half of consumers uncomfortable
Altimeter Group
June 2015
Notes: http://www.altimetergroup.com/pdf/reports/Consumer-Perceptions-Privacy-IoT-Altimeter-Group.pdf

## Slide 32: Local processing for efficiency privacy
indoor
thermometer
publicly visible script
cloud storage and access
fuzz
anonymize
average
rate limit
node
observable storage
fog computing model

## Slide 33: Building large IoT systems

## Slide 34: IoT = Internet at scale
Security at scale
  still largely “add password to configuration file”
  identify by IP address
Management at scale
  device-focused
  SNMP, at best
  CLI, at worst
  no performance diagnostics capabilities (“why is this so slow?”
Naming at scale
  identify by node name
Programming at scale
system
& rack
data center

## Slide 35: Lessons from early IoT (and cousins)
ATC
proprietary network architecture
"Ongoing problems continue to threaten NextGen's costs and timeline."
PTC
220 MHz dedicated network
"[NTSB] has advocated for some form of positive train control for more than 45 years."
ITS
5.9 GHz
allocated in 1999

## Slide 36: Lesson: sensor networks may be (tiny) niche
http://eschatologist.net/blog/?p=266
Most IoT systems will be near power since they’ll interact with energy-based systems (lights, motors, vehicles)
Most IoT systems will not be running TinyOS (or similar)
Protocol processing overhead is unlikely to matter
Low message volume  cryptography overhead is unlikely to matter
$35.00
A 900MHz quad-core ARM Cortex-A7
1 GB RAM

## Slide 37: The age of application-specific {sensors, spectrum, OS, protocol …} is over
Computing system: dedicated function  OS
   abstract into generic components
  e.g., USB human interface device (HID)
What are the equivalent sensor and actuator classes?
Networks: generic app protocols
  request/response  HTTP
  event notification  SMTP, SIP, XMPP
Spectrum: from new application = new spectrum to generic data transport

## Slide 38: IoT varies in communication needs
1/hour
1/minute
1/second
10/second
sensors
actuators
CPS
IoT
Notes: http://www.nytimes.com/2012/10/02/world/europe/device-sends-message-to-swiss-farmer-when-cow-is-in-heat.html?pagewanted=all

## Slide 39: 5G is not the only option
indoor
unmanaged
indoor
ext. managed
outdoor
urban
outdoor
rural
outdoor
remote

## Slide 40: Niche networks
short range
low energy; mesh
ubiquity; low cost
speed; public APs

## Slide 41: 5G = low latency + mmW + …
X
X
V2I2V
X
one-to-many!
EEW
(< 5 s)

## Slide 42: Protocols matter, but programmability matters more
Nobody wants to program raw protocols
Most significant network application creation advances:
  1983: socket API  abstract data stream or datagram
  1998: Java network API  mostly names, HTTP, threads
  1998: PHP  network input as script variables
  2005: Ruby on Rails  simplify common patterns
Many fine protocols and frameworks failed the programmer hate test
  e.g., JAIN for VoIP, SOAP for RPC
Most IoT programmers will not be computer scientists

## Slide 43: What is the best generic (simple) architecture?
SQL (via HTTP RESTful API)
Streaming (JSON web stream … RTP)
cloud, fog, …
user-delivered code
event notification
mediate access
SENML?

## Slide 44: Challenge: integrate embedded, mobile & virtual
magnetometer
accelerometer
location
gyroscope

## Slide 45: Some of IoT is streaming
update rate of 10 to 250 Hz

## Slide 46: IoT communication modalities
get
set
HTTP GET
COAP GET
MQTT?
HTTP POST
CoAP POST
MQTT?
subscribe
publish
HTTP long poll
CoAP observe
MQTT
stream
WebRTC
SUBSCRIBE
PUBLISH
MSRP
SIP world
INVITE + RTP
RTSP
DO?
MESSAGE?
MESSAGE?

## Slide 47: MQTT model
kitchen/+/temperature matches kitchen/foo/temperature but not kitchen/foo/bar/temperature

## Slide 48: Example: AllJoyn bus
publish-subscribe model (implicit)
Wi-Fi
UDP multicast
BT SDP

## Slide 49: Device control
Do sip:lamp@cs.columbia.edu SIP/2.0
…..
<Control>
<Action>turn lamp on</Action>
</Control>
serial port
2001

## Slide 50: We could do better
Somewhat unsatisfactory
  AllJoyn model only for LAN operations
  CoAP & HTTP better for get/set operations
  MQTT simpler for publish/subscribe
  SIP (or RTSP) better for media streaming
Lots of proprietary network protocols
  BAC for building automation
Same device or source, multiple identifiers
  HTTP URL or SIP URL or MQTT IP address/domain name
  none are particularly useful or semantically meaningful
    e.g., likely change if device is replaced

## Slide 51: Lifecycle

## Slide 52: Windows XP, Corolla & Revolv
available
12/2001
end of sales
6/2008
end install
10/2010
end support
4/2009
end ext. support 4/2014
13 years
1996 Corolla
- still can get parts
founded 2012
acquired by Nest 2014
shut down May 2016
$2,359
Notes: http://windows.microsoft.com/en-us/windows/lifecycle

## Slide 53: Design for 20 years

## Slide 54: IoT needs a life cycle model
feature support
EoL?
security support
safe mode
conservator
support
services
company hands over control
(bond or insurance model)
X
services
local only
guardian

## Slide 55: IoT needs an economic model
Do you own or rent a device?
  and do you know what rights you have (transfer, sale, …)?
  and for how long?
What is expected lifetime?
  in what mode?
  with what enhancements?
Who pays for computation and storage?
  printer & ink? stove & electricity?
  subscription model  doesn’t scale except with aggregator
  advertising model  creepiness-factor, no direct interaction
  third party model: health or fire insurance, research (“your data for science”), electric utility

## Slide 56: Development lifecycle
network
emulation
Currently, hard to design large-scale reliable systems
  failure modes, server load, control algorithms, …
See Jan Janak’s talk at 1.30 today
y = f(x)
y = f(t)
physics emulator
VM
Mininet
http://mininet.org/
set network
parameters
5G

## Slide 57: Conclusion
IoT is finding lots of boring niches
But IoT security is exposing almost all the security deficiencies of the Internet eco system
  “thoughts and prayers” approach
  continuing to do the same thing for the next 5 years and hoping for better results is not a strategy
Start thinking beyond stove pipes of applications
 engineering large scale systems