## Slide 1: NG911: Time to dispatch = 15 years and counting
Henning Schulzrinne
Columbia University & FCC (with usual disclaimers)

## Slide 2: Quick history of 911 in the US
proposal for national emergency number by NAFC
1957
Presidential Commission recommends single number
first 9-1-1 call in Haleyville, AL
17% of US has 9-1-1
1967
1968
selective call routing trials
1970s
1976
50% of US has 9-1-1
1987
1998
2001
Jan
2013
Phase I for cellular: deliver tower & sector to PSAP
Phase II for cellular: handset or network location (carrier req.)
NENA NG911 i3 spec.
2011
1999
National 911 Act (Congress)
2015
Carriers must support text-to-911
June
2013
Text-to-911 bounce-back
Aug.
2016
Location test bed
50/67%, 150m/80% (handset)
Feb.
2017
NEAD privacy & security plan
Apr.
2017
50 m for 40% of calls
Apr.
2018
50 m for 50% of calls
Aug.
2018
barometric data PSAPs
Apr.
2020
70% 50m
Notes: Sep 2010: https://apps.fcc.gov/edocs_public/attachmatch/FCC-10-176A1.pdf location accuracy
Dec 2012: https://www.fcc.gov/document/text-911-further-notice-proposed-rulemaking
May 2013: https://www.fcc.gov/document/text-911-bounce-back-message-order
Jan 2015: https://apps.fcc.gov/edocs_public/attachmatch/FCC-15-9A1.pdf
text-to-911: https://apps.fcc.gov/edocs_public/attachmatch/FCC-14-118A1.pdf (December 31, 2014)

## Slide 3: What distinguishes US 911 from elsewhere?
5,894 PSAPs (in 3,135 U.S. counties)
  some very large (NYC, LA, Chicago), some tiny
  technical services provided by contractors and “system service providers”
240 million 9-1-1 calls per year
  70% cellular
Emphasis on location delivery
  98.6% of population have some Phase II (July 2016)
  most carriers use hybrid location (GPS + network-based such U-TDOA)
Funded by variety of add-on 9-1-1 charges on phone bills, not taxes
  some of these charges are diverted to other purposes
Limited regulatory authority for national regulator (FCC)
  Mostly, iVoIP and cellular providers, not PSAPs
  some oversight by state public utilities commission or state 911 office
Strong professional associations (APCO & NENA), with standard setting efforts and training

## Slide 4: US landline phone service
TEMU 2016
FCC Voice Telephone Services: Status as of December 31, 2014

## Slide 5: About half of households are wireless-only

## Slide 6: Text-to-911 architecture
TEMU 2016
Intrado, “Text-to-9-1-1 saves Lives”, 2013

## Slide 8
Insanity is … Doing something 6,200 times and expecting a speedy result.
(Einstein + Heisenberg)

## Slide 9: US NG911 status
TEMU 2016
 | 2011 (27 responses) | 2013 (39 responses)
Statewide NG911 plan | 9 | 15
Concept of operations | 3 | 12
Request for proposals released |  | 13
Contracts |  | 13
Testing parts, functions and components at state level |  | 9

## Slide 10: What are the causes?
Bottom up: small groups of PSAPs get together
  build (have built) their own ESInet
  Deploy their own ESRP, ECRF, LNG
  Each requires educating the late adopters, consultants, RFP, negotiation with carriers, coordinated funding, …
Engineered as one-offs
  Custom interconnect, equipment, configuration, …
600 selective routers
Capital investment
  But 911 entities typically cannot issue bonds
  No significant national funding sources
  Diversion of 911 fees collected by many U.S. states
Expertise uneven (GIS, IP networks, cybersecurity, …)
Carrier obligations – make PSAPs pay for legacy services

## Slide 11: Alternative network models
Current deployment model
  network islands with SBC moats
  one county, one network, one server rack, one purpose, one decade
Similar to early academic Internet  Internet2
  initially custom, then re-use dark fiber
  membership model?
Suomenlinna

## Slide 12: Alternative network models
national network(s)
LoST
LIS
VPNs
major network interconnect points:
SEA, LAX, SJC, DEN, CHI, BOS, DC, NYC

## Slide 13: 911 apps emerging
Offer advanced features
  Notify family & friends
  Share images
  Avoid delays in the carrier – PSAPs – system service provider dependency circle
Challenges
  Are 911 calls delivered to the right PSAP?
  911 features on handsets
  Funding model – consumer pays? PSAP pays?
  Privacy concerns
Notes: https://www.apcointl.org/doc/advocacy/623-the-status-of-9-1-1-apps/file.html
http://appcomm.org/

## Slide 14: Caller location
Builds on long history of FCC location accuracy requirements
  implicitly outdoor: 50m (67%)/150m (80%-90%) circles (1996), with geographic exclusions
dispatchable location or x/y within 50 m
  ~70% calls are wireless
  unknown % indoor
  residential indoor may allow GPS
z axis:
  3 years: uncompensated barometric
  6 years: 80% of top 25 CMAs
open issues:
  nomadic iVoIP
  separation of location & call delivery
  reliable location w/o power
Chart: 
| 2.0 | 3.0 | 5.0 | 6.0
% | 40 | 50 | 70 | 80

## Slide 15: Indoor location
TEMU 2016
NEAD
indoor or
outdoor?
crowdsourced database
commercial Wi-Fi database
building/street
WiFi AP
floor, apartment, office
GPS or GNSS
known location?
location = f(observed APs, barometer)
“where are you?”
record common locations?

## Slide 16: Indoor location challenges
 | Advantage | Challenges | Possible approaches
GNSS | near-universal in handsets no infrastructure | fails in dense urban canyons steel frame buildings | Long-term: L2C & L1C GPS
Wi-Fi | near-universal in handsets existing infrastructure | ground truth (room-level) moves | crowdsourcing
BlueTooth | universal in newer handsets | mapping beacons to location maintenance | crowdsourcing build into infrastructure
Barometric | cheap to add | limited handset availability indoor air pressure weather compensation mapping elevation to floor | building-level calibration combine with Wi-Fi
Accelerometer (dead reckoning) | near-universal in handsets no infrastructure | accuracy & mode detection mapping elevation to floor | use in hybrid systems

## Slide 17: E911 location accuracy requirements (9/2010)
 | Handset-based |  | Network-based | 
 | 50 m/67% | 150m/80-90% | 100m/67% | 300m/90%
Year 1 – Jan. 2012 |  |  | 60% of counties covering 70% of pops | 
Year 2 – Jan. 2013 | 50 m/67% ea. county | 150m/80% ea. county |  | 
 | Carriers must provide confidence and uncertainty data on a per call basis upon PSAP request |  |  | 
Year 3 – Jan 2014 |  |  | 70% of counties covering 80% of pops (can use blended data) | 60% of counties with 70% pops (can use blended data)
Year 5 – Jan 2016 |  |  | 100% of counties (can use blended or handset data) | 70% of counties with 80% of pops (can use blended data)
Year 8 – Jan 2019 |  | 150m/90% ea. county |  | 85% of counties (can use blended or handset data)
Exclusions |  | May exclude 15% of counties w/forestation (no sunset) | May exclude counties where triangulation not feasible (< 3 sites) – sunsets after Year 8 | 
47 CFR 20.18(h)
Notes: https://www.law.cornell.edu/cfr/text/47/20.18

## Slide 18: US voice telephony connections
TEMU 2016
FCC Voice Telephone Services: Status as of December 31, 2014
Notes: https://apps.fcc.gov/edocs_public/attachmatch/DOC-338629A1.pdf