## Slide 1: 5G: What can we learn from the previous four generations?
Henning Schulzrinne
Columbia University

## Slide 2: Design for 20 years

## Slide 3: Generations are distinct
4G
3G
2G
land
line

## Slide 4: Generations overlap
2G
3G
4G
5G

## Slide 5: Generational surprises
Generation | Expectation | Surprise
2G | better voice quality (“digital!”) | SMS
3G | WAP | web
4G | IMS | YouTube, WhatsApp, notifications
5G | IoT (low latency) | ?
underestimated cost and fixed-equivalence as drivers

## Slide 6: Lessons, in brief
Experience | Lessons
VoLTE, IMS | avoid complexity avoid entanglement plan intercarrier interfaces
Wi-Fi | don’t trust the RAN/AP
disaggregation of functions | clear & simple interfaces don’t assume trust between elements
app stores | keep it application-neutral
FTTH, backhaul cost | re-use backhaul where you can find it

## Slide 7: Complexity kills
IMS
Notes: http://voices.canonical.com/jussi.pakkanen/files/2012/01/synaptics-statemachine.png
http://upload.wikimedia.org/wikipedia/en/9/9c/TISPAN_IMS_Reference_Architecture.png

## Slide 8: Niche networks
short range
low energy; mesh
ubiquity; low cost
speed; public APs

## Slide 9: Long-range networks
Wide-area Wireless Communication Challenges for the Internet of Things
Harpreet S. Dhillon, Howard sHuang, Harish Viswanathan

## Slide 10: SIGFOX, Ingenu and LoRa

## Slide 11: New cellular domains
Fixed wireless  compete with DSL and maybe cable
  > 10 Mb/s bandwidth
  probably more rural than urban  ample spectrum available
  Comcast median usage:
    August 2013: 16 GB
    mid-2015: 40 GB  roughly 50% YoY growth
     2020 usage of 300 GB
  typical cost: cellular $10/GB  $400 today, $3,000 in 2020
    median wireline: $55 month for unlimited
     cost problem (differentiate fixed from mobile)
IoT and other embedded applications
  many (most?) IoT applications are not mobile
  but are very cost-sensitive

## Slide 12: What happens if this moves to IP?
Thus, for 146 hours/month of HD  410 GB/month
(does not count separate viewing among household members)

## Slide 13: Example wireless plan

## Slide 14: IoT requirements
Wide-area Wireless Communication Challenges for the Internet of Things
Harpreet S. Dhillon, Howard sHuang, Harish Viswanathan

## Slide 15: Broadband pricing
https://www.newamerica.org/oti/the-cost-of-connectivity-2014/

## Slide 16: Attenuation by frequency

## Slide 17: Propagation issues
Rural (low density)  coverage limited
  √ tower height (ft) ≈ coverage range (miles)
  e.g., 400 ft (120 m) tower  20 miles
  but 4-5 miles more typical
  GSM: timing advance  35 km
Urban outdoors
  cell spacing: 100 ft
  capacity-limited
  power-limited (5-20 W base station, 2 W mobile)  5-8 miles
Urban indoors
  radio propagation

## Slide 18: 28 GHz attenuation & reflection
Rappaport, 2013
multipath reflections
highly directional antennas

## Slide 19: 10 GHz+
Unlicensed

## Slide 20
20
30-40GHz mmW – Spectrum Overview
Note: The Commission’s Fixed Microwave (Part 101) and Satellite Communications (Part 25) service rules govern most of US Mobile allocations shown above
Source : Samsung Communications Research Team

## Slide 21: Changing spectrum environment
Except at highest frequencies, all new spectrum likely to be shared
  e.g., 3.5 GHz
  in time & space
 need frequency-agile systems that can shift capacity to different bands, quickly

## Slide 22: Example: 3.5 GHz (April 2015)
150 MHz at 3.550 GHz
incumbents: DoD radars + fixed satellite service (FSS) receive-only
exclusion zones: 60% pop. unsuitable for macrocell
access: incumbent, priority (PAL), general authorized
  Incumbent: authorized federal & grandfathered Fixed Satellite Service
  PAL: 3 years non-renewable, 10 MHz channel, census tract
  hospitals, utilities, state/local gov’t
see also TVWS, MBAN

## Slide 23: Networks 1G through 4Gish
national carrier
one subscriber,
one phone,
one provider

## Slide 24: LTE – one carrier, plus roaming

## Slide 25: 5G – what exactly is a carrier?
LTE-U
802.11n
LTE
Level3
Cogent
Spectrum DB
Spectrum DB
40k towers each (US)

## Slide 26: 5G: Carriers as consumer brand
Outside
Inside

## Slide 27: Cell towers
Tower owner | Number of towers
Crown Castle | 39,739
American Tower | 40,000 (with VZW)
SBA Communications | 15,151
United Cellular Co. | 4,802
Verizon Wireless | 1,400
T-Mobile Towers | 1,003
Time Warner | 950
Mediacom Communications | 750
Charter Communications | 650
Diamond Communications | 637
Trillion Partners | 635
cost/tower: $150k
total US: 205k
Notes: http://www.statisticbrain.com/cell-phone-tower-statistics/
http://ir.sbasite.com/releasedetail.cfm?ReleaseID=908348

## Slide 28: What are carriers good at?
Research?
Software development?
  Who is going to develop those 5G SDN applications?
OTT applications?
API-based services?
  Why did Twilio and Tropo offer voice service APIs and not the ILECs?

## Slide 29: What’s the simplest network?
AAA
HLR
(?)
IPv6 access
(any network)
DHCP
registrar
network characteristics (QoS)
IP address
AAA (incl. payment)
discovery
network
resources
one subscriber, multiple devices, multiple providers

## Slide 30: Where do we need mobility?
likely to have access provider diversity
  what is expected lifetime of IP address?
PMIP and MIP complex
  need to re-create application-layer security at L3
not really needed for HTTP video
  use mTCP?
  or HTTP restart?
maybe not even for real-time media
  registrar for new-call reachability
  application layer (SIP) mobility for mid-call hand-off?
or tunnels, tunnels everywhere?

## Slide 31: Make the network location-aware
2G/3G/4G are location-ignorant: “I only know your cell sector”
All mobile devices will be location-aware to the ~5 m
Some know where they will likely be in the near future
  public transit
  road navigation systems
   predict access and hand-off
All devices will have multiple radios
  use macro cell network to query for local access

## Slide 32: Simplify enrollment
enable access

## Slide 33: The law of new networks
“Any new network technology will be justified on (finally) providing QoS”
To succeed, they have to provide good-enough QoS for best effort
  at least with competition
The business model for QoS is difficult
  see bypass toll roads
QoS is usually not accessible to applications
  or not end-to-end

## Slide 34: Providing a network API
Currently, applications can detect Wi-Fi vs. cellular
What is the correct API for discovering network properties?
  available options (“BE”, “LBE”, “low latency”)
  not RSVP flow specs…
cost?
($ or count for bucket?)
predicted performance?

## Slide 35: Mobile = events, not (just) video
Focus on bandwidth, but wearables and
Polling (outbound) and events (inbound)
  sleeping apps
Current models difficult for developers

## Slide 36: IMS /VoLTE
IMS = It Mostly Speaks
VoLTE = Voice-Only Later than Expected

## Slide 37: Surge pricing – non-telecom
BI, 1/13/2015
Notes: Techcrunch

## Slide 38: Aggressive competitors compete on simplicity

## Slide 39: Capital investment
Company | Revenue | Capital expenditures | %
Comcast (US) [3Q14] | $11.04B | $1.644B | 14.9
Telekom (DE) [3Q14] | €15.6B | $2.58B | 16.5
Safaricom (KE) [H1FY15] | Ksh 79.34B | Ksh 12.37 | 15.5

## Slide 40: The value of bits
Technologist: A bit is a bit is a bit
Economist: Some bits are more valuable than other bits
  e.g., $/bit(email) >> $/bit(video)
  no-QoS bits dominate in volume
Application | Volume | Cost per unit | Cost / MB | Cost / TB
Cable video | 660 GB |  | $0.06 | $60
Voice (13 kb/s GSM) | 97.5 kB/minute | 10c | $1.02 | $1M
Mobile data | 5 GB | $40 | $0.008 | $8,000
MMS (pictures) | < 300 KB, avg. 50 kB | 25c | $5.00 | $5M
SMS | 160 B | 10c | $625 | $625M
Notes: T-Mobile 2010
AT&T data
http://www.nowsms.com/discus/messages/12/8500.html

## Slide 41: 5G prototype: Eduroam

## Slide 42: Growing-up lessons
Complexity kills
Play fair
CapEx is once, OpEx is forever
Know where you are
Share everything
Don’t trust strangers

## Slide 43: Backup

## Slide 44: LTE architecture
Notes: http://alcatel-lucent.com/enrich/v1i12007/article_c4a4.html

## Slide 45: Wireless market evolution