## Slide 1: Internet access and backbone technology
Henning Schulzrinne
Columbia University
COMS 6181 – Fall 2018

## Slide 2: Key objectives
Fundamental models for communication
How are bits switched?
How does a large router work internally?
What are the limits to communication capacity?
How do DSL and cable modems work?

## Slide 3: Overview
Physical layer for CS majors
  modulation
  spectral efficiency
Residential last-mile technologies
  DSL
  Cable (DOCSIS)
  Residential fiber
Backbone networks
Wireless networks

## Slide 4: Circuits, VCs and packets
 | Circuits | virtual circuits | packets
Resources | copper circuit (space) time | switching capacity (maybe) | none (except with resource reservation)
Information unit | bit, byte | cell, frame | packet
Routing | switched (e.g., timeslot 15 to timeslot 13) | VC identifier (switch-local) | IP address (network-global)
Examples | phone, ISDN, X.21 | ATM, MPLS | IP, Ethernet
Notes: http://people.seas.harvard.edu/~jones/cscie129/nu_lectures/lecture11/switching/xbar/xbar.html

## Slide 5: Circuit switching: crossbar space switch
N
1
2
1
N
2
N –1
…
…
N x N array of crosspoints
Connect an input to an output by closing a crosspoint
Non-blocking: Any input can connect to idle output
Complexity: N2 crosspoints
Notes: http://www.cc.gatech.edu/classes/AY2005/cs4251_fall/
C. Dovrolis

## Slide 6: CS: multistage space switch



nk
nk
nk
nk
N/n  N/n
N/n  N/n
N/n  N/n
kn
1
2
N/n
N
inputs
1
2
3
3
N/n
N
outputs
1
2
k
2(N/n)nk + k (N/n)2 crosspoints
kn
kn
kn
…
…
…
Large switch built from multiple stages of small switches
n inputs to a first-stage switch share k paths through intermediate crossbar switches
Larger k (more intermediate switches) means more paths to output
In 1950s, Clos asked, “How many intermediate switches required to make switch non-blocking?
N/n first stage, each
with n inputs, k outputs
k intermediate
Notes: http://www.cc.gatech.edu/classes/AY2005/cs4251_fall/

## Slide 7: CS: Clos Non-Blocking Condition: k=2n-1
nxk
nxk
nxk
N/n x N/n
N/n x N/n
N/n x N/n
kxn
1
N/n
Desired
input
1
j
m
N/n
Desired
output
1
2n-1
kxn
kxn
n-1
N/n x N/n
n+1
N/n x N/n
2n-2
Free path
Free path
n-1
busy
n-1
busy
…
…
…
…
Request connection from last input to input switch j to last output in output switch m
Worst Case: All other inputs have seized top n-1 middle switches AND all other outputs have seized next n-1 middle switches
If k=2n-1, there is another path left to connect desired input to desired output
# internal links = 2x # external links
Notes: http://www.cc.gatech.edu/classes/AY2005/cs4251_fall/

## Slide 8: Backbone router
Route processor
cross-connect
(“backplane”)
may have
buffers
TCAM = ternary content addressable memory
Notes: http://ipj.dreamhosters.com/wp-content/uploads/2014/12/ipj17.2.pdf

## Slide 9: Example: Cisco CRS-1

## Slide 10: Physical media: capacity
Capacity has theoretical limit
  Shannon’s Law: capacity limit given by
  C = B log2 (1 + S/N) with spectral bandwidth B
  E.g., phone has B = 3000 Hz, S/N = 35 dB, C = 34.8 kb/s
dB =
  E.g., 25 dB =
Speed has physical limits: c in free space, 0.66 c in fiber

## Slide 11: Bypassing Shannon
Multiple channels
  polarization
Spatial re-use
  directional antennas (120o “sectors”)
  smaller cell sizes
    macro, micro, femto, … cells
Notes: LTE - Anritsu

## Slide 12: Modulation
Time
  TDxxx
  typically, “time slots”
Frequency
  one signal  one frequency
  multiple frequencies  OFDM
    e.g., DSL, LTE, 802.11a/n, …
Phase (time-shift)
T1 circuit (1.54 Mb/s – 24 voice ch.)
Notes: http://electronicdesign.com/communications/fundamentals-communications-access-technologies-fdma-tdma-cdma-ofdma-and-sdma

## Slide 13: Mapping bits to symbol
Phase (+ amplitude)
symbol rate vs. bit rate
Amplitude

## Slide 14: Spectral efficiency
Medium | Spectrum | Data rate | b/Hz
Modem (V.92) | 3,100 Hz | 56 kb/s | 18.1
2G cellular (GSM) | 0.2 MHz |  | 0.52
LTE | 20 MHz | 326 Mb/s | <16.3
ADSL downlink | 0.962 | 12 Mb/s | 12.5
WiFi 802.11 a/g | 20 MHz | < 54 Mb/s | < 2.7
WiFi 802.11 n | 20 MHz | < 144 Mb/s | < 7.2
Notes: http://en.wikipedia.org/wiki/Spectral_efficiency

## Slide 15: Broadband
What (is Broadband Internet Access)?
    FCC: was >200 kb/s or 4 Mb/s down & 1 Mb/s up
      now 25 Mb/s down/3 Mb/s up
    NTIA: >768 kb/s downstream/200 kb/s upstream
    YouTube recommendation: >500 kb/s
    Multimedia: >10 Mb/s downstream
      Unicast/broadcast
Where?
    Rural: Low density (<100 pop/km2)
      Minimize fixed infrastructure cost
    Urban: High density (>1000 pop/km2; >10,000 in cities)
      Maximize Mb/s/km2
Notes: http://globalgeeknews.com/2010/07/23/fcc-changes-broadband-definition-to-4mbps-up-and-1mbps-down/

## Slide 16: Cost for providing access
cost
distance
possibly another step when crossing oceans
within home
within campus/AS
(multiple L2s)
same L2 switch
(non-blocking)
across provider boundaries

## Slide 17: Broadband Access Technologies
FBWA or 4G
BPL
DSL
HFC
4G
Digital
Subscriber Line
Telco or ILEC
10s of Mbps
Entertainment, data, voice
Broadband Power Line
PowerCo
Data, voice
~few Mbps
Fixed Broadband Wireless Access
Wireless ISP
WiMAX or LTE:
  -10s of Mbps
Satellite: few Mbps
4G/LTE
Cellular operators
5-10 Mbps (100 kph)
Hybrid Fiber Coax
CableCo (MSO)
Entertainment, data, voice
10s of Mbps
Fiber PON
Fiber -- Passive
Optical Network
Telco or ILEC
~75 Mb/s
Futureproof?
Paul Henry (AT&T), FCC 2009
FTTHome
FTTCurb
Notes: http://www.broadband.gov/ws_fixed_bb.html

## Slide 18: Available access speeds
100 Mb/s
20 Mb/s
10 Mb/s
5 Mb/s
1 Mb/s
20%
80%
90%
97%
100%
avg. sustained
throughput
of households (availability)
marginal VOIP

## Slide 19: Maximum Theoretical Broadband Download Speeds
Multiple Sources: Webopedia, bandwidthplace.com, PC Magazine, service providers, ISPs, Phonescoop.com, etc.
Paul Garnett, CTIA, June 2007

## Slide 20: Access costs
DSL VDSL: 100 Mb/s over short distances, ready to double with DSM
  Bonding also doubles speed.
  DSL repeaters very cheap way to bring “up to 6 meg” longer distances (~$200).
Cable 30M homes can now get 50 Mb/s down
  DOCSIS 3.0. 60% of U.S. in 2010-2011
  85+% in 2013-2014. Upstream 50 meg at Comcast starting in months.
  Specification designed to go to a shared gigabit. 95-99% reliable speed; balance still over 10 megabits. < $100/home, fast to deploy
David Burstein (DSL Prime) 2009
Notes: http://www.broadband.gov/ws_fixed_bb.html

## Slide 21: Access costs
Fiber  GPON 200 Mb/s both directions
  $200-400 for gear
  Verizon FiOS < $700/home passed -- dropping
  $20K/mile to run fiber
Wireless LTE/WiMAX
  4-10 Mb/s typical
  95% of U.S. population 2013 (McAdam, VZ)
  Shared 30-120 Mb/s, so heavy HD TV use a problem

## Slide 22: Residential access: DSL
Uses single copper pair
  shared with analog or ISDN phone service
  but “bonding” proposed since most residences have 2 pairs
ADSL = asymmetric digital subscriber line
  “web browsing”
  but: sending photos, video conferencing
distance-limited
IDSL: ISDN encoding; 144 kb/s, but longer loops
ADSL: typically, < 20 Mb/s down, 2 Mb/s up
  G.lite: 1.5 Mb/s down, 384 kb/s up; no splitter
SDSL: symmetric 2.3 Mb/s
SHDSL: ITU rate-adaptive
VDSL: short distance to ONU
  up to 55 Mb/s

## Slide 23: ADSL standards
Standard name | Common name | Downstream rate | Upstream rate
ITU G.992.1 | ADSL (G.DMT) | 8 Mbit/s | 1.0 Mbit/s
ITU G.992.2 | ADSL Lite (G.Lite) | 1.5 Mbit/s | 0.5 Mbit/s
ITU G.992.3/4 | ADSL2 | 12 Mbit/s | 1.0 Mbit/s
ITU G.992.3/4 Annex J | ADSL2 | 12 Mbit/s | 3.5 Mbit/s
ITU G.992.3/4 Annex L | RE-ADSL2 | 5 Mbit/s | 0.8 Mbit/s
ITU G.992.5 | ADSL2+ | 24 Mbit/s | 1.0 Mbit/s
ITU G.992.5 Annex L | RE-ADSL2+ | 24 Mbit/s | 1.0 Mbit/s
ITU G.992.5 Annex M | ADSL2+ | 28 Mbit/s | 3.5 Mbit/s
Michal, Angel, Igor
Notes: Miturski Michal
Mirkovski Angel
Sacevski Igor

## Slide 24: ADSL Range
Range for DSL without a repeater: 5.5 km
As distance decreases toward the telephone company office, the data rate increases
Data Rate | Wire gauge | Wire size | Distance
1.5 or 2 Mbps | 24 AWG | 0.5 mm | 5.5 km
1.5 or 2 Mbps | 26 AWG | 0.4 mm | 4.6 km
6.1 Mbps | 24 AWG | 0.5 mm | 3.7 km
1.5 or 2 Mbps | 26 AWG | 0.4 mm | 2.7 km

## Slide 25: ADSL (ITU G.992.1)
ADSL spectral power repartition (PSTN)
FDD: Frequency Division Duplexing
=>no interferences between Up and Down
Frequency
POTS
300 Hz
3,4 kHz
22 kHz
133kHz
Upstream
Downstream
203 kHz
1.1 MHz
Power
DATA
POTS
300 Hz
3,4 kHz
22 kHz
133kHz
Upstream
Downstream
203 kHz
1.1 MHz
DATA
POTS
300 Hz
3,4 kHz
22 kHz
133kHz
Upstream
Downstream
203 kHz
1.1 MHz
DATA

## Slide 26: The DMT frequency bands
Frequency Division Multiplexing (FDM)
Echo Cancellation

## Slide 27: Functional scheme of a DSLAM
DSLAM: Digital Subscriber Line Access Multiplexer
POTS/ISDN
LT
POTS
ISDN
Split.
NT
POTS
ISDN
Split.
ADSL
modem
Copper access line
ADSL + POTS/ISDN
ATM network
POTS/ISDN
STM-1
ATM cells
DSLAM

## Slide 28: Residential access: cable modems
HFC: hybrid fiber coax
  asymmetric: up to 10 Mb/s upstream, 1 Mb/s downstream
network of cable and fiber attaches homes to ISP router
  shared access to router among home
  issues: congestion, dimensioning
deployment: available via cable companies
Kurose/Ross

## Slide 29: Residential access: cable modems
Diagram: http://www.cabledatacomnews.com/cmic/diagram.html

## Slide 30: Cable network architecture
home
cable headend
cable distribution
network (simplified)
Typically 500 to 5,000 homes

## Slide 31: Cable network architecture
home
cable headend
cable distribution
network (simplified)

## Slide 32: Cable network architecture
home
cable headend
cable distribution
network
server(s)

## Slide 33: Cable network architecture
home
cable headend
cable distribution
network
Channels
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
D
A
T
A
D
A
T
A
C
O
N
T
R
O
L
1
2
3
4
5
6
7
8
9
FDM:

## Slide 34: Simplified access network diagram
Jason Livingood (Comcast) FCC 2009
Notes: 34
http://www.broadband.gov/ws_fixed_bb.html

## Slide 35: DOCSIS 3.0 Channel Bonding
6 MHz
6 MHz
6 MHz
6 MHz
38 Mbps
38 Mbps
38 Mbps
38 Mbps
152 Mbps
Logical Channel Bonding Technology
DOCSIS 3.0 is the next generation of the DOCSIS standard
DOCSIS 2.0 is limited to single channel’s capacity
DOCSIS 3.0 employs packet bonding across multiple channels
  Initially will bond 4 channels
  8 channel-capable silicon coming soon
  Upstream bonding in 2010
  Increased speeds 100Mbps+
Notes: 35

## Slide 36: Network cost
Electronic and electro-optic costs are dropping rapidly
  GigE switch : 2001 - $15K 2003 - $1.2K 2009 - $600 (12 port)
  GigE transceivers 2001 - $750 2003 - $180
  CWDM transceivers $400-800 for 50-100km reach!
Direct fiber cost is relatively low
  $60/fiber-km in 80-fiber bundle
But – fiber installation cost is still tall pole
  Europe: >$20/m (or any populous wide-area)
  U.S.: >$10m (in simplest desert environment)
A. Whitney (2003, modified)
Notes: http://fiberinfrastructure.blogspot.com/2008/11/construction-cost-estimates.html

## Slide 37: Fiber installation cost
Construction cost (Oct, 2008) estimate for Northern California for a 1" fiber optic cable where aerial infrastructure (poles) are already in place
Method | Cost
Aerial | $3.30/ft
Open trench | $10/ft
Rockwheel (24” depth) | $28/ft
Light underground (trench or bore) | $38.93/ft
Heavy underground (backhoe asphalt) | $72.93/ft
Notes: http://fiberinfrastructure.blogspot.com/2008/11/construction-cost-estimates.html
http://www.liteaccess.com/

## Slide 38: Passive Optical Networks
serves 16-128 premises
  20-32 split common
  1490 nm down, 1310 nm upstream
ITU-T G.984
  2.488 Gb/s down
  1.244 Gb/s upstream
  variable-length packets (GEM)
G.987 (10G-PON): 10 Gb/2.5 Gb/s
EPON: Ethernet frames

## Slide 39: Example: FiOS TV architecture
Fiber
Serving
Office
Serving
Office
Hub
Office
Super
Headend
Broadcast Video
Voice, Data, IP TV
Voice, Data, IP TV
Super
Headend
Serving
Office
Splitter
Fiber
J. Savage (Telecom ThinkTank), Nov. 2006
2 national super headends
9 video hub offices
292 video serving offices
Notes: Joseph Savage, Nov. 29, 2006
http://www.glgroup.com/glgi-presentations/iptv-11-29-06/Savage%20NYC%2011%2029%20seminar%20(3).ppt

## Slide 40: Verizon’s FTTP architecture
ONT
Optical Network Terminal
OLT
Optical Line Terminal
Optical Couplers (WDM)
Voice & Data Downstream 1490 nm
Upstream 1310 nm
Voice, Data & Video 1490 nm, 1310 nm, 1550 nm
1x32
Optical Splitter
EDFA
Erbium Doped Fiber Amplifier
Video 1550 nm
Bandwidth & Services
Upstream
Downstream
Voice, Data & VOD at 622 Mbps
Voice & Data at 155 to 622 Mbps
Broadcast Video
1310 nm
1490 nm
1550 nm
Analog TV
Digital TV and HDTV
54 MHz
864 MHz
CENTRAL OFFICE
customer premise
Brian Whitton, Verizon
Notes: by Brian Whitton, Verizon Networks

## Slide 41: Internet structure: network of networks
roughly hierarchical
at center: “tier-1” ISPs (e.g., UUNet, Level3, Sprint, AT&T), national/international coverage
  treat each other as equals
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-1 providers interconnect (peer) privately
NAP
Tier-1 providers also interconnect at public network access points (NAPs)
Kurose/Ross

## Slide 42: More precisely…
Tier 1 = those ISPs that run no-default routing tables on their backbones
  operations in more than one country
  own and operate their own physical networks
  revenue-neutral peering agreements with other tier 1
  may only be tier-1 regionally
Tier-2 ISPs buy connectivity (upstream transit) from one or more Tier-1 ISPs

## Slide 43: Tier-1 providers
Wikipedia
Provider | AS | Degree
AOL | 1668 | 74
AT&T | 7018 | 1382
Level 3 (with Global Crossing) | 3356 / 3349 | 499
Verizon Business (was UUNET) | 701 | 1452
NTT Communications (was Verio) | 2914 | 254
Centurylink (was Qwest & Savvis) | 209 / 3561 | 828
Sprint | 1239 | 880
Telecom Italia Sparkle (Seabone) | 6762 | 
TeliaSonera International Carrier | 1299 | 
Deutsche Telekom AG (DTAG) | 3320 | 501
NTT Communications | 2914 | 
other major
carriers:
Cogent
XO
AboveNet

## Slide 44: 1901 “data” backbone

## Slide 45: Submarine cable map
http://www.telegeography.com/
Notes: http://www.telegeography.com/

## Slide 46: Backbone: Internet2 architecture

## Slide 47: Internet2 loading
http://atlas.grnoc.iu.edu/I2.html

## Slide 48: Internet topology
AS (Autonomous System) - a collection of routers under the same technical and administrative domain.
EGP (External Gateway Protocol) - used between two AS’s to allow them to exchange routing information so that traffic can be forwarded across AS borders. Example: BGP
large ISP
large ISP
medium ISP
WISP
dedicated
access ISP
EGP
Nina Taft

## Slide 49: Purpose: to share connectivity information
R
border router
internal router
BGP
R2
R1
R3
A
AS1
AS2
you can reach net A via me
traffic to A
table at R1:
dest next hop
A R2
Nina Taft
Notes: BGP is a protocol that happens between 2 nodes.
It uses TCP as its transport protocol. In other words, 2 routers establish a BGP session using TCP and then exchange BGP messages.
During session establishment routers identify themselves. Each neighbor can accept or reject the connection.

## Slide 50: BGP sessions
One router can participate in many BGP sessions.
Initially … node advertises ALL routes it wants neighbor to know (could be >50K routes)
Ongoing … only inform neighbor of changes
BGP Sessions
AS1 (Level3)
AS2 (UDel)
AS3
(MIT)
Nina Taft

## Slide 51: Routing protocols
R
border router
internal router
R1
AS1
R4
R5
B
AS3
E-BGP
R2
R3
A
AS2
announce B
IGP: Interior Gateway Protocol
Examples: IS-IS, OSPF
I-BGP
Nina Taft

## Slide 52: Address arithmetic: address blocks
The <address/prefix> pair defines an address block:
Examples:
  128.15.0.0/16 => [ 128.15.0.0 - 128.15.255.255 ]
  188.24.0.0/13 => [ 188.24.0.0 - 188.31.255.255 ] consider 2nd octet in binary:
Address block sizes
  a /13 address block has 232-13 addresses (/16 has 232-16)
  a /13 address block is 8 times as big as a /16 address block because 232-13 = 232-16 * 23
13th bit
198.00011000.0.0
settable
Nina Taft
Notes: The 2nd example is the case that shows how it works on arbitrary bit boundaries.

## Slide 53: CIDR: longest prefix match
Because prefixes of arbitrary length allowed, overlapping prefixes can exist.
Example: router hears 124.39.0.0/16 from one neighbor and 124.39.11.0/24 from another neighbor
Router forwards packet according to most specific forwarding information, called longest prefix match
  Packet with destination 124.39.11.32 will be forwarded using /24 entry.
  Packet w/destination 124.39.22.45 will be forwarded using /16 entry
Nina Taft

## Slide 54: Four Basic Messages
Open: Establishes BGP session (uses TCP port #179)
Notification: Report unusual conditions
Update: Inform neighbor of new routes that become active Inform neighbor of old routes that become inactive
Keepalive: Inform neighbor that connection is still viable

## Slide 55: BGP attributes
ORIGIN:
  Who originated the announcement? Where was a prefix injected into BGP?
  IGP, EGP or Incomplete (often used for static routes)
AS-PATH:
  a list of AS’s through which the announcement for a prefix has passed
  each AS prepends its AS # to the AS-PATH attribute when forwarding an announcement
  pick shortest route
  useful to detect and prevent loops
Prefix | Next hop | AS Path
128.73.4.21/21 | 232.14.63.4 | 1239 701 3985 631

## Slide 56: Wireless networks

## Slide 57: Frequencies
Licensed vs. unlicensed
  Unlicensed = ISM (door openers to WiFi) + UNII
    902-928 MHz (26 MHz - UHF)
    2.450 – 2.5 GHz (50 MHz - 802.11b/g)
    5.125-5.25 (125 MHz), 5.25-5.35, 5.5250-5.8250, 5.650 – 5.925 GHz
  + whiteband
Roughly:
  lower frequency  longer range
  but smaller capacity (smaller bands)
  2.45 GHz: microwave oven (interference)
  2.5 GHz: foliage issues (beware pine needles!)
    light-light (~380-750 nm = 400-789 THz)
Same technology may be used in different frequency bands
  e.g., WiMAX: 700 MHz, 2.3, 2.4, 2.5, 5.8 GHz
Notes: http://www.ntia.doc.gov/osmhome/allochrt.pdf

## Slide 58: Radio spectrum 1-3 GHz
http://www.ntia.doc.gov/osmhome/allochrt.pdf

## Slide 59: But often lightly used
http://www.sharedspectrum.com/measurements/
NYC, August 2004
Notes:   www.fcc.gov/sptf

## Slide 60: The wireless “stack”
channel coding
sub-channels
(OFDM)
modulation
(QAM, PSK)
multiple access
bits into frequency & phase
protect against bit errors
L1
L2
FDM
large number of orthogonal channels

## Slide 61: WiFi
802.11b: spread-spectrum
  83.5 MHz @ 2.4 GHz: CCK using QPSK
  1 Mb/s - 11 Mb/s nominal, 4.5 Mb/s typical
  11 channels, some countries 2, 4 or 14; 1-6-11 typical
802.11a: OFDM
  480 MHz in 24 (US) 20 MHz channels @ 5 GHz
  23 Mb/s typical, 54 Mb/s max.
802.11g
  2.4 GHz
  23 Mb/s typical, 54 Mb/s max.
802.11n: MIMO
  2.4 or 5 GHz
  74 Mb/s typical, 300 Mb/s max.
not in US

## Slide 62: Cellular wireless technologies
Cell radius: hundreds of m to 35 km (GSM)
  power-controlled
  also: macro cell (tower), micro cell (below roof level), pico cell (indoor)
  900 or 1800 MHz
    US: 850, 1900 MHz
    Scandinavia: 400, 450 MHz (range!)
    GSM: 25 MHz uplink + downlink, 200 kHz channels
Generations:
  1G: analog
  2G:
    TDMA (time-division multiple access)
    CDMA (code-division multiple access)
    GSM (Global System for Mobile Communications)
    iDEN (Integrated Enhanced Digital Network) - Nextel

## Slide 63: Wireless
Markus Isomäki (Nokia), 2008

## Slide 64: 2.5G & 3G wireless
CDMA
  CDMA 1X, 1XEV-DO
    400 kb/s to 2 Mb/s total
    Verizon, Sprint/Nextel
TDMA - GSM
  GPRS (General Packet Radio Services)
    up to 60 kb/s per subscriber
  EDGE (Enhanced Data rates for GSM Evolution)
    up to 150 kb/s per subscriber
    AT&T (iPhone), T-Mobile
  HSDPA (High-Speed Downlink Packet Access)
    1.8 to 14.4 Mb/s
    South Korea
  UMTS/WCDMA

## Slide 65: Evolution of Wireless Technologies
OFDM
MIMO
CDMA |  |  |  | 
GSM |  |  |  | 
Other Technologies |  |  |  | 
Availability: | Now | Now through Mid-2007 |  | 2009
Benefits: | Higher speeds, lower costs, greater efficiencies |  |  | 
1X RTT
EV-DO
Rev. 0
EV-DO
Rev. A
UMB
EDGE
HSDPA
HSPA+
LTE
WiMAX
(802.16e)
New Entrants
4G
3G
2G
Paul Garnett, CTIA, June 2007

## Slide 66: Wireless backhaul
= BS  backbone network
  one of the largest carrier OpEx components (30-40%)
Traditional: T1 (1.5 Mb/s) - $600/month
New solutions:
  microwave
    800 Mb/s to 3 Gb/s (future)
  CableCo fiber ($100/month/Mb/s)
  bonded DSL
  FiOS
  Femtocells – in subscriber home
Notes: http://www.cellular-news.com/tags/backhaul/opex/
http://www.cellular-news.com/story/32737.php
http://www.intomobile.com/2009/09/21/att-3g-microcell-kills-dead-spots-in-charlotte.html
http://www.networkworld.com/news/2008/010808-femtocell.html