## Slide 1: Modern Internet architecture, technology & philosophy
Advanced Internet Services
Dept. of Computer Science
Columbia University
Henning Schulzrinne
Fall 2018

## Slide 3: IP as a core infrastructure interface

## Slide 4: The great infrastructure
Technical structures that support a society  “civil infrastructure”
  Large
  Constructed over generations
  Not often replaced as a whole system
  Continual refurbishment of components
  Interdependent components with well-defined interfaces
  High initial cost
water
energy
transportation

## Slide 5: The Internet as core civil infrastructure
Involved in all information exchange
  (in a few years)
Crucial to
  commerce
  governance
  coordination
  inter-personal communication
Assumed to just be there
  “plumbing”, “pipes”, …

## Slide 6: The Internet as core civil infrastructure

## Slide 7: What’s different?
What | Utilities (gas, water, electricity) | Internet | Consumer electronics
Geographic scope | regional | local, national, international | mostly international
Economics | enabler | entry, competition, enabler | Trade, patents
Impact on culture | minimal | foundational | rarely (Walkman, iPhone)
Impact on domestic politics | in LDCs | jobs, education, health, transportation, copyright, income inequality | health & education (smartphones)
Impact on international politics | water rights? | trade, espionage, propaganda, cyberattacks, copyright, … | trade

## Slide 8: What problems do networks solve?
Diversity in technologies
  wired vs. terrestrial wireless vs. satellite
  trade-off capacity vs. cost vs. distance
Variation in load
  intermittent demand  shared networks
  cannot design capacity for top 5 minutes of load
“Noise”
  electric noise
  radio interference
Human adversaries
  denial-of-service attacks
  information theft
  impersonation

## Slide 9: Interfaces: Energy
1904
1901
110/220V
Lots of other (niche) interfaces
Replaced in a few applications

## Slide 10: Interfaces: Paper-based information
1798, 1922 (DIN)

## Slide 11: Interfaces: Transportation
1435 mm
1830 (Stephenson)
1846 UK Gauge Act
12’
About 60% of world railroad mileage

## Slide 12: Interfaces: Phone system
1970s
1949
Modular: 1975-
RJ11
4 kHz spectrum
48 V off-hook
275 mV audio

## Slide 13: Other long-lived interfaces
Cigarette lighter
(1956)
1878
1993
fuel nozzle
1982
SQL
1974
1992

## Slide 14: What makes interfaces permanent?
Widely distributed, uncoordinated participants
Capital-intensive
  depreciated over 5+ years
  see Y2K problem
Allocation of cost vs. savings
  ISP saves money, end user pays
Hard to have multiple at once
  “natural monopoly”

## Slide 15: Extrapolating from history
IP now “the” data interface
Unclear that any packet-based system can be
  ≥ 10 times cheaper
  ≥ 10 times more functionality
  ≥ 10 times more secure
Replacing phone system due to generality, not performance
  IP offers general channel
 We’re stuck with IPv4/IPv6
  except for niche applications (car networks, BlueTooth, USB, …)
"Bill Gross, founder of tech incubator idealab, operates on the principle that new technology has to be ten times the Fidelity or 10 times the convenience of an entrenched product just to get the Public's attention." Kevin Maney, page 51, trade-off, Ed 2010.

## Slide 16
I was first introduced to the concept of 10x in Peter Thiel’s 2014 book, Zero to One. He says, “As a good rule of thumb, proprietary technology must be at least 10 times better than its closest substitute in some important dimension to lead to a real monopolistic advantage.”
I believe it is not just technology, but the entire customer proposition that needs to be 10x better than the status quo. In my article on the topic, The 2 Principles of Startup Success, I incorporate Clayton Christensen's concept of “jobs to be done,” which gives us a simple premise: Truly innovative or disruptive products and services offer at least a 10x improvement over how things are currently done.
Notes: http://www.mikedp.com/articles/2017/4/12/10x-and-the-largest-technological-improvements-of-all-time

## Slide 17: Integrating infrastructures: Energy
Much of the improvement in civil infrastructure needs networks  information networks complement other networks
  transportation
  energy
Energy time management
  Plug-in hybrid is notified when it should charge
  Dishwasher, water heater run after midnight
  “when can I get 100 kW?”
Utility requests load reduction
  “please reduce load by 1 MW”
Energy management
  “Dear fridge, how many kWh have you used?”

## Slide 18: Example: SmartGrid
Discover controllers and elements
  Utility (gas, electric)
  Local controllers
Authenticate
  Prices and actions may depend on customer contract
Control
Information
“charge at 2300”
“wash at 1900”
“what’s the projected cost of a kWh at 1500?”

## Slide 19: What has changed?
1980s/1990s | 2000s+
Rapid technology evolution in network core | Relatively stable core technology
Internet exceptionalism (no distance! no borders!) | National laws & customs
Internet utopianism | “Big Switch”, harms & limitations
Performance! | Reliability?
Cost-insensitive (and “free” phone access) | Deployment cost barriers
Separated from commercial media (newspaper, magazines, radio, TV) | Affects all media
Self-revealed data (email, BBS) | Intimate data (information access, behavioral)
Little economic impact | One of the largest US exports

## Slide 20: Who runs communication systems and networks?
radio & TV stations
(1,784 TV, 15,470 radio)
cable companies
(“MVPD”)
communities (“muni networks”)
cellular providers (3-4)
wholesaler providers
(“carriers’ carrier”)
incumbent local exchange carriers
(“ILEC”)
satellite providers
private land mobile radio (public safety, transit, taxis, …)
competitive local exchange carriers
(“CLEC”)
rural local exchange carriers
(“RLEC”)
~1,000
# with ~90% marketshare
~12
~2

## Slide 21: Basic Internet money routing
content & service aggregators
Internet
OTT
(over-the-top)
consumer spending
($11.9T)
ISP
$285B (NA, 2016)
$191B (2016)
$56B fixed
$141B mobile
Notes: http://www.tradingeconomics.com/united-states/consumer-spending
https://tradingeconomics.com/united-states/consumer-spending
$56B total wireline revenue is estimated by taking FCC 477 estimate of 104M connections, at $45/month ARPU. Those are estimated from AT&T, Comcast & Charter data.

## Slide 22: Internet applications

## Slide 23: Converging communities
data
voice
(telephone)
broadcast
(radio, TV)
generality
data integrity
access control
machine  machine
machine  human
human  human
low cost
scalability
copyright prot. (DRM)
ease of use
universality
reliability
privacy
since 1900: separate networks, companies, professions
Internet
1960s
1896
1915
1876
IM

## Slide 24: Internet applications
Variations on three themes: messaging, retrieval, continuous media
  distinguish protocol vs. application behavior
Messaging
  datagram model  no direct confirmation of final receipt
  e.g., email (optional confirmation now) and IM
  emphasis on interoperation (SMS, pagers, …)
  delays measured in minutes
Retrieval & query (request/response)
  “client-server”
  e.g., ftp, HTTP
  RPC (Sun RPC, DCE, DCOM, Corba, XML-RPC, SOAP)
  emphasis on fast & reliable transmission
  delays measured in seconds

## Slide 25: Internet applications, cont’d
Continuous media
  generation rate ~ delivery rate ~ rendering rate
  audio, video, measurements, control
    Internet telephony
    Multimedia conferencing
  related: streaming media slightly longer timescales for rate matching
    video-on-demand
  emphasis is on timely and low-loss delivery  real-time
  delays measured in milliseconds

## Slide 26: Network architecture

## Slide 27: Inside a Single Network
Packet filters
Data Plane
  Distributed routers
  Forwarding, filtering, queuing
  Based on FIB or labels
Management Plane
Figure out what is happening in network
Decide how to change it
Shell scripts
Traffic Eng
Databases
Planning tools
OSPF
SNMP
netflow
modems
Configs
OSPF
BGP
Link metrics
OSPF
BGP
OSPF
BGP
Control Plane
Multiple routing processes on each router
Each router with different configuration program
Huge number of control knobs: metrics, ACLs, policy
FIB
FIB
FIB
Routing policies
Notes: Jennifer Rexford, Albert Greenberg, Gisli Hjalmtysson
ATT Labs Research
David A. Maltz, Andy Myers, Geoffrey Xie,
Jibin Zhan, Hui Zhang
Carnegie Mellon University
http://www.cs.princeton.edu/~jrex/talks/cmu-hotnets04.ppt

## Slide 28: Server-based vs. peer-to-peer
Hard to define precisely
  resource sharing?
  no central control?
All Internet applications are peers in a network sense
requests and responses
request
response
smaller number
permanently on-line
diverse power
maybe mobile
disconnects

## Slide 29: Defining peer-to-peer systems
Each peer must act as both a client and a server.
Peers provide computational or storage resources for other peers.
Self-organizing and scaling.
1 & 2 are not sufficient: DNS resolvers provide services to others
Web proxies are both clients and servers
SIP B2BUAs are both clients and servers
Notes: See P2P08 keynote: http://www.cs.columbia.edu/~hgs/2008/P2P08-keynote.pptx

## Slide 30: P2P systems are …
NETWORK ENGINEER’S WARNING
P2P systems may be
inefficient
slow
unreliable
based on faulty and short-term economics
mainly used to route around copyright laws
P2P

## Slide 31: Distributed vs. centralized
Property | Distributed computation | Centralized
Terms | P2P, fog computing, blockchain, TOR | client-server, cloud computing
Who owns resources? | end users (mostly) | enterprise, IaaS, PaaS providers
Isolation | necessary | processes, hypervisor
Virtualization | fog computing | mostly
Functionality | storage, restricted computation | generic (IaaS) or language environment (PaaS)
Advantages | somebody else is paying heat homes for free! limit legal exposure | management trust
Challenges | trust (Tor, P2P) - byzantine free riders failure management | 

## Slide 32: Aside: alternatives to the big-I model
Assumes end-to-end (logical) single network
But reality messier
  split address spaces (NATs)
  UDP and TCP port numbers
  middle boxes
  cf. PBX extensions, mail stops, in-office mail delivery, PO boxes
Architectural themes
  separate “public” from “private” network
  address space? tunneling?
  IPv6 addressing
Internet

## Slide 33: Protocols & layers

## Slide 34: Fundamental interaction patterns
Request-response
  paced by requestor
Continuous media
  paced by sender
Events
  publish/subscribe
unknown
interval

## Slide 35: Internet protocols
Protocols support these applications:
  data plane
    HTTP, ftp data part, SMTP, IMAP, POP, NFS, SMB, RTP
  control plane
    identifier mapping (id  id, id  data)
      ARP, DNS, LDAP
    configuration (= specialized version of identifier  data)
      DHCP, NETCONF, SNMP, XCAP, LoST, …
    control and setup
      RTSP, SIP, ftp control, RSVP, NSIS, SNMP, BGP, OSPF, RIP
May be integrated into one protocol or general service function (“middleware”?)

## Slide 36: Protocols
Protocols define format & order of messages sent and received among network entities
  and actions taken on message transmission or receipt
Often includes notions of time
  what happens if there is no response?
Similar to Application Programming Interfaces (APIs)
  size_t fwrite ( const void * ptr, size_t size, size_t count, FILE * stream );
  differences?
Can also consider a “contract”
  “if I provide you X, you will provide Y”

## Slide 37: Why layering?
Perform functions once
  upper layers rely on lower layers
  in theory (see: “end-to-end principle”)
Common in engineering and society
  postal system, operating systems & other APIs, buildings, …
  but not always formal or deep
  model of a (legal) contract
    “The elements of a contract are "offer" and "acceptance" by "competent persons" having legal capacity who exchange "consideration" to create "mutuality of obligation.” (Wikipedia)
Change implementation without affecting relying parties
  minimize communications, “information hiding”, “isolation”
  “black box”
Topological, economic and administrative scoping
  single physical connection technology
  single vs. multiple administrative domains

## Slide 38: Layers  (sometimes) wrapping
different from APIs!
Notes: http://www.laneye.com/network/ethernet-network-packet-holding-an-ip-packet.gif

## Slide 39: How many layers
2!  industry structure
4!  core Internet protocols
7!  classical layering
9!  sub-layers

## Slide 40: The two-layer model
content
apps & software
services
“Lower layers”
infrastructure
“the network”
copyright
universal service
disability access
investment
technology innovation
patents
resource scarcity
data privacy
location privacy
IP
data theft
disruption

## Slide 41: The Internet Protocol Hourglass (S. Deering)
email WWW phone...
SMTP HTTP RTP...
TCP UDP…
IP
ethernet PPP…
CSMA async sonet...
copper fiber radio...

## Slide 42: Why the hourglass architecture?
Why an internet layer?
  make a bigger network
  global addressing
  virtualize network to isolate end-to-end protocols from network details/changes
Why a single internet protocol?
  maximize interoperability
  minimize number of service interfaces
Why a narrow internet protocol?
  assumes least common network functionality to maximize number of usable networks
Deering, 1998

## Slide 43: Layer splitting
Traditionally, L2 (link), L3 (network = IP), L4 (transport = TCP), L7 (applications)
Layer 2: Ethernet  PPPoE (DSL)
Layer 2.5: MPLS, L2TP
Layer 3: tunneling (e.g., GPRS)
Layer 4: UDP + RTP
Layer 7: HTTP + real application

## Slide 44: Why 4 core layers?
Layer | Colloquial name | Function
1 | PHY | photons & electrons  bits
2 | MAC | bits  packets on one technology
3 | L3 | packets end-to-end, on heterogeneous technologies, to interface
4 | L4 | unreliable  reliable host/interface  application
(5) | Presentation, data | application data structure encoding
7 | Application | Application behavior (email, web)

## Slide 45: Internet layer functions
Layer | Key protocols | Control protocol | Transmission technologies | Administrative domains | Main function | Addresses
PHY | Ethernet, 4G |  | single, but may be diverse (fiber, copper) | 1 | analog-to-digital | none
MAC | Ethernet | 3GPP | same | 1 | framing | MAC address
network | IPv4, IPv6 | DHCP, OSPF, BGP | agnostic | many | end-to-end delivery | IP addresses
transport | UDP, TCP | built-in | agnostic | 2 (ends) | reliability, congestion control | ports
application | HTTP, RTP | SIP | agnostic (except for properties) | 2 (ends) | framing, description, sessions | URLs, email addresses

## Slide 46: The real model

## Slide 47: Layer violations
Layers offer abstraction  avoid “Internet closed for renovation”
Cost of information hiding
  wireless networks
  cost in $ and performance
Cost of duplication of information when nothing changes
  fundamental design choice of Internet = difference between circuit and datagram-oriented networks
Assumption: packets are large and getting larger
  wrong for games and audio
Cost prohibitive on wireless networks
  will see: 10 bytes of payloads, 40 bytes of packet header
  header compression  compress into state index on one link

## Slide 48: Internet acquires presentation layer
All learn about OSI 7-layer model
OSI: ASN.1 as common rendering of application data structures
  used in LDAP and SNMP (and H.323)
Internet never really had presentation layer
  approximations: common encoding (TLV, RFC 822 styles)
Now, XML (& JSON?) as the design choice by default

## Slide 49: Internet acquires session layer
Originally, meant for data sessions
Example (not explicit): ftp control connection
Now, separate data delivery from session setup
  address and application configuration
  deal with mobility
  will see later as RTSP, SIP and H.323

## Slide 50: Putting on Weight
email WWW phone...
SMTP HTTP RTP...
TCP UDP…
IP + mcast
+ QoS +...
ethernet PPP…
CSMA async sonet...
copper fiber radio...
requires more functionality from underlying networks

## Slide 51: Classical Internet philosophy
Almost all functions except packet routing are in end systems
  reliability, security, mobility
   facilitate edge innovation
The network is common carrier
  common carrier: “Under the law, a common carrier is required to make its infrastructure available to everyone willing to pay to access it.”
  does not differentiate (or discriminate against) traffic types or applications or customers
   facilitate edge innovation
  see “network neutrality” discussion

## Slide 52: Network philosophy: End-to-end argument
“All functions need to be performed at the edge”
  edge (end) needed for correctness
  middle can get in the way or sometimes help (performance)
   design vs. “moral” argument (“networks should respect e2e”)
   transparency
   The Rise of the Dumb Network
    common carriage = don’t discriminate against
But:
  ISPs and carriers prefer to sell services, not bit pipes  price differentiation
  network protection against “bad” users
  user protection against “bad” data
  dealing with badly designed protocols (e.g., caching, wireless)
see also http://www.aarnet.edu.au/engineering/wgs/video/presentations/2004Feb/clark.ppt

## Slide 53: Some end-vs-middle issues
Issue | Why middle? | Why end?
Error recovery (FEC, ARQ) | Smaller recovery time (link RTT << e-e RTT) | “real” reliability (including router-induced losses)
Congestion control | Faster feedback more accurate link congestion information | simpler end system
Caching | Disruption tolerance | Access control, visibility
Buffering | Higher TCP throughput (but: buffer bloat) | Cheaper memory
Encryption | Traffic source/destination hiding | Untrustworthy networks

## Slide 54: Internet architecture documents (readings)
http://www.ietf.org/rfc/rfcXXXX.txt
  http://www.zvon.org/ in HTML format with cross-referencing
RFC 1287 (Towards the Future Internet Architecture)
RFC 2101 (IPv4 Address Behaviour Today)
RFC 2775 (Internet Transparency)
RFC 3234 (Middleboxes: Taxonomy and Issues)

## Slide 55: Guidelines
Middleboxes:
  firewalls, network address translators, transparent caches
  connection disruptions
  application surprises
  energy consumption (refresh)
  see (e.g.,) SIGCOMM 2011 “An Untold Story of Middleboxes in Cellular Networks”
Minimize pain 
  Coordinated
  Discoverable (not today)
  Discoverable behavior
    e.g., timeouts, port blocking, NAT behavior
Notes: http://conferences.sigcomm.org/sigcomm/2011/papers/sigcomm/p374.pdf

## Slide 56: Serialization

## Slide 57: Serialization
It lets you take an object or group of objects, put them on a disk or send them through a wire or wireless transport mechanism, then later, perhaps on another computer, reverse the process: resurrect the original object(s). The basic mechanisms are to flatten object(s) into a one-dimensional stream of bits, and to turn that stream of bits back into the original object(s).
  Like the Transporter on Star Trek, it's all about taking something complicated and turning it into a flat sequence of 1s and 0s, then taking that sequence of 1s and 0s (possibly at another place, possibly at another time) and reconstructing the original complicated "something.” [C++ FAQ]
Notes: http://www.parashift.com/c++-faq-lite/serialize-overview.html

## Slide 58: Problem: squeezing 8 bits into 7 (or 6)  base64
Many Internet channels (e.g., email & URL) are subset of ASCII  6 or 7 bits
  other characters may be dropped or converted
  base64 as a common encoding
  convert 3 octets (8-bit characters = 24 bits) into 4 characters of 6 bits (24 bits)

## Slide 59: Serialization: TLV
IPv6
Notes: http://www.openwall.com/presentations/IPv6/img23.png

## Slide 60: Serialization: ASN.1
30 13 02 01 05 16 0e 41 6e 79 62 6f 64 79 20 74 68 65 72 65 3f
serialization = convert data structure into
(linear) byte stream
like C, without pointers…

## Slide 61: Serialization: RFC 822
Delivered-To: hgs10@lionmailmx.cc.columbia.edu
Received: by 10.140.158.132 with SMTP id e126csp131562qhe;
Thu, 28 Aug 2014 14:01:48 -0700 (PDT)
Return-Path: etickets@amtrak.com
Return-Path: etickets@amtrak.com
Received: from unknown (HELO etvswas01p) ([10.14.128.202])
by phlsmtprelay01.amtrak.com with ESMTP; 28 Aug 2014 16:55:42 -0400
Date: Thu, 28 Aug 2014 17:01:30 -0400 (EDT)
From: etickets@amtrak.com
To: HGS@cs.columbia.edu, HENNING.SCHULZRINNE@FCC.GOV
Message-ID: <633700356.JavaMail.TDDServerProd@amtrak.com>
Subject: Amtrak: eTicket and Receipt for Your 09/10/2014 Trip
MIME-Version: 1.0
Content-Type: multipart/mixed;
boundary="----=_Part.1409259690306”
MIME-Version: 1.0
Content-Type: multipart/mixed;

## Slide 62: Serialization: XML
<note>
<id>1</id>
<name>A green door</name>
<price>12.50</price>
<tags>
<tag>home</tag>
<tag>green</tag>
</tags>
</note>

## Slide 63: Serialization: JSON
{
"id": 1,
"name": "A green door",
"price": 12.50,
"tags": ["home", "green"]
}

## Slide 64: Serialization trade-offs
Property | TLV | ASN.1 | JSON, XML, RFC 822
Space | compact | somewhat | inefficient
Time | efficient | not aligned | inefficient
Energy | efficient | somewhat | inefficient
Structured | yes | yes | JSON, XML
Self-describing | backwards-compatible | backwards-compatible | labeled
Signable | mostly | DER | canonical formats

## Slide 65: Network evolution & research

## Slide 66: Networking is getting into middle years
 | idea | current
IP | 1969, 1980? | 1981(RFC 791)
TCP | 1974 (RFC 675) | 1981(RFC 793)
telnet | 1969 (RFC15) | 1983 (RFC 854)
ftp | 1971 (RFC 114) | 1985 (RFC 959)
Notes: http://www.cs.utexas.edu/users/chris/think/ARPANET/Telnet/Telnet.shtml

## Slide 67: Internet/broadband: one of the fastest applications ever introduced
0
20
40
60
80
100%
0
120
100
80
60
40
20
Years since introduction
% of Households
(US)
Automobile
1886
Telephone
1876
Electricity
1873
Television
1926
Radio
1905
VCR
1952
Internet
1975
Broadband
Access
1995
Source: Michael Fox and Forbes Magazine, Morgan Stanley
2005 = 30% broadband / 2010 = 70% broadband estimate
Notes: Access technologies for communication between branch offices and central network
ICT academy May, 26th, 2004
Alex Lorette
Product Line Manager –
Data Access Professional market

## Slide 68: Adoption S-curve
https://www.researchgate.net/figure/S-curve-adoption-model-of-music-streaming-adoption-rate-The-arrow-indicates-an_fig7_307991686

## Slide 69: Residential broadband penetration (US)

## Slide 70: Standardization
Oscillate: convergence  divergence
  continued convergence clearly at physical layer
  connectivity trumps functionality
  niches larger  support separate networks
Two facets of standardization:
  public, interoperable description of protocol, but possibly many (Tanenbaum)
  reduction to 1-3 common technologies
    L2: Arcnet, tokenring, DECnet, ATM, FDDI, DQDB, SONET …  Ethernet
    L3: IP, IPX, X.25, OSI  IP
    OS: dozens  Windows, MacOS, Linux

## Slide 71: Standardization
Have reached phase 2 in most cases
  RPC (SOAP, REST) and presentation layer (XML, JSON) most recent 'conversions‘
Often, non-standardized technologies can be deployed faster
  single (dominant) vendor
    Skype vs. SIP and H.323
    AOL IM and XMPP (Jabber) vs. SIMPLE
    SMB vs. NFS vs. WebDAV
 Standardization after success?
IETF one-protocol-for-application vs. everything-is-RPC
  not enough network experts  standardization scales better
  see OASIS, OMA standardization groups

## Slide 72: Technologies at ~30 years
Other technologies at similar maturity level:
  air planes: 1903 – 1938 (Stratoliner)
  cars: 1876 – 1908 (Model T)
  analog telephones: 1876 – 1915 (transcontinental telephone)
  railroad: 1820s – 1860s (transcontinental railroad)

## Slide 73: Observations on progress
1960s: military  professional  consumer
  now, often reversed
Communications technologies rarely disappear (as long as operational cost is low):
  exceptions:
    telex, telegram, semaphores  fax, email
    X.25 + OSI, X.400  IP, SMTP
  analog cell phones
   thus, NGN (post-IP, future Internet) discussions likely academic

## Slide 74: Lifecycle of technologies
military
corporate
consumer
traditional technology propagation:
opex/capex doesn’t matter;
expert support
capex/opex sensitive, but amortized;
expert support
capex sensitive;
amateur
Can it be done?
Can I afford it?
Can my mother use it?

## Slide 75: Example: Telex

## Slide 76: Transition of networking
Maturity  cost dominates
  can get any number of bits anywhere, but at considerable cost and complexity
  casually usable bit density still very low
Specialized  commodity
  OPEX (= people) dominates
  installed and run by 'amateurs'
  need low complexity, high reliability

## Slide 77: User challenges vs. research challenges
Are we addressing real user needs?
  Engineering vs. sports scoring
My guesses
reliability
ease of use
cost
no manual
integration
limited risk
phishing
data loss
no re-entry
no duplication

## Slide 78: Example: Email configuration
Application configuration for (mobile) devices painful
SMTP port 25 vs. 587
IMAP vs. POP
TLS vs. SSL vs. “secure authentication”
Worse for SIP...

## Slide 79: Example: SIP configuration
highly technical parameters, with differing names
inconsistent conventions for user and realm
made worse by limited end systems (configure by multi-tap)
usually fails with some cryptic error message and no indication which parameter
out-of-box experience not good
partially explains

## Slide 80: Internet and networks timeline
1960
1970
1980
1990
2000
2010
theory
university
prototypes
production use
in research
commercial
early residential
broadband
home
email
ftp
DNS
RIP
UDP
TCP
SMTP
SNMP
finger
ATM
BGP, OSPF
Mbone
IPsec
HTTP
HTML
RTP
100 kb/s
1 Mb/s
10 Mb/s
XML
OWL
SIP
Jabber
100 Mb/s
1 Gb/s
port
speeds
Internet
protocols
queuing
architecture
routing
cong. control
DQDB, ATM
QoS
VoD
p2p
ad-hoc
sensor

## Slide 81: Cause of death (or delay) for the next big thing
 | QoS | multi- cast | mobile IP | active networks | IPsec | IPv6
not manageable across competing domains |  |  |  |  |  | 
not configurable by normal users (or apps writers) |  |  |  |  |  | 
no business model for ISPs |  |  |  |  |  | 
no initial gain |  |  |  |  |  | 
80% solution in existing system |  |  |  |  |  |  (NAT)
increase system vulnerability |  |  |  |  |  | 

## Slide 82: Why do good ideas fail?
Research: O(.), CPU overhead
  “per-flow reservation (RSVP) doesn’t scale”  not the problem
      at least now -- routinely handle O(50,000) routing states
Reality:
  deployment costs of any new L3 technology is probably billions of $
Cost of failure:
  conservative estimate (1 grad student year = 2 papers)
  10,000 QoS papers @ $20,000/paper  $200 million

## Slide 83: CS research to reality
CS as science
CS as engineering

## Slide 84: CS tech transfer, mode 1

## Slide 85: CS tech transfer, mode 2

## Slide 86: Networking research is fashion-driven
networking courses
First (European) workshop
on X --
YAP on X
workshop
white paper
DARPA, NSF
 $$
secondary
conferences
EU
Nth framework
Sigcomm
Infocom
Mobicom
ICNP
ATM
DQDB
QoS
mobile networks
wireless
ad-hoc, sensor
active networks
trailing-edge
research

## Slide 87: Research: Network evolution
Only three modes, now thoroughly explored:
  packet/cell-based
  message-based (application data units)
  session-based (circuits)
Replace specialized networks
  left to do: embedded systems
    need cost(CPU + network) < $10
    cars
    industrial (manufacturing) control
    commercial buildings (lighting, HVAC, security; now LONworks)
    remote controls, light switches
    keys replaced by biometrics

## Slide 88: Research: Pasteur’s quadrant
Quest for Fundamental Understanding? | Yes | Pure basic research (Bohr) | Use-inspired basic research (Pasteur)
 | No |  | Pure applied research (Edison)
 |  | No | Yes
 |  | Considerations of Use? | 
Pasteur’s Quadrant: Basic Science and Technological Innovation, Stokes 1997 (modified)
Guessing at problems
(Infocom)
Most networking research
is here
Most networking research
wants to be here

## Slide 89: Maturing network research
Old questions:
  Can we make X work over packet networks?
    All major dedicated network applications (flight reservations, embedded systems, radio, TV, telephone, fax, messaging, …) are now available on IP
  Can we get M/G/T bits/s to the end user?
  Raw bits everywhere: “any media, anytime, anywhere”
New questions:
  Dependency on communications  Can we make the network reliable?
  Can non-technical users use networks without becoming amateur sys-admins?  auto/zeroconfiguration, autonomous computing, self-healing networks, …
  Can we make networks affordable to everyone?
  Can we prevent social and financial damage inflicted through networks (viruses, spam, DOS, identity theft, privacy violations, …)?

## Slide 90: New applications
New bandwidth-intensive applications
  Reality-based networking
  (security) cameras  “ambient video”
Distributed games often require only low-bandwidth control information
  current game traffic ~ VoIP
Computation vs. storage vs. communications
  communications cost has decreased less rapidly than storage costs

## Slide 91: Change is hard
No new network services deployed since 1980s
  universal upgrade
  chicken/egg (network/OS) problem
“Innovation at edges”
Applications easier, as long as
  TCP-based
  client-server
  … but there are exceptions (p2p)
routers
OS
applications
needs +
wait for usage
networks

## Slide 92: Time of transition
Old | New
IPv4 | IPv6
circuit-switched voice | VoIP
separate mobile voice & data | LTE + LTE-VoIP
911, 112 | NG911, NG112
digital cable (QAM) | IPTV
analog & digital radio | Pandora, Internet radio, satellite radio
credit cards, keys | NFC
end system, peers | client-server v2 aka cloud
all the energy into transition  little new technology

## Slide 93: Internet challenges
  IP address depletion
  NAT, middle boxes and the loss of transparency
  Routing infrastructure
  Quality of service
  Security
  DNS scaling
  Dealing with privatization
  Interplanetary Internet
Wu-Chi Feng

## Slide 94: Complexity

## Slide 95: Mid-Life Crisis
email WWW phone...
SMTP HTTP RTP...
TCP UDP…
IP4 IP6
ethernet PPP…
CSMA async sonet...
copper fiber radio...
doubles number of service interfaces
requires changes above & below
major interoper-ability issues

## Slide 96: “Why architectural complexity is like body fat”
You naturally tend to gain it while you grow older
Very easy to gain and very hard to get rid of
  Designing complex solutions and protocols easier than designing simple ones.
Healthy to have some, but not too much
Having it on waist may be worse than elsewhere
Younger and slimmer will eventually beat you
  Architectural complexity  reduced agility  younger and less complex systems eventually replace older and more complex system.
Sometimes surgery is a good way to start
Long term results require constant exercise
http://www.tml.tkk.fi/~pnr/FAT/

## Slide 97: Causes of complexity
Complexity: implementation vs. run-time
  system vs. protocol
After-the-fact enhancements:
  security
  NAT traversal
  mobility
  internationalization (e.g., DNS)
Wrong layer for function
  multicast? IP security?
Options
  e.g., multiple transport protocols, IPv4 & IPv6
Lots of special protocols
  e.g., IMAP, POP, SMTP
Manual configuration

## Slide 98: Network traffic & economics

## Slide 99: Mobile traffic distribution – 2017 prediction

## Slide 100: Mobile traffic is mostly Wi-Fi

## Slide 101: Video, video and more video
Sandvine Internet Phenomena
Notes: Sandvine Spring 2011

## Slide 102: Bandwidth generations

## Slide 103: Cost of bandwidth
Notes: http://www.tccomm.com/Literature/Default.aspx/Ethernet-Network-White-Papers/SONET-to-Ethernet-comparisonhttp://www.flickr.com/photos/ciena/4860340282/in/photostream/
http://www.westernsystems-inc.com/comm_ethernetappintrafficcontrol.ht
http://www.ciena.com/corporate/blog/Bandwidth-explosion-vs-revenue-growth-Why-service-providers-are-not-going-broke.htmlService Speed (mbps) Average
Price Price
per Meg
DS1 (T1) 1.54 $450 $292.20
DS3 45 $5,000 $111.11
Ethernet over Copper 10 $950 $95.00
Fast Ethernet 100 $5,000 $50.00
Metro Ethernet 1000 $25,000 $25.00

## Slide 104: Transit prices
Chart: 
| 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
$/Mbps | 1200 | 800 | 675 | 400 | 200 | 120 | 90 | 75 | 50 | 25 | 12 | 9 | 5 | 3.25 | 2.34 | 1.57 | 0.94 | 0.63
http://drpeering.net/white-papers/Internet-Transit-Pricing-Historical-And-Projected.php

## Slide 105: Bandwidth costs
Amazon EC2
  $50 - $90/TB out, $0/TB in
CDN (Internet radio)
  $600/TB (2007)
  $30-90/TB (2017 – CDNpricing.com)
NetFlix (7 GB DVD)
  postage $0.70 round-trip  $100/TB
FedEx – 2 lb disk
  5 business days: $6.55
  Standard overnight: $43.68
  Barracuda disk: $91 - $116/TB
DVD-R (7 GB)
  $0.25/disk  $35/TB
Notes: FedEx and EC2 prices as of 09/15/09
CDN: http://www.mindbranch.com/listing/product/R678-29.html
http://www.cdnpricing.com/

## Slide 106: Amazon Snowball
50-80 TB
47 lbs
$200-$250  $3.12/TB
shipping not included
$37.49  $0.47 TB

## Slide 107: Network reality

## Slide 108: Textbook Internet vs. real Internet
Ideal | Reality
end-to-end (application only in 2 places) | middle boxes (proxies, ALGs, …)
permanent interface identifier (IP address) | time-varying (DHCP)
globally unique and routable | network address translation (NAT)
multitude of L2 protocols (ATM, ARCnet, Ethernet, FDDI, modems, …) | dominance of Ethernet, but also L2’s not designed for networks (1394 Firewire, Fibre Channel, MPEG2, …)

## Slide 109: Textbook Internet vs. real Internet
mostly trusted end users | hackers, spammers, con artists, pornographers, …
small number of manufacturers, making expensive boxes | Linksys, Dlink, Netgear, …, available at Walmart
technical users, excited about new technology | grandma, frustrated if email doesn’t work
4 layers (link, network, transport, application) | layer splits
transparent network | firewalls, L7 filters, “transparent proxies”

## Slide 110: Which Internet are you connected to?
multicast
QoS
IPv6
IPv4
PIA
IPv4
DHCP
IPv4
NAT
port 80 + 25

## Slide 111: The two-port Internet
Many public access systems only allow port 80 (HTTP) and maybe 25 (SMTP)
  e.g., public libraries
Everything tunneled over HTTP
  Web-based email
  Flash video delivery (e.g., YouTube)
  HTTP CONNECT for remote login
Dave Thaler

## Slide 112: Causes
Link-layer technologies
  satellite, DSL
  NBMA
Network-layer technologies
  security: broken by design vs. broken by accident?
  NATs
  Ill-defined meaning of IP addresses and names
    theoretically, single network interface
    practically, often more than that
      virtualization
      multi-homing
      fail-over

## Slide 113: Private Internet -- challenges
Public Internet = collection of privately-owned (mostly) for-profit networks
Incentives for greedy behavior
Special-purpose networks
  VoIP networks
  3GPP, NGN, …  “walled garden”
  sub-applications large enough to support own infrastructure
Private protocols
  e.g., most IM protocols
Patent encumbrances
  see https://datatracker.ietf.org/public/ipr_disclosure.cgi
D. Clark, J. Wroclawski, K. Sollins, R. Braden, “Tussle in Cyberspace: Defining Tomorrow’s Internet”, ToN, June 2005

## Slide 114: Tussle in Cyberspace
Traditional view: design technology to make choices
Tussle view: design technology to allow choices
  “we are designing the social contract that the Internet embodies”
  not a final outcome, on-going process  lawyers vs. engineers
Multiple competing interests
  application value capture
    high value content looks the same to ISP
  traffic price differentiation
    willingness to pay
  investment in infrastructure vs. open interfaces
    sunk costs
  greed (local traffic optimization vs. social optimum)
  privacy and anonymity vs. societal goals
    CALEA, network resource protection, spam, DRM
 Allow multiple outcomes, but give users choice (competition)
  user-selected routes and servers
see also http://www.aarnet.edu.au/engineering/wgs/video/presentations/2004Feb/clark.ppt

## Slide 115: Other network types
network | partially disconnected | mobile end systems | wireless links | mobile routers | energy optimization | node computation
“classical” Internet | caching, sync. | fixed nomadic mobile | last hop |  |  | 
mesh networks |  |  | all links | slowly |  | 
MANET |  | only | only | fast |  | 
delay-tolerant networks | possibly | planets space craft | only |  |  | 
sensor networks | some systems | yes | common | some | crucial | common