## Slide 1: Mixing IoT technologies for better performances
By: Khaldoun Al Agha
With: Henning Schulzrinne
Jean Schwoerer
Raouf Boutaba
CIOT 2018
https://www.ciot-conference.org

## Slide 2: Presentation of the Panelists
Prof. Henning Schulzrinne: Julian Clarence Levi Professor of Computer Science at Columbia University
Raouf Boutaba: Professor of Computer Science and Associate Dean Research of the faculty of Mathematics at the University of Waterloo
Jean Schwoerer leader of the project "Massive IoT Connectivity" at Orange Labs

## Slide 3: Technologies for IoT
10 100 1000 10000
100 Mbit/s
10 Mbit/s
1 Mbit/s
100 Kbit/s
10 Kbit/s
1 Kbit/s
100 bit/s
Ultra Narrow Band (Sigfox, etc.)
Bluetooth 5.0
Bluetooth 4.0
Bluetooth1.0
LoRa
LTE
WiFi
HaLow
WiGig
LTE-M
LTE NB-IoT
Zigbee, Z-Waze, BLE

## Slide 4: Vertical constraintes
Vertical | Power | Range | Débit | Location | Security
Health | Years | Body + | low | Indoor | High+
Home Building | Years | Home | low | Indoor | Medium
Security | Years | Home+ | High (video surveillance) | Not mandatory | Medium
Energy Management | Months | Local and long range | Low | Not mandatory | Low
Remote monitoring | Solar Panel | Long | Low | Outdoor | High+

## Slide 5: Technologies assets
 | Power | Range | Data rate | Location
PAN (Zigbee, BLE, Zwave…) | Low | Home | Low | Indoor
LAN (WiFi n, ac, ax…) | Medium | Home+ | Medium to high | Indoor
LPWAN and NB (Sigfow, LoRa NB-IoT…) | Low+ | Up to 10 Km | Low | No
Cellular (GSM, 3G, LTE…) | Medium | Up to 30 Km | Medium to High | No

## Slide 6: Multiple constraintes
What happen if my system needs:
  Low power and high bitrate?
  No solution from existing technologies
For example:
  An independent system for surveillance
  Pollution done by oil dumping (de-ballasting)
  Video surveillance in isolated areas
  …
We need high bitrate while power source is poor

## Slide 7: Solution: integration of different technologies
Low power system (for example LoRa, Zigbee) for sensors that detect an event (pollution, presence)
This system will be a trigger to wake up a high bit rate system to provide surveillance (for example WiFi Mesh)
Need a smart algorithms to optimize the On-Off cycles.
Smart buoy with pollution sensors connected by LoRa
Cameras connected by WiFi Mesh
When pollution detection, camera are turned ON for surveillance