## Slide 1: Gigabit measurements – quality, not (just) quantity
Henning Schulzrinne
Columbia University

## Slide 2: Bottlenecks move
1990-2010: last mile
2015: interconnection
2010-2018ish: home Wi-Fi
2012-5G: mobility
2016-2020: servers
also, bottlenecks less predictable
fewer end points (greater HHI…)

## Slide 3: What are we trying to achieve?
Compare actual to advertised performance?
  Speed metrics may fade in visibility (see 4G)
Determine application QoE?
Determine consumer satisfaction?
  What about network reliability?
Determine average speed of Internet in country X and “X faster than Y”?
Estimate contributions of Internet bottlenecks (over time)?
Evaluate changes in metrics over time?
What if bandwidth changes over time (down-grading in mobile)?
 gather enough data to allow reasoned discussion for all of these

## Slide 4: Two audiences
Research, consumer protection agencies, journalists?
Advertised vs. actual
Which version of TCP or QUIC?
Changes over time
Performance inputs: latency, packet loss, loss bursts
DNS and interconnect performance
Reliability at different timescales (500 ms and up)
Consumers
What broadband service should I choose? Which provider?
Is something wrong with my service?
Will I get 8K video?
Without stalls?
For all video services I care about?
Can I count on doing that video conference from home?

## Slide 5: What should we measure?
Single-server performance – but capture destination and path
  with TCP changes (e.g., BBR and QUIC), fairness may be more unpredictable
Multi-server parallel performance (diverse data centers & CDNs)
Real world video (see next)
End-to-end & component reliability
  partial reachability
  temporary performance degradation (vs. discarding worst samples)
  carrier DNS resolver
  CDNs
  probably now more critical than raw performance

## Slide 6: The goal is invisibility
No longer raw speed, but “invisibility”  the Internet should not get in the way of what people want to do
Comparison: no longer indicate FLOPS, CPU clock speeds
What is the threshold?

## Slide 7
  Adaptive bitrate comparison chart
Feature | Adobe HDS | Apple HLS | Microsoft SS | MPEG- DASH
Deployment on ordinary HTTP servers |  |  |  | 
Flexible DRM support |  |  |  | 
HTML5 support |  |  |  | 
Agnostic to video and audio codecs |  |  |  | 
HEVC Ready (UHD/4K) |  |  |  | 
Typical segment duration | 2-4s | 10s | 2-4s | Flexible
[2] Bitmovin - MPEG-DASH vs. Apple HLS vs. Microsoft Smooth Streaming vs. Adobe HDS

## Slide 8
  QoS and QoE in video streaming
Network
Application
Service
End-user
QoS domain
QoE
domain
delay, throughput and packet loss
frame rate, resolution, color, video and audio codec type
VoD, video conference and IPTV
Viewing experience

## Slide 9
Common QoE metrics in video streaming
Start-up delay
Rebuffering
Avg. bitrate
Bitrate change
Time from the instant a play button is clicked to when the player actually starts to play the main video
  Video stalling or buffer underrun
  Occurs when the playback rate is higher than what the network can handle
Average played bitrate during playback
Bitrate increases or decreases while a video is being played

## Slide 10
  Video quality report by OTT service providers
    Google Video Quality Report – A friendly, consumer focused report card [4]
    Netflix ISP Speed Index – Focused on ISP QoE rankings [5]

## Slide 11
  YouSlow platform
https://dyswis.cs. columbia.edu/youslow/
Initial buffering
Video ads
Bitrate change
Rebuffering
Abandonment
Video QoE analysis metrics
Avg. played bitrate
Avg. rebuffering ratio
Avg. HTTP latency
Others
QoE report metrics
YouSlow app.
Chrome plug-in
End-user device
User-friendly QoE report
Initial buffering
Pre-roll ads length
Bitrate change
Rebuffering
Video buffering status
ISP and location info.*
Monitor playback events from within video players
* MaxMind: IP Geolocation

## Slide 12
YouSlow Chrome extension
Internet
YouSlow server
Access YouTube player
via YouTube Player API [17]
End-user’s Chrome browser
YouSlow extension
Inject a script when a viewer watches video at www.youtube.com
Background scripts
Chrome local storage
Chrome Web request
YouSlow core content scripts
Obtain various playback status directly from the video players e.g., start-up latency, quality changes, rebuffering status, location and ISP info.

## Slide 13
YouSlow monitoring site
Date
Date
Avg. HTTP latency (ms)
Avg. rebuffering ratio (%)
Approximate location of events
Played bitrates and avg. HTTP latency
Rebuffering ratio
https://dyswis.cs.columbia.edu/youslow/
HTTP latency during playback
Rebuffering ratio

## Slide 14
  Distribution of YouTube played bitrates

## Slide 15
  Comparison of YouTube played bitrates
Different types of Internet connections
U.S. ISPs

## Slide 16
Rebuffering ratio on abandonment rate
More viewers abandoned the videos as the rebuffering ratio increased
Ad-free
Rebuffered
Non-initial buffered