## Slide 1: Making networks slower: 5G and IoT
Henning Schulzrinne (Columbia University)
NAE 5G Colloquium
November 2018
This material is based upon work supported by the National Science Foundation under Grant No. (CNS-1218977). Any opinions, findings, and conclusions or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the National Science Foundation.

## Slide 3: Natural evolution

## Slide 4: Key enablers
IoT
Cheap SOCs
Mature Internet protocols
Cellular connectivity
Unlicensed
Analytics
(“big data”)
Applications
Cloud-hosted applications & data

## Slide 5: Pick your number
IEEE
Spectrum
8/2016
 the keynote estimator: the higher, the more likely to be cited in a keynote
Notes: https://www.cisco.com/c/dam/en/us/products/collateral/se/internet-of-things/at-a-glance-c45-731471.pdf

## Slide 6: IoT is not exactly new (1978)

## Slide 7: IoT – an idea older than the web (1985)
Peter Lewis (panel discussion 1985)
From Chetan Sharma Consulting 2016

## Slide 8: The IoT killer app
http://www.traptec.eu/

## Slide 9: For public safety, plan for surprises
Generation | Expectation | Surprise | Cost per GB
0G (landline) | voice | fax & modem | 
1G | corporate limousine | eavesdropping | 
2G | better voice quality (“digital!”) | SMS | $1000
3G | WAP | web | $100
4G | IMS | YouTube, WhatsApp, notifications | $10
5G | IoT (low latency) | ? | $1?
underestimated cost and WiFi-equivalence as drivers
are the even generations the successful ones?

## Slide 10: 20 billion devices ≠ 20 billion device 5G connections
hybrid connectivity: cheap +
ubiquitous
managed connectivity
cheap connectivity

## Slide 11: IoT is not a helpful term
The only common thread is what doesn’t matter: absence of a human
Otherwise, spans every dimension of networking
mobility
high-speed train
aeronautical
fixed infrastructure
bandwidth
latency
geography
4K video
10 ms protective relay
industrial control
remote pipeline
message/week
minutes
or hours
indoors or urban
easy
hard
cost constraints
$1/year
$5/device
1% of $1B bridge

## Slide 12: Special case of IoT: Ultra-Reliable Low Latency Communication
Rapeepat Ratasuk, Nokia
NB-IOT (Rel 13)
LTE CAT1

## Slide 13: URLLC use cases
Rapeepat Ratasuk, Nokia
competing
with fiber
and proprietary
networks

## Slide 14: What is the scale of outdoor and distributed applications?
one per household or business (e.g., 136M housing units in US)
31,100 in US
but often connected to city fiber network
5 million (US)
62,000 in NYC
26.5M (44M) in US
$2B energy cost / year
Boston: 64k street lights
but: often connected to fiber (5G!)
268.8M (US) cars, trucks, …
Notes: http://64.27.51.222/media/overview-of-the-us-parking-industry.aspx parking meters
https://www1.eere.energy.gov/buildings/publications/pdfs/ssl/nlc-streetlight2013_smalley.pdf

## Slide 16: Trading bandwidth – coverage - cost
Notes: Keysight 2017: https://www.keysight.com/upload/cmc_upload/All/20170612-A4-JianHuaWu-updated.pdf

## Slide 17: Cellular narrowband IoT
 | LTE Cat 1 | LTE Cat 0 | LTE Cat M1 (eMTC) | LTE Cat NB1 (NB-IoT)
3GPP Release | Release 8 | Release 12 | Release 13 | Release 13
Mobility | Full | Full | Full | Only idle mode reselection
DL peak | 10 Mb/s | 1 Mb/s | 1 Mb/s | 50 kb/s
UL peak | 5 Mb/s | 5 Mb/s | 375 kb/s (HD) 1 Mb/s | 250 kb/s (multi tone) 20 kb/s (single tone)
Latency | 50-100 ms | Not deployed | 10-15 ms | 1.6-10 s
Duplex mode | Full | Full & half | Full & half | Half
Device receive bandwidth | 1.4 – 20 MHz | 1.4 – 20 MHz | 375 kHz 1.4 MHz | 180 kHz
MCL (path loss) | 142 dB | 142 dB | 156 dB 164 dB (claimed) | 164 dB (but)
Notes: https://www.iot-now.com/2016/06/21/48833-cat-m1-vs-nb-iot-examining-the-real-differences/
https://altair-semi.com/wp-content/uploads/2017/02/Coverage-Analysis-of-LTE-CAT-M1-White-Paper.pdf
https://www.keysight.com/upload/cmc_upload/All/20170612-A4-JianHuaWu-updated.pdf

## Slide 18: 5G low latency
X
X
V2I2V
X
one-to-many!
EEW
(< 5 s)
tight control loop  near-100% availability in time & space
X
LAN
protective
relay

## Slide 19: T-Mobile (US) example
NB-IoT
u-blox SARA-N410-02B (20k+ at $5 ea.)
Notes: https://iot.t-mobile.com/pricing/#annual-plans

## Slide 20: Alternative: satellite communication
Iridium
two-way
GlobalStar
GPS fix every 10 minutes
LEO
NEXT
Notes: http://www.oneweb.world
https://www.iridiumnext.com/2016/09/22/new-platform-new-possibilities/

## Slide 21: Conclusion
There is no IoT – there are lots of them and very different
  low-bandwidth, infrequent, resilient  URLLC
  outdoor vs. factory (replace Ethernet, Wi-Fi) vs. home
  business models: “free” Wi-Fi vs. paid, licensed spectrum
Economic model changes
  Traditional applications: capacity + cost per GB
    $50/month/device
  Many IoT applications: annual cost per device
    $6/year/device
Application areas for URLLC are still speculative
  change in factory model (wireless) + business model (external)