## Slide 1: Network Neutrality is About Money, not Packets (Price discrimination, not packet discrimination)
Henning Schulzrinne
SDP Workshop
May 2018
This material is based upon work supported by the National Science Foundation under Grant No. (CNS-1218977). Any opinions, findings, and conclusions or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the National Science Foundation.

## Slide 2: A simplified evolution of network neutrality
Early (2003-2009)
Intermediate (2010)
Advanced (2015-)
no blocking
attach non-harmful devices
competition
no blocking
no discrimination
transparency
privacy
interconnection
semi-voluntary?
Reversal (2017?)
zero rating & caps
anti-trust?
tethering
Section 706
Authority unclear
Title II
Information service?

## Slide 3: How to be non-neutral
deep packet inspection
block Skype
user tracking
block transport protocol
block ports
insert RST
block IP addresses
QoS discrimination
zero-rating
application
transport
network
Not all practices are necessarily violations

## Slide 4: Some high-profile cases
VPN blocking (Comcast, roughly 2001) - unconfirmed
WiFi blocking (AT&T AUP, 2002)
Madison River (2005)
  DSL provider blocked SIP ports
  fined $15,000 by FCC
  based on Section 201 “just and reasonable”
Comcast (late 2007)
  insert TCP RST into BitTorrent traffic
  later overturned on appeal in DC Circuit Court
RCN (2009): P2P
FaceTime on AT&T
Comcast vs. Level 3 (2010, in dispute) - interconnection
Comcast, Verizon, AT&T, … vs. Netflix termination (2013-2014)
Zero-rating (AT&T, T-Mo, VZ, Comcast)
Notes: http://hraunfoss.fcc.gov/edocs_public/attachmatch/DA-05-543A1.pdf
http://www.zeropaid.com/news/88573/comcast-prevails-in-bittorrent-throttling-case/
http://www.practicallynetworked.com/news/comcast.htm
AT&T 2002 terms for DSL - https://www.wired.com/story/how-the-fccs-net-neutrality-plan-breaks-with-50-years-of-history/
Examples of prohibited programs and equipment include, but are not limited to, mail, ftp, http, file sharing, game, newsgroup, proxy, IRC servers, multi-user interactive forums and Wi-Fi devices
Theft of Service. Customer shall not connect the Service or any AT&T Broadband Equipment to more computers, either on or outside of the Premises, than are reflected in Customer’s account with AT&T Broadband. Customer acknowledges that any unauthorized receipt of the Service constitutes theft of service, which is a violation of federal law and can result in both civil and criminal penalties.

## Slide 5: 2015 Open Internet rules
Applied to both fixed and mobile wireless networks
Transparency  Measuring Broadband America reports
No blocking
No unreasonable discrimination (“reasonable network management” exception)
  historically, not contentious
Interconnection as ”area of observation”
General conduct rule

## Slide 6: It used to be simple (ca. 1990)
cable
(CATV)
satellite
(SAT)
LEC
CLEC
RLEC
ILEC
MVPD
ISP

## Slide 7: Vertical integration happened
content
video
distribution
advertising

## Slide 8: Residential telecom is highly concentrated
Leichtman, 1Q18

## Slide 9: Economic incentives for carriers
Reducing competition for vertically-integrated services
  make competitor less attractive (quality, price)
    e.g., only offer higher speed tiers for MVPD subscribers
  volume discrimination (zero-rating for own content or service)
   Madison River VoIP, Comcast RST, Netflix interconnection
Two-sided market
  termination monopoly  no “fair” price
    cost for incremental quality or traffic can’t be determined objectively
    very little of the fixed network cost depends on volume
  overlaps with first concern
  third-party paid services
   Netflix interconnection, ”intercarrier compensation”
Leveraging customer information

## Slide 10: QoS
Well-known: no end-to-end (inter-provider) QoS
But local QoS  “specialized services”
  VoIP, MVPD video
Problem: for any reasonable service, most of the time, high-QoS ≡ basic-QoS
   users will only upgrade rarely (see Paris Metro pricing)
No good charging mechanism:
  carrier-provided application: advantages provider
  negotiated individually: scaling problems for small providers or small ISPs
  paid by third party automatically: end-to-end signaling?
    block chain!
  subscriber paid by bucket: plausible
  zero cost: e.g., “get 2 Mb/s at low latency, up to 1 GB/month”  consumer choice

## Slide 11: Principle 1: User choice
User choice as metric for reasonable carrier behavior
  in addition to network protection against attack or abuse
Encapsulate no blocking, no discrimination
Allows QoS differentiation
  users can designate traffic
  requires UNI signaling mechanism  SDN simplifies
  probably API rather than (say) RSVP
    easy except for differential charging

## Slide 12: Principle 2: Virtual Structural Separation
Structural separation theoretically avoids vertical integration concerns
  traditionally, separate layer 3 and layer ½
  here, layer 3 vs. applications
But price setting is unsolved problem
  easier for QoS than base rate (smaller $!)
    margin squeeze problem
  use non-vertically-integrated provider as benchmark?

## Slide 13: Principle 3: Transparency
Not just performance, but price
  see 2015 OI order
  ISPs are only large consumer expenditure that’s non-transparent
    and health care – but there is no Packet Insurance
    “taxes, fees, and surcharges not included”
    Try predicting second-year charge for residential ISP
Price discrimination by obfuscation

## Slide 14: NN challenge: customer differentiation
Inconvenient for both sides of NN debate: business vs. residential users
  with fiber, speed, quality, facilities likely similar
Download speed increases reaching diminishing returns
Volume limitations are unpopular
  but may be sufficient to separate home ”edge computing” from residential use
Prediction: three tiers
  Variable-speed mobile for price-sensitive (small) households
  Near-flat fiber access with below-server cap
  Business volume metered (similar to cloud services)

## Slide 15: Conclusion
NN is an economics (charging) problem, not a QoS or network management problem
  Price discrimination, not packet discrimination
Made much more difficult by vertical integration and lack of competition
  Including difficulty of using multiple services at once
Reach same conclusion as for voice telephony: flat rate, with $0 ICC