## Slide 1: Network technology review
Henning Schulzrinne
material drawn from various online sources, reports & author
Spring 2019

## Slide 3: Dividing the problem

## Slide 4: The great infrastructure
Technical structures that support a society  “civil infrastructure”
  Large
  Constructed over generations
  Not often replaced as a whole system
  Continual refurbishment of components
  Interdependent components with well-defined interfaces
  High initial cost
water
energy
transportation
communication

## Slide 5: The Internet as core civil infrastructure

## Slide 6: Broadband, Internet, communications
Broadband (Internet, EU NGA)
dial-up
LMR
LEO, MEO, GEO

## Slide 7: Interdependencies with other lifelines
Trans
Power
Pipelines
Water
towers & antennas
outside plant
CO & data centers
Telecom
shared
RoW
shared
poles
flooding
fuel
parts
recovery coordination
control

## Slide 8: Who runs communication systems and networks?
radio & TV stations
(1,784 TV, 15,470 radio)
cable companies
(“MVPD”)
communities & cooperatives (“muni networks”, REC)
cellular providers (3-4)
wholesaler providers
(“carriers’ carrier”)
incumbent local exchange carriers
(“ILEC”)
satellite providers
private land mobile radio (public safety, transit, taxis, …)
competitive local exchange carriers
(“CLEC”)
rural local exchange carriers
(“RLEC”)
~1,000
# with ~90% marketshare
~6
~2

## Slide 9: US pay TV providers (2018)

## Slide 10: US broadband providers (2018)

## Slide 11: What do communications networks do that’s different?
Any-to-any: multiparty, coordination & cooperation, conflict
  less of a concern in (say) civil engineering
Economics: network effect, scale effects
Challenges:
  geographic distribution
  long-lived
  different industries participating
  remote attacks through infrastructure itself

## Slide 12: What problems do networks solve?
Diversity in technologies
  wired vs. terrestrial wireless vs. satellite
  trade-off capacity vs. cost vs. distance
Variation in load
  intermittent demand  shared networks
  cannot design capacity for top 5 minutes of load
“Noise”
  electric noise
  radio interference
Human adversaries
  denial-of-service attacks
  information theft
  impersonation

## Slide 13: Network trade-offs
capacity per user
cost per user
* incremental cost assuming legacy networks;
“green field” cost is roughly the same

## Slide 14: A bit of (US) history
1895-1901: G. Marconi demonstrates wireless communications
1912: Titanic
Radio Act of 1912
  all radio stations licensed
  monitor distress channel (500 kHz)
Radio Act of 1927
  deal with AM (“medium wave”) chaos  licensing “in the public interest”

## Slide 15: Communications as a regulated industry
free-market economies, subject to government regulation
  “why” (and objections) later
telephony: federally regulated since 1910
broadcasting: 1927
telecommunications: 1934
  but dates back to Interstate Commerce Act of 1887 (railroads)
  cousins: railroads, electricity, air service, …
  specialized administrative agency for sector-specific regulation
    vs. general regulation (environmental, safety, employment, contracts, consumer protection, …)
Notes: Benjamin

## Slide 16: Interfaces: Energy
~1915 (2 prong)
1901
110/220V
Lots of other (niche) interfaces
Replaced in a few applications
NEMA 1-15R
http://www.centennialbulb.org/cam.htm
Notes: http://www.iec.ch/worldplugs/history.htm
https://rustbeltanthro.wordpress.com/2015/04/02/mapping-electrical-sockets-and-plugs-a-history-of-colonialism-war-and-non-globalization/
http://www.mosaicshades.com/antique2005/sockets/

## Slide 17: Other long-lived interfaces
Cigarette lighter
(1956)
1878
1993
fuel nozzle
1982
SQL
1974
1992

## Slide 18: Interfaces: Paper-based information
1798, 1922 (DIN)

## Slide 19: Interfaces: Transportation
1435 mm
1830 (Stephenson)
1846 UK Gauge Act
12’
About 60% of world railroad mileage

## Slide 20: The two-layer model
content
apps & software
services
“Lower layers”
infrastructure
“the network”
copyright
universal service
disability access
investment
technology innovation
patents
resource scarcity
data privacy
location privacy
IP
data theft
disruption

## Slide 21: Why layering?
Perform functions once
  upper layers rely on lower layers
  in theory (see: “end-to-end principle”)
Common in engineering and society
  postal system, operating systems & other APIs, buildings, …
  but not always formal or deep
  model of a (legal) contract
Change implementation without affecting relying parties
  minimize communications, “information hiding”, “isolation”
  “black box”
Topological and administrative scoping
  single physical connection technology
  single vs. multiple administrative domains

## Slide 22: OSI model background
Introduced in 1978 and revised in 1984
  first formal attempt to codify engineering practice
  slice big problem into manageable areas of concern
Formulates the communication process into structured layers
There are seven layers in the model  the 7-Layer model

## Slide 23: The function of a layer
Each layer deals with a subset of aspects of networking
  e.g., Layer 1 deals with the communication media
Each layer communicates with the adjacent layers
  In both directions
  Example: Network layer communicates with:
    transport layer
    data link layer
Each layer formats the data packet
  Example: adds or deletes addresses

## Slide 24: Layers  wrapping
applies to other “networks” – FireWire, USB, SCSI, SS7 (telecom), …
Notes: http://www.laneye.com/network/ethernet-network-packet-holding-an-ip-packet.gif

## Slide 25: The (theoretical) layered approach to communication
7. Application
message format, human-machine interface
6. Presentation
serialization, encryption, compression
5. Session
authentication, permissions, restoration, state
4. Transport
end-to-end reliability, flow & congestion control
3. Network
network addressing, end-to-end routing
2. Data Link
link flow control, error detection, framing
Physical
analog-digital (bit stream)
“OSI model”
bit stream
packets
(“frames”)
messages
byte stream
structured content

## Slide 26: Layering
generality
functionality
email
any digital
communications
unreliable bits
over one link
secure, reliable, world-wide
L7
PHY (L1)

## Slide 27: The real model

## Slide 28: The real model, xkcd
https://xkcd.com/2105/

## Slide 29: The Internet Protocol Hourglass
email WWW phone...
SMTP HTTP RTP...
TCP UDP…
IP
ethernet PPP…
CSMA async sonet...
copper fiber radio...
small number of long-term stable interfaces
S. Deering

## Slide 30: Why four (core) layers?
Layer | Colloquial name | Function
1 | PHY | photons & electrons  bits
2 | MAC | bits  packets on one technology
3 | L3 | packets end-to-end, on heterogeneous technologies, to interface
4 | L4 | unreliable  reliable host/interface  application
(5) | Presentation, data | application data structure encoding
7 | Application | Application behavior (email, web)

## Slide 31: Internet layer functions
Layer | Key protocols | Control protocol | Transmission technologies | Administrative domains | Main function | Addresses
PHY | Ethernet, 4G |  | single, but may be diverse (fiber, copper) | 1 | analog-to-digital | none
MAC | Ethernet | 3GPP | same | 1 | framing | MAC address
network | IPv4, IPv6 | DHCP, OSPF, BGP | agnostic | many | end-to-end delivery | IP addresses
transport | UDP, TCP | built-in | agnostic | 2 (ends) | reliability, congestion control | ports
application | HTTP, RTP | SIP | agnostic (except for properties) | 2 (ends) | framing, description, sessions | URLs, email addresses

## Slide 32: The problems with layering
Doesn’t capture whole story
  control protocols
Information hiding
  inefficiency: more than needed
Information and implementation leakage
Ossification
Duplication
  “If you want it done right, you have to do it yourself”
Notes: Charles-Guillaume Étienne

## Slide 33: Node functions
Error detection
  bit errors are detected with high probability
Error correction
  bit errors are repaired via redundancy (“forward error correction”)
ARQ
  lost or corrupted packets are re-transmitted
Flow control
  prevent fast sender overwhelming slow receiver
Congestion control
  prevent fast sender overwhelming slower network

## Slide 34: Network building blocks
Network addresses
  and mapping
Data serialization
Protocols
  Cooperation algorithms

## Slide 35: “Algorithms + Data Structures = Programs”
Protocols + serialization = networking
1976
human protocols:
“what’s the time?”
“I have a question”
air traffic control
introductions
… specific messages sent
… specific actions taken when message received, or other events
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols

## Slide 36: Protocols
Protocols define format & order of messages sent and received among network entities
  and actions taken on message transmission or receipt
Often includes notions of time
  what happens if there is no response?
Similar to Application Programming Interfaces (APIs)
  size_t fwrite(const void *ptr, size_t size, size_t count, FILE *stream);
  differences?
Can also consider a “contract”
  “if I provide you X, you will provide Y”

## Slide 37
a human protocol and a computer network protocol:
Q: other human protocols?
Hi
Hi
Got the
time?
2:00
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time
TCP connection
request
What’s a protocol?

## Slide 38: Names, identifiers and addresses
Any large system needs to be able to identify its components
  Societal examples?
Names, identifier
  unique label for something
    DOI: doi:10.1038/nphys1170
  may be function, not device
  often unchanged when “thing” moves or changes providers
Address
  how do I get to that identifier?
  geography, routing  typically changes when the ”thing” (person) moves
Reality is less clearly divided

## Slide 39: Names & addresses in the Internet
domain name
(example.com)
IPv6 address(es)
2606:2800:220:1:248:1893:25c8:1946
IPv4 address(es)
93.184.216.34
MAC address
14:02:ec:35:02:8c
URL: https://example.com 
email: jane@example.com
DNS
ARP

## Slide 40: Domain names

## Slide 41: Internet addresses

## Slide 42: Serialization: turning data structures into bytes
Internal data structures (data bases, arrays, lists, dictionaries, …) need to be transported across network or stored in a file
  efficiently, without too much empty space
  without memory references
  without depending on computer architecture of sender
Networks and files are sequences of bytes (“byte stream”)
 convert internal structure into nested text elements
  references (“pointers”) by name or identifier, not memory location

## Slide 43: Serialization: ASN.1
30 13 02 01 05 16 0e 41 6e 79 62 6f 64 79 20 74 68 65 72 65 3f
serialization = convert data structure into
(linear) byte stream
like C, without pointers…

## Slide 44: Serialization: RFC 822
Delivered-To: hgs10@lionmailmx.cc.columbia.edu
Received: by 10.140.158.132 with SMTP id e126csp131562qhe;
Thu, 28 Aug 2014 14:01:48 -0700 (PDT)
Return-Path: etickets@amtrak.com
Return-Path: etickets@amtrak.com
Received: from unknown (HELO etvswas01p) ([10.14.128.202])
by phlsmtprelay01.amtrak.com with ESMTP; 28 Aug 2014 16:55:42 -0400
Date: Thu, 28 Aug 2014 17:01:30 -0400 (EDT)
From: etickets@amtrak.com
To: HGS@cs.columbia.edu, HENNING.SCHULZRINNE@FCC.GOV
Message-ID: <633700356.JavaMail.TDDServerProd@amtrak.com>
Subject: Amtrak: eTicket and Receipt for Your 09/10/2014 Trip
MIME-Version: 1.0
Content-Type: multipart/mixed;
boundary="----=_Part.1409259690306”
MIME-Version: 1.0
Content-Type: multipart/mixed;

## Slide 45: Serialization: XML
<note>
<id>1</id>
<name>A green door</name>
<price>12.50</price>
<tags>
<tag>home</tag>
<tag>green</tag>
</tags>
</note>

## Slide 46: Serialization: JSON
{
"id": 1,
"name": "A green door",
"price": 12.50,
"tags": ["home", "green"]
}

## Slide 47: Internet architecture

## Slide 48: What’s the Internet: “nuts and bolts” view
millions of connected computing devices: hosts
  running network apps
  end point = origination and destination of Internet traffic
communication links
  fiber, copper, radio, satellite, light, sound, …
  characterized by bandwidth and delay
routers
  forward packets (chunks of data)
  typically, lots of interfaces
“middleboxes”
  lots of devices that are technically hosts, but part of the infrastructure
  firewalls, web proxies (caches)
J. Kurose (Ch. 1)
Notes: 48
Kurose, Ch. 1

## Slide 49: Internet: “Nuts & bolts” view
protocols control sending, receiving of messages
  e.g., TCP, IP, HTTP, Skype, Ethernet
Internet: “network of networks”
  loosely hierarchical
  public Internet versus private intranet
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
mobile network
global ISP
regional ISP
home
network
institutional
network
J. Kurose (Ch. 1)

## Slide 50: Internet traffic flows today
50
backbone (transit)
content
access network
(data center provider)
eyeball ISP
comm.
CDN
CDN
Level3
Cogent
Comcast
Google
Facebook
YouTube
Yahoo
Live
Baidu
Akamai
server farm
video
conferencing
content CDN
Netflix

## Slide 51: Network types
Access
  “last mile”
Regional or metro
  “metro fiber”, “metro Ethernet”
Wholesale
  connect points-of-presence across
  may also provide access to commercial buildings & data centers
Trans-oceanic
  often, owned separately (consortium), but integrated into wholesale networks

## Slide 52: A backbone network

## Slide 53: 1901 “data” backbone

## Slide 54: Submarine cable map
http://www.telegeography.com/
Notes: http://www.telegeography.com/

## Slide 55: The usage of cables is changing
Notes: Optical Illusions: Content Providers and the Impending Transformation of International Transport
Tim Stronge TeleGeography, NANOG 71

## Slide 56: But content providers aren’t building

## Slide 57: Wireline & wireless
100’ to ~3 miles
fiber or copper
(rarely, microwave)
“almost all networks are 99% wired”
exceptions?

## Slide 58: It’s all spectrum - phone
Notes: http://www.voipsupply.com/images/voice_freq_range.jpg

## Slide 59: It’s all spectrum - wires
200 - 347 THz
1 GHz
10 MHz
copper
4 kHz

## Slide 60: Classical division of spectrum
Band | range | commonly called | sample current usage
VLF | 3-30 kHz |  | navigation, submarine
LF | 30-300 kHz |  | WWVB (clock 60 kHz)
MF | 300-3 MHz |  | AM radio
HF | 3-30 MHz |  | short wave radio
VHF | 30-300 MHz |  | TV 2-6, 7-13, FM radio, CB, LMR
UHF | 0.3-3 GHz |  | LMR, TV 14-50, cellular, Wi-Fi
SHF | 3-30 GHz | microwave | radars, Wi-Fi
EHF | 30-300 GHz | mmWave | radars, satellite, p2p links

## Slide 62: Commercial wireless spectrum (US)
LTE band class | frequency | origin | usage
71 | 617-698 MHz | incentive auction (TV) | TMo, AT&T, Dish
12 & 13 (A, B, C) | 700 MHz | digital dividend (TV) | AT&T, TMo, VZ
14 (D) | 700 MHz | digital dividend (TV) | FirstNet
5 | 850 MHz | cellular | AT&T, US Cellular
4 | 1700 MHz | AWS | many
25 | 1900 MHz | PCS | many
30 | 2300 MHz | WCS | AT&T
41 | 2500 MHz | EBS | Sprint

## Slide 63: It’s all spectrum - radio
typical cell channel:
5-10 MHz
FM radio: 100 kHz
TV: 5 or 6 MHz
AM radio: 9 or 10 kHz

## Slide 65: Spectrum for wireless broadband
Wells-Fargo
2017

## Slide 66: LTE holdings

## Slide 67: Spectrum per user

## Slide 68: Geographic sizing: CMA

## Slide 69: Spectrum geography: EA
Notes: http://wireless.fcc.gov/auctions/data/maps/ea.pdf

## Slide 70: It’s all spectrum - modem
Notes: http://hackadaycom.files.wordpress.com/2013/01/dial-up-handshake-infographic.png

## Slide 71: Fundamental limit to channel capacity
channel capacity
(bits/second)
bandwidth
(Hz)
signal-to-noise ratio
(typically, dB)
Shannon-Hartley limit

## Slide 72: Amplitude, frequency & phase modulation
Wikipedia

## Slide 73: Phase modulation
Wikipedia

## Slide 74: Quadrature amplitude modulation (QAM)
Wikipedia

## Slide 75: Shannon examples
SNR (dB) = 10 log10 (S/N)
Telephone modem
  SNR = 20 dB (1:100)
  frequency range ~3 kHz  3,000 log2 (101) = 19.97 kb/s
Noise can be larger than signal!
   negative SNR
Less noise  higher signal power
Only true for simple channel models
  “additive Gaussian white noise” (AWGN)
Spectral efficiency: bits per second per Hz
  often, around 1-2 b/s/Hz, but can be much higher
Notes: See ITU Q.552

## Slide 76: Circuit switching: FDM versus TDM
FDM
frequency
time
TDM
frequency
time
4 users
Example:
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 77: All networks are similar
time-division multiplexing
modulation
frequency division
medium = spectrum
packets
packets

## Slide 78: Reference architecture
L3 Router
SBC and
L3 Router
Set top box
command&control
Video
Cache
Users
Comm Complex
Transport Core
Regional Broadband
Network
Access Network
Video Complex
ISP
Interconnected Networks
Service Core
Internet
Peering
OTT
Other
Communications
Networks
Video Feeds
and 3rd Party
CDNs
Other Cores
Within the
Network
Interconnected Networks
Local Video
Feeds

## Slide 79: Broadband Access Technologies
FBWA or 4G
BPL
DSL
HFC
4G
Digital
Subscriber Line
Telco or ILEC
10s of Mbps
Entertainment, data, voice
Broadband Power Line
PowerCo
Data, voice
~few Mbps
Fixed Broadband Wireless Access
Wireless ISP
WiMAX or LTE:
  -10s of Mbps
Satellite: few Mbps
4G/LTE
Cellular operators
5-10 Mbps (100 kph)
Hybrid Fiber Coax
CableCo (MSO)
Entertainment, data, voice
10s of Mbps
Fiber PON
Fiber -- Passive
Optical Network
Telco or ILEC
~75 Mb/s
Futureproof?
Paul Henry (AT&T), FCC 2009
FTTHome
FTTCurb
Notes: http://www.broadband.gov/ws_fixed_bb.html

## Slide 80: Local loop

## Slide 81: Physical architecture
Feeder Cables
  Carries traffic serving multiple endpoints form an “office” to a neighborhood (local convergence point, LCP, or serving area interface, SAI)
Distribution Cables
  Carry traffic for one or more households from LCP to the curb (network access point)
Drop Cables (above ground) or service wire (underground)
  Carry traffic from curb to dwelling unit
Depending upon the architecture
  Cables may be fiber, twisted pair or coax
  Local convergence point and/or network access point could host a patch panel, a DSLAM, an optical splitter, an Ethernet switch, or a fiber/coax interface.

## Slide 82: Broadband access
-48v

## Slide 83: Logical architecture
Access network extends from Residential Gateway (RG) to Broadband Network Gateway (BNG)
Flow management between AN and RG depends upon the architecture
Flow management in the Ethernet Aggregation Network similar across architectures but may differ from how flows are managed between the AN and the RG
In Metro Network flows are typically distinguished by layer 3 QoS tags and/or separate VPNs
http://www.broadband-forum.org/technical/download/TR-101_Issue-2.pdf

## Slide 84: xDSL logical architecture
http://www.broadband-forum.org/technical/download/TR-101_Issue-2.pdf

## Slide 85: ADSL (ITU G.992.1)
ADSL spectral power repartition (PSTN)
FDD: Frequency Division Duplexing
 no interference between up and down
Frequency
POTS
300 Hz
3,4 kHz
22 kHz
133kHz
Upstream
Downstream
203 kHz
1.1 MHz
Power
DATA
POTS
300 Hz
3,4 kHz
22 kHz
133kHz
Upstream
Downstream
203 kHz
1.1 MHz
DATA
POTS
300 Hz
3.4 kHz
22 kHz
Upstream
Downstream
203 kHz
1.1 MHz
DATA

## Slide 86: Access: cable network
data, TV transmitted at different
frequencies over shared cable
distribution network
cable
modem
splitter
…
cable headend
CMTS
ISP
cable modem
termination system
HFC: hybrid fiber coax
  asymmetric: up to 30Mbps downstream transmission rate, 2 Mbps upstream transmission rate
network of cable, fiber attaches homes to ISP router
  homes share access network to cable headend
  unlike DSL, which has dedicated access to central office

## Slide 87: Cable architecture

## Slide 88: Cable spectrum
Notes: Telecom & Networking Equipment The Cable Equipment Playbook – Opportunity for Investors, Oct. 4, 2017, Jefferies

## Slide 89: Simplified access network diagram
Jason Livingood (Comcast) FCC 2009
Notes: 89
http://www.broadband.gov/ws_fixed_bb.html

## Slide 90: DOCSIS 3.0 channel bonding
6 MHz
6 MHz
6 MHz
6 MHz
38 Mbps
38 Mbps
38 Mbps
38 Mbps
152 Mbps
Logical Channel Bonding Technology
DOCSIS 2.0 is limited to single channel’s capacity
DOCSIS 3.0 employs packet bonding across multiple channels
  Initially will bond 4 channels
  8 channel-capable silicon coming soon
  Upstream bonding in 2010
  Increased speeds 100Mbps+
Notes: 90

## Slide 91: Verizon’s FTTP architecture
ONT
Optical Network Terminal
OLT
Optical Line Terminal
Optical Couplers (WDM)
Voice & Data Downstream 1490 nm
Upstream 1310 nm
Voice, Data & Video 1490 nm, 1310 nm, 1550 nm
1x32
Optical Splitter
EDFA
Erbium Doped Fiber Amplifier
Video 1550 nm
Bandwidth & Services
Upstream
Downstream
Voice, Data & VOD at 622 Mbps
Voice & Data at 155 to 622 Mbps
Broadcast Video
1310 nm
1490 nm
1550 nm
Analog TV
Digital TV and HDTV
54 MHz
864 MHz
CENTRAL OFFICE
customer premise
Brian Whitton, Verizon
Notes: by Brian Whitton, Verizon Networks

## Slide 92: Communication satellites
Communication satellites, some properties, including: altitude above earth, round-trip delay time, number of satellites for global coverage.

## Slide 93: Satellite frequency bands

## Slide 94: Geostationary satellites (2)
VSATs using a hub.
“bent pipe”

## Slide 95: HTS launches per year
Dedicated HTS | Hybrid Payload HTS | 
Thaicom 4 | Anik F2 | 
WildBlue 1 | AMC-15 | 
Spaceway 3 | AMC-16 | 
Ka-Sat | Ciel-2 | 
ViaSat-1 | Hylas 1 | 
Jupiter-1 | Arabsat 5C | 
Inmarsat 5F2 | YahSat 1B | 
Inmarsat 5F1 | Hylas 2 | 
Inmarsat 5F3 | Hispasat AG1 | 
NBN Co 1A | Express AM5 | 
GSAT-11 | Astra 2F | 
NBN Co 1B | Express AM6 | 
 | Amazonas 3 | 
 | Astra 2E | 
 | Thor 7 | 
 | Astra 2G | 
 | Jabiru-1 | 
David Hartshorn, 2014

## Slide 97: Low-Earth orbit satellites
The Iridium satellites form six necklaces around the earth.

## Slide 98: OneWeb (2018+)
LEO – 1,200 km orbit
648 satellites in 18 orbital planes
  50-70 gateway sites
Ku & Ka-band spectrum
Service area: 1,080 by 1,080 km per satellite
  7.5 Gb/s
OneWeb presentation at International Satellite Symposium 2016
Notes: https://www.itu.int/en/ITU-R/space/workshops/SISS-2016/Documents/OneWeb%20.pdf

## Slide 99: GSO protection
OneWeb presentation at International Satellite Symposium 2016
Notes: https://www.itu.int/en/ITU-R/space/workshops/SISS-2016/Documents/OneWeb%20.pdf

## Slide 100: Exede beam map
http://www.wildbluetools.com/content/dealer/email/Beam_map-high-mid-low.html

## Slide 101: Satellite
Advantages
Near-universal geographic availability
  low incremental cost
    satellite terminal + installation
Resilient after natural disasters
  often used as backup
Disadvantages
Latency
  MBA 2014: RTT 671 ms
Temporary disruptions
  sun alignment
  rain fade
Capacity
  Viasat-1: 140 Gb/s (for 300,000 customers)
  usually, usage-capped

## Slide 102: Example: Exede satellite plans
Oklahoma County, OK

## Slide 103: Project Loon
LTE at 850 MHz
solar powered
wind layers
< 20 km altitude

## Slide 104: The cost of networks

## Slide 105: Network economics, (over)simplified
Chart: % of revenue
| Equipment | Construction | Operations
Costs | 4.5 | 10.5 | 85
70%
30%
traditional: 12-15 staff/10k customers
Iliad, FR: 3-4 staff/10k
Notes: opex ratios: Deloitte

## Slide 106: Fiber deployment
wastewater pipe
(3-5 km/week)

## Slide 107: Broadband network cost - FTTP
Category | Details | Outside plant
FTTP in existing right-of-way | All underground, not including drops or electronics | $1,200…$1,300 per passing
 | 40% aerial, 60% underground, not including drops or electronics | $1,000…$1,100 per passing
FTTP drops | Range of distances and complexity | $300…$700 per connected home
Crown Fibre Holdings (Govt. of New Zealand); provided by CTC

## Slide 108: Broadband network cost – Fiber middle mile
Category | Details | Outside plant | Source
aerial, new attachment | Northeastern city municipal utility; 96% aerial, 4% underground; 87.6 miles | $30,000/mile | Public utility (actual cost)
aerial overlash | Major metropolitan area (U.S. east coast) | $15,000/mile | 
buried | Mixed suburban/urban locations and pot/bore construction | $89,000/mile | Washington, D.C.-area BTOP project (actual cost)
Data provided by CTC

## Slide 109: Middle mile cost example
CTC, 2009 (“Brief Engineering Assessment: Efficiencies available through simultaneous construction and co-location of communications conduit and fiber”)

## Slide 110: More fiber observations
Fiber middle-mile cost: $50-70k/mile
Fiber cost: 144 strands = $10k/mile, 48 strands = $4.7k/mile
Common characteristics:
  avoid active elements in network  power, maintenance  PON
  recently: avoid anything except fiber (including splitters)
    cf. wireless last mile approach
  fiber home run, even if PON (Google Fiber, Stockholm)
Fiber cost higher for buried, but cheaper if conduit or aerial
Recent FTTH:
  avoid indoor installation (cf. Verizon FiOS)
  one box in home (ONT + 802.11ac), not ONT + MoCa STB

## Slide 111: FTTH estimates
Bell Alliant in Western Canada has now passed over half a million homes with fiber home, the largest deployment in North America after Verizon. Their latest financial report showed capex of less than $500 per home passed.
Verizon reported costs fell below $700/home passed several years ago and headed to $600. Add the cost of actually installing a large fraction of those homes, and your cost per home passed by the network comes closer to $1,000.
Installing each home at Verizon added $500-600. Digging lawns and drilling holes into the homes is labor intensive.
Includes equipment whose price is rapidly dropping. Early Verizon gear cost $300-400/home, but today they are probably paying half that.
  Very large fiber builds in China are paying less than $100/home.

## Slide 112: FTTx cost vs. DSL
Alcatel-Lucent, 2013

## Slide 113: Capital investment
Company | Revenue | Capital expenditures | %
Comcast (US) [3Q14] | $11.04B | $1.644B | 14.9
Telekom (DE) [3Q14] | €15.6B | $2.58B | 16.5
Safaricom (KE) [H1FY15] | Ksh 79.34B | Ksh 12.37 | 15.5

## Slide 114: Accidental broadband
DSL patents
94.2% of US
households have
phone service
G.992.2
ADSL
1988-1991
1993
1999
1995
62.1 million US
households have
cable TV
2008
“peak CATV”:
82% of HH
1997
DOCSIS 1.0
(40M/1M)
2016
DOCSIS 3.1
(10G/1G)
Notes: file:///Users/hgs/Downloads/1997_Mar_Trends.pdf

## Slide 115: Network competition models
single provider
(any technology)
cable
copper, fiber
shared copper, fiber
PHY
MAC
(Ethernet)
IP
regulated: pricing? behavior?
how many entrants? where?
poles & conduits
“bit stream”
margin squeeze

## Slide 116: Sharing models: US
sharing (incumbent + new entrant) vs. neutral third party
DSL
(ILEC)
ducts & poles
(electric utilities or ILEC)
towers
HFC
fiber
(ILEC, CATV, overbuilder)
spectrum
PHY (LTE)
+ WISP & satellite

## Slide 117: Sharing models: Canada, Europe, Australia
DSL
ducts & poles
(electric utilities or ILEC)
towers
HFC
fiber
unbundling
varies
mostly not unbundled
spectrum
PHY (LTE)
usually
unbundled
Notes: http://dx.doi.org/10.1787/20716826
http://www.oecd.org/sti/broadband/2-7.pdf

## Slide 118: Broadband competition challenges

## Slide 119: The difficulty of competition
Static vs. dynamic (new entrants)
  existing, converging infrastructures
    coax cable + copper + wireless
Difficulties for new entrants (“overbuilder”)
  capital investment vs. amortized network
  legal barriers
  customer acquisition (“sticky” customers)
  incumbent pricing
Notes: https://aws.amazon.com/blogs/aws/aws-importexport-snowball-transfer-1-petabyte-per-week-using-amazon-owned-storage-appliances/

## Slide 120: Google Fiber

## Slide 121: Network costs
middle mile
backbone
last mile
CDN
yes, but mostly
electronics
DSL | no
HFC | homes/service node
fiber | no
cellular | densification
largely unaffected
by video
ISP-owned
vs. leased!
lack of IXPs in LDCs!

## Slide 122: Transit prices
Chart: 
| 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
$/Mbps | 1200 | 800 | 675 | 400 | 200 | 120 | 90 | 75 | 50 | 25 | 12 | 9 | 5 | 3.25 | 2.34 | 1.57 | 0.94 | 0.63
http://drpeering.net/white-papers/Internet-Transit-Pricing-Historical-And-Projected.php

## Slide 123: Bandwidth costs
Amazon EC2
  $50 - $120/TB out, $0/TB in
CDN (Internet radio)
  $600/TB (2007)
  $7-20/TB (Q1 2014 – CDNpricing.com)
NetFlix (7 GB DVD)
  postage $0.70 round-trip  $100/TB
FedEx – 2 lb disk
  5 business days: $6.55
  Standard overnight: $43.68
  Barracuda disk: $91 - $116/TB
DVD-R (7 GB)
  $0.25/disk  $35/TB
Notes: FedEx and EC2 prices as of 09/15/09
CDN: http://www.mindbranch.com/listing/product/R678-29.html
http://www.cdnpricing.com/

## Slide 124: rural broadband

## Slide 125: What is rural?
Census:
  Urban = Urbanized Areas (UAs) of 50,000 or more people
    OR Urban Clusters (UCs) of 2,500 to 50,000 people.
    core of population density of 1000 people/mi2
      all of NJ: 1210 / mi2
  Rural = everywhere else
OMB:
  Metropolitan Statistical Areas (MSAs): >= one urbanized area of >= 50,000 population, plus adjacent territory that has a high degree of social and economic integration with the core as measured by commuting ties.
  Micropolitan Statistical Areas: >= one urban cluster of at least 10,000 but less than 50,000 population, plus adjacent territory that has a high degree of social and economic integration.
USDA
  based on counties

## Slide 126: Rural areas (USDA)
Notes: https://www.ers.usda.gov/topics/rural-economy-population/rural-classifications/what-is-rural.aspx

## Slide 127: Broadband access by speed & geography
15% of US population

## Slide 128: Rural broadband US
Notes: https://fivethirtyeight.com/features/the-worst-internet-in-america/

## Slide 130: Rural electrification
Early 1920s, between 2 and 3% (likely less)
  1921: DC had 98.2%, MA 97.8%
“In 1935, only 10.9% of American farms (744,000) enjoyed central station power, compared with Germany and Japan at 90%, France between 90 and 95%, and New Zealand at 60%.”
“In 1940, just four and a half years after Roosevelt signed Executive Order No. 7037 (followed by 1936 ”Rural Electrification Act”), 25% of American farms had been electrified.”
1950: 90% had been electrified nationally
Today: 850 distribution coops serving 14 M homes
Notes: http://remagazine.coop/flashbacks-rural-electrification-cartogram-numbers/

## Slide 131: Rural electrification
“In 1935, Morris Llewellyn Cooke, a mechanical engineer who had devised efficient rural distribution systems for power companies in New York and Pennsylvania, had written a report that detailed a plan for electrifying the nation's rural regions. Appointed by Roosevelt as the REA's first administrator, Cooke applied an engineer's approach to the problem, instituting what was known at the time as "scientific management"—essentially systems engineering. Rural electrification became one of the most successful government programs ever enacted. Within 2 years it helped bring electricity to some 1.5 million farms through 350 rural cooperatives in 45 of the 48 states. By 1939 the cost of a mile of rural line had dropped from $2,000 to $600. Almost half of all farms were wired by 1942 and virtually all of them by the 1950s.”
Cost of aerial fiber installation: $14k/mile material, $39k/mile installation (Singer, 2017)
USDA loans at 5% (hardship rate) for telecom
  but currently Treasure rate is lower (2.81% for 30 years)
  others at rates equivalent to municipal bonds
$10,958 in 2017
Notes: “Assessing the Impact of Removing Regulatory Barriers on Next Generation Wireless and Wireline Broadband Infrastructure Investment”, 2017
http://www.greatachievements.org/?id=2990 (rural electric)
https://fas.org/sgp/crs/misc/RL33816.pdf

## Slide 132: Density determines network choices
1
10
100
1000
50
Alaska roadmiles
20
1454
7
HH/road mile
cable
FTTH
DSL (common)
REC
WISP
satellite
Notes: Manhattan: 508 road miles - http://venus.fcny.org/cmgp/streets/pages/2001PDF/Report/DFMN.pdf ; Wikipedia: 738,644 households in Manhattan
Alaska: 15,178 miles; 741,894 population

## Slide 133: Rural deployment options
Technology | Capacity in rural areas (typical) | Advantage | Disadvantage
DSL | < 5 Mb/s | mostly deployed | speed increase requires active components deep in network
4G LTE | ~ 5 Mb/s | existing deployment, MF II | limited capacity (current avg.: 2.1 GB/month)
5G (3.5 GHz, not mmWave) | depends on deployment model | saves fiber drop | spectrum OpEx
satellite (current geo) | 12 Mb/s nominal | no incremental deployment cost | expensive, capacity-limited, latency
HFC (“cable”) | 25-100 Mb/s | low upgrade cost to 1 Gb/s+ | 85% of households
FTTH & FTTC | 100 Mb/s – 1 Gb/s | 20 year life time passive outside plant | cost to deploy

## Slide 134: cost recovery

## Slide 135: Consumer expenditures
“Americans spent $116 more a year on telephone services in 2011 than they did in 2007, according to the Labor Department, even as total household expenditures increased by just $67.
Meanwhile, spending on food away from home fell by $48, apparel spending declined by $141, and entertainment spending dropped by $126. The figures aren't adjusted for inflation.” (WSJ 2012)
Notes: Morgan Stanley, Macro Meets Micro: A Five- Year View of the Telecom Services Industry, July 2014.
http://online.wsj.com/articles/SB10000872396390444083304578018731890309450
http://www.bls.gov/opub/btn/archive/consumer-spending-in-2010-pdf.pdf

## Slide 136: The value of bits
Technologist: A bit is a bit is a bit
Economist: Some bits are more valuable than other bits
  e.g., $(email) >> $(video)
Application | Volume | Cost per unit | Cost / MB | Cost / TB
Voice (13 kb/s GSM) | 97.5 kB/minute | 10c | $1.02 | $1M
Mobile data | 5 GB | $40 | $0.008 | $8,000
MMS (pictures) | < 300 KB, avg. 50 kB | 25c | $5.00 | $5M
SMS | 160 B | 10c | $625 | $625M
Notes: T-Mobile 2010
AT&T data
http://www.nowsms.com/discus/messages/12/8500.html

## Slide 137: Problem likely capacity, not speed
June 2017: 100 GB

## Slide 138: The challenges of service differentiation
Method | Used by | Advantage | Drawbacks | Customer dislike estimate
Speed tiers | C, DSL | Differentiates basic usage modes | Less effective above 10 Mb/s | 😦
Usage-based charging (caps, metered) | M, (C, DSL), LD | heavy vs. light users encourages Wi-Fi use | complaints about meter accuracy adaptive applications (4G bill shock) pay for ads hard to predict | 😦😦😦
Application-based charging | M | Easier to predict Business model | Affects content competition barriers to entry | 😦😦😦
Differentiated privacy | AT&T, NetZero | Full functionality | Low-income users may not be attractive to advertisers | 😦 or 😦😦😦

## Slide 139: The challenges of service differentiation
Method | Used by | Advantage | Drawbacks | Customer dislike estimate
Priority | ? | Better experience for VoIP | Other experience must be bad  economy class in airline | ?
Time-of-day | LD, Sat | Approximates congestion Easy to understand | Not optimally efficient Possible bill shock | 😦😦
Congestion-based | ? | Encourages time shifting | Limited shift Unpredictability | 😦😦😦😦
The words you won't say on your deathbed are, "If only I had spent more time watching the bandwidth meter (or phone bill)."

## Slide 140: Cable TV vs. Internet
Lots of advocates of “fairness” for metering
Very few advocate scaling the monthly TV fee (Europe) or the cable TV fee by hours watched
  eminently feasible with STBs
  content tiers but not viewing tiers
“but cost of cable TV does not depend on viewers”
not really: content cost to MVPD is based on popularity