## Slide 1: A Platform for Experimental Research in Critical Voice Communications
Jan Janak, Artiom Baloian, Dan Rubenstein, Henning Schulzrinne
(with Norman Groner & Charles Jennings - John Jay College)
PSCR 2020: The Digital Experience

## Slide 2: Disclaimer
This presentation was produced by guest speaker(s) and presented at the National Institute of Standards and Technology’s PSCR 2020: The Digital Experience. The contents of this presentation do not necessarily reflect the views or policies of the National Institute of Standards and Technology or the U.S. Government.
Posted with permission

## Slide 3: Project Objectives
Four phase approach:
  Build a communication testbed
    Emulate real mission critical voice (MCV) systems
    Configurable audio & network impairments
  Experiment with trained first responders
    Communicate using the testbed in a controlled environment
  Measure communication performance
    Analyze data collected during experiments
  Build mathematical models
    Channel conditions -> performance measures
How does the quality of the communication channel affect first responder communications?

## Slide 4: Quality of Experience (QoE) Measures
Comprehension errors
  e.g., repeat transmitted messages
Task errors
  e.g., wrong information recorded
Usage errors
  e.g., pressing push-to-talk (PTT) button too early or too late
Length and latency of responses
  e.g., pauses between requests and start of transmission
Subjective ratings of user experience
  e.g., rated frustration with radios

## Slide 5: Testbed Overview
Open hardware & software
Affordable off-the-shelf components (Raspberry Pi for user terminals)
Scalable design (up to 10 user terminals)
Emulates analog & digital MCV systems (including P.25)
Programmable audio & network impairments
Testbed & experiment management from the browser
APIs for experiment evaluation & analysis
Allow for limited remote (at-home) experiments

## Slide 6: Testbed Architecture (May 2020)

## Slide 7: Testbed Architecture (May 2020)

## Slide 8: Testbed User Interface
User Terminal Control
Audio Recordings
Experiment Management

## Slide 9: User Terminal: Block Diagram

## Slide 10: User Terminal: Services
Custom controller application
  NodeJS, TypeScript, HTTP, WebSocket
PulseAudio for audio processing
  Mixing, volume control, audio filtering
Baresip SIP user agent (custom P.25 codec)
Linux kernel network emulator
  delay, bandwidth, packet loss, error rate
Custom event & audio recorder
  Time-synchronized events & audio recordings
  Uploaded to base station for processing

## Slide 11: User Terminal: Supported Impairments
Background noise injection
Fine-grained volume control
Audio filtering (bandwidth, low-pass)
Variable PTT delay (mic audio cut-off)
Voice compression (CODEC selection)
Configurable mouth-to-ear delay
Maximum bandwidth limitation
Modulation rate (baud rate)
Packet loss
Bit error injection
Audio
Network

## Slide 12: User Terminal: Custom Hardware
Connect Motorola speaker to Raspberry Pi
USB soundcard with volume buttons
Connect PTT to volume up button
  Custom circuit with a transistor
  Access via the Linux input subsystem
Challenges
  Speaker power limited by USB power (5V, 1A)
  Speaker PA needed to match real radios

## Slide 13: Base Station: Block Diagram

## Slide 14: Base Station: Services
Custom AMBE CODEC server
ZeroConf for service discovery
SIP conference server emulates RF channels
NTP for user terminal time synchronization
  Millisecond-level accuracy
  Global event ordering
Data storage
  MongoDB (configuration, events, other data)
  Local filesystem for audio recordings
Backend services
  User terminal configuration & management
  Experiment management & data collection
  Experiment analysis & evaluation

## Slide 15: AMBE CODEC Integration
P.25 systems use DVSI’s AMBE codec
Available only as hardware (USB dongle)
  USB-3000: One channel
  USB-3003: Three channels
Supporting USB-3003 is challenging:
  Share the device across LAN
  Near real-time operation
  Fair request scheduling
Solution:
  CODEC service
  Accessed remotely from terminals
  Uses the gRPC protocol

## Slide 16: Support for Remote Experiments
Execute experiments remotely from home
  Browser UI for playback and data collection
Pre-recorded audio clips with impairments:
  CODECs, noise, PTT delay, loss & errors
  Anti-cheat design (play once only, no pause)
Collect subject’s answers:
  Free-form text
  Single-choice
  Multiple-choice
Accessible over the Internet

## Slide 17: Support for Remote Experiments
Execute experiments remotely from home
  Browser UI for playback and data collection
Pre-recorded audio clips with impairments:
  CODECs, noise, PTT delay, loss & errors
  Anti-cheat design (play once only, no pause)
Collect subject’s answers:
  Free-form text
  Single-choice
  Multiple-choice
Accessible over the Internet

## Slide 18: Initial Human Subject QoE Intelligibility Metrics
One way, no delay impairment
MRT as baseline
License plates as semi-realistic use case of low-context information transfer
Street addresses as medium context
  “A burglary has been reported at 539 Zachary Lane”
  Which of the following addresses must closely matches what you heard?
    Thackery Lane
    Zachary Lane
    Tannery Lane
    Saxony Lane

## Slide 19: Future QoE Metrics: Multi-person
Task performance when faced with voice impairments
Key metric: PTT delay (fixed and variable) & mouth-to-ear delay
Requires (at least) two parties
Need to identify both naturalistic and artificial scenarios
  Naturalistic scenario example: DHS active shooter training (EDGE)?
  Artificial scenario example: e.g., Fischer & Mosier (2014) using space craft controls or Krauss & Bricker (1967) using picture identification
Notes: https://www.youtube.com/watch?v=v5pBdwkXd70

## Slide 20: Ongoing Work & Next Steps
Offline mode for running listening experiments from home
Environment for experiment evaluation & analysis
  Integration with third-party tools (Google speech-to-text, Dragon Audio)
  Optional integration with cloud services (Google Cloud, AWS, Jupyter Notebooks)
Calibrate speaker & microphone levels
Measure true mouth-to-ear delay
Collect background noise recordings from real MCV systems
Initial experiments with Columbia University students
  IRB approved
  Validate tools & methodology