## Slide 1: Accelerating Digital Inclusion – Making the Internet Available and Affordable to Everyone
Henning Schulzrinne
Columbia University

## Slide 2: Overview
Availability, affordability and relevance
What makes deploying fixed broadband necessary & expensive?
Technology may help – if it can dig trenches & automate operations
Affordability may become a larger problem than availability
Government is likely to play a major role
Mostly focus on United States, but basic problems similar elsewhere

## Slide 3: OECD/high-income vs. lower-income issues
wired (or fixed) broadband widely available
transition from copper to fiber (and FWA)
least-connected 10%
affordability for low-income households
adoption – digital literacy
applications (“Factory 4.0”, telehealth, distance learning)
wired broadband uncommon: mobile first
transition from 2G to 4G
middle mile, transoceanic fiber
IXPs to avoid tromboning through US
broad-based affordability
applications like banking, health, jobs

## Slide 4: Universal Service is more than a century old
cross-subsidies: long-distance  local (& rural) service
universal service obligation (utility) in service territory
example: inter-carrier compensation (ICC)
monopoly phone company  1996 TA
local competition  ”cream skimming” 
explicit universal service fund

## Slide 5: How bad is the problem?

## Slide 6: Global Internet users
Notes: Internet Trends 2019 (Mary Meeker)

## Slide 7: Global internet growth – 2009–2018
Notes: Internet Trends 2019 (Mary Meeker)

## Slide 8: US: Income plays a major role
Pew Research
Notes: https://www.pewresearch.org/internet/fact-sheet/internet-broadband/

## Slide 9: Rural broadband US
Notes: https://fivethirtyeight.com/features/the-worst-internet-in-america/

## Slide 10: By race, too

## Slide 11: 15% of U.S. adults are smartphone-only
Smartphones = mostly consumption devices
+ TikTok!
Hard to do homework on a smartphone
Hard to do telework
Notes: https://www.pewresearch.org/internet/2021/06/03/mobile-technology-and-home-broadband-2021/

## Slide 12: Broadband access by speed & geography
15% of US population
2017
Notes: https://broadbandnow.com/research/fcc-broadband-overreporting-by-state
https://www.brookings.edu/research/signs-of-digital-distress-mapping-broadband-availability/

## Slide 13: What are the causes?

## Slide 14: Lower population density, easier broadband
2.91/km2
3.49/km2
32.45/km2
Deloitte, 2017
to be covered requires

## Slide 15: Availability, affordability and relevance are coupled
Availability
Relevance
Affordability
not available – don’t know what
you don’t have
if not relevant, low on spending priority
if can’t afford, easier to claim “don’t want it”
carriers don’t build or improve in low-income areas (“digital redlining”)

## Slide 16: Reason for non-adoption
https://www.digitalinclusion.org/measuring-the-gap/

## Slide 17: It all depends on your (network) roots

## Slide 18: Accidental broadband
DSL patents
94.2% of US
households have
phone service
G.992.2
ADSL
1988-1991
1993
1999
1995
62.1 million US
households have
cable TV
2008
“peak CATV”:
82% of HH
1997
DOCSIS 1.0
(40M/1M)
2016
DOCSIS 3.1
(10G/1G)
 DSL and cable infrastructure near-universally or widely available well before use as Internet access
1980
16 million
US subscribers
Notes: 1997_Mar_Trends.pdf
https://www.calcable.org/learn/history-of-cable/

## Slide 19: Broadband technology 2021
Chart: Per 100 inhabitants
| Switzerland | France | Norway | Denmark | Germany | Korea | Netherlands | Canada | Belgium | Portugal | United Kingdom | Sweden | Greece | Iceland | Luxembourg | United States | Czech Republic | New Zealand | Australia | Estonia | Japan | Spain | Hungary | OECD | Finland | Slovak Republic | Slovenia | Ireland | Italy | Austria | Lithuania | Israel | Latvia | Poland | Chile | Turkey | Costa Rica | Mexico | Colombia
DSL | 23.41 | 20.3 | 3.35 | 10.82 | 30.49 | 0.92 | 13.18 | 9.38 | 18.54 | 3 | 30.67 | 2.83 | 40.32 | 10.51 | 13.82 | 5.47 | 9.13 | 6.46 | 17.5 | 7.49 | 0.76 | 3.17 | 5.81 | 9.71 | 4.43 | 8.41 | 7.54 | 15.88 | 7.83 | 16.53 | 4.22 | 16.59 | 5.22 | 4.21 | 0.96 | 13.51 | 2.98 | 4.66 | 2.33
Cable | 11.81 | 6.41 | 10.44 | 15.33 | 10.56 | 5.26 | 20.02 | 21.18 | 21.96 | 11.62 | 7.94 | 6.72 | 0 | 0.29 | 3.93 | 24.02 | 5.78 | 0.92 | 7.95 | 6.77 | 5.21 | 4.36 | 15.76 | 11.41 | 9.04 | 3.2 | 8.76 | 7.57 | 0 | 10.9 | 0.69 | 8.4 | 0.79 | 7.34 | 8.69 | 1.61 | 12.26 | 7.66 | 10.16
Fibre | 11.17 | 18.34 | 28.17 | 17.65 | 2.8 | 37.53 | 10.22 | 9.11 | 0.9 | 23.69 | 2.34 | 30.83 | 0.15 | 27.91 | 20.27 | 6.35 | 6.93 | 22.53 | 8.01 | 15.28 | 28.18 | 26.03 | 11.02 | 10.85 | 19.49 | 11.72 | 14.61 | 6.2 | 3.79 | 1.49 | 22.06 | 3.4 | 18.28 | 7.1 | 10.33 | 5.18 | 4.47 | 5.5 | 3.29
Satellite | 0.02 | 0 | 0.04 | 0 | 0.03 | 0 | 0 | 0 | 0 | 0.01 | 0.04 | 0 | 0.03 | 0 | 0 | 0.58 | 0.01 | 0.04 | 0.47 | 0 | 0 | 0.02 | 0.01 | 0.16 | 0 | 0.02 | 0 | 0.04 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.02 | 0 | 0.02 | 0.03
Fixed wireless | 0 | 0.82 | 2.72 | 0.36 | 0.01 | 0 | 0 | 2.6 | 0 | 2.71 | 0 | 0.07 | 0.02 | 0.08 | 0 | 0.73 | 14.75 | 5.41 | 1.41 | 5.53 | 0 | 0.56 | 1.39 | 0.79 | 0.16 | 8.12 | 0.27 | 1.52 | 2.74 | 0.22 | 1.49 | 0 | 0.39 | 2.03 | 0.81 | 0 | 0.09 | 0.07 | 0.8
Other | 1.01 | 0 | 0.22 | 0.44 | 0.06 | 0 | 0 | 0.06 | 0.11 | 0.05 | 0 | 0.06 | 0 | 0 | 0.21 | 0.16 | 0 | 0 | 0 | 0.24 | 0 | 0 | 0 | 0.88 | 0.24 | 0.02 | 0.07 | 0 | 16.36 | 0.03 | 0.13 | 0 | 0.99 | 1.45 | 0.22 | 0.5 | 0.04 | 0.3 | 0.01
OECD (June 2021)
Notes: https://ipcarrier.blogspot.com/2021/07/
https://www.oecd.org/sti/broadband/1.2.OECD-FixedMobileBB-2021-06.xls

## Slide 20: FTTH internationally (OECD)
Chart: %
| Korea | Japan | Lithuania | Spain | Sweden | Iceland | Latvia | New Zealand | Norway | Finland | Portugal | Luxembourg | Chile | Slovenia | Estonia | France | Denmark | Slovak Republic | Hungary | OECD | Poland | Mexico | Turkey | Switzerland | Netherlands | Australia | Costa Rica | Canada | Ireland | Colombia | Czech Republic | United States | Italy | Israel | Germany | United Kingdom | Austria | Belgium | Greece
Fibre | 85.86 | 82.52 | 77.15 | 76.24 | 76.08 | 71.95 | 71.2 | 63.71 | 62.68 | 58.43 | 57.67 | 53.03 | 49.15 | 46.75 | 43.27 | 39.98 | 39.57 | 37.87 | 32.41 | 32.1 | 32.09 | 30.21 | 24.9 | 23.55 | 23.53 | 22.65 | 22.53 | 21.52 | 19.87 | 19.76 | 18.94 | 17.01 | 12.33 | 11.98 | 6.37 | 5.71 | 5.11 | 2.16 | 0.36
DSL | 2.11 | 2.21 | 14.77 | 9.27 | 6.99 | 27.08 | 20.33 | 18.27 | 7.46 | 13.28 | 7.29 | 36.15 | 4.58 | 24.11 | 21.21 | 44.26 | 24.25 | 27.19 | 17.11 | 28.74 | 19.03 | 25.59 | 64.89 | 49.37 | 30.36 | 49.52 | 15.01 | 22.15 | 50.89 | 14.05 | 24.94 | 14.67 | 25.49 | 58.44 | 69.38 | 74.82 | 56.67 | 44.66 | 99.52
Cable | 12.04 | 15.26 | 2.43 | 12.78 | 16.58 | 0.75 | 3.09 | 2.6 | 23.24 | 27.1 | 28.29 | 10.28 | 41.36 | 28.03 | 19.17 | 13.96 | 34.38 | 10.34 | 46.37 | 33.77 | 33.17 | 42.09 | 7.71 | 24.9 | 46.11 | 22.49 | 61.79 | 50.04 | 24.25 | 61.16 | 15.8 | 64.39 | 29.58 | 24.02 | 19.37 | 37.38 | 52.91
Notes: http://www.oecd.org/internet/broadband/broadband-statistics-update.htm
https://www.oecd.org/sti/broadband/broadband-statistics/

## Slide 21: Improving availability

## Slide 22: How much speed do we need?
industry: most applications don’t need lots of bandwidth
advocates: but we want future-proof networks!
Technology Policy Institute, 3/21
Notes: https://techpolicyinstitute.org/2021/03/29/youve-been-served/
https://broadbandnow.com/report/fcc-broadband-definition/

## Slide 23: For non-fiber networks, problem is likely capacity, not speed
Chart: Comcast Median Household Usage in GB/month
| 39722 | 40148 | 40695 | 41061 | 41609 | 41791 | 42278 | 42522 | 42644 | 42705 | 42887 | 43070 | 43252 | 43435 | 43617 | 43800 | 43983 | 44166 | 44348 | 44531
GB/month | 0.3 | 3 | 4 | 9 | 17 | 23 | 40 | 60 | 75 | 88 | 100 | 131 | 151 | 174 | 191 | 220 | 308 | 346 | 356 | 355
Notes: https://www.xfinity.com/support/articles/data-usage-average-network-usage

## Slide 24: Metrics: not Gb/s or b/s/Hz, but $/GB and $/year
GB/subscriber or GB/square mile
2nd GEO satellite
switch to small cells
in-building cells
$/month

## Slide 25: Density determines network choices
1
10
100
1000
50
Alaska roadmiles
20
1454
7
HH/road mile
cable
FTTH
DSL (common)
REC
WISP
satellite
Notes: Manhattan: 508 road miles - http://venus.fcny.org/cmgp/streets/pages/2001PDF/Report/DFMN.pdf ; Wikipedia: 738,644 households in Manhattan
Alaska: 15,178 miles; 741,894 population
https://www.pcmag.com/news/tested-spacexs-starlink-satellite-internet-service-is-fast-but-itll-cost

## Slide 26: Challenges for rural broadband
Who is going to build out?
  some incumbent local exchange carriers (ILECs) are not interested
  municipalities may be prohibited by state laws
    or hurdle is extremely high
  rural electric cooperatives – serve 14M homes in US (out of ~110M)
    average, 5.8 electric meters per mile
Upgrade copper or new infrastructure?
  fiber closer to the home (“FTTN”) OR
  fiber to the home (FTTH) or fixed wireless (FWA) or LEO
Who is going to pay for broadband?
  subsidize once, for N years, or forever?
Are non-landline approaches scalable?
  TV white spaces, HAPS
  satellite – NGS like OneWeb (600 satellites) or StarLink
    currently, about 500k residential satellite subscribers
      ”better than nothing”
      lacking capacity, high delay, low reliability, expensive
    LEOs change the picture
      but same concerns + spectrum + horizon visibility
50-150 Mb/s, 40 ms RTT
$99/month
$499 antenna
Notes: https://www.tesmanian.com/blogs/tesmanian-blog/ufo-starlink-terminal

## Slide 27: Network economics, (over)simplified
Chart: % of revenue
| Equipment | Construction | Operations
Costs | 4.5 | 10.5 | 85
70%
30%
traditional: 12-15 staff/10k customers
Iliad, FR: 3-4 staff/10k
Notes: opex ratios: Deloitte

## Slide 28: Fiber observations
Fiber middle-mile cost: $50-70k/mile
Fiber per home passed: $1,250 (bottom 90%)
Fiber is cheap: 144 strands = $10k/mile, 48 strands = $4.7k/mile
Common characteristics:
  avoid active elements in network  power, maintenance  PON
  recently: avoid anything except fiber (including splitters)
    cf. wireless last mile approach
  fiber home run, even if PON (Google Fiber, Stockholm)
Fiber cost higher for buried, but cheaper if conduit or aerial
Notes: https://www.bbcmag.com/broadband-applications/to-reduce-network-operating-expenses-choose-ftth
https://www.telecompetitor.com/report-for-an-extra-70-billion-ftth-could-be-available-to-90-of-u-s-homes-by-2029/

## Slide 29: How do we pay for this?

## Slide 30: Universal Service Fund (USF)
Contributions from telecom providers
(assessment of ~25-30% on their interstate end-user revenues)
wireline telco
wireless telco
Universal Service Fund
lifeline
($854M)
e-rate (schools & libraries) ($2.1B)
disbursement of funds to eligible entities
reduce costs for rural telcos
reduce costs for low-income consumers
cable
high-cost
($5.1B)
rural health care
($298M)
reduce costs for schools & libraries
reduces costs for rural health providers
Allison Baker, 2017; modified 2021

## Slide 31: We’ve tried this for a while: Connect America Fund (CAF) and off-spring
Connect America Fund
Rate-of-Return Areas
Mobile Services
Mobility Fund Phase I
Mobility Fund Phase II
CAF ICC (RoR)
HCLS (SNA, SVS)
CAF-BLS (ICLS)
CAF Phase II (Auction)
CAF - ACAM
Legacy Competitive ETCs
Frozen High Cost Support
Future Programs
CAF Programs
Legacy Programs
Key
Price Cap Area
CAF Phase I
CAF Phase II
Rural Broadband Experiments
CAF ICC (PC)
Remote Areas Fund (Auction)
Alaska Plan (RoR)
Fixed Services
Alaska Plan (Mobile)
RDOF
5.0B for 2019
4.7B for 2021
Notes: https://docs.fcc.gov/public/attachments/DOC-362272A1.pdf
https://opendata.usac.org/High-Cost/High-Cost-Funding-Disbursement-Search/cegz-dzzi
https://www.fcc.gov/general/federal-state-joint-board-monitoring-reports

## Slide 32: Your (mobile) phone bill at work
911 fee
USF
funds the FCC

## Slide 33: Rural Digital Opportunity Fund (RDOF) - 2020
Old (pre-1996) model: incumbent is obligated to provide “universal service”
  even if economically inefficient
  “carrier of last resort” (COLR)
Transition model: large incumbent telephone companies get money
  based on cost estimates  often upgrade DSL from really slow to slow
New model: reverse auction  lowest subsidy wins support
  non-traditional providers, new entrants, satellite, …

## Slide 34: RDOF (2020) outcome
https://www.ctcnet.us/analytics/rdof-winners/

## Slide 35: 2021 Infrastructure Investment & Jobs Act
Broadband Equity, Access, and Deployment (BEAD)
  $42.45B: NTIA  states  providers
    distributed to states based on their fraction of unserved locations
    competitive bidding, reverse auction, …?
    first, unserved (≤ 25/3 Mb/s), then underserved (≤ 100/20, i.e., no HFC territory), then community anchors ≤ 1 Gb/s
    build-out of ≥ 100 Mb/s download, 20 Mb/s upload ( FWA or fiber)
    ≤ 48 hour outage per year (99.5% reliability)
    must offer low-cost broadband service option
DATA Act  broadband ”Fabric”
  street-level, geo-coded database of broadband availability
Enabling Middle Mile Broadband Infrastructure Program ($1B)
Tribal Broadband Connectivity Program ($2B)

## Slide 36: Affordability

## Slide 37: Lifeline
Established in 1985 by the FCC and mandated by Congress in the Telecommunications Act of 1996
  used to be mostly local phone, now mostly mobile
Federal program that lowers the monthly cost of phone and internet for qualified low income consumers
  Program qualification based on income or participation in a qualifying assistance program (e.g., SNAP, Medicaid, SSI, Public Housing Assistance)
  Basic support amount is $9.25 per month and up to $34.25 for consumers living on Tribal lands
    e.g., 1,000 minutes of voice, 4.5 GB of data
Concerns about fraud
  unused phones
  multiple phones in one household
  phones to ineligible consumers

## Slide 38: But Lifeline has reached (mostly) the end of its line
one per household – who gets the phone?
too little data even if tethering enabled
  3 hours of Zoom per month
not all children can get access
Notes: https://www.usac.org/lifeline/learn/program-data/

## Slide 39: Provider-based: Comcast Internet Essentials
Fear of bills
It’s free – must be a scam
Not available in 58% of households
”have not subscribed within 90 days”
“no overdue bill within 12 months”
Some school districts give out bulk
vouchers
see also

## Slide 40: COVID-19 changed thinking
Pre-COVID-19
Biggest problem: no broadband in small parts of rural America
Low income households have Lifeline for basic connectivity
Need to solve mapping problem first to understand scope of unavailability
10-year programs (USF CAF II, RDOF)
Can always go to the local library or school
25/3 is plenty fast
With COVID-19
Biggest problem: lots of people can’t afford broadband
  and quality of supposedly-covered areas is low
  no 25/3 broadband in urban areas
    only 1.5%, but that’s 3.9 M people
    vs. 11.1 M rural
    “digital redlining”
  or cannot afford devices
Students cannot wait 10 years
Local library (and school) is closed
Multiple video conferences bust 3 Mb/s upstream

## Slide 41: IIJA Affordable Connectivity Program
$30/month subsidy
  + $100 subsidy for laptop, tablet, desktop computer
eligibility:
  income must be at or below 200% of the Federal Poverty Guidelines
    e.g., $25.6k for single person, $53k for family of 4
    cf. median family household income: $86k
  receive benefits from Medicaid, Supplemental Nutrition Assistance Program, Supplemental Security Income, Federal Public Housing Assistance, or Veterans and Survivors Pension Benefit
  student on free and reduced-price lunch program or the school breakfast program (including the Community Eligibility Provision)
  has received a Federal Pell Grant in the current award year
National Lifeline Verifier
EBB: about 20% participation
Notes: https://www.benton.org/blog/how-infrastructure-investment-and-jobs-act-will-make-broadband-more-affordable
https://www.census.gov/library/publications/2021/demo/p60-273.html

## Slide 42: NTIA Digital Equity Act Programs ($2.75B)
“digital inclusion and equity to ensure that all individuals and communities have the skills, technology, and capacity needed to reap the full benefits of our digital economy. The goal of these programs is to promote the meaningful adoption and use of broadband services across the targeted populations in the Act, including low-income households, aging populations, incarcerated individuals, veterans, individuals with disabilities, individuals with a language barrier, racial and ethnic minorities, and rural inhabitants.”

## Slide 43: Conclusion
Availability, affordability & relevance
Except for large cable companies, challenging economics for ISPs
Introducing competitive fiber speeds is difficult everywhere
Who should subsidize high-cost and low-income areas? Taxes or fees?
Emphasis on automation (+ staff cuts) and simplified service structure
  not new services, protocols, speeds
Research directions:
  why do certain regions not get (subsidized) broadband
  fully autonomous, self-configuring networks