## Slide 1: Scaling networks up and down: new network architectures for 6G
Henning Schulzrinne
Columbia University
This material is based upon work supported by the National Science Foundation under Grant No. 1932418. Any opinions, findings, and conclusions or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the National Science Foundation.

## Slide 2: Classical ecological niches
laptops
Wi-Fi offload
peripherals
lowest-end
devices
smartphones
international roaming
voice
IoT WAN
mesh
low energy
pairing
profiles
speed
authentication
voice
mobility
international roaming

## Slide 3: Classical requirements pyramid
mostly PHY requirements!
Notes: http://jultika.oulu.fi/Record/isbn978-952-62-2354-4

## Slide 4: The most important metric is missing!
BLS data (Internet services and electronic information providers)
Chart: Comcast Median Household Usage in GB/month
| 39722 | 40148 | 40695 | 41061 | 41609 | 41791 | 42278 | 42522 | 42644 | 42705 | 42887 | 43070 | 43252 | 43435 | 43617 | 43800 | 43983 | 44166 | 44348 | 44531
GB/month | 0.3 | 3 | 4 | 9 | 17 | 23 | 40 | 60 | 75 | 88 | 100 | 131 | 151 | 174 | 191 | 220 | 308 | 346 | 356 | 355
average: 500 GB/month
 $0.12/GB
Notes: https://data.bls.gov/timeseries/CUUR0000SEEE03
https://openvault.com/ovbi-2-tb-usage-growth-surging-as-subscriber-speeds-increase/

## Slide 5: Without cost (and price) decrease, no advanced applications
 The key performance metric is $/GB (and maybe $/km2 coverage)
Notes: https://support.google.com/stadia/answer/9607891?hl=en
https://www.telecompetitor.com/report-mobile-revenue-per-gigabyte-is-under-1/

## Slide 6: Generational surprises
Generation | Expectation | Surprise | Cost per GB
0G (landline) | voice | fax & modem | 
1G | corporate limousine | eavesdropping | 
2G | better voice quality (“digital!”) | SMS | $1000
3G | WAP | web | $100
4G | IMS | YouTube, WhatsApp, notifications | $10
5G | IoT (low latency) | FWA | $1?
underestimated cost and fixed-equivalence as drivers
are the even generations the successful ones?

## Slide 7: Network cost and price are highly variable
avg. about 5.1 GB/month
T-Mobile: 10 GB tethering
March 2020
Notes: https://451research.com/blog/1662-featured-data-1

## Slide 8: Mobile data usage
US ARPU (2022) = $35
 $2.40/GB
~20 times more expensive per GB than home (“Wi-Fi”)
Ericsson Mobility Report Nov. 2021
Notes: https://www.ericsson.com/en/reports-and-papers/mobility-report/dataforecasts/mobile-traffic-forecast

## Slide 9: Networks 1G through 4Gish
national carrier
one subscriber,
one phone,
one provider

## Slide 10: What exactly is a carrier?
LTE-U
802.11n
LTE
Level3
Cogent
Spectrum DB
Spectrum DB
40k towers each (US)

## Slide 11: Investment incentives for 5G are modest – are they going to be better for 6G?
Notes: https://www.lightreading.com/mobile/5g/a-big-5g-investment-cycle-dont-hold-your-breath/d/d-id/751698

## Slide 12: Cell towers as cost driver (or revenue source)
* Cost does not include radio equipment and backhaul!
https://www.celltowerleaseexperts.com/cell-tower-lease-news/cell-tower-industry-facts-figures-2016
cellular revenue per cell site:
$190B US total  $175k

## Slide 13: New operator models – cable (HFC) industry
All major US cable operators are offering cellular service
hybrid model:
MVNO + Wi-Fi + CBRS
Comcast | 4M
Charter | 3.56 M
Altice | 186k
LightReading, 3/22
LightReading, 7/19
Notes: https://www.lightreading.com/cable/cable-wi-fi/an-inside-look-at-cables-mvno-business-model/d/d-id/752938
https://www.lightreading.com/cable-tech/us-cable-holds-steady-with-29-of-mobile-adds-in-q4/d/d-id/776127

## Slide 14: FTTH as the new backhaul
https://www.fiberbroadband.org/
Notes: https://www.fiberbroadband.org/d/do/4335

## Slide 15: FTTH now dominates fiber deployment
https://www.fiberbroadband.org/
Notes: https://www.fiberbroadband.org/d/do/4335

## Slide 16: The Things Network
Notes: https://ttnmapper.org/heatmap/

## Slide 17: The Things Network
April 2022 (Columbia U.)

## Slide 18: Helium LoRa model for IoT
Helium: 0.001c per 24-byte message ( $416/GB)
$3.46 per month and hotspot
5W of energy  $0.37 electricity
Notes: https://www.steelintheair.com/cell-tower-lease-rates/
https://www.celltowerleaseexperts.com/cell-tower-lease-news/cell-tower-industry-facts-figures-2016
https://www.fiercewireless.com/operators/dish-partners-helium-hotspot-model-featuring-cbrs-blockchain

## Slide 19: Helium in Manhattan

## Slide 20: But blockchain models are volatile
https://www.coinbase.com/price/helium

## Slide 21: LTE EPC
Notes: https://www.slideshare.net/aliirfan04/lte-and-epc-specifications

## Slide 22: 5G & 4G EPC
Ericsson, Oct. 2020
Notes: Ericsson: Your guide to building a cloud native 5G Core

## Slide 23: Users per ASN roughly constant
https://www.cidr-report.org/
https://itu.foleon.com/itu/measuring-digital-development/internet-us
roughly unchanged at 60k users per AS
(slight decrease in users / routing table entry)

## Slide 24: Home networks are now small enterprise networks
Largely self-managed:
routing (mesh)
device management
device & user authentication
Notes: https://www.telecompetitor.com/report-connected-devices-have-more-than-doubled-since-2019/

## Slide 25: Scaling down is harder than scaling up
large enterprise
management
mesh backhaul
firewall
DNS
edge computing
identity management and trust still deficient
no PhD (or carrier training) needed!

## Slide 26: Network value is (much) more than PHY
Property | Requirements? | Example
Universality | Can I operate my system (almost) anywhere in the world? | Adaptive frequency use by region (device knows location)
Incremental system cost | How much does it cost to add the functionality to the system? | < $5 for IoT devices
Data cost | Can I build “free” data systems, even if restricted? Can I leverage cheap landline BW? | < $0.10/GB for in-home use
Network architecture | Can I build my own network? | peer-to-peer  mesh  access point  cellular  long-range
User management | Can I design my own user management? | database + credential device-based model coupled to other systems (e.g., combined with other services)
System management | Can the system largely manage itself? | Frequencies & power, but also users and traffic restrictions

## Slide 27: Parallel timelines
1980
1985
1990
1995
2000
2005
2010
2015
2020
approximate standardization
or first deployment
1G
2G
3G
4G
5G
2.4 GHz
ISM
802.11g
~20 Mb/s
802.11a
~20 Mb/s
802.11
~2 Mb/s
802.11b
~6 Mb/s
802.11n
~100 Mb/s
802.11ac
~200 Mb/s
802.11ax
~1 Gb/s
0.1-1.5 Mb/s
5-50 Mb/s
realistic top speeds
150-200 Mb/s
< 0.1 Mb/s
Notes: https://www.tomsguide.com/us/best-mobile-network,review-2942.html
https://kenstechtips.com/index.php/download-speeds-2g-3g-and-4g-actual-meaning

## Slide 28: Wi-Fi & 5G technology likely similar
Revisiting Wireless Internet Connectivity: 5G vs Wi-Fi 6
Notes: Revisiting Wireless Internet Connectivity: 5G vs Wi-Fi 6
https://arxiv.org/abs/2010.11601

## Slide 29: What made Wi-Fi successful?
Scalable complexity – 802.11b/g/n to 802.11ax
Architectural flexibility
  peer-to-peer, access point, mesh, long haul Pt2MP & Pt2Pt
  re-use cheap local wired network and shared (managed & firewalled) access
Multiple authentication models
  from open access to federated 802.1x RADIUS
Minimal viable network functionality
  Ethernet frames + IP
  local multicast
International usability
  universal “bootstrap” band (2.4 GHz)
  locally-discoverable spectrum availability

## Slide 30: Wi-Fi (and BT & LoRa) ”won” by integration
$6.95
ESP8266
Arduino Uno WiFi R2
$45
Arduino MKR1000
$36
Adafruit Feather M0 with RFM95 LoRa Radio - 900MHz – RadioFruit $35
Wi‑Fi 802.11b/g/n
$7.84
Wi-Fi + computer

## Slide 31: Currently, 3G/4G is ~10-15x expensive – why?
Cellular 3G (AT&T) Transceiver Module 850MHz, 900MHz, 1.8GHz, 1.9GHz, 2.1GHz
$69
Bluetooth, Cellular 4G LTE CAT-M1 (AT&T/Verizon) Transceiver Module
$69
Cellular LTE Transceiver Module 700MHz, 850MHz, 1.7GHz, 1.9GHz
$104
AT&T: >72¢ /MB
Notes: https://www.multitech.com/brands/multiconnect-dragonfly-nano
Digi XBee3 Cellular

## Slide 32: What’s bad about having both Wi-Fi and (nG) cellular?
System hardware complexity (e.g., for IoT devices)
No seamless roaming
Maintain multiple user identities
Difficult to do consistent traffic restriction
  cellular bypasses corporate firewall
Inconsistent network behavior
  e.g., IPv6 support
More limited competition

## Slide 33: Current authentication models
picket fence security
federated (RADIUS, DIAMETER)
WPA2-Personal
802.1x
international roaming
hard to scale
to IoT

## Slide 34: Stacks always focus on data – complexity is in control

## Slide 35: Requirements for simple networks
Separate link layer from network architecture
  Why can’t 5G (or 6G) NR operate on a home router, without a carrier?
  Assume flexible spectrum access (geo database)
Every interface must be testable and self-testing
Interface neutrality = every control needs to be accessible to network consumer, not just operator (bounded by slice or authorization)
Clean interfaces particularly at layer 2 and 3
No configuration files, ever
No hard-coded addresses (e.g., gateways), ever

## Slide 36: What’s needed for down-scalable networks?
Better frequency coordination for CBRS GAA (and similar systems)
  e.g., allow time-domain (slot?) coordination
Support simple self-contained EPC that can run on AP
  or OpenRAN with many untrusted participants  zero-trust networks
Simplified roaming and settlement mechanisms
  GSMA unlikely to scale
May need new mobility models, but most new applications are likely nomadic and (somewhat) disruption-tolerant, not mobile and voice-like

## Slide 37: Protocols matter, but programmability matters more
Nobody wants to program raw protocols
Most significant network application creation advances:
  1983: socket API  abstract data stream or datagram
  1998: Java network API  mostly names, HTTP, threads
  1998: PHP  network input as script variables
  2005: Ruby on Rails  simplify common patterns
Many fine protocols and frameworks failed the programmer hate test
  e.g., JAIN for VoIP, SOAP for RPC
Most IoT programmers and factory automation specialists will not be computer scientists (and won’t have a telecom background)
Nobody learns ONAP in their CS BS

## Slide 38: What has changed in network technology since 3G?
Cheap & universal GNS (GPS, Beidou, Galileo, …)
   accurate time and position for every device  mobility and discovery
Multiple simultaneous connections
   simplify hand-off and spectrum discovery
Low-cost Certificate Authorities (e.g., letsencrypt.org)
   simplify authentication
Trusted execution environments on all but lowest-end devices
   simplify authentication and device integrity

## Slide 39: What has changed?
FTTH provides access networks
  BEAD project will add $42.5B (mostly) fiber connections
Most new applications are nomadic, not mobile
  i.e., no need for voice-like continuity of connectivity
Multiple transparent access modalities common
  Wi-Fi to cellular vertical “hand-off” mostly transparent to users

## Slide 40: Two evolutionary paths for 6G
lowest bandwidth cost
like 4G & 5G, just more
highest mobility
mostly not a PHY problem

## Slide 41: Conclusion
The key performance metric is $/GB (and maybe $/km2 coverage)
The key challenge is incentivizing investment
6G needs an architecture re-think, not (only) better PHY
Cleaner separation between media/complexity-dependent layers, common data transport and control planes
Design scalable, IP-based control plane for everything from peer-to-peer mode to managed national cellular network
Cleanly separate access from backbone
  since likely continue to be both locally (enterprise) and third-party managed
Opportunity to bridge the Wi-Fi - cellular chasm