## Slide 1: Genuity Voice over IP Services Overcoming Obstacles to Delivering Reliable, Scalable Voice over IP Services
June 29, 2000
Nick Damenti
Director VoIP Services
tel: 781-262-7207
email: ndamenti@genuity.com

## Slide 2: Discussion Topics:
Network Architecture Overview
Genuity Voice over IP Infrastructure Objectives
Service Implementation--Challenges and Issues
Looking Forward
Genuity Voice over IP Current Status

## Slide 3: Genuity’s Voice over IP Service Infrastructure Objectives...
Reliable, Scalable network
Guaranteed Quality of Service
No Single Point of Failure
Open Standards Based Infrastructure
National Central Office Capability
National Local Inward Dial Reach
Global Transport and Termination

## Slide 4: Genuity Voice over IP Presentation Outline:
Network Architecture Overview
Genuity Voice over IP Infrastructure Objectives
Service Implementation--Challenges and Issues
Looking Forward
Genuity Voice over IP Current Status

## Slide 5: Architecture Overview
Open standards, H.323 based VoIP network with guaranteed QoS, built on GENUiTY’s Global Network Infrastructure
Equipment configuration and network connectivity engineered to provide no single point of failure
VoIP Gateways (Cisco AS5300s) located across the U.S. in 8 interconnected superPoPs
Local dial inbound/outbound reach achieved through CLEC Interconnections - reaching top 54 U.S. metro areas
Global outbound transport and termination worldwide

## Slide 9: Genuity Voice over IP Presentation Outline:
Network Architecture Overview
Genuity Voice over IP Infrastructure Objectives
Service Implementation--Challenges and Issues
Looking Forward
Genuity Voice over IP Current Status

## Slide 10: Service Implementation-- Challenges We Overcame
  Marketplace Acceptance of Voice over IP
    Implemented Enterprise VoIP Trial (9 Genuity Buildings)
    MOS score of 3.9, ranking comparable to PSTN
  Immature Software and Hardware
    Two Years to Reach Acceptable Quality Standards
  CLEC Interconnection Difficulties
    Provisioning delays
    Outbound dial holes
    Lack of network capacity

## Slide 11: Service Implementation--Challenges We Overcame
  Integrated Billing Solution
    Scalable solution for CDR Aggregation and Rating
  Testing Requirements
    Customer Integration Testbed
    End to End Network Element Testing
  Complex Network Configuration and Management
    Over 1000 Network Elements
    Each VoIP Gateway Contains Complex Configuration Data (4-6k)
    Management of a Large number of DIDs (>2M)
    National local dial coverage
      80% U.S. metro population, 450 rate centers, 58k (out of 100k) local exchanges

## Slide 12
Telco Provisioning
Network
Engineering
NOC
Customer
Provisioning
Legacy DB
COMIT
Network Monitoring
Trouble Ticketing
data center
CARE
ip network
gateway
gateway
router
router
router
Traffic
Engineering
application servers
infrastructure servers
(IP Comm. Services, radius, etc.)
gatekeepers
PSTN switch
Built Proprietary Network Configuration and Management Tool

## Slide 13: COMIT -- Configuration Management for Internet Telephony Features...
IP- PSTN Routing
  Manages PSTN Number Plan--allows for unlimited DID provisioning in under an hour
  Maps E.164 addresses  Circuits  Gateways  IP Addresses
  Queries: local calling scope, service availability, service degradation
  Automatic management of area-code splits and overlays

## Slide 14: COMIT Features
Real-time network configuration (gw, gk, app platform, radius, usage mediation, …..)
Sophisticated router config. management tool set:
  Dynamic (in-service) configuration changes, full configuration downloads
  Network audit / data consistency checking
  Configuration version management

## Slide 15: Genuity Voice over IP Presentation Outline:
Network Architecture Overview
Genuity Voice over IP Infrastructure Objectives
Service Implementation--Challenges and Issues
Looking Forward
Genuity Voice over IP Current Status

## Slide 16: Genuity is the leading VoIP service provider in the world
  Currently handling well over 100 million minutes per month
  Proven ability to scale rapidly
  Won numerous awards for VoIP services
    Financial Times 1999 Global Telecom Award for “Best Use of Internet Technology.”
    Internet Telephony Magazine’s Product of the Year Award in the services category.
    Tele.com Ovation award in the category of Access Network Design and Engineering for Dr. Robert Olshansky’s, Genuity Director of Engineering, individual achievement in engineering.
“Best Use of Internet Telephony”
Ovation Award:
“Access Network Design and Engineering”

## Slide 17: High Quality VoIP
Quality of Service (QoS)
  99.9% network availability outside of planned outages
  One-way latency delay of less than 100ms between any two points on GENUiTY VoIP network (Currently delivering around 40ms delay)
  One-way jitter of less than 15ms between any two points on GENUiTY IP Voice network
  Packet loss of less than 1% between any two points on GENUiTY IP Voice network (actual packet loss near 0%)
First Voice over IP Carrier to Implement Low Latency Priority Queuing on the Tail Circuits.
No Tail Circuit QoS
QoS Enabled Tail Circuit

## Slide 18: Carrier Quality Back-End Support
24x7 Network Monitoring
  GENUiTY’s Network Operations Center (NOC) is available to customers 24x7
  Continual monitoring, testing and diagnoses of all components of the network including partners’ network connections and equipment
24x7 Customer Care
  Tier II through IV customer care via telephone with reliable escalation and response processes
  On-line customer support system with access to network status, call detail records, and trouble ticket tracking

## Slide 19: Multi-service network deployed to 54 LATAs
  Local inbound access to over 80% US metro population
  World-wide egress
  “National Central Office” with local calling from 100 million telephone lines
  All services on every PRI
  Easily scaled by adding PRIs and gateways
  New customers and services by activating local access numbers
  Rapid deployment of new services

## Slide 20: Genuity Voice over IP Presentation Outline:
Network Architecture Overview
Genuity Voice over IP Infrastructure Objectives
Service Implementation--Challenges and Issues
Looking Forward
Genuity Voice over IP Current Status

## Slide 21: Looking forward...
Expanding egress capacity to approximately 1Billion MMoUs by year end.
Investigating deployment of:
  End to end PC to Phone QoS.
  Next generation IP Communication Infrastructure Capabilities
  Integrated Enterprise voice/data services

## Slide 22: In Summary, Genuity offers reliable, scalable VoIP ...
No Single Point of Failure
Open Standards Based Infrastructure
National Central Office Capability
Guaranteed Quality of Service
National, local inbound dial reach in major metros
Global Transport and Termination
VoIP Service Provider Market Leader

## Slide 23: Thank You