## Slide 1: Software Defined Networking COMS 6998-10, Fall 2014
Instructor: Li Erran Li (lierranli@cs.columbia.edu)
http://www.cs.columbia.edu/~lierranli/coms6998-10SDNFall2014/
11/21/2014: SDN Wireless Networks

## Slide 2: Outline
Review of SDN Security
SDN Wireless Networks
  Motivation
  Data Plane Abstraction:
    OpenRadio
    PRAN
  Control Plane Architecture
    Radio Access Networks: SoftRAN
    Core Networks: SoftCell
    Cellular WAN: SoftMoW

## Slide 3: Review of Previous Lecture: Defense Against Control Plane Attacks
Security extension to the OpenFlow data plane
  Connection migration
    To address scalability
    issue
  Actuating trigger
    To address responsiveness
    issue
Control Plane Interface
Flow Table (TCAM and SRAM)
Flow Table Lookup
Packet Processing
Control Plane
Data Plane
Connection Migration
Actuating Trigger
Avant-Guard
Source: S. Shin, et al.

## Slide 4: Connection Migration – Packet Diagram
A
B
Control Plane
(1) TCP SYN
(2) TCP SYN/ACK
(3) TCP ACK
(6) TCP SYN
(7) TCP SYN/ACK
(8) TCP ACK
(11) TCP ACK
TCP Data
(12) TCP ACK
TCP Data
(4)
(5)
(9)
(10)
A-1: A --> B: Migrate
A-2: A --> B: Relay
Data Plane
Classification stage
Relay stage
Migration stage
Relay stage
Report stage
Report stage
Source: S. Shin, et al.
Review of Previous Lecture: Defense Against Control Plane Attacks (Cont’d)

## Slide 5
Source: G. Gu, et al, Texas A&M &SRI
Review of Previous Lecture: Controller Security Framework (Cont’d)

## Slide 6: FRESCO Modular Design
parameter
action
input
output
event
key
values
Module
F-DB instance
Source: G. Gu, et al, Texas A&M &SRI
Review of Previous Lecture: Controller Security Framework (Cont’d)

## Slide 7
Security Apps
Native C
OF Apps
PY OF
Apps
FortNOX
Python SWIG
OF IPC Proxy
Separate
Process
Directive Translator
IPC Interface
Actuator
Aggregate Flow Table
Operator Rules
SECURITY Rules
OF App Rules
FT_Send_OpenFlow_Command
Role-based Source Auth
State Table Manager
Conflict Analyzer
OF Mod Commands
Add (conflict enforced)
Modify (conflict enforced)
Delete (priority enforced)
Switch Callback Tracking
Source: G. Gu, et al, Texas A&M &SRI
Review of Previous Lecture: Controller Security Framework (Cont’d)

## Slide 8: Outline
Review of SDN Security
SDN Wireless Networks
  Motivation
  Data Plane Abstraction:
    OpenRadio
    PRAN
  Control Plane Architecture
    Radio Access Networks: SoftRAN
    Core Networks: SoftCell
    Cellular WAN: SoftMoW

## Slide 9: Wireless Data Growth
Exponential traffic growth
Source: CISCO Visual Networking Index (VNI) Global Mobil Data Traffic Forecast 2011 to 2016
Question: How to substantially improve wireless capacity?
Chart: Exabyte
| 2007.0 | 2008.0 | 2009.0 | 2010.0 | 2011.0 | 2012.0 | 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0
Total Mobile Data Traffic | 0.026 | 0.033068 | 0.091 | 0.23668 | 0.54605 | 0.88491 | 1.5772 | 2.797 | 4.7005 | 7.4385 | 11.1555

## Slide 10: Outline
Review of SDN Security
SDN Wireless Networks
  Motivation
  Data Plane Abstraction:
    OpenRadio
    PRAN
  Control Plane Architecture
    Radio Access Networks: SoftRAN
    Core Networks: SoftCell
    Cellular WAN: SoftMoW

## Slide 11: OpenRadio: Access Dataplane
OpenRadio APs built with merchant DSP & ARM silicon
  Single platform capable of LTE, 3G, WiMax, WiFi
  OpenFlow for Layer 3
  Inexpensive ($300-500)
Control
CPU
Forwarding
Dataplane
Baseband &
Layer 2 DSP
RF
RF
RF
Exposes a match/action interface to program how a flow is forwarded, scheduled & encoded
Source: Katti, Stanford

## Slide 12: Design goals and Challenges
Programmable wireless dataplane using off-the-shelf components
  At least 40MHz OFDM-complexity performance
    More than 200 GLOPS computation
    Strict processing deadlines, eg. 25us ACK in WiFi
  Modularity to provide ease of programmability
    Only modify affected components, reuse the rest
    Hide hardware details and stitching of modules
Source: Katti, Stanford
12
Notes: The goal in providing flexibility is to enable implementation of a wide set of optimizations and variations, but not arbitrary modifications. The cost in providing arbitrary flexibility is loss in performance (eg. SDRs). We want to cover modifications but retain performance. This will affect the granularity of protocol decomposition and the selection of processing abstractions, as we will discuss next.

## Slide 13: Wireless Basebands
OFDM Demod
Demap (BPSK)
Deinterleave
Viterbi Decode
Descramble
CRC Check
Hdr Parse
WiFi 6mbps
Deinterleave
OFDM Demod
Demap (BPSK)
Demap (64QAM)
WiFi 6, 54mbps
Descramble
CRC Check
Hdr Parse
Decode
(1/2)
Decode
(3/4)
Descramble
OFDM Demod
Demap (BPSK)
Demap (64QAM)
Deinterleave (UEP)
Hdr Parse
CRC Check
Descramble
Hdr Parse
Deinterleave
(WiFi)
Decode
(1/2)
Decode
(3/4)
WiFi 6, 18mbps and UEP
13
Source: Katti, Stanford
Notes: Goal: We want to understand the nature of “programmability” in the context of wireless radios.
Outline: Lets consider a PHY protocol, say WiFi and list the operations that are performed. Then, let’s look at different modes of the protocol, like different modulation schemes and different coding rates. Based on the parts that are common and the parts that need modification or need to be turned off/on from mode to mode, we can partition the sequence of operations. This gives us the natural granularity of blocks that make up wireless protocols and the level of abstraction needed for programming.
We formalize this approach by identifying that the nature of “programming” involved here is the decision of whether to use a processing block and the associated parameters. The design of the “programming interface” involves the choice of processing blocks and their granularity. It is also the tradeoff between flexibility and ease of programming. (As we will see, it is also the tradeoff between flexibility and performance).
Give examples of what we DO NOT want to program: The specific algorithm used for Fourier Transform, the specific algorithm used for ML decoding, the specific algorithm used for computing the CRC etc.
Note: The list of blocks here is not exhaustive, only an example. Also, the division is not laid out in stone. A block can always be further subdivided – you may split an OFDM Demod block into “subcarrier demapper”, “CP remove” and “FFT”. We are only using this to drive to the principle of processing and decision plane separation.

## Slide 14: Modular declarative interface
Inserting RULES
Composing ACTIONS
  Blocks
OFDM Demod
A
Demap (BPSK)
B
Demap (64QAM)
C
Deinterleave
(WiFi)
D
Deinterleave (UEP)
E
Decode
(1/2)
F
Decode
(3/4)
G
Descramble
H
CRC Check
I
Hdr Parse
J
A
B
D
F
H
I
J
A
C
D
G
H
I
J
A
C
E
G
H
I
J
F
H
J
6M
54M
UEP
A
B
D
F
H
I
J
6M
A
B
D
F
H
I
J
C
G
6M, 54M
  Rules: Branching logic
Data
flow
Control
flow
  Actions: DAGs of blocks
Source: Katti, Stanford
Notes: Convenient abstraction level means that declarative description of protocol is possible with blocks as units; hardware is abstracted in the blocks so that the imperative execution plan need not be specified.
Sufficient expressiveness means that most protocol variants of interest can be realized with this API.

## Slide 15: State machines and deadlines
Rules and actions encode the protocol state machine
  Rules define state transitions
  Each state has an associated action
Deadlines are expressed on state sequences
deadline
A
C
B
D
G
F
H
I
J
Start
decoding
Finish
decoding
15
Source: Katti, Stanford

## Slide 16: Design principle I Judiciously scoping flexibility
Provide just enough flexibility
Keep blocks coarse
Higher level of abstraction
High performance through hardware acceleration
  Viterbi co-processor
  FFT co-processor
Off-the-shelf heterogeneous multicore DSPs
  TI, CEVA, Freescale etc.
Algorithm | WiFi | LTE | 3G | DVB-T
FIR / IIR | √ | √ | √ | √
Correlation | √ | √ | √ | √
Spreading |  |  | √ | 
FFT | √ | √ |  | √
Channel Estimation | √ | √ | √ | √
QAM Mapping | √ | √ | √ | √
Interleaving | √ | √ | √ | √
Convolution Coding | √ | √ | √ | √
Turbo Coding |  | √ | √ | 
Randomi-zation | √ | √ | √ | √
CRC | √ | √ | √ | 
Notes: Balance flexibility and performance.

## Slide 17: Design principle II Processing-Decision separation
Logic pulled out to decision plane
Blocks and actions are branch-free
  Deterministic execution times
  Efficient pipelining, algorithmic scheduling
  Hardware is abstracted out
A
B
C
D
E
F
60x
A
B
D
F
H
I
J
C
G
6M, 54M
Regular compilation | OpenRadio scheduling
Instructions | Atomic processing blocks
Heterogeneous functional units | Heterogeneous cores
Known cycle counts | Predictable cycle counts
Argument data dependency | FIFO queue data dependency

## Slide 18: Prototype
COTS TI KeyStone multicore DSP platform (EVM6618, two chips with 4 cores each at 1.2GHz, configurable hardware accelerators for FFT, Viterbi, Turbo)
Prototype can process 40MHz, 108Mbps 802.11g on one chip using 3 of 4 cores
RF signal
I/Q base-
band
samples
Antenna chain(AX)
Radio front end (RFE)
Baseband-processor unit (BBU)
(Digital)
(Analog)
Layer 0
Layer 0 & 1
Layer 1 & 2
Source: Katti, Stanford
18

## Slide 19: OpenRadio: Current Status
OpenRadio APs with full WiFi/LTE software on TI C66x DSP silicon
OpenRadio commodity WiFi APs with a firmware upgrade
Network OS under development
Source: Katti, Stanford

## Slide 20: Software architecture
Bare-metal with drivers
OR Wireless Processing Plane
deterministic signal processing blocks, header parsing, channel resource scheduling, multicore fifo queues, sample I/O blocks
OR Wireless Decision Plane
protocol state machine, flowgraph composition, block configurations, knowledge plane, RFE control logic
OR Runtime System
compute resource scheduling, deterministic execution ensuring protocol deadlines are met
data in
data out
monitor & control
RFE
BBU
(Digital)
(Analog)
AX

## Slide 21: Outline
Review of SDN Security
SDN Wireless Networks
  Motivation
  Data Plane Abstraction:
    OpenRadio
    PRAN
  Control Plane Architecture
    Radio Access Networks: SoftRAN
    Core Networks: SoftCell
    Cellular WAN: SoftMoW

## Slide 22: PRAN Programmability
Hardware/software radio
  Not easy to program
Programmable Radio
  Flexible datapath, interfaces
Scheduler
Base Station Information Base
Data Flow
Control Flow
State Flow
Control Plane
Data Plane
I & Q
Samples
Transport
Block
Modulation
Turbo
Decoding
Reed-Muller
Decoding
Demodulation
Channel
Estimation
Down Link
Up Link
Turbo
Coding
Reed-Muller
Coding
Scrambling
Scheduler
Scheduler
Scheduler
Scheduler
Notes: hardware to offload
Hardware offload

## Slide 23
Internet
RRH
Gateway
Fiber
Data Plane
Control Plane
Resource Manager
Management
Plane
Cloud
Infrastructure
server
Radio Plane
L1/L2
Scheduler
L1/L2
Scheduler
L1/L2
Scheduler
Operator1
Operator2
RAN Scheduler
RAN Scheduler
Notes: PRAN architecture

## Slide 24: Summary
Provides programmatic interfaces to monitor and program wireless networks
  High performance substrate using merchant silicon

## Slide 25: Outline
Review of SDN Security
SDN Wireless Networks
  Motivation
  Data Plane Abstraction:
    OpenRadio
    PRAN
  Control Plane Architecture
    Radio Access Networks: SoftRAN
    Core Networks: SoftCell
    Cellular WAN: SoftMoW

## Slide 26: Carrier’s Dilemma
Chart: Exabyte
| 2007.0 | 2008.0 | 2009.0 | 2010.0 | 2011.0 | 2012.0 | 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0
Total Mobile Data Traffic | 0.026 | 0.033068 | 0.091 | 0.23668 | 0.54605 | 0.88491 | 1.5772 | 2.797 | 4.7005 | 7.4385 | 11.1555
Chart: 
| -15.0 | -12.5 | -10.0 | -5.0 | -2.5 | 0.0 | 2.5 | 5.0 | 7.5 | 10.0 | 12.5 | 15.0 | 17.5 | 20.0
Shannon | 0.06 | 0.1 | 0.15 | 0.4 | 0.7 | 1 | 1.5 | 2 | 2.7 | 3.5 | 4.2 | 5 | 5.9 | 6.8
Shannon (3dB) | 0.05 | 0.09 | 0.13 | 0.2 | 0.4 | 0.7 | 1 | 1.5 | 2 | 2.6 | 3.3 | 4.1 | 5 | 5.7
4G | 0.05 | 0.09 | 0.125 | 0.19 | 0.39 | 0.68 | 0.96 | 1.45 | 1.92 | 2.45 | 3.12 | 3.8 | 4.6 | 5.1
Exponential Traffic Growth
Limited Capacity Gain
Poor wireless connectivity if left unaddressed

## Slide 27: LTE Radio Access Networks
access
core
Packet Data Network Gateway
Serving Gateway
Internet
Serving Gateway
Base Station (BS)
User Equipment (UE)
Goal: high capacity wide-area coverage
  Dense deployment of small cells
Notes: This figure shows the architecture of today’s cellular core networks. User equipment connect to base stations via radio channels.
Base stations connect to the Internet via the cellular core network. There are two main components in the cellular core network, serving gateway and packet data network gateway.

## Slide 28: Dense and Chaotic Deployments
Dense: high SNR per user leads to higher capacity
  Small cells, femto cells, repeaters, etc

## Slide 29: Problems
Current LTE distributed control plane is ill-suited
  Hard to manage inter-cell interference
  Hard to optimize for variable load of cells
Dense deployment is costly
  Need to share cost among operators
  Maintain direct control of radio resources
    Lacking in current 3gpp RAN sharing standards
29

## Slide 30: SoftRAN: Big Base Station Abstraction
time
frequency
time
frequency
time
frequency
frequency
radio element
time
controller
Radio Element 1
Radio Element 2
Radio Element 3
Big Base Station
30

## Slide 31: Radio Resource Allocation
frequency
radio element
time
Flows
3D Resource Grid
31

## Slide 32: SoftRAN: SDN Approach to RAN
BS1
BS2
BS3
BS4
BS5
PHY & MAC
Control Algo
Coordination :
X2 Interface
PHY & MAC
Control Algo
PHY & MAC
Control Algo
PHY & MAC
Control Algo
PHY & MAC
Control Algo

## Slide 33: SoftRAN: SDN Approach to RAN
RE1
RE2
RE3
RE4
RE5
Network OS
Control Algo
Operator Inputs
PHY & MAC
RadioVisor
PHY & MAC
PHY & MAC
PHY & MAC
PHY & MAC
Radio Element (RE)

## Slide 34: SoftRAN Architecture Summary
RADIO ELEMENTS
CONTROLLER
Radio
Element API
Controller
API
Interference
Map
Flow
Records
Bytes
Rate
Queue
Size
Network
Operator
Inputs
QoS
Constraints
RAN Information Base
Radio Resource
Management
Algorithm
POWER
FLOW
Time
Frequency
Radio Element
3D Resource Grid
Periodic Updates
34

## Slide 35: SoftRAN Architecture: Updates
Radio element -> controller (updates)
  Flow information (downlink and uplink)
  Channel states (observed by clients)
Network operator -> controller (inputs)
  QoS requirements
  Flow preferences
35

## Slide 36: SoftRAN Architecture: Controller Design
RAN information base (RIB)
  Update and maintain global network view
    Interference map
    Flow records
Radio resource management
  Given global network view: maximize global utility
  Determine RRM at each radio element
36

## Slide 37: SoftRAN Architecture: Radio Element API
Controller -> radio element
  Handovers to be performed
  RF configuration per resource block
    Power allocation and flow allocation
  Relevant information about neighboring radio elements
    Transmit Power being used
37

## Slide 38: Refactoring Control Plane
Controller responsibilities:
  Decisions influencing global network state
    Load balancing
    Interference management
Radio element responsibilities:
  Decisions based on frequently varying local network state
    Flow allocation based on channel states
38

## Slide 39: SoftRAN Advantages
  Logically centralized control plane:
  Global view on interference and load
    Easier coordination of radio resource management
    Efficient use of wireless resources
  Plug-and-play control algorithms
    Simplified network management
  Smoother handovers
    Better user-experience
39

## Slide 40: SoftRAN: Evolving the RAN
Switching off radio elements based on load
  Energy savings
Dynamically splitting the network into Big-BSs
  Handover radio elements between Big-BSs
40

## Slide 41: RadioVisor Design
Slice manager
  Slice configuration, creation, modification, deletion and multi-slice operations
Traffic to slice mapping at RadioVisor and radio elements
3D resource grid allocation and isolation
  Considers traffic demand, interference graph and policy
RadioVisor
Slice
Manager
3D Resource Grid
Allocation & Isolation
Traffic to Slice
Mapping

## Slide 42: Slice Manager
Slice definition
  Predicates on operator, device, subscriber, app attributes
    A slice can be all M2M traffic of operator 1
Slice configuration at data plane and control plane
  PHY and scheduler: narrow band PHY for M2M slice
  Interference management algorithm
Slice algebra to support flexible slice operations
  Slice merge, split, (un)nest, duplicate

## Slide 43: Resource Grid Allocation and Isolation
Slices present resource demands every time window
Max min fair allocation
Example
  Red slice entitles 2/3 and demands 2/3 RE1 only
  Blue slice entitles 1/3 and demand 1/3 RE2 and 1 RE3
Radio
Element 1
Radio
Element 2
Radio
Element 3
Interference Edge
Time
Radio Element
Frequency

## Slide 44: Summary
Dense deployment calls for central control of radio resources
Deployment costs motivate RAN Sharing
We present the design of RadioVisor
  Enables direct control of per slice radio resources
  Configures per slice PHY and MAC, and interference management algorithm
  Supports flexible slice definitions and operations

## Slide 45: Outline
Review of SDN Security
SDN Wireless Networks
  Motivation
  Data Plane Abstraction:
    OpenRadio
    PRAN
  Control Plane Architecture
    Radio Access Networks: SoftRAN
    Core Networks: SoftCell
    Cellular WAN: SoftMoW

## Slide 46: LTE Cellular Network Architecture
access
core
Packet Data Network Gateway
Serving Gateway
Internet
Serving Gateway
Base Station (BS)
User Equipment (UE)
Notes: This figure shows the architecture of today’s cellular core networks. User equipment connect to base stations via radio channels.
Base stations connect to the Internet via the cellular core network. There are two main components in the cellular core network, serving gateway and packet data network gateway.

## Slide 47: Cellular core networks are not flexible
Most functionalities are implemented at
Packet Data Network Gateway
  Content filtering, application identification,
  stateful firewall, lawful intercept, …
This is not flexible
Packet Data Network Gateway
Combine functionality from different vendors | 
Easy to add new functionality | 
Only expand capacity for bottlenecked functionality | 
Notes: Most functionalities are implemented at the packet gateway today, including application identification, content filtering, monitoring and billing, and so on.
It is not flexible because carriers cannot combine functionality from different vendors.
It is also not easy to add new functionality because vendors have to integrate the functionality with other functionalities that might have already exist for more than 10 years.
It is also no possible to only expand capacity for bottlenecked functionality. Carriers have to buy a new equipment in order to expand the capacity.

## Slide 48: SoftCell Overview
Internet
Controller
Simple hardware
+ SoftCell software
Notes: To be free from such control bottlenecks, we designed a new cellular network architecture called SoftCell. SoftCell applies the principle of software defined networking. Instead of using specialized data plane equipment, we will just use SDN switches. The SoftCell controller coordinates the data plane functions.
To enable direct control and flexibility, we propose a new architecture. It uses the principle of software defined networking. We will make use of commodity hardware which will be controlled by a controller. We make no changes to user equipment and the Internet.
It makes no change no user equipment, the radio access technology, or the Internet.
It only replaces the core network with commodity switches and middleboxes, controlled by a logically centralized controller.
Data Plane:
Switch: connectivity, traffic steering
Middlebox: various network services
~mix-match, combine functionality from different vendors
~easy to add new functionality
~up-/down-scale
~cheap
Control Plane:
Logically centralized controller, centralized control, rather than distributed protocol (hard to reason, debug, trouble shooting)
~Easy to manage
~Easy to change

## Slide 49: SoftCell Design Goal
Fine-grained service policy for diverse app needs
  Video transcoder, content filtering, firewall
  M2M services: fleet tracking, low latency medical device updates
with diverse needs!
Notes: Due to the diverse needs from subscriber mobile apps and M2M apps, we need to support fine-grained policies such as video transcoder, content filtering, fleet tracking.
We wan three things. First, we want unified control of data plane. Second, we would like to flexibly control routing and Internet exit points. Third,
Given the different needs of subscribers and the many user scenarios of machine type communication (also known as Internet of Things), we would like to design the network for high performance and scalable support of fine-grained policies.

## Slide 50: Characteristics of Cellular Core Networks
“North south” traffic pattern
Asymmetric edge
Traffic initiated from low-bandwidth access edge
Access Edge
Internet
Gateway Edge
~1K Users
~10K flows
~1 – 10 Gbps
~1 million Users
~10 million flows
~400 Gbps – 2 Tbps
Notes: How should we design SoftCell to support fine-grained policies? Can we just apply data center SDN solutions? Before we can answer the question, lets try to understand the characteristics of cellular networks.
First, the dominant traffic in cellular core networks are to or from the Internet, while in data centers, most traffic stays inside the data center. Second, cellular core networks have asymmetric edge. The access edge has lower bandwidth than the gateway edge. At the access, we are talking about 1K users, 10K flows and a few Gbps. At the gateway edge, we are talking about millions of Users, 10s of millions of flows and Tera bits per second. Third, traffic are initiated from low-bandwidth access edge.
First, cellular core networks have fine-grained and sophisticated policies. A cellular core network serves millions of customers with diverse needs.

## Slide 51: Challenge: Scalability
Packet classification: decide which service policy to be applied to a flow
  How to classify millions of flows per second?
Traffic steering: generate switch rules to implement policy paths, e.g. traversing a sequence of middleboxes
  How to implement million of paths?
    Limited switch flow tables: ~1K – 4K TCAM, ~16K – 64K L2/Ethernet
Network dynamics: setup policy paths for new users and new flow?
  How to handle million of control plane events per second?
Notes: SoftCell design faces key scalability challenges. First, we have to do packet classification. Given a flow, we have to decide which service policy to be applied to a flow. The challenge is how to classify millions of flows. Second, we have to generate switch rules to implement policy paths. A policy path needs to go through a sequence of middleboxes. As switches have limited flow table size, how to implement millions of paths in switches is a big challenge. Third, users and M2M devices come and go. They generate millions of control plane events per second. How to scalably handle them is challenging.

## Slide 52: SoftCell Design
Scalable system design
  Classifying flows at access edge
  Offloading controller tasks to switch local agent
Intelligent algorithms
  Enforcing policy consistency under mobility
  Multi-dimension aggregation to reduce switch rule entries
~1K Users
~10K flows
~1 – 10 Gbps
Gateway Edge
~1 million Users
~10 million flows
~up to 2 Tbps
Access Edge
Controller
LA
LA
LA
LA
Notes: We will apply the principle of design-in-the-large to address the challenges. We leverage the strength of the numerous access switches. In our system design, we move the packet classification function to the access edge. We offload controller tasks to switch local agent. For example, we can cache service policies. We do not need the controller involvement for flows which matches cached policies.
We use intelligent algorithms to enforce policy consistency under mobility and reduce the number of rules we put in switches.
We would like to move the service functions out of P-GW. To support fine-grained polices, we will need intelligent algorithms to minimizes the number of service routing entries in switch tables.

## Slide 53: Multi-Dimensional Aggregation
Use multi-dimensional tags rather than flat tags
Exploit locality in network topology and traffic pattern
Selectively match on one or multiple dimensions
  Supported by the multiple tables in today’s switch chipset
Policy Tag
BS ID
User ID
Aggregate flows going to the same Users.
Aggregate flows going to the same (group of) base stations
Aggregate flows that share a common policy (even across Users and BSs)
Notes: Let me show you the basic idea of multi-dimensional aggregation. We aggregate in three dimensions, policy tag, BS ID and UE ID. Policy tag aggregate flows that share a common policy, even across devices or base stations. BS ID aggregates flows going to the same base station. UE ID aggregates flows going to the same device. This is especially useful in UE handoff. Multi-dimensional tags allow us to exploit locality in the network. And we can selectively match on one or multiple dimensions in order to further reduce flow table size.

## Slide 54: Location-Based Hierarchical IP Address
BS 1
BS 2
BS 3
BS 4

## Slide 55: Location-Based Hierarchical IP Address
BS ID: an IP prefix assigned to each base station
BS 1
BS 2
BS 3
BS 4
10.0.0.0/16
10.1.0.0/16
10.2.0.0/16
10.3.0.0/16
10.1.0.7
192.168.0.5
UE ID
BS ID
UE ID: an IP suffix unique under the BS ID

## Slide 56: Route to different BSs with BS ID
Forward to base station with prefix matching
Can aggregate nearby BS IDs
10.0.0.0/16
10.1.0.0/16
BS 1
BS 2
Match | Action
10.0.0.0/16 | Forward to BS 1
10.1.0.0/16 | Forward to BS 2
Match | Action
10.0.0.0/15 | Forward to Switch 3
SW 4
SW 3
SW 2
SW 1

## Slide 57: MB load balancing with policy tag and BS ID
BS 1
BS 2
BS 3
BS 4
Transcoder 1
10.0.0.0/16
10.1.0.0/16
10.2.0.0/16
10.3.0.0/16
SW 1
SW 4
SW 3
Transcoder 2
SW 2
SW 5
Notes: Cannot do with VLAN

## Slide 58: MB load balancing with policy tag and BS ID
BS 1
BS 2
BS 3
BS 4
10.0.0.0/16
10.1.0.0/16
10.2.0.0/16
10.3.0.0/16
Match | Action
tag1, 10.2.0.0/15 | Forward to Transcoder 2
Transcoder 1
Transcoder 2
SW 1
SW 4
SW 3
SW 2
SW 5
Match | Action
tag1, 10.0.0.0/15 | Forward to Transcoder 1
10.2.0.0/15 | Forward to Switch 5
Notes: Cannot do with VLAN

## Slide 59: Policy Consistency
UE Mobility: frequent, unplanned
Policy consistency:
  Ongoing flows traverse the same sequence of middlebox instances, even in the presence of UE mobility
  Crucial for stateful middleboxes, e.g., stateful firewall

## Slide 60: Policy Consistency
An ongoing flow traverses stateful Firewall 1 before handoff
  Use 10.0.0.7 (old IP under BS1), go via the old path
New Flow can go via stateful Firewall 2
  Use 10.1.0.11 (new IP under BS2), go via the new path
BS 1: 10.0.0.0/16
192.168.0.5
192.168.0.5
Old flow
Old Path
Old Flow
10.0.0.7
New Flow
New Flow
10.1.0.11
New Path
BS 2: 10.1.0.0/16
Firewall 1
Firewall 2
10.0.0.7
10.1.0.11
Handoff

## Slide 61: Multi-Dimensional Identifier Encoding
Encode multi-dimensional identifiers to source IP and source port
Return traffic from the Internet:
  Identifiers are implicitly piggybacked in destination IP and destination port
Commodity chipsets (e.g., Broadcom) can wildcard on these bits
Policy Tag
BS ID
UE ID
Src IP
Src Port
BS ID
UE ID
Tag
Flow ID
Encode
Notes: Don’t use flat tags
note that each UE has (say) 10 flows, so there is plenty of space in the TCP/UDP port number for the tag. even if all ten flows go to the same external service, you'd still have a ton of bits left to store the tag.
somewhere you should mention that, although OpenFlow 1.0 only does prefix matching on IP addresses and TCP/UDP port numbers, today's commodity chipsets (e.g., BroadCom Trident chipset) can wildcard on any of those bits, and as such is not limited to prefix matching.

## Slide 62: Scalable Data Plane Summary
Steering Fabric
Packet classification based on service policy
Encoding results to packet headers
Traffic steering based on traffic management policy
Selectively multi-dimensional aggregation
Simple forwarding
based on multi-dimensional tags

## Slide 63: Control Plane Load
Internet
Packet classification
Handle every flow
Frequent switch update
Multi-dimensional aggregation
Handle every policy path
Infrequent switch update
Notes: Finally, let’s take a look at the control plane load.
The access edge does packet classification.
So it has to handle every flow.
The switches are updated very frequently.
In the core, it only needs to setup up policy paths.
So the switches are updated less frequently.
Handling all these switch update in one controller can overwhelm the controller.

## Slide 64: Summary
SoftCell uses commodity switches and middelboxes to build flexible and cost-effective cellular core networks
SoftCell achieves scalability with
Data Plane
Control Plane
Asymmetric Edge Design
Multi-dimensional Aggregation
Hierarchical Controller Design
Exploit multi-stage tables in modern switches
  Reduce m×n rules to m+n rules
Notes: In conclusion, CellSDN uses commodity switches and middleboxes to build flexible and cost-effective cellular core networks.
It supports fine-grained service policies and traffic management policies.
It achieves scalability with asymmetric edge design, multi-dimensional aggregation and hierarchical controller.

## Slide 65: Outline
Review of SDN Security
SDN Wireless Networks
  Motivation
  Data Plane Abstraction:
    OpenRadio
    PRAN
  Control Plane Architecture
    Radio Access Networks: SoftRAN
    Core Networks: SoftCell
    Cellular WAN: SoftMoW

## Slide 66: LTE Cellular Network Architecture
access
core
Packet Data Network Gateway
Serving Gateway
Internet
Serving Gateway
Base Station (BS)
User Equipment (UE)
Notes: This figure shows the architecture of today’s cellular core networks. User equipment connect to base stations via radio channels.
Base stations connect to the Internet via the cellular core network. There are two main components in the cellular core network, serving gateway and packet data network gateway.

## Slide 67: Current Mobile WANs
Organized into rigid and very large regions
Minimal interactions among regions
Leads to poor user experience and poor resource utilization
Two Regions

## Slide 68: SoftMoW Solution
Hierarchically builds up a network-wide control plane
  Lies in the family of recursive SDN designs (e.g. XBAR, ONS’13)
In each level, abstracts both control and data planes and exposes a set of “dynamically-defined” logical components to the control plane of the level above.
  Virtual Base stations (VBS), Gigantic Switches (GS), and Virtual Middleboxes (VMB)
Core Net
GS
Latency Matrix
RadioAccess Network
VBS
Union of Coverage
Policy
VMB
Sum of capacities

## Slide 69: SoftMoW Solution
New Dynamic Feature: In each level, the control logic can modify its logical components for optimization purposes
  E.g., merge/spilt and move operations
Move and Split
Merge/Split

## Slide 70: First Level-SoftMoW Architecture
Replace inflexible and expensive hardware devices (i.e., PGW, SGW) with SDN switches
Perform distributed policy enforcement using middle-box instances
Partition the network into independent and dynamic logical regions
A child controller manages the data plane of each regions
Bootstrapping phase:
based on location and processing capabilities of child controllers

## Slide 71: Second Level-SoftMoW Architecture
A parent runs a global link discovery protocol
  Inter-region links are not detected by BDDP and LLDP
A parent participates in the inter-domain routing protocol
A parent builds virtual middlebox chains and egress-point policies, and dictates to GSs
Notes: Add inter-domain routing protocol.

## Slide 72
Southbound API
Northbound API
Eastbound API
Topology Discovery
Path Implementation
Routing
NIB
Core Services
Topology Abstraction
RecA
Agent
Region Optimization
Mobility
…
Operator Applications
SoftMoW Controller
To Parent Controller
G-switch
G-BS
Controller Architecture

## Slide 73: Recursive Link Discovery Protocol

## Slide 74: Path Implementation
Latency (P1,E2)=300
Latency (P1,E4)=100
Web
Voice
GS Rules
A parent pushes a global label into each traffic group
Child controllers perform label swapping
  Ingress point: pop the global label and push some local labels for intra-region paths
  Egress point: pop the local labels and push back the global label
Push W
Pop W
Push W
Push W
Push W2
Push W1
Pop W2
Pop W
Pop W1

## Slide 75: Time-of-day Handover Optimization
Handover graph
Q: How can an operator reduce inter-region handovers in peak hours?
Abstraction update
GS Rule:
Move Border VBS1
coordination

## Slide 76: Summary
SoftMoW:
Brings both simplicity and scalability to the control plane of very large cellular networks
  decouples control and data planes at multiple levels ( focused only on two levels here)
Makes the deployment and design of network-wide applications feasible
  E.g., seamless inter-region mobility, time-of-day handover optimization, region optimization, and traffic engineering

## Slide 77: Conclusion and Future Work
Software defined cellular networks address fundamental limitations of current cellular architecture
  Control plane abstractions: 3D resource grid, big base station, virtual data plane
  Intelligent algorithms in the control plane to achieve global objects: interference management, traffic engineering
Future work on software defined cellular networks
  Security
  Scalable real-time monitoring and analytics

## Slide 78: Questions?