## Slide 1: Software Defined Networking COMS 6998-10, Fall 2014
Instructor: Li Erran Li (lierranli@cs.columbia.edu)
http://www.cs.columbia.edu/~lierranli/coms6998-10SDNFall2014/
9/15/2014: SDN Basics

## Slide 2: Outline
Review of previous lecture
SDN Basics
  Concepts
  OpenFlow
  Controller: Floodlight
  OF-Config
  Mininet

## Slide 3: Review of Previous Lecture
What is the control plane of a network?
  The functions in the network that control the behavior of the network, e.g., network paths, forwarding behavior
What is the data plane of a network?
  The functions in the network that are responsible for forwarding or not forwarding traffic. Typically, the data plane is instantiated as forwarding tables in routers, switches, firewalls, and middleboxes

## Slide 4: Review of Previous Lecture (Cont’d)
Which network first had the separation of control plane and data plane?
  The telephone network, specifically AT&T introduced then Network Control Point in 1981 to support a wide range of network applications such as 800 Service and Calling Card Service.
Why separate control?
  More rapid innovation: control logic is not tied to hardware
  Network wide view: easier to infer and reason about network behavior
  More flexibility: can introduce services more rapidly

## Slide 5: Review of Previous Lecture
What is the definition of SDN?
  The separation of control plane from data plane
  A specific SDN: configuration, distribution and forwarding abstraction
What is one API between control plane and data plane?
  OpenFlow protocol

## Slide 6: Outline
Review of previous lecture
SDN Basics
  Concepts
  OpenFlow
  Controller: Floodlight
  OF-Config
  Mininet

## Slide 7: SDN in a Nutshell
SDN is defined precisely by these three abstractions
  Distribution, forwarding, configuration
SDN not just a random good idea…
  Fundamental validity and general applicability
SDN may help us finally create a discipline
  Abstractions enable reasoning about system behavior
  Provides environment where formalism can take hold….
OK, but what are these abstractions?
Source: Scott Shenker, UC Berkeley
9/8/14
Software Defined Networking (COMS 6998-10)

## Slide 8: 1. Distributed State Abstraction
Shield control mechanisms from state distribution
  While allowing access to this state
Natural abstraction: global network view
  Annotated network graph provided through an API
Implemented with “Network Operating System”
Control mechanism is now program using API
  No longer a distributed protocol, now just a graph algorithm
  E.g. Use Dijkstra rather than Bellman-Ford
Source: Scott Shenker, UC Berkeley
9/15/14
Software Defined Networking (COMS 6998-10)

## Slide 9: Software Defined Network (SDN)
Control Program
Network OS
Global Network View
Traditional Control Mechanisms
Network of Switches and/or Routers
Distributed algorithm running between neighbors
e.g. routing, access control
Source: Scott Shenker, UC Berkeley
9/15/14
Notes: Project 2 would have been trivial: Dijkstra on a graph.

## Slide 10: Major Change in Paradigm
No longer designing distributed control protocols
  Design one distributed system (NOS)
  Use for all control functions
Now just defining a centralized control function
  Configuration = Function(view)
Source: Scott Shenker, UC Berkeley
9/15/14
Software Defined Networking (COMS 6998-10)
Notes: Stop. Does everyone get this. Unless I see everyone’s hands up, I am not going further.

## Slide 11: 2. Specification Abstraction
Control program should express desired behavior
It should not be responsible for implementing that behavior on physical network infrastructure
Natural abstraction: simplified model of network
  Simple model with only enough detail to specify goals
Requires a new shared control layer:
  Map abstract configuration to physical configuration
This is “network virtualization”
Source: Scott Shenker, UC Berkeley
9/8/14
Software Defined Networking (COMS 6998-10)
Notes: Just like VMs. Virtualizing network with abstractions, rather than physical topology.

## Slide 12: Simple Example: Access Control
Global
Network View
Abstract Network
Model
How
What
Source: Scott Shenker, UC Berkeley
9/15/14
Notes: What is access control?

## Slide 13: Software Defined Networks
Network OS
Global Network View
Abstract Network Model
Control Program
Network Virtualization
Source: Scott Shenker, UC Berkeley
9/15/14

## Slide 14: What Does This Picture Mean?
Write a simple program to configure a simple model
  Configuration merely a way to specify what you want
Examples
  ACLs: who can talk to who
  Isolation: who can hear my broadcasts
  Routing: only specify routing to the degree you care
    Some flows over satellite, others over landline
  TE: specify in terms of quality of service, not routes
Virtualization layer “compiles” these requirements
  Produces suitable configuration of actual network devices
NOS then transmits these settings to physical boxes
Source: Scott Shenker, UC Berkeley
9/15/14
Software Defined Networking (COMS 6998-10)

## Slide 15: Software Defined Networks
Network OS
Global Network View
Abstract Network Model
Control Program
Network Virtualization
Specifies behavior
Compiles to topology
Transmits to switches
Source: Scott Shenker, UC Berkeley
9/15/14

## Slide 16: Outline
Review of previous lecture
SDN Basics
  Concepts
  OpenFlow
  Switches and Controllers
  OF-Config
  Mininet

## Slide 17: OpenFlow
Why OpenFlow?
How does OpenFlow work?

## Slide 18: Why OpenFlow?

## Slide 19: The Ossified Network
Million of lines of source code
5400 RFCs
Barrier to entry
Billions of gates
Bloated
Power Hungry
Many complex functions baked into the infrastructure
    OSPF, BGP, multicast, differentiated services, Traffic Engineering, NAT, firewalls, MPLS, redundant layers, …
An industry with a “mainframe-mentality”, reluctant to change
Specialized Packet Forwarding Hardware
Operating
System
Feature
Feature
Routing, management, mobility management, access control, VPNs, …
19
Notes: 19

## Slide 20: Research Stagnation
Lots of deployed innovation in other areas
  OS: filesystems, schedulers, virtualization
  DS: DHTs, CDNs, MapReduce
  Compilers: JITs, vectorization
Networks are largely the same as years ago
  Ethernet, IP, WiFi
Rate of change of the network seems slower in comparison
  Need better tools and abstractions to demonstrate and deploy
Notes:   In these other areas, you can real systems on top of high-quality, open platforms, and you don’t need to reinvent the wheel

## Slide 21: Closed Systems (Vendor Hardware)
Stuck with interfaces (CLI, SNMP, etc)
Hard to meaningfully collaborate
Need a fully open system – a Linux equivalent

## Slide 22: OpenFlow: a pragmatic compromise
+ Speed, scale, fidelity of vendor hardware
+ Flexibility and control of software and simulation
Vendors don’t need to expose implementation
Leverages hardware inside most switches today (ACL tables)

## Slide 23: How does OpenFlow work?
23

## Slide 24
Ethernet Switch

## Slide 25: Ethernet Switch
Data Path (Hardware)
Control Path
Control Path (Software)

## Slide 26
Data Path (Hardware)
Control Path
OpenFlow
OpenFlow Controller
OpenFlow Protocol (SSL/TCP)

## Slide 27
Controller
PC
Hardware
Layer
Software
Layer
Flow Table
MAC
src
MAC
dst
IP
Src
IP
Dst
TCP
sport
TCP
dport
Action
OpenFlow Client
*
*
5.6.7.8
*
*
*
port 1
port 4
port 3
port 2
port 1
1.2.3.4
5.6.7.8
OpenFlow Example

## Slide 28: OpenFlow Basics Flow Table Entries
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
L4
sport
L4
dport
Rule
Action
Stats
Forward packet to zero or more ports
Encapsulate and forward to controller
Send to normal processing pipeline
Modify Fields
Any extensions you add!
+ mask what fields to match
Packet + byte counters
VLAN
pcp
IP
ToS
Notes: Now I’ll describe the API that tries to meet these goals.

## Slide 29: Examples
Switching
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
00:1f:..
*
*
*
*
*
*
*
port6
Flow Switching
port3
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
00:20..
00:1f..
0800
vlan1
1.2.3.4
5.6.7.8
4
17264
80
port6
Firewall
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
*
*
*
22
drop

## Slide 30: Examples
Routing
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
5.6.7.8
*
*
*
port6
VLAN Switching
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
vlan1
*
*
*
*
*
port6,
port7,
port9
00:1f..

## Slide 31: Centralized vs Distributed Control Both models are possible with OpenFlow
Centralized Control
OpenFlow
Switch
OpenFlow
Switch
OpenFlow
Switch
Controller
Distributed Control
OpenFlow
Switch
OpenFlow
Switch
OpenFlow
Switch
Controller
Controller
Controller

## Slide 32: Flow Routing vs. Aggregation Both models are possible with OpenFlow
Flow-Based
Every flow is individually set up by controller
Exact-match flow entries
Flow table contains one entry per flow
Good for fine grain control, e.g. campus networks
Aggregated
One flow entry covers large groups of flows
Wildcard flow entries
Flow table contains one entry per category of flows
Good for large number of flows, e.g. backbone

## Slide 33: Reactive vs. Proactive (pre-populated) Both models are possible with OpenFlow
Reactive
First packet of flow triggers controller to insert flow entries
Efficient use of flow table
Every flow incurs small additional flow setup time
If control connection lost, switch has limited utility
Proactive
Controller pre-populates flow table in switch
Zero additional flow setup time
Loss of control connection does not disrupt traffic
Essentially requires aggregated (wildcard) rules

## Slide 34: What can you not do with OpenFlow ver1.0
Non-flow-based (per-packet) networking
  ex. Per-packet next-hop selection (in wireless mesh)
  yes, this is a fundamental limitation
  BUT OpenFlow can provide the plumbing to connect these systems
Use all tables on switch chips
  yes, a major limitation (cross-product issue)
  BUT OpenFlow 1.3 version will expose these

## Slide 35: What can you not do with OpenFlow ver1.0
New forwarding primitives
  BUT provides a nice way to integrate them through extensions
New packet formats/field definitions
  BUT a generalized OpenFlow (2.0) is on the horizon
Optical Circuits
  BUT efforts underway to apply OpenFlow model to circuits
Low-setup-time of individual flows
  BUT can push down flows proactively to avoid delays

## Slide 36: Where it’s going
OF v1.3
  multiple tables: leverage additional tables
  tags and tunnels
  multipath forwarding
  per flow meters
OF v2+
  generalized matching and actions: protocol independent forwarding

## Slide 37: Outline
Review of previous lecture
SDN Basics
  Concepts
  OpenFlow
  Switches and Controllers
  OF-Config
  Mininet

## Slide 38: Switches and Controllers
OpenFlow switches and vendors
Controllers
  Floodlight

## Slide 39: OpenFlow building blocks
Controller
POX
Slicing
Software
FlowVisor
FlowVisor
Console
39
Applications
Traffic Engineering
Firewall
Mobility
Load Balancing
NetFPGA
Broadcom
Ref. Switch
OpenWRT
Commercial Switches
Software switches and experimental platforms
OpenFlow
Switches
ONOS
Monitoring/ debugging tools
oflops
ndb
OpenVSwitch
HP, NEC, Pronto, Juniper.. and many more
Floodlight
OpenDayLight
Ryu
Frenetic
Notes: There are components at different levels that work together in making it work
The commercial switch details will follow in next slide
There are a plethora of applications possible. I only list those available at Stanford

## Slide 40: Current SDN hardware
Ciena Coredirector
NEC IP8800
More coming soon...
Juniper MX-series
HP Procurve 5400
Pronto 3240/3290
WiMax (NEC)
PC Engines
Netgear 7324
40

## Slide 41: Commercial Switch Vendors
Model | Virtualize | Notes | 
HP Procurve 5400zl or 6600 | 1 OF instance per VLAN | LACP, VLAN and STP processing before OpenFlow Wildcard rules or non-IP pkts processed in s/w Header rewriting in s/w CPU protects mgmt during loop | 
NEC IP8800 | 1 OF instance per VLAN | OpenFlow takes precedence Most actions processed in hardware MAC header rewriting in h/w | 
Pronto 3240 or 3290 with Pica8 or Indigo firmware | 1 OF instance per switch | No legacy protocols (like VLAN and STP) Most actions processed in hardware MAC header rewriting in h/w | 
41
Notes: All support ver 1.0
All have approx 1500 flow table entry limit

## Slide 42: Controller Vendors
Vendor | Notes
Nicira’s NOX | Open-source GPL C++ and Python Researcher friendly
Nicira’s ONIX | Closed-source Datacenter networks
Ryu | Open-source GPL Python
Vendor | Notes
Stanford’s Beacon | Open-source Researcher friendly Java-based
BigSwitch controller | Ha open source version Based on Beacon Enterprise network
OpenDayLight | Open-source Based on Java
Frenetic | Open-source Written in functional programming languages
42

## Slide 43: Floodlight Architecture
Overview
  Floodlight is a collection of modules
  Some modules (not all) export services
  All modules in Java
  Rich, extensible REST API
DeviceManager
(IDeviceService)
FloodlightProvider
(IFloodlightProviderService)
TopologyManager
(ITopologyManagerService)
RestServer
(IRestApiService)
StorageSource
(IStorageSourceService)
Forwarding
StaticFlowPusher
(IStaticFlowPusherService)
LinkDiscovery
(ILinkDiscoveryService)
VirtualNetworkFilter
(IVirtualNetworkFilterService)
Source: Big Switch Networks
Notes: Our topology, device manager know about host attachment points and make it possible to deal with integrating openflow and non openflow networks.

## Slide 44: Floodlight Architecture
Module descriptions
DeviceManager
(IDeviceService)
FloodlightProvider
(IFloodlightProviderService)
TopologyManager
(ITopologyManagerService)
RestServer
(IRestApiService)
StorageSource
(IStorageSourceService)
Forwarding
StaticFlowPusher
(IStaticFlowPusherService)
LinkDiscovery
(ILinkDiscoveryService)
VirtualNetworkFilter
(IVirtualNetworkFilterService)
DB style storage (queries, etc)
Modules can access all data and subscribe to changes
44
Computes shortest path using Dijsktra
Keeps switch to cluster mappings
Installs flow mods for end-to-end routing
Handles island routing
Tracks hosts on the network
MAC -> switch,port, MAC->IP, IP->MAC
Implements via Restlets (restlet.org)
Modules export RestletRoutable
Supports the insertion and removal of static flows
REST-based API
Maintains state of links in network
Sends out LLDPs
Create layer 2 domain defined by MAC address
Used for OpenStack / Quantum
Translates OF messages to Floodlight events
Managing connections to switches via Netty
Source: Big Switch Networks
Notes: Our topology, device manager know about host attachment points and make it possible to deal with integrating openflow and non openflow networks.

## Slide 45: Floodlight Programming Model
Northbound APIs
Switch
Switch
vSwitch
Switch
IFloodlight-Module
External Application
REST
IFloodlightModule
Java module that runs as part of Floodlight
Consumes services and events exported by other modules
  OpenFlow (ie. Packet-in)
  Switch add / remove
  Device add /remove / move
  Link discovery
External Application
Communicates with Floodlight via REST
  Quantum / Virtual networks
  Normalized network state
  Static flows
Floodlight Controller

## Slide 46: REST API Reference
Network State
List Hosts
List Links
List Switches
GetStats (DPID)
GetCounters (OFType…)
A moving target…but…
Static Flows
Add Flow
Delete Flow
List Flows
RemoveAll Flows
Virtual Network
Create Network
Delete Network
Add Host
Remove Host
User Extensions
…
Floodlight Controller
Switch
Switch
vSwitch
Switch
Source: Big Switch Networks

## Slide 47: Floodlight Installation and Tutorial
Download
  http://www.projectfloodlight.org/getting-started/
Tutorial:
  http://docs.projectfloodlight.org/display/floodlightcontroller/Tutorials

## Slide 48: Programming Floodlight
Fine-grained ability to push flows over REST
Access to normalized topology and device state
Extensible access to add new APIs
Using the REST API

## Slide 49: Programming Floodlight
Handle OpenFlow messages directly (ie. PacketIn)
Expose services to other modules
Add new REST APIs
Creating a module
Source: Big Switch Networks

## Slide 50: Outline
Review of previous lecture
SDN Basics
  Concepts
  OpenFlow
  Switches and Controllers
  OF-Config
  Mininet

## Slide 51
Bootstrap OpenFlow network
  Switch connects to controller
  Controller(s) to connect to must be configured at switches
Allocate resources within switches
  Ports
  Queues
  . . .
OpenFlow configuration and Management Protocol
controller
switch
switch
switch
switch
controller

## Slide 52
Configuration Point
  Source of switch configuration
OpenFlow Capable Switch
  Hosts one or more logical switches
OpenFlow configuration and Management Protocol: Reference Model
OpenFlow
Capable Switch
resources (ports, queues)
OpenFlow Controller
OpenFlow Logical Switch
  instance of an OpenFlow Switch
OF Logical Switch
OF Logical Switch
Configuration Point
Configuration Point
OF-CONFIG
Configuration Point
OpenFlow
Controller
Configuration Point
OpenFlow
Controller
OpenFlow
OpenFlow
using IETF Netconf & XML data models

## Slide 53
OF-CONFIG 1.0 (Jan 2012) based on OpenFlow 1.2
  assigning controllers to logical switches
  retrieving assignment of resources to logical switches
  configuring some properties of ports and queues
OF-CONFIG 1.1 (Apr 2012) based on OpenFlow 1.3
  added controller certificates and resource type "table"
  retrieving logical switch capabilities signaled to controller
  configuring of tunnel endpoints
OF-CONFIG 1.1.1 (Aug 2012) based on OpenFlow 1.3.1
  consolidation of version 1.1, fixing small inconsistencies
OF-CONFIG 1.2 (early 2013) based on OpenFlow 1.3.1
  features still under discussion, candidates include
    retrieving capable switch capabilities, configuring logical switch capab.
    assigning resources to logical switches
    simple topology detection
    event notification
OF-CONFIG Scope and Releases
WG established
in Sep 2011

## Slide 54
Netconf was chosen as management protocol
  not necessarily accepted as ideal solution
  still discussing alternatives
XML schema was chosen as modeling language
  Yang is also used, but XML is normative
  normative XML schema generated from Yang code
So far, the focus has been on configuration
  bootstrap of an OpenFlow network is the obvious first thing to do
Use of Netconf and Yang

## Slide 55: Outline
Review of previous lecture
SDN Basics
  Concepts
  OpenFlow
  Switches and Controllers
  OF-Config
  Mininet

## Slide 56: Mininet
Machine-local virtual network
  great dev/testing tool
Uses linux virtual network features
  Cheaper than VMs
Arbitrary topologies, nodes

## Slide 57: Mininet (Cont’d)
Rapidly prototype, develop and test
  Interestingly-sized networks (16-100 nodes) start up in seconds
  No lengthy lab reconfiguration or rebooting required
  Always-accessible network resources, in any topology, at essentially no cost
  Designs that work on Mininet transfer seamlessly to hardware for full speed operation

## Slide 58: Mininet (Cont’d)
Repeatably test, analyze, and predict network behavior
  Easy replication of experimental and test results
  Examine effects of code or network changes before testing/deploying on hardware
  Allows automated system-level tests and experiments
  Recreate real-world network and test cases for a variety of topologies and configurations

## Slide 59: Mininet (Cont’d)
Quickly get up and running
  Free and permissively licensed (BSD)
  Minimal hardware requirements
  Accessible to novices thanks to simple CLI
  Smooth learning curve thanks to walkthrough, tutorial, examples and API documentation
  Strong users and support community

## Slide 60: Mininet (Cont’d)
Download: http://mininet.org/download/
Tutorial: http://mininet.org/walkthrough/
Python API: https://github.com/mininet/mininet/wiki/Introduction-to-Mininet
Remote (host computer) access of mininet VM
  ssh –Y mininet@[minnet VM IP]
    Use ifconfig –a to find mininet VM IP

## Slide 61: Mininet (Cont’d)
Basic commands:
  Display an xterm for switch s1
    mininet> xterm s1
  Inspect flow tables at switch xterm
    dpctl dump-flows tcp:127.0.0.1:6634
To view OpenFlow protocol messages, at mininet-VM xterm:
  sudo wireshark &
  Capture the interface to controller
  In wireshark filter box, enter filter to filter OpenFlow messages: of

## Slide 62: Mininet (Cont’d)
Basic commands:
  Create a network consists of one OpenvSwitch, three hosts and is controlled by a remote controller with IP address 192.168.56.1
    sudo mn --topo single,3 --controller remote,ip=192.168.56.1 --switch ovsk
  mininet> help
  mininet> dump nodes
  mininet> h1 ping h2

## Slide 63: Questions?