## Slide 1: Software Defined Networking COMS 6998-10, Fall 2014
Instructor: Li Erran Li (lierranli@cs.columbia.edu)
http://www.cs.columbia.edu/~lierranli/coms6998-10SDNFall2014/
10/13/2014: SDN Updates

## Slide 2: Midterm Date
Two options
  Oct 27
  Nov 10
A quick show of hands
Result: midterm on Nov 10

## Slide 3: Outline
Announcement: project proposal due Oct 23
Review of Previous Lecture
  Verification of network properties
  Verification of controller correctness
  Verification of software data plane
SDN Updates
  Per Switch Consistent and Minimal Updates
  Network-wide Updates
    Consistent Updates
    Congestion-Free Updates
    Network Partition

## Slide 4: Review of Previous Lecture (Cont’d)
NetPlumber graph:
  Creates a dependency graph of all forwarding rules in the network and uses it to verify policy
  Nodes: forwarding rules in the network
  Directed Edges: next hop dependency of rules and intra table dependency
R1
R2
Switch 1
Switch 2
Notes: Internally, NetPlumber creates a dependency graph of al rules in the network and uses it to verify network policy. The nodes of this graph are forwarding rules of networks and directed edges show the next hop relationship between edges, meaning that there is an edge from Rule R1 to R2, if there is a physical link from switch 1 to switch 2 in the network and also the input header space of R1, has some intersection with the input header space of R2. In another word, all this next hop dependency is saying is that there is at least one packet header processed by R1, can be processed next by R2.

## Slide 5: Review of Previous Lecture (Cont’d)
S
S
0
1
X
X
Source: P. Kazemian, Stanford
1 0 0 1
1 0 X X
Example NetPlumber graph
Where is the missing edge?
Notes: To understand how NetPlumber works, Let’s look at one simple example, consisting of these 4 switches. NP look at the forwarding rules of each of these switch and for each rule, create one rule node in the net plumber graph. We use a completely visual representation of the rules in this example. We assume that headers are only 4 bits long. The match pattern of each rule that specify which packets should be processed by the rule is represented by these 8 squares. The upper square corresponds to value 0, and the lower squares corresponds to value 0. For example this rule matches on 1001 headers and forward them to the green box. This one matches on 01xx headres, rewrite them to 001x and forward ot the green box. NP puts one node for every rule in the switches. Then it creates directed edges between the rules. For example we have this directed edge because the output headers of this this rule has some intersection with input headers of this rule

## Slide 6: Review of Previous Lecture (Cont’d)
S
S
0
1
X
X
Source: P. Kazemian, Stanford
1 0 0 1
1 0 X X
Example NetPlumber graph
Notes: To understand how NetPlumber works, Let’s look at one simple example, consisting of these 4 switches. NP look at the forwarding rules of each of these switch and for each rule, create one rule node in the net plumber graph. We use a completely visual representation of the rules in this example. We assume that headers are only 4 bits long. The match pattern of each rule that specify which packets should be processed by the rule is represented by these 8 squares. The upper square corresponds to value 0, and the lower squares corresponds to value 0. For example this rule matches on 1001 headers and forward them to the green box. This one matches on 01xx headres, rewrite them to 001x and forward ot the green box. NP puts one node for every rule in the switches. Then it creates directed edges between the rules. For example we have this directed edge because the output headers of this this rule has some intersection with input headers of this rule

## Slide 7: Review of Previous Lecture (Cont’d)
Frenetic DSL
Frenetic
OX
implemented using
implemented using
Domain-specific language
predicates and policies
monitoring
mac learning
network address translation
OCaml embedding
predicates and policies
queries
OCaml OpenFlow Platform
similar to Nox, Pox, Floodlight, etc.
Frenetic
Ox
The System
Source: Nate Foster, Cornell

## Slide 8: Review of Previous Lecture (Cont’d)
NetKAT
Flow tables
OpenFlow messages
Compiler
Run-time system
Optimizer
Each level of abstraction formalized in Coq
Machine-checked proofs that the transformations between levels preserve semantics
Code extracted to OCaml and deployed with real switch hardware
Certified NetKAT Controller
Source: Nate Foster, Cornell

## Slide 9: Review of Previous Lecture (Cont’d)
Verification of software dataplane
Proof of bounded execution property
  no more than X instructions per packet
Proof of crash-freedom property
  No packet will cause the pipeline to abort
Need to handle
  Pipelines
  Loops (may exceed time constraint)
  Data structures (can crash)

## Slide 10
m elements
intrusion detection
application acceleration
do not share mutable state
verification time ∼ 2 n m
n branches
per element
IP forwarding

## Slide 11
intrusion detection
application acceleration
do not share mutable state
verification time ∼ m 2 n
...
assert(src != dst);
...
IP forwarding

## Slide 12: Review of Previous Lecture (Cont’d)
Rule: pipeline structure
  distinct packet-processing elements
  do not share mutable state
Effect: compose at the element level
  can reduce #paths from ∼ 2 n m
  to ∼ m 2 n
Pipeline decomposition

## Slide 13
IP options

## Slide 14
m options
...
option #1
option #m
option #2
verification time ∼ n m
n option
types

## Slide 15
m options
option #1
option #m
option #2
...
...
verification time ∼ m n
n option
types
little state sharing across iterations

## Slide 16: Review of Previous Lecture (Cont’d)
Rule: “mini-pipeline” structure
  little state shared across iterations
  made explicit by the programmer
Effect: compose at the iteration level
  can reduce #paths from ∼ n m
  to ∼ m n
Loop decomposition

## Slide 17: Review of Previous Lecture (Cont’d)
Use pre-allocated arrays
  no dynamic memory (de)allocation
  hash table, longest prefix match
Trade-off memory for “verifiability”
  at least as fast (array lookups)
  but larger memory footprint (pre-allocation)
Verified data structures

## Slide 18: Outline
Announcement: project proposal due Oct 23
Review of Previous Lecture
  Verification of network properties
  Verification of controller correctness
  Verification of software data plane
SDN Updates
  Per Switch Consistent and Minimal Updates
  Network-wide Updates
    Consistent Updates
    Congestion-Free Updates
    Network Partition

## Slide 19: Updates Happen
Desired Invariants
No black-holes
No loops
No security violations
Network Updates
Maintenance
Failures
ACL Updates
Notes: Updates are a fact of life for network administrators. Configuration changes happen whenever an administrator brings device down for maintenance, performs traffic engineering, or does essentially anything on the network.

## Slide 20: Update one Switch
Priority | Predicate | Action
Priority | Predicate | Action
10 | SSH | Drop
5 | dst_ip = H1 | Fwd 1
5 | dst_ip = H2 | Fwd 2
Priority | Predicate | Action
5 | dst_ip = H1 | Fwd 1
Priority | Predicate | Action
5 | dst_ip = H1 | Fwd 1
5 | dst_ip = H2 | Fwd 2
update re-ordering
Priority | Predicate | Action
10 | SSH | Drop
Priority | Predicate | Action
10 | SSH | Drop
5 | dst_ip = H1 | Fwd 1
⊆
⊆
⊆
Distributed Programming: non-atomic table updates
Source: Nate Foster, Cornell

## Slide 21: Update one Switch (Cont’d)
Solution: insert barrier messages to enforce partial ordering of rule updates
Question: what is the algorithm?

## Slide 22: Minimal Number of Updates
Minimum dependency can be inferred from rule patterns
A
B
C
D
E
F
 | Pattern | Priority
A | <1, 2, *> | 5
B | <*, 2, 3> | 4
C | <1, *, 4> | 4
D | <1, *, 3> | 3
E | <*, *, 4> | 3
F | <*, *, 3> | 2
A
B
G
D
C
F
E
Old
New
 | Pattern | Priority
A | <1, 2, *> | 5
B | <*, 2, 3> | 4
G | <*, 2, 4> | 3
C | <1, *, 4> | 2
D | <1, *, 3> | 3
E | <*, *, 4> | 1
F | <*, *, 3> | 2

## Slide 23: Minimal Number of Updates (Cont’d)
With minimum dependency graph, one can always generate minimum-size flowtable update if priority value is continuous
A
B
C
D
E
F
 | Pattern | Priority
A | <1, 2, *> | 5
B | <*, 2, 3> | 4
C | <1, *, 4> | 4
D | <1, *, 3> | 3
E | <*, *, 4> | 3
F | <*, *, 3> | 2
 | Pattern | Priority
A | <1, 2, *> | 5
B | <*, 2, 3> | 4
G | <*, 2, 4> | 3-> 4.5
C | <1, *, 4> | 2 -> 4
D | <1, *, 3> | 3
E | <*, *, 4> | 1 -> 3
F | <*, *, 3> | 2
A
B
G
D
C
F
E
Take-away: Minimum dependency helps eliminate priority updates

## Slide 24: How to obtain minimum dependency
Restored from prioritized flowtable after compilation
  Incurs complicated header space computation
Constructed along with compilation
  Rule dependency can be recursively inferred from policy composition process
  Incurs little additional overhead over compilation
  See paper for the algorithm

## Slide 25: Maintaining Priority Value Distribution
Discrete priority values
  Integers ranging [0-65535] for OpenFlow
  If new rule is inserted between adjacent priority values, we have to shift existing rules to make room for them
Problem Statement
  Assign priority values for priority levels
  Objective: minimize the estimation of priority shifts
Online strategy
  Unknown future policy update sequence
Pattern | Priority
<1, 2> | 5 -> 3
<2, *> | 4 -> 2.5
<1, *> | 3 -> 2
<*, 2> | 3 -> 2
<3, *> | 2 -> 1.5
<*, *> | 1

## Slide 26: Outline
Announcement: project proposal due Oct 23
Review of Previous Lecture
  Verification of network properties
  Verification of controller correctness
  Verification of software data plane
SDN Update
  Per Switch Update
  Network-wide Updates
    Consistent Update
    Congestion-Free Update
    Network Partition

## Slide 27: Network Updates Are Hard
Source: M. Reitblatt, Cornell
Notes: Unfortunately, performing updates is quite tricky. Networks are large distributed systems and completing an update can take some time. Changes on one part of the network can begin affecting traffic before the full update has been rolled out, introducing forwarding loops, blackholes or worse.

## Slide 28: Network Update Abstractions
Goal
Tools for whole network update
Approach
Develop update abstractions
Endow them with strong semantics
Engineer efficient implementations
Source: M. Reitblatt, Cornell
Notes: Instead of having network administrators sit down and work out how to perform an update rule by rule, switch by switch, we instead propose they should use a simple abstraction that updates the entire network in one fell swoop. The abstraction will provide powerful, reasonable semantics that allow administrators to understand how the network will behave during update, and leave the exact implementation details to a runtime that figures out the most efficient way to perform the actual update.

## Slide 29: Example: Distributed Access Control
Security Policy
Src | Traffic | Action
 | Web | Allow
 | Non-web | Drop
 | Any | Allow
Traffic
F1
F2
F3
I
Source: M. Reitblatt, Cornell

## Slide 30: Naive Update
Security Policy
Src | Traffic | Action
 | Web | Allow
 | Non-web | Drop
 | Any | Allow
Traffic
F1
F2
F3
I
F1
F2
F3
I
Order
Source: M. Reitblatt, Cornell

## Slide 31: Use an Abstraction!
UPDATE
Security Policy
✓
✓
✓
Source: M. Reitblatt, Cornell

## Slide 32: Per-Switch Atomic Update?
Traffic
F1
F2
F3
Security Policy
Src | Traffic | Action
 | Web | Allow
 | Non-web | Drop
 | Any | Allow
I
Source: M. Reitblatt, Cornell
Notes: “As-if all the switches moved to the new configuration at the same time” Atomic Updates lead to Nuclear explosions

## Slide 33: Per-Packet Consistent Updates
Security Policy
Src | Traffic | Action
 | Web | Allow
 | Non-web | Drop
 | Any | Allow
Obeys policy:
Obeys policy:
Per-Packet Consistent Update
Each packet processed with old or new configuration, but not a mixture of the two.
Source: M. Reitblatt, Cornell

## Slide 34: Universal Property Preservation
Trace Property
Any property of a single packet’s path through the network.
Theorem: Per-packet consistent updates preserve all trace properties.
Examples of Trace Properties:
Loop freedom, access control, waypointing ...
Trace Property Verification Tools:
NetPlumber, ConfigChecker ...
Source: M. Reitblatt, Cornell
10/13/14
Notes: Emphasize universal guarantee: programmers don’t need to write down specific properties or specifications. ANY path property is preserved, without having to tell us what property you want “As it turns out”

## Slide 35: Formal Verification
Corollary: To check an invariant, verify the old and new configurations.
✓
Analyzer
✓
Analyzer
Security Policy
Security Policy
Verification Tools
Anteater [SIGCOMM ’11]
NetPlumber [SIGCOMM ’13]
ConfigChecker [ICNP ’09]
Source: M. Reitblatt, Cornell

## Slide 36: Mechanisms

## Slide 37: 2-Phase Update
Overview
Runtime instruments configurations
Edge rules stamp packets with version
Forwarding rules match on version
Algorithm (2-Phase Update)
Install new rules on internal switches, leave old configuration in place
Install edge rules that stamp with the new version number
update(config,topo)
Calculate rules,
generate messsages
Source: M. Reitblatt, Cornell
Notes: The natural question is: when can we perform a per-packet update? Is it always possible?
It turns out the answer is yes: we can always perform a per-packet update between configurations. There is a general mechanism, the 2-phase update mechanism, that always works, regardless of the configuration or topology.
The mechanism works by instrumenting the entire network configuration with version numbers. The rules are then predicated upon a packet having a specific version number.
To perform the update, first install the new configuration rules on the internal switches. Then, install rules on the edge switches that stamp incoming packets with the new version. Then, when all the old version packets are gone, delete the old configuration.

## Slide 38: 2-Phase Update in Action
Traffic
F1
F2
F3
I
Source: M. Reitblatt, Cornell

## Slide 39: Optimized Mechanisms
Optimizations
Extension: strictly adds paths
Retraction: strictly removes paths
Subset: affects small # of paths
Topological: affects small # of switches
Runtime
Automatically optimizes
Power of using abstraction
update(config,topo)
Calculate rules,
generate messsages
Source: M. Reitblatt, Cornell
Notes: Pronounce optimizations and explain that they reduce overhead in common situations

## Slide 40: Subset Optimization
Traffic
F1
F2
F3
I
Source: M. Reitblatt, Cornell
Notes: To make all of this concrete, lets consider the simple network here. It has 4 switches: an ingress switch on the left and 3 switches in the middle that perform filtering. Traffic flows from left to right and it’s connected to two external networks: a trusted white-hat network and an untrusted black-hat network. The network has a security policy that allows trusted white-hat traffic unrestricted access to the internal network on the right, and restricts the untrusted black-hat network to only send web traffic.
Note: Make example completely graphical (add ingress routing), remove text configurations

## Slide 41: Correctness
Example: 2-Phase Update
Install new rules on internal switches, leave old configuration in place
Install edge rules that stamp with the new version number
}
Unobservable
One-touch
}
Theorem: Unobservable + one-touch = per-packet.
Question: How do we convince ourselves these mechanisms are correct?
Solution: built an operational semantics, formalized our mechanisms and proved them correct
Source: M. Reitblatt, Cornell
Notes: To answer this question, we used a common technique from the PL community and built a formal model...
Maybe Q, Solution, Insight

## Slide 42: Implementation
Runtime
  NOX Library
  OpenFlow 1.0
  2.5k lines of Python
  update(config, topology)
  Uses VLAN tags for versions
  Automatically applies optimizations
Verification Tool
  Checks OpenFlow configurations
  Computation Tree logic (CTL) specification language to specify legal paths (e.g. waypoints) a packet may take
    CTL is a branching time temporal logic
  Uses NuSMV model checker
update(config,topo)
Source: M. Reitblatt, Cornell
Notes: Make other boxes more transparent/gray out

## Slide 43: Evaluation
Setup
  Mininet VM
Applications
  Routing and Multicast
Scenarios
  Adding/removing hosts
  Adding/removing links
  Both at the same time
Fattree
Small-world
Waxman
Question: How much extra rule space is required?
Topologies
Source: M. Reitblatt, Cornell
Notes: Thought: are these useful opts in practice? Ran simulations to test. Make set-up graphical, illustrate topos + set-up structure etc

## Slide 44: Results: Routing Application
Fattree
Small-world
Waxman
Source: M. Reitblatt, Cornell

## Slide 45: Conclusion
Update abstractions
  Per-packet
  Per-flow
Mechanisms
  2-Phase Update
  Optimizations
Formal model
  Network operational semantics
  Universal property preservation
Source: M. Reitblatt, Cornell
Notes: Without an update abstraction, you have two choices: either work very hard to figure out how to implement your update to preserve the properties you care about, or just throw your update at the network and hope it will work. With an update abstraction, you can just throw your update at the runtime and know it will work.

## Slide 46: Outline
Announcement: project proposal due Oct 23
Review of Previous Lecture
  Verification of network properties
  Verification of controller correctness
  Verification of software data plane
SDN Update
  Per Switch Consistent and Minimal Updates
  Network-wide Updates
    Consistent Updates
    Congestion-Free Updates
    Network Partition

## Slide 47: DCN is constantly in flux
Upgrade  Reboot
Traffic Flows
New Switch
Source: J. Liu, Yale
Notes: In data centers, applications generate traffic flows and rely on network to deliver them.
The traffic distribution of these flows can change with the updates in network.
For example, before shutting down a switch, we typically move flows on the switch out to other switches.
After the switch goes online again, we move the flows back.
For another example, when a new switch is connected into the network, we often conduct some existing flows to go through it to test it or make a use of it.

## Slide 48: DCN is constantly in flux
Virtual Machines
Traffic Flows
Source: J. Liu, Yale
Notes: While the network is in flux, applications’ behaviors are also changing the traffic distribution simultaneously.
For instance, an application owns some virtual machines and these virtual machines have some traffic flows with each other.
When the application decides migrate some virtual machines to other locations, the VM migration can reshape the traffic flows.
In production data center networks, updates like our examples are happening everyday.

## Slide 49: Network updates are painful for operators
Bob: An operator
Two weeks before update, Bob has to:
Coordinate with application owners
Prepare a detailed update plan
Review and revise the plan with colleagues
At the night of update, Bob executes plan by hands, but
Application alerts are triggered unexpectedly
Switch failures force him to backpedal several times.
Eight hours later, Bob is still stuck with update:
No sleep over night
Numerous application complaints
No quick fix in sight
Complex Planning
Unexpected Performance Degradation
Laborious Process
Switch Upgrade
Source: J. Liu, Yale
Notes: One day, to fix an operating system level bug in the switches, Bob needs to upgrade all switches in the network as soon as possible. He knows the applications hosted in the data center can have serious concerns about their performance during the update, so he firstly spends two weeks to coordination the applications owners to learn their requirements. Based on what he learns, he made a detailed update plan including which part of the network he will touch, what are the steps of the upgrade, and even configuration scripts he will uses.
He also asked his colleagues to review and revise the plan to make sure it is good to go.
To make the update even safer, he decides to do it in off-peak hours at night.
However, his cautious attitude does not give him a smooth process. He triggered some application alerts unexpectedly.
What makes it worse is that some switch failures prevent him from following his original plan, and force him to backpedal several times.
Eight hours later, Bob is still struggling without any sleep. He makes little progress, but receives many complaints from applications. He has to suspend the update now, because he sees no quick fix currently. And he gets upset.

## Slide 50: Congestion-free DCN update is the key
Applications want network updates to be seamless
  Reachability
  Low network latency (propagation, queuing)
  No packet drops
Congestion-free updates are hard
  Many switches are involved
  Multi-step plan
  Different scenarios have distinct requirements
  Interactions between network and traffic demand changes
Congestion
Source: J. Liu, Yale
Notes: The problems in network update make application nervous, because from network they always want reachability, low network latency and no packet drop. For reachability, data center networks offer multiple paths for flows so typically we do not loss reachability during an update. For network delay, the propagation delay is within 1ms so we do not worry about that. But the queuing delay and packet drop, they both depend on whether there are congestions in the network. So essentially, what applications want is a congestion-free update.
However for operators, performing a congestion-free update is hard. It is because an update typically involves many switches, and to avoid the congestion a plan with multiple steps is needed. There are various scenarios and each of them has a distinct requirement for the network update. So one update plan made for one scenario cannot be re-used in others.
And moreover, sometimes network updates should interact with the traffic demand changes from applications, which make the situation even more complex.
To better understand the preceding challenges, let us do a case study.

## Slide 51: A clos network with ECMP
300
Link capacity: 1000
300
150
150
= 920
620
+ 150
+ 150
300
300
600
600
150
150
All switches: Equal-Cost Multi-Path (ECMP)
Source: J. Liu, Yale
Notes: Now let us take a look at an example to see why a congestion-free update is difficult.
We have a small FatTree network. The capacity of each link is 1000.
There are two flows with size 620 from two CORE switches to ToR3. We highlight the two bottleneck links on the network. The two flows put 620 load on the two links.
At the same time, there is a flow from ToR1 to ToR2. This flow has multiple paths to reach ToR2 and each switch is using ECMP which equally splits the traffic loads among the out-going links.
We can find that this flow’s load on the two bottleneck links are 150.
Similarly, another flow from ToR5 to ToR4 with size 600 also has 150 load on the two links.
The total load of the bottleneck links is 920 which is less than the capacity. Therefore, now the network has no congestions.

## Slide 52: Switch upgrade: a naïve solution triggers congestion
+ 150
Link capacity: 1000
Drain AGG1
600
+ 300
= 1070
= 920
620
+ 150
Source: J. Liu, Yale
Notes: Now we want to shutdown AGG1. Before doing that, we want to move out all the traffic on AGG1. We try to simply reconfigure ToR1 and make it never forwards the flow green to AGG1 anymore. However, this naïve solution causes congestions. Because the reconfiguration on the green flow will change its traffic distribution over the network which congests one of the bottleneck link.

## Slide 53: Switch upgrade: a smarter solution seems to be working
Link capacity: 1000
Drain AGG1
100
500
+ 50
= 970
620
+ 300
+ 150
= 1070
Weighted ECMP
Source: J. Liu, Yale
Notes: To avoid the congestion, we can change ToR5 to make it split the flow blue as 500, 100. This change will redistribute the loads of the blue flow over the network. As a result, we get a good traffic distribution over the network: it has no congestions, and it has no traffic on AGG1. It looks perfect.

## Slide 54: Traffic distribution transition
Initial Traffic Distribution
Congestion-free
Final Traffic Distribution
Congestion-free
300
300
300
300
0
600
500
100
?
Asynchronous Switch Updates
Transition
Simple?
NO!
Source: J. Liu, Yale
Notes: Let us make a summary. Initially we have a traffic distribution, and for draining a switch we want the network gets a new traffic distribution. Both of the traffic distributions have no congestion. And now the only problem is whether the transition process is congestion-free or not. To realize the transition, we need to reconfigure two switches. Is it so simple in the end? Of course not!. At least we should know which switch is to update first.

## Slide 55: Asynchronous changes can cause transient congestion
600
300
300
Drain AGG1
Link capacity: 1000
620 + 300 + 150 = 1070
Not Yet
When ToR1 is changed but ToR5 is not yet:
Source: J. Liu, Yale
Notes: Let us see what happens if ToR1 is changed first. During the period that ToR1 is updated but ToR5 has not yet. The bottleneck link on the right will be congested.

## Slide 56: Solution: introducing an intermediate step
Initial
Final
Intermediate
Congestion-free regardless the asynchronizations
Congestion-free regardless the asynchronizations
300
300
300
300
0
600
500
100
200
400
450
150
?
Transition
Source: J. Liu, Yale
Notes: So overall, we see that despite we have no congestion on both the initial and the final traffic distributions, it is impossible the make the direct transition congestion-free. Then what shall we do? A method we can try is to introduce some intermediate step which has the property that the transitions from the initial to it and from it to the final are congestion-free regardless the update orders.
So does this intermediate step exist? Yes, and this is an example. I will talk about how we can find it later. But now from this example we can see that even playing with two flows on such a small network it has already been hard enough to make a congestion-free update. In real production network, when we have thousands of switches and millions of flows, it is impossible to plan and execute a congestion-free update by operators.

## Slide 57: How zUpdate performs congestion-free update
Data Center Network
zUpdate
Current Traffic Distribution
Target Traffic Distribution
Routing Weights
Reconfigurations
Update
Scenario
Update requirements
Operator
Intermediate
Traffic Distribution
Intermediate
Traffic Distribution
Source: J. Liu, Yale
Notes: zUpdate stands in the middle between operators and data center network. It keeps monitoring the current traffic distribution in the network. When operator has an update scenario to perform, zUpdate translate the update requirement into the constraint to the target traffic distribution. Then, zUpdate will automatically find a target traffic distribution, and a chain of intermediate traffic distributions which bridges the current and the target traffic distributions and makes sure that the whole transition process is congestion-free.
After that, zUpdate configures the network according to the plan.

## Slide 58: Key technical issues
Describing traffic distribution
Representing update requirements
Defining conditions for congestion-free transition
Computing an update plan
Implementing an update plan
Source: J. Liu, Yale
Notes: To achieve the goal of zUpdate, we should address some key technical issues.
In the following of this talk, we will first formulate traffic distribution, and use this formulation to express the update requirements in different scenarios. Then we will find the condition for a congestion-free transition, and compute and implement an update plan based on the preceding formulations and conditions.

## Slide 59: Describing traffic distribution
600
300
150
=150
=300
: flow f’s load on link v, u
Source: J. Liu, Yale
Notes: To formulate a traffic distribution we first define lv, u f which means the flow f’s load on link from switch v to u.
For example, on this network, a flow with flow size 600 comes in. If s1 equally split the traffic load, f’s load on the link from s1 to s2 is 300. Its load on link from s2 to s4 is 150.
Traffic distribution is a set of lv, u f when we enumerate all flows and links.

## Slide 60: Representing update requirements
Drain s2
When s2 recovers
Constraint: no flow to s2
Constraint: ECMP equal split
Source: J. Liu, Yale
Notes: With the formulations, we can easily represent the requirements on target traffic distributions.
For example, when we want to drain s2, we can simply require that ls1s2f should be 0. Generally, we require that each flow’s loads on the incoming links of s2 should be 0.
For another example, when s2 recovers, we want all the switch to get back to equally splitting the traffic, we require that ls1s2f is equal to ls1s2f. Generally, we require that for each flow, the flows load on each out-going link of a switch should be equal.
Here we only offer two examples. We have formulated all the requirements for the scenarios we mentioned.
Please look into the paper for more details.

## Slide 61: Switch asynchronization exponentially inflates the possible load values
Asynchronous updates can result in 2^5 possible load values on link (7,8) during transition.
f
ingress
egress
f
In large networks, it is impossible to check if the load value exceeds link capacity.
Transition from old traffic distribution to new traffic distribution
1
2
3
4
6
7
8
5
Source: J. Liu, Yale
Notes: Now we consider a traffic distribution transition.
We start from a single flow case.
To realize a transition, we insert new rules of flow f into all the switches.
Therefore, in large network, switch asynchronization causes too many potential loads on each link, which prevents us from judging whether a link will be overloaded during the transition.

## Slide 62: Two-phase commit reduces the possible load values to two
With two-phase commit, f’s load on link (7,8) only has two possible values throughout a transition
f
version flip
ingress
egress
f
Transition from old traffic distribution to new traffic distribution
1
2
3
4
6
7
8
5
Source: J. Liu, Yale
Notes: To solve this problem, we leverage two-phase commit for a transition.
The process is as following:
At the beginning of a transition, we push out the new rules. The flow keeps using the old rules until all the new rules are installed in each switch. Finally, we indicate the ingress switch to make a version flip, so that the flowing switches all use the new rules to process the flow.
Eventually, it comes to the new traffic distribution.
We proof that with two-phase commit, a flow’s load on a link throughout the transition only have two possible values, the load in the old traffic distribution or the one in the new traffic distribution.

## Slide 63: Flow asynchronization exponentially inflates the possible load values
f1
f2
1
2
3
4
5
6
7
8
0
Asynchronous updates to N independent flows can result in 2^N possible load values on link (7,8)
f1 + f2
Source: J. Liu, Yale
Notes: In last example, we only consider a single flow in the network. However, in practice, a link can carry multiple flows simultaneously.
For example, if this network has two flows f1 and f2 and either of the flows is using two-phase commit, the total load on the link from switch 7 to 8 will have four potential values. We can see the asynchronization among flows still exponentially inflates the possible link load values.

## Slide 64: Handling flow asynchronization
The load on link switch 7 to 8 has four potential values, but it is no more than the sum of f1’s maximum potential value and f2’s maximum potential value.
f1
f2
1
2
3
4
5
6
7
8
0
Source: J. Liu, Yale
Notes: To handle the flow asynchronizaiton, we first make an observation. The load on link switch 7 to 8 has four potential values, but it is no more than the sum of f1’s maximum potential value and f2’s maximum potential value.
When we generalize this observation, we get the constraint of a congestion-free transition. On each link, we sum up each flow’s potential maximum load. If this worst case does not congestion the link, the link is congestion-free during the transition.

## Slide 65: Computing congestion-free transition plan
Constant:
Current Traffic Distribution
Variable:
Target Traffic
Distribution
Variable:
Intermediate
Traffic Distribution
Constraint:
Congestion-free
Constraint:
Update Requirements
Constraint:
Deliver all traffic
Flow conservation
Variable:
Intermediate
Traffic Distribution
Linear Programming
Source: J. Liu, Yale
Notes: Given all the previous analysis, computing a transition plan becomes straightforward.
The current traffic distribution is a constant for us, and our variables are the target and the intermediate traffic distributions. We have some constraints on our variables. The first one is the update requirements to the target traffic distribution. Then to avoid congestion, we require that all the adjacent traffic distributions satisfy the congestion-free transition constraint. Additionally, each traffic distribution should also satisfy some other constraints, such that they should deliver all the traffic demands and they respect the flow conservation.
Fortunately, all the constraints are linear. We can compute the variable traffic distributions with LP.

## Slide 66: Implementing an update plan
Computation time
Switch table size limit
Update overhead
Failure during transition
Traffic demand variation
Other Flows
Critical
Flows
Weighted-ECMP
ECMP
Flows traversing bottleneck links
Source: J. Liu, Yale
Notes: For implementing a plan, we still need to solve some practical issues.
In large scale data centers, we could have millions of flows. It is infeasible if we manipulate all the flows over the network. Because if so the computation time of an update plan could be too long, and the limited flow table in switches cannot accommodate so many flow rules. Moreover, the more rules we update, the more overhead on the switch we create. Therefore, we only want to manipulate a small number of critical flows and leave other flows as pure ECMP. We define the flows traversing the bottleneck links as critical flows. Because in practice, a DCN typically only has several bottleneck links, the critical flows are only a small fraction in the total.
Additionally, we also consider how to re-compute a plan or rollback when failure happens during a transition.
Finally, when traffic demands are changing simultaneously during the transition, we simply use the maximum flow size of each flow as the flow size in the plan computation, which can guarantee the transition is still congestion-free.

## Slide 67: Evaluations
Testbed experiments
Large-scale trace-driven simulations
Notes: Next we will show the evaluation results from both testbed experiments and large-scale trace-driven simulations.

## Slide 68: Testbed setup
Drain AGG1
ToR5: 6Gbps
ToR8: 6Gbps
ToR6,7: 6.2Gbps
ToR6,7: 6.2Gbps
ToR6,7: 6.2Gbps
ToR6,7: 6.2Gbps
Source: J. Liu, Yale
Notes: We build a testbed with 22 switches forming a FatTree. Each switch is enabled with OpenFlow 1.0 and the capacity of the links is 10Gbps. We leverage a traffic generator to insert flows into the network. The update scenario is to drain AGG1 and then upgrade its firmware. It is indeed a replay of the example we saw in the beginning of this talk.

## Slide 69: zUpdate achieves congestion-free switch upgrade
Chart: Real-time link utilization
| 0.0 | 2.0 | 4.0 | 6.0 | 8.0 | 10.0 | 12.0 | 14.0 | 16.0 | 18.0 | 20.0 | 22.0 | 24.0
Link: CORE1-AGG3 | 0.92 | 0.92 | 0.92 | 0.92 | 0.87 | 0.945 | 0.945 | 0.945 | 0.945 | 0.845 | 0.87 | 0.87 | 0.87
Link: CORE3-AGG4 | 0.92 | 0.92 | 0.92 | 0.92 | 0.97 | 0.895 | 0.895 | 0.895 | 0.895 | 0.995 | 0.97 | 0.97 | 0.97
Initial
Final
Intermediate
3Gbps
3Gbps
3Gbps
3Gbps
0
6Gbps
5Gbps
1Gbps
2Gbps
4Gbps
4.5Gbps
1.5Gbps
Source: J. Liu, Yale
Notes: We show the real-time link utilization of the two bottleneck links: the blue link the orange link. Initially, the loads on both of the links are stable. During the transition from the initial to the intermediate, the link loads are shifted twice without any congestion. In the transition from the intermediate to the final, we did not see any congestion either.

## Slide 70: One-step update causes transient congestion
Chart: Real-time link utilization
| 0.0 | 2.0 | 4.0 | 6.0 | 8.0 | 10.0 | 12.0 | 14.0
Link: CORE1-AGG3 | 0.92 | 0.92 | 0.92 | 0.92 | 0.77 | 0.87 | 0.87 | 0.87
Link: CORE3-AGG4 | 0.92 | 0.92 | 0.92 | 0.92 | 1.095 | 0.97 | 0.97 | 0.97
Initial
3Gbps
3Gbps
3Gbps
3Gbps
Final
0
6Gbps
5Gbps
1Gbps
Source: J. Liu, Yale
Notes: However, if we make the transition from the initial directly to the final, a transient congestion will happen during the transition.

## Slide 71: Conclusion
Switch and flow asynchrony can cause severe congestion during DCN updates
zUpdate provides congestion-free DCN updates
  Novel algorithms to compute update plan
  Practical implementation on commodity switches
  Evaluations in real DCN topology and update scenarios
Source: J. Liu, Yale
Notes: Here we come to the conclusion.
In this paper, we learn that asynchronous changes in network updates can arouse severe congestions.
We introduce zUpdate to perform congestion-free network updates. We formulate the problem, design a novel algorithm to compute the update plan automatically, build a prototype on OpenFlow 1.0 and showing it works well in different real scenarios.

## Slide 72: Outline
Announcement: project proposal due Oct 23
Review of Previous Lecture
  Verification of network properties
  Verification of controller correctness
  Verification of software data plane
SDN Update
  Per Switch Consistent and Minimal Updates
  Network-wide Updates
    Consistent Updates
    Congestion-Free Updates
    Network Partition

## Slide 73: Network Partition
Out-of-band control network
Routing and forwarding based on addresses Policy specification using end-host names Controller only aware of local name-address bindings

## Slide 74: Network Partition
Consider policy isolating A from B. A control network partition occurs. Only possible choices
  Let all packets through (including from A to B) (bad for correctness)
  Drop all packets (including from A to D) (bad for availability)

## Slide 75: Solution to Network Partition
Network can label packets with sender’s identity
  Route based on identity instead of address
Inband control

## Slide 76: Other Update Problems
Consistent updates in the controller itself
Minimize rule space used
Scheduling updates to optimize completion time

## Slide 77: Questions?