## Slide 1: Software Defined Networking COMS 6998-10, Fall 2014
Instructor: Li Erran Li (lierranli@cs.columbia.edu)
http://www.cs.columbia.edu/~lierranli/coms6998-10SDNFall2014/
11/10/2014: SDN Traffic Engineering

## Slide 2: Outline
Announcement
  December 1 lecture reschedule to November 21 (Friday) at 545 Mudd
SDN Traffic Management (20 min)
  Motivation
  Why SDN
  Challenges
  Architecture and Algorithms
  Implementation and Evaluation
  Conclusions and Future Work
Midterm (90 min)

## Slide 3: Motivation
Inter-DC WANs bandwidth demand is high
Content distribution both between servers and to end clients
Site replication for geographic locality and bandwidth efficiency
Availability zones: cross-zone replication

## Slide 4: Motivation (Cont’d)
Inter-DC WANs are highly expensive

## Slide 5: Two key problems
Poor efficiency
average utilization over time of busy links is only 30-50%
Poor sharing
little support for flexible resource sharing
Why?
Source: Ming Zhang, MSR

## Slide 6: One cause of inefficiency: lack of coordination
Background traffic
Non-background traffic
Norm. traffic rate
Time (~ one day)
peak before rate adaptation
peak after rate adaptation
> 50% peak reduction
mean
Source: Ming Zhang, MSR

## Slide 7: Poor sharing
Mapping services onto different queues at switches helps, but # services ≫ # queues
(4 - 8 typically)
When services compete today, they can get higher throughput by sending faster
Borrowing the idea of edge rate limiting, we can have better sharing without many queues
(hundreds)

## Slide 8: Outline
SDN Traffic Management
  Motivation
  Why SDN
  Challenges
  Architecture and Algorithms
  Implementation and Evaluation
  Conclusions and Future Work
Midterm

## Slide 9
Why SDN
Status Quo
SDN Approach
Forwarding and control
Separate forwarding hardware
intermixed on a single box
from control software
Manage network as 1000s of
Manage network as a single
individual boxes
fabric
Decentralized, non-
Logically centralized control
deterministic protocols
with traffic engineering
All bits are created equal
Allocate resources based on
application priority
Apps regulated by per-flow
Demand measurement and
TCP “fair” share
resource shaping at the edge

## Slide 10: Challenges
High performance distributed control systems
Inter-operation with legacy networks (other non-SDN sites or the Internet)
Scalable computation of max-min fair allocation among flows with different priority
Congestion-free data plane update
Working with limited switch memory

## Slide 11: Outline
SDN Traffic Management
  Motivation
  Why SDN
  Challenges
  Architecture and Algorithms
  Implementation and Evaluation
  Conclusions and Future Work
Midterm

## Slide 12
B4 Architecture
NCS: Network Control Servers
RAP: Routing Application Proxy
OFC: OpenFlow Controller
OFA: OpenFlow Agent
NCS and switches share
Out of band
control network

## Slide 13
B4 Architecture: Data Plane
OFA
Switch
OFA
Switch
Site A
OFA
iBGP
Switch
OFA
Switch
eBGP
Clusters
Site B
Site C
Google Confidential and Proprietary
OpenFlow Agent (OFA): is a user-level process running on switch hardware
  implement extended OpenFlow to manage the hardware pipeline
  Forward BGP routing packets to OFC, in turn to BGP stack.

## Slide 14
B4 Architecture: Control Plane
Gateway
Site A Controllers
Cental TE
Server
Quagga
Rout
Prox
TE Agent
Paxos
OFC
NCS 2
NCS 3
NCS 1
Google Confidential and Proprietary
Route Proxy: controller app to connect Quagga and OF switches
  BGP/ISIS route updates
  Routing protocol packets
  Interface updates from switches to Quagga

## Slide 15
Hybrid SDN Deployment
Data Center Network
Cluster
Border
Router
EBGP IBGP/ISIS to
remote sites
(not representative of actual topology)

## Slide 16
Hybrid SDN Deployment
Data Center Network
Cluster
Border
Router
EBGP IBGP/ISIS to
remote sites
Quagga
OFC
Paxos
Glue
Paxos
Paxos

## Slide 17
Hybrid SDN Deployment
IBGP/ISIS to
remote sites
Data Center Network
Cluster
Border
Router
EBGP
OFA OFA
EBGP
IBGP/ISIS to remote sites
Quagga OFC
Paxos Glue
Paxos Paxos
OFA OFA

## Slide 18
Hybrid SDN Deployment
Data Center Network
OFA OFA
Cluster OFA OFA
Border
Router
OFA OFA
EBGP
IBGP/ISIS to remote sites
Quagga OFC
Paxos Glue
Paxos Paxos
OFA OFA
● SDN site delivers full interoperability with legacy sites

## Slide 19
Hybrid SDN Deployment
Data Center Network
OFA OFA
Cluster OFA OFA
Border
Router
OFA OFA
EBGP
IBGP/ISIS to remote sites
Quagga OFC
Paxos RCS
Paxos Paxos
OFA OFA
TE Server
● Ready to introduce new functionality, e.g., TE

## Slide 20
Traffic Engineering Architecture

## Slide 21
TE Optimization Problem
● Max-min fair bandwidth allocation to FlowGroups
  ○ FlowGroups: {DC Pairs, priority class}
● FlowGroup’s priority represented by bandwidth function ● HW capabilities constrains solution:
○ Maximum number of paths ○ Splits quantization

## Slide 22
TE Optimization Algorithm
● Max-min fair bandwidth allocation to FlowGroups
● Fill higher priority along shortest paths and then move to longer paths if needed
● Example: FG1 HIPRI, FG2 LOPRI

## Slide 23: Congestion-free update Problem
How to update forwarding plane without causing transient congestion?
See lecture 6 on congestion free updates

## Slide 24: Outline
SDN Traffic Management
  Motivation
  Why SDN
  Challenges
  Architecture and Algorithms
  Implementation and Evaluation
  Conclusions and Future Work
Midterm

## Slide 25
SDN Switch with legacy Routing Protocols
● Built from merchant silicon ○ 100s of ports of
nonblocking 10GE ● OpenFlow support
● Open source routing stacks for BGP, ISIS
● Does not have all features ● Multiple chassis per site ○ Fault tolerance
○ Scale to multiple Tbps

## Slide 26
Benefits of Centralized TE
Relative to Shortest Path
Main benefit comes from reduced provisioning for fault tolerance on high priority traffic

## Slide 27
B4 WAN History

## Slide 28
Conclusions and Future Work
● Dramatic growth in WAN bandwidth requirements
○ Existing software/hardware architectures make it impractical to deliver necessary bandwidth globally ● Software Defined Networking: it works and at scale
○ Separation of hardware from software
○ Efficient logically centralized control/management ○ Incremental migration path
● Convergence to public facing WAN

## Slide 29: Questions?