## Slide 1: Cellular Networks and Mobile Computing COMS 6998-7, Spring 2014
Instructor: Li Erran Li (lierranli@cs.columbia.edu)
http://www.cs.columbia.edu/~lierranli/coms6998-7Spring2014/
2/17/2014: Ebug debugging, Power Models, and Profiling

## Slide 2: Review of Previous Lecture
What are the four major app components?
Which file to declare these components?
What is the mechanism for inter-component communication?
Which file declares your view hierarchy?
How to access your resources in your program?

## Slide 3: Review of Previous Lecture (Cont’d)
Four major app components: Activity, Service, Broadcast receiver, Content Provider.
Declare app components in AndroidManifest.xml
Components communicate using Intent
View hierarchy are declared in layout.xml
Access your resources by R.* (e.g. R.id.button1)

## Slide 4: Outline
The Rise of Ebugs
Debugging no-sleep Ebugs
Methods of Measuring Power Usage
Power Models
  Usage based
  System call trace based
Profiling
Conclusion

## Slide 5: The Rise of Energy Bugs
Single Symptom:
Severe, Unexpected Battery Drain
Apps Need Not Crash
No Blue Screen Of Death
Common Perception:
Kill some apps to fix
Courtesy: Pathak et al

## Slide 6: User Frustration (Dialer App EBug)
Courtesy: Pathak et al

## Slide 7: Crawling Internet Forums
4 Online
Mobile Forums
1.2M Posts
(~400 mobile devices;
Several mobile OSes)
grep “power drain”,
“battery drain”, etc.
39K Posts
K-means
1000 Clusters
Human
EBug Taxonomy
1.
2 Mobile Bugs/Issues Repository
2.
Indepth Analysis
Courtesy: Pathak et al

## Slide 8: Ebug Taxonomy
Ebug
Hardware
23%
Software
35%
External
12%
Unknown
30%
OS
Apps
No Sleep Bug
Loop Bug
Immortality Bug
External Service
Network Signal Strength
Wireless Handovers
Courtesy: Pathak et al

## Slide 9: Hardware EBug
Ebug
Hardware
23%
Software
35%
External
12%
Unknown
30%
Battery
Exterior Hardware Damage
SDCard
Sim Card
External Hardware
Courtesy: Pathak et al

## Slide 10: Ebug Taxonomy
Ebug
Hardware
23%
Software
35%
External
12%
Unknown
30%
OS
Apps
No Sleep Bug
Loop Bug
Immortality Bug
External Service
Network Signal Strength
Wireless Handovers
Courtesy: Pathak et al

## Slide 11: OS Ebugs
IOS Version: 4.0 – 4.3.3 (5% posts)
2.5% posts
Why does OS Leak Energy?
  Hard to infer
  OS Processes
  System Configuration
Courtesy: Pathak et al

## Slide 12: Apps EBug: No Sleep Bug
Aggressive Sleeping Policies: Smartphone OSes freeze system after brief inactivity
Power encumbered Programming: Programmer has to manage sleep/wake cycle of components
No Sleep Bug: At least one component is kept awake due to mismanagement
Courtesy: Pathak et al

## Slide 13: External Conditions
External Services (<1%)
Network Signal Strength (11%)
Wireless Handovers (<1%)
Ebug
Hardware
23%
Software
35%
External
12%
Unknown
30%
Courtesy: Pathak et al

## Slide 14: EDB: Energy Debugging Framework
Courtesy: Pathak et al

## Slide 15: Mobile Programming EcoSystem: The EBug Blame Game
App Developers
Framework Developers
Kernel Developers
Firmware/OEM Developers
Hardware Manufacturers
Network Operators
Courtesy: Pathak et al

## Slide 16: Outline
The Rise of Ebugs
Debugging no-sleep Bugs
Methods of Measuring Power Usage
Power Models
  Usage based
  System call trace based
Profiling
Conclusion

## Slide 17: Smartphones are Energy Constrained
CPU
Screen
3G/4G
WiFi
GPS
Camera
Battery energy density only doubled in last 15 years
Courtesy: Jindal et al

## Slide 18: Paradigm Shift in Power Management
Desktop/Server/Laptop: Default ON
  CPU turned off when idle for long time
Smartphones: Default OFF
  Smartphone OSes aggressively turn off Screen/CPU after brief user inactivity
  Helps increasing standby time period
Courtesy: Jindal et al

## Slide 19: Consequences of Aggressive Sleeping Policy
Background jobs
User is not always touching phone
public void DoNetwork ( )
{
}
Sync_Over_Network ( ); //Sync state with remote server
//Can take up to a minute
Need a mechanism to explicitly keep components awake.
Keep the screen on !
Courtesy: Jindal et al

## Slide 20: Android API to Explicitly Keep Components Awake
PowerManager pm = (PowerManager) getSystemService(Context.POWER_SERVICE);
PowerManager.WakeLock wakelock= pm.newWakeLock(PowerManager.PARTIAL_WAKE_LOCK, null);
API | Component (s)
PARTIAL_WAKE_LOCK | CPU
SCREEN_DIM_WAKE_LOCK | CPU and Screen (DIM)
SCREEN_BRIGHT_WAKE_LOCK | CPU and Screen (Bright)
Camera.startPreview() Camera.release() | Camera
Courtesy: Jindal et al

## Slide 21: Android API to Explicitly Keep Components Awake (Cont’d)
public void DoNetwork ( ) {
wakelock.acquire ( ); //Don’t let CPU sleep till I say so
wakelock.release ( ); //CPU is now free to sleep
}
Sync_Over_Network ( ); //Sync state with remote server
//Can take up to a minute
Courtesy: Jindal et al

## Slide 22: iOS API to Explicitly Keep Components Awake
Screen: idleTimerDisabled property in UIApplication
  If NO, the idle timer turns off the device’s screen after a specified period of inactivity
GPS: enable/disable location updates, and set the distance filter and accuracy levels
  Core Location uses the available GPS, cell, and Wi-Fi networks to determine the user’s location
  Core Location minimizes the use of these radios
  Setting the accuracy and filter values gives Core Location the option to turn off hardware altogether in situations where it is not needed.
WiFi: UIRequiresPersistentWiFi key in the app’s Info.plist file
  System will not shut down the Wi-Fi hardware while your app is running.

## Slide 23: Power Encumbered Programming
App programmer has to manage sleep/wake cycle of components
Courtesy: Jindal et al

## Slide 24: NoSleep Energy Bugs
An error in smartphone app, where a component is woken up, but not put to sleep
Component | Impact (Google Nexus)
CPU | 50-60% battery in 12 hrs
Screen | 100% battery in 4-6 hrs
GPS | 100% battery in 3-5 hrs
Courtesy: Jindal et al

## Slide 25: Collecting and Characterizing Bugs
Online mobile forums
Bug lists
Open source code repositories
Running the detection tool
Courtesy: Jindal et al

## Slide 26: Types of NoSleep Bugs
NoSleep Race Conditions
NoSleep Code Paths
NoSleep Dilations
Courtesy: Jindal et al

## Slide 27: (a) NoSleep CodePaths
public void DoNetwork ( )
{
}
try
{
} catch (SomeException e){
Print.Error ( e ); //Print Error for Debugging purposes
}
wakelock.acquire ( ); //Don’t let CPU sleep till I say so
wakelock.release ( ); //CPU is now free to sleep
Sync_Over_Network ( ); //Sync state with remote server
//Can take upto a minute
;throws
;exception
At least one path in program wakes up a component and does not put it to sleep
Courtesy: Jindal et al

## Slide 28: (b) NoSleep Race Condition (1)
Process
Thread 1
Thread 2
Time
Process
Thread 1
Thread 2
Time
acquire
acquire
release
release
Courtesy: Jindal et al

## Slide 29: (b) NoSleep Race Conditions (2)
public class WorkerThread
{
}
while(true){ //Infinite Loop
}
public class MainThread
{
}
wakelock.acquire ( ); //CPU Cant Sleep
WorkerThread.start ();//start worker
WorkerThread.interrupt();//stop worker
wakelock.release ( ); //CPU can sleep now
boolean KillFlag = false; //Kill Flag
KillFlag = true; //Kill the worker thread
if(KillFlag) break; //Exit
NetSync(); //Critical Section
Thread.Sleep (3 Mins);//Sleep for 3 mins
wakelock.release ( ); //CPU can sleep
wakelock.acquire ( ); //CPU Cant Sleep
…….
…….
......
…….
…….
Correct Execution
Buggy Execution
Courtesy: Jindal et al

## Slide 30: (c) NoSleep Dilations
Components are eventually turned off but are kept on for unusually long duration of time
public void onCreate( )
{
}
public long startNewTrack( )
{
..
}
+ wakelock.acquire ( ) ;
wakelock.acquire ( ) ;
Courtesy: Jindal et al

## Slide 31: Detecting NoSleep Bugs
NoSleep Code Paths
NoSleep Race Conditions
Static Data Flow Analysis
  Reaching Definitions Data Flow Problem
Courtesy: Jindal et al

## Slide 32: Reaching Definitions Data Flow Problem
: {}
: {d1, d2}
: {d1, d2}
: {d1, d2}
: {d3, d4}
: {d2, d5, d6}
: {d2, d3, d4, d5, d6}
y = 3;
x = 10;
y = 11;
if( y > 5 ) {
x = 1;
y = 2;
} else {
z = x;
x = 4;
}
Problem Statement: For each point in the program, determine which definition of variable are reachable
exit
entry
d0: y = 3
d1: x = 10
d2: y = 11
if (y>5)
B0
d3: x = 1
d4: y = 2
d5: z = x
d6: x = 4
B1
B2
IN[B0]
OUT[B0]
OUT[B2]
IN[B2]
IN[B1]
IN[exit]
OUT[B1]
OUT[entry] = {}
Courtesy: Jindal et al

## Slide 33: NoSleep Code Path DataFlow Analysis
try
{
} catch (SomeException e){
Print.Error ( e ); //Print Error for Debugging purposes
}
wakelock.acquire ( ); //Don’t let CPU sleep till I say so
wakelock.release ( ); //CPU is now free to sleep
Sync_Over_Network ( ); //Sync state with remote server
//Can take upto a minute
;throws
;exception
exit
Entry
d0: wakelock = 1;
Sync_over_network()
B0
d1: wakelock = 0;
Print.error(e);
B1
B2
exit
Entry
d0: wakelock.acquire();
Sync_over_network()
B0
d1: wakelock. realease();
Print.Error(e)
B1
B2
: {d0, d1}
IN[exit]
: {d1}
: {d0}
Apply reaching definitions to NoSleep CodePaths
Courtesy: Jindal et al

## Slide 34: Implementation
Soot Implementation
  Open source framework for analyzing java bytecode from Sable research group at McGill University
  Added ~2 KLOC
Runs on Java byte code
  No need for source code
Courtesy: Jindal et al

## Slide 35: Evaluation: NoSleep Code Paths
Total Apps 86 | BUG in reality | No BUG in reality
Tool reports BUG (55) | True Positive 42 | False Positive 13
Tool reports no BUG (31) | False Negative 0 | True Negative 31
500 Apps
Apps Manipulating components
187
Apps which could be decompiled
86
Find NoSleep Bugs
55
Courtesy: Jindal et al

## Slide 36: Causes of Detected NoSleep Bugs
Category | Number of Apps | Examples
Incorrect Wakelock Handling in Events | 26 | MyTracks
If, else + exception Paths | 12 | Facebook
Forgot Release | 4 | K9Mail
Courtesy: Jindal et al

## Slide 37: Common Cause of False Positives
EXIT
If(caller != BLACKLISTED)
Wl.release();
If(caller != BLACKLISTED)
Wl.acquire();
ENTER
.
.
Courtesy: Jindal et al

## Slide 38: Summary
Paradigm shift in power management
  Power encumbered programming
NoSleep energy bugs
  Code paths, race, dilation
Reaching definition data flow analysis
  Found 30 new previously unreported bugs
Courtesy: Jindal et al

## Slide 39: Future Work
Comprehensive approaches to No-Sleep bug
  Detection: e.g. Symbolic execution
  Prevention: e.g. Better abstraction for power management API
  Mitigation: e.g. Runtime detection, Limiting damage of the bug
Courtesy: Jindal et al

## Slide 40: Measuring Power Usage
Approach 1: Use power meter (offline)
  Buy an expensive equipment ($770)
  Problems:
    Only reports entire device energy consumption
Approach 2 : Use built-in battery sensor (online)

## Slide 41: iOS Battery API
Use UIDevice class to obtain information and notifications about
  charging state (property batteryState)
  charging level (property batteryLevel)
[[UIDevice currentDevice] setBatteryMonitoringEnabled:YES];
NSArray *batteryStatus = [NSArray arrayWithObjects:
@"Battery status is unknown.",
@"Battery is in use (discharging).",
@"Battery is charging.",
@"Battery is fully charged.", nil];
if ([[UIDevice currentDevice] batteryState] == UIDeviceBatteryStateUnknown)
NSLog(@"%@", [batteryStatus objectAtIndex:0]);
else
{
NSString *msg = [NSString stringWithFormat:
@"Battery charge level: %0.2f%%\n%@", [[UIDevice currentDevice] batteryLevel] * 100,
[batteryStatus objectAtIndex:[[UIDevice currentDevice] batteryState]] ];
NSLog(@"%@", msg);
}

## Slide 42: Android Battery API
Sample updates stored in files:
  Current: /sys/class/power_supply/battery/batt_chg_current
  Voltage: /sys/class/power_supply/battery/batt_vol
  Capacity: /sys/class/power_supply/battery/capacity
  File fcur = new File("/sys/class/power_supply/battery/batt_chg_current");
  if (fcur.exists())
  …
File names are vendor dependent
Access using Android Debug Bridge (adb)
  <sdk>platform-tools
  Command: adb shell

## Slide 43: Outline
The Rise of Ebugs
Debugging no-sleep Bugs
Methods of Measuring Power Usage
Power Models
  Usage based
  System call trace based
Profiling
Conclusion

## Slide 44: Smartphone is Energy Constrained
Energy: One of the most critical issues in smartphones
  Limited battery lifetime
Battery energy density only doubled in last 15 yrs
Smartphone capability has increased drastically
  Multiple Components: GPS, 3G, retina display, ….
Courtesy: Pathak et al

## Slide 45: Towards Understanding Energy Drain
Key Question: Where is energy being spent?
  Which component/process/thread/function(?)
Courtesy: Pathak et al

## Slide 46: Generic Power Modeling
Prediction
Phase
Actual Power Consumption
Power meter
Triggers
Model
Predicted Power
Consumption
Triggers
Training
Phase
Courtesy: Pathak et al
Notes: Make fonts large
Blue color not visible
Put down LR somewhere

## Slide 47: Smartphone Power Modeling: Utilization Based (1/3)
Prediction
Phase
Actual Power Consumption
Power meter
Triggers
Utilization
Model
Predicted Power
Consumption
Triggers
Utilization
Training
Phase
Model = (UtilNet)* ENet + (UtilCPU)* ECPU + (UtilDisk)* EDisk
Linear Regression (LR) and Superimposition
Courtesy: Pathak et al

## Slide 48: Smartphone Power Modeling: Utilization Based (2/3)
Sesame paper has two optimizations: model molding, principle component analysis (PCA)
PowerTutor model

## Slide 49: Smartphone Power Modeling: Utilization Based (3/3)
Fundamental (yet intuitive) assumption (Only active) Utilization => power consumption
Second assumption Energy scales linearly with amount of work
Third assumption Components power consumption add linearly
Desired Feature
Which process/thread/function? Hard to correlate
Model = (UtilNet)* ENet + (UtilCPU)* ECPU + (UtilDisk)* EDisk
Courtesy: Pathak et al

## Slide 50: (Only active) Utilization => Power Consumption
File open/delete/ close/create change power state
Several components have tail states (3G, disk, wifi, gps)
Courtesy: Pathak et al
Notes: Write down what have to say

## Slide 51: Energy scales linearly with amount of work
(1) Send packets
@ < 50pkts/s
+100-125mA
(2) Send packets
@ > 50pkts/s
+325mA
WM6.5 on Tytn II
Courtesy: Pathak et al

## Slide 52: Components power consumption add linearly
+180mA
+110mA
Send
start
Send done
Socket close
Spin_CPU
Spin_CPU Stop
Send(2mb)
(i = 1)
Spin_CPU(2M)
(i = 1)
Send(2mb)
(i = 5)
Send(10mb);
sleep();
Socket.close();
(2) Spin_CPU(10M);
(3)
for (i in 1 to 5){
Send(2mb);
Spin_CPU(2M);
}
Sleep();
Socket.close();
+200mA
+180mA
+200mA
Spin_cpu(2M)
(i = 5)
Network tail
Socket close
+110mA
WM6.5 on HTC Touch
Courtesy: Pathak et al

## Slide 53
What have we learnt so far?
Simple (state-of-art) energy modeling assumptions are wrong
There exits a notion of power states
What have we hinted so far?
Device drivers have intelligent power control rules
System calls play a role in power consumption
Challenges in fine-grained power modeling?
Device drivers are closed source (no code/no information)
Courtesy: Pathak et al

## Slide 54: System Calls As Power Triggers
Advantages:
  Encapsulates utilization based triggers
    Parameters of system calls
  Captures power behavior of ones that do not necessarily imply utilization
  Can be traced back to process, thread, function
    Eases energy accounting
Key observation: System call is the interface through which an application communicates with the underlying system (hardware) and outside world (Internet, GPS, etc.)
Key Idea: Use System Calls as triggers in power modeling
Courtesy: Pathak et al

## Slide 55: Finite-State-Machine (FSM) as Power Model Representation
We Use Finite-State-Machine (FSM)
Nodes: Power states
  Base State: No activity on phone
  Productive state: Actual utilization
  Tail state: No-useful work
Edges: Transition rules
  System calls (start/completion)
  Workload (Ex: 50 pkts/sec)
  Timeout
State 1
State 2
State 3
Transitions
Courtesy: Pathak et al

## Slide 56: FSM Power Model Construction
Systematic ‘Brute Force’ Approach
  Step 1 : Model Single System Call
  Step 2 : Model Multiple System Calls for Same Component
  Step 3 : Model Multiple Components (Entire Phone)
Requires domain knowledge
  Semantics of system calls
Courtesy: Pathak et al

## Slide 57: Step 1: Single System Call FSM
System call: read (fd, buf, size);
WM6.5 on HTC Touch
Measured power consumption + system calls (trigger)
Modeled power consumption
FSM
Courtesy: Pathak et al

## Slide 58: Step 2: Modeling Multiple System Calls of Same Component
Observation: A component can only have a small finite number of power states
Methodology
  Identify and merge similar power states
  Obey programming order
  Model concurrent system calls
Courtesy: Pathak et al

## Slide 59: Step 2: WiFi NIC
Base State +0mA
Low Net
+125 mA
Send done
Send < 50
Pkts/sec
Net Tail
+280 mA
High Net
+325 mA
Send done
Send
Send > 50
Pkts/sec
Base State +0mA
Socket close
Net Tail
+280 mA
Socket close
Base State +0mA
Low Net
+125 mA
Send done
Send < 50
Pkts/sec
Net Tail
+280 mA
High Net
+325 mA
Send done
Send
Send > 50
Pkts/sec
Socket close
Socket close
SEND
CLOSE
WM6.5 on HTC Tytn II
Courtesy: Pathak et al

## Slide 60: Step 3: Modeling Multiple Components
Observation: Different components may interact with each other’s power consumption
Methodology
  Try to reach different combination of states
  Construct new states and transitions in FSM
Courtesy: Pathak et al

## Slide 61: Implementation
Windows Mobile 6.5
  Extended CeLog
Android
  System Tap: Logs kernel events
  Android debugging framework: Custom logging in Dalvik VM
Courtesy: Pathak et al

## Slide 62: Evaluation: Handsets Used
HTC Tytn II | HTC Touch | HTC Magic
Win 6.5 (CE 5.2) | Win 6.5 (CE 5.2) | Android (Linux 2.6.34)
Courtesy: Pathak et al

## Slide 63: Snapshot of FSM for Entire Phone
Base State +0mA
Low Net
+125 mA
Send done
Send < 50
Pkts/sec
Send
Net Tail
+270 mA
High Net
+325 mA
Send done
Send > 50
Pkts/sec
Net Tail + CPU
+300 mA
CPU
Timeout 1.7s
High CPU
+130
mA
CPU (ctx_in) ctx_out
High Disk
+125
mA
Disk: Read /write/open/close/create/delete
Disk Tail
+75
mA
Disk
Call completed
Timeout 3s
DTail+ CPU
+130
mA
CPU
WM6.5 on HTC Tytn II
Courtesy: Pathak et al

## Slide 64: End-To-End Energy Estimation Error
Chart: Error %
| csort | dropbear | maps | facebook | youtube | game | chess | diskB | netB | ie.cnn | pviewer | docConv | virusScan | youtube | puploader
FSM | 0.23 | 0.8 | 0.54 | 3.58 | 3.4 | 3.1 | 1.2 | 1.1859 | 1.47 | 2.08 | 1.1 | 1.539 | 2.7315 | 3 | 1.1
LR | 5.2 | 10.2 | 3.77 | 6.75 | 1.2 | 3.1 | 20.25 | 7.67 | 0.3737 | 17.81 | 3.5 | 4.2 | 12.1 | 13
FSM: under 4%
LR: 1% – 20%
Courtesy: Pathak et al
Notes: Say what are applications

## Slide 65: Fine-Grained Energy Estimation
FSM based on System calls | Linear Regression (State-of-art)
FSM: 80th percentile error less than 10% for all apps
LR: 10th percentile error less than 10% for all apps
CDF of energy estimation error per 50ms time interval
Courtesy: Pathak et al
Notes: What to say here
Make fig fonts larger

## Slide 66: Outline
The Rise of Ebugs
Methods of Measuring Power Usage
Power Models
  Usage based
  System call trace based
Profiling
Conclusion

## Slide 67: Energy Profiling
eprof published in Eurosys 2012
QCOM Trepn Profiler
  Trepn leverages hardware sensors built into the Snapdragon MDP
  Analyze power consumption of hardware blocks in the Snapdragon MDP, including:
    CPU (system and auxiliary)
    GPS
    Bluetooth
    Camera
    Audio
    Memory
    Network data (optimizes data transfer frequency)
Courtesy: Pathak et al

## Slide 68: Towards Energy Profiling
1970’s-80’s
2010
Energy Profiler…?
Gnu Profiler
(gprof PLDI’82)
Performance
Energy: One of the most critical issues in smartphones
Battery energy density only doubled in last 15 yrs
Courtesy: Pathak et al

## Slide 69: Approach (a) : Power Meters
Time (seconds)
Power Consumed by mobile
Courtesy: Pathak et al

## Slide 70: Approach (a) : Power Meters
Time (seconds)
Power Consumed by mobile
Courtesy: Pathak et al

## Slide 71: Approach (b) : Software Energy Profiling
Tracking power activities
Tracking app activities
Mapping power activities to app activities
Courtesy: Pathak et al

## Slide 72: Tracking Power Activities Power Modeling
State-of-art ‘utilization based’ power models are inaccurate on smartphones
  Only active utilization => power consumption
  Energy is consumed linearly w.r.t utilization
  Hard to map power triggers to fine grained app activities
System call triggered FSM based fine-grained power model [Eurosys ‘11]
  Use system calls as power triggers
  System calls drive Finite-State-Machine
Base
State
Prod.State
Tail
State
Courtesy: Pathak et al

## Slide 73: Tracking App Activities
Granularity of Energy Accounting
Multi Processing:
Multi Threading:
Third Party Ad Module
Collect information
Upload information
Download ads
Multiple Routines:
Courtesy: Pathak et al

## Slide 74: Tracking App Activities
Granularity of Energy Accounting
  eprof supports per Process/Thread/Routine granularity
I/O Devices
  Track system call to program entity
    Process – getpid()
    Thread – gettid()
    Routine – backtrace()
CPU
  Just like gprof [PLDI ‘82]
  Periodic sampling of routine call stack
Courtesy: Pathak et al

## Slide 75: Where is Energy Spent Inside My App?
Tracking power activities
  System call based online power model
Tracking app activities
  IO: Backtrace system calls
  CPU: Just like gprof [PLDI ‘82]
Mapping power activities to app activities
  Accounting Policy: Lingering Energy Consumption
Courtesy: Pathak et al

## Slide 76: Lingering Energy Consumption (a) Tail Energy
Effect on power/energy consumed by a component because of an activity lasts beyond the end of the activity
Components with tail: Sdcard
3G
WiFi
GPS
Power Consumed (mW)
Time
send 10 KB
Tail (upto 7 seconds)
send completed
foo()
Courtesy: Pathak et al

## Slide 77: Lingering Energy Consumption (b) Persistent State Wakelock
Aggressive Sleeping Policies: Smartphone OSes freeze system after brief inactivity
Power encumbered Programming: Programmer has to manage sleep/wake cycle of components
Power Consumed (mW)
Time
Acquire
wakelock
Release
wakelock
foo()
Keep the screen on !
Courtesy: Pathak et al

## Slide 78: Lingering Energy Consumption Case 1: Single Call Single Tail
Power Consumed (mW)
Time
send 10 KB
Tail (upto 7 seconds)
send completed
Energy represented in terms of an energy tuple (U, T)
(U, T) is attributed to entity (s) containing send system call
T
U
Courtesy: Pathak et al

## Slide 79: Lingering Energy Consumption Case 2: Multiple Calls Multiple Tails
Power Consumed (mW)
Time
send1
T1
U1
T2
U2
send2
How to split tail T2 among?
Average Policy: Split tail energy T2 in weighted ratio
Not easy to define weights
Policy gets complicated in presence of multiple system calls
Courtesy: Pathak et al

## Slide 80: Lingering Energy Consumption Case 2: Multiple Calls Multiple Tails
send1 : (U1, T1 )
send2 : (U2, T2 )
Last-Trigger-Policy: Assign asynchronous (tail) energy to the last active system call
Not easy to define weights
Policy gets complicated in presence of multiple system calls
Power Consumed (mW)
Time
send1
T1
U1
T2
U2
send2
Courtesy: Pathak et al

## Slide 81: eprof System (Android and Windows Mobile)
Logging Overhead:
2-15% Run Time,
1-13% Run Energy
Courtesy: Pathak et al

## Slide 82: eprof Implementation
SDK routine tracing: extend Android routine profiling framework
  http://developer.android.com/reference/android/os/Debug.html
NDK routine tracing: use gprof port of NDK
  http://code.google.com/p/android-ndk-profiler/
System call tracing: insert ADB logging APIs in framework code and log CPU (sched.switch) scheduling event in kernel using systemtap
  http://www.cyanogenmod.com/
AndroidManifest.xml
<uses-permission android:name="android.permission.WRITE_EXTERNAL_STORAGE" />
MainActivity.java
import android.os.Debug;
---
public void onCreate(Bundle savedInstanceState) {
…
Debug.startMethodTracing("HelloTest");
…
Debug.stopMethodTracing();
}
adb pull /mnt/sdcard/HelloTest.trace .
traceview HelloTest.trace

## Slide 83: eprof Implementation (Cont’d)
Augmented TraceView in Dalvik
  gprof-like tracing + syscall tracing
eprof API: StartEnergyTracing() StopEnergyTracing()
  Needs app recompile
Modified Android framework to trace each app by default
(no need for app source)
Courtesy: Pathak et al

## Slide 84: Using eprof
Profiled popular mobile apps using EProf
App | Num Routine calls | Num Threads | 3rd Party Modules
Browser | 1M | 34 | --
AngryBirds | 200K | 47 | 
FChess | 742K | 37 | 
NYTimes | 7.4M | 29 | 
MapQuest | 6M | 43 | 
Courtesy: Pathak et al

## Slide 85: Case Studies: (a) Android Browser Google Search
Chart: Energy Percentage (%)
| main | IdleReaper | HeapWorker | http1 | http0 | WVCore
CPU | 11 | 0.41 | 1 | 2.51 | 2 | 8.8
Net | 0 | 0.1 | 0.46 | 0.21 | 1 | 0.01
NetTail | 0 | 9 | 12.12 | 6.47 | 25.7 | 2.3
GPS | 0 | 0 | 0 | 0 | 0 | 8.7
GPSTail | 0 | 0 | 0 | 0 | 0 | 4.5
Activity | Energy %
HTTP | 38%
TCP Conditioning | 25%
User Tracking | 16%
GUI Rendering | 5%
Courtesy: Pathak et al

## Slide 86: Case Studies: (c) – Angry Birds
Activity | Energy %
User Tracking & Uploading Information | 45%
Fetching Ads | 28%
Game Play | 20%
Google Nexus (3G)
Courtesy: Pathak et al

## Slide 87: Case Studies (d): Facebook Wakelock Bug
Power Consumed (mW)
Time
AppSession.acquireWakelock()
FaceBookService: 25%
Google Nexus (WiFi)
Courtesy: Pathak et al

## Slide 88: App Energy Drain Characteristics
IO consumes the most energy
  Most apps spent 50% - 90% of their energy in IO
  A linear energy presentation does not help with debugging
IO energy is spent in bursts, called bundles
  A bundle is defined as a continuous period where IO component actively consumes energy
  Very few IO bundles per app
Power Consumed (mW)
Time
IO Energy Bundles
Chart: 
| Browser | AngryBirds | Fchess | NYTimes | Mapquest | Photo Upload
IO Energy | 69 | 80 | 75 | 67 | 72 | 70
Courtesy: Pathak et al

## Slide 89: IO Bundle Representation
Power Consumed (mW)
TimeLine
send1
T1
U1
T2
U2
send2
send3
T3
U3
One Network Bundle
Base State +0mA
Net Send
+265 mA
Net Tail
+150 mA
Net send
Net send
5 seconds inactivity
SendPacket()
Very Few Routines
?????
What is the app doing here?
Courtesy: Pathak et al

## Slide 90: Optimizing IO Energy using Bundles
Why is a bundle so long?
Why are there so many bundles?
Reduced energy consumption of 4 apps by 20-65% by minimizing number of bundles and reducing bundle lengths
Base State +0mA
Net Send
+265 mA
Net Tail
+150 mA
Net send
Net send
5 seconds inactivity
AdWhirl.FetchAd()
PID 0 (null loop)
Base State +0mA
Net Send
+265 mA
Net Tail
+150 mA
Net send
Net send
5 seconds inactivity
DownloadMgr. Read()
GZipStream.read()
JsonNode.Deserialize()
SQLiteDB.insert()
18
Courtesy: Pathak et al

## Slide 91: Summary
eprof: fine-grained energy profiler
  Enables opportunities for in-depth study of app energy consumption
Case studies of popular apps energy consumption
  65-75% of app energy spent in tracking user and fetching ads (for example angrybirds)
Bundles: IO energy representation
  Helps debugging smartphone app energy

## Slide 92: Conclusion and Future work
Ebugs need to be dealt with
  No-sleep ebug debugging studied
Fine-grained energy modeling and profiling very important to pinpoint energy bottleneck and ebugs
  Accounting is tricky
  I/O energy consumption is a major part
Display energy modeling and profiling is still lacking

## Slide 93: Online Resources
Soot: open source framework for analyzing java bytecode
  http://www.sable.mcgill.ca/soot/
ded: decompiling android application tool
  http://siis.cse.psu.edu/ded/
SDK routine tracinghttp://developer.android.com/reference/android/os/Debug.html
gprof: NDK routine tracing
  http://code.google.com/p/android-ndk-profiler/
systemtap: system call tracing

## Slide 94: Questions?

## Slide 95: Case Studies: (b) Map Quest
Chart: Energy Percentage (%)
| SHW. run() | NetworkRequest. DoInBackgrnd() | Search.Gas() | MapView. OnDraw() | JsonParser. parseJSON()
CPU | 1.3 | 5 | 3.2 | 9.57 | 4.13
Net | 0 | 3 | 1 | 0 | 0
NetTail | 0 | 15 | 4 | 0 | 0
GPS | 24 | 0 | 0 | 0 | 0
GPSTail | 3.03 | 0 | 0 | 0 | 0
Courtesy: Pathak et al