## Slide 1: Cellular Networks and Mobile Computing COMS 6998-7, Spring 2014
Instructor: Li Erran Li (lierranli@cs.columbia.edu)
http://www.cs.columbia.edu/~lierranli/coms6998-7Spring2014/
3/10/2014:Future Directions of Cellular Networks

## Slide 2: Outline
Review of Previous Lecture
Future Direction of Cellular Networks
  Introduction to SDN and NFV
  Software Defined Cellular Networks

## Slide 3: Review of Previous Lecture
What are the physical layer technologies in LTE?

## Slide 4: LTE Physical Layer
The key improvement in LTE radio is the use of OFDM
Orthogonal Frequency Division Multiplexing
  2D grid: frequency and time
  Narrowband channels: equal fading in a channel
    Allows simpler signal processing implementations
  Sub-carriers remain orthogonal under multipath propagation
One resource element
One resource block
12 subcarriers during one slot (180 kHz × 0.5 ms)
One OFDM symbol
One slot
12 subcarriers
time
frequency
Frame (10 ms)
Subframe (1 ms)
Slot (0.5 ms)
Time domain structure

## Slide 5: Review of Previous Lecture (Cont’d)
What are the mobility protocols used in cellular networks?

## Slide 6: Mobility Protocol: GTP
SGW
PDN GW
S5
eNodeB
S1-CP
MME
S1-U
S11
SGi
HSS
MSC
RNC
IuCS
NodeB
Iub
SGSN
IuPS
GTP
UE
GTP
GTP
Gn
Courtesy: Zoltán Turányi

## Slide 7: Mobility Protocol: Proxy Mobile IP (PMIP)
SGW
PDN GW
S5
eNodeB
S1-CP
MME
S1-U
S11
SGi
HSS
GTP
UE
PMIP
EPC – Evolved Packet Core
Non-3GPP Access
(cdma2000, WiMax, WiFi)
S2
PMIP
Courtesy: Zoltán Turányi

## Slide 8: Review of Previous Lecture (Cont’d)
Is carrier sensing multiple access (CSMA) used in cellular networks?

## Slide 9: Random Access
Base station
UE 2
UE 1
Why not carrier sensing like WiFi?
Base station coverage is much larger than WiFi AP
  UEs most likely cannot hear each other
How come base station can hear UEs’ transmissions?
  Base station receivers are much more sensitive and expensive
Notes: Time-frequency resource on which random-access preamble is transmitted on the PRACH channel

## Slide 10: Review of Previous Lecture (Cont’d)
What is the current LTE network architecture and its problems?

## Slide 11: Current LTE Architecture
Problem with Inter-technology (e.g. 3G to LTE) handoff
Problem of inefficient radio resource allocation
User Equipment (UE)
Gateway (S-GW)
Mobility Management Entity (MME)
Network Gateway
(P-GW)
Home Subscriber Server (HSS)
Policy Control and Charging Rules Function (PCRF)
Station (eNodeB)
Base
Serving
Packet Data
Control Plane
Data Plane
No clear separation of control plane and data plane
Hardware centric

## Slide 12: Outline
Review of Previous Lecture
Future Direction of Cellular Networks
  Introduction to SDN and NFV
  Software Defined Cellular Networks

## Slide 13
Million of lines of source code
6,000 RFCs
Billions of gates
Bloated
Power Hungry
Vertically integrated, complex, closed, proprietary
Networking industry with “mainframe” mind-set
Custom Hardware
OS
Routing, management, mobility management, access control, VPNs, …
Feature
Feature
Source: Nick Mckeown, Stanford

## Slide 14: The network Should Change to
Custom Hardware
Custom Hardware
Custom Hardware
Custom Hardware
Custom Hardware
OS
OS
OS
OS
OS
Network OS
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Source: Nick Mckeown, Stanford

## Slide 15: Software Defined Network (SDN)
Feature
Feature
Network OS
1. Open interface to packet forwarding
3. Consistent, up-to-date global network view
2. At least one Network OS probably many. Open- and closed-source
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Source: Nick Mckeown, Stanford

## Slide 16: Network OS
Network OS: distributed system that creates a consistent, up-to-date network view
  Runs on servers (controllers) in the network
  Floodlight, POX, Pyretic, Nettle ONIX, Beacon, … + more
Uses forwarding abstraction to:
  Get state information from forwarding elements
  Give control directives to forwarding elements
Source: Nick Mckeown, Stanford

## Slide 17: Software Defined Network (SDN)
Control Program A
Control Program B
Network OS
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Source: Nick Mckeown, Stanford

## Slide 18: Control Program
Control program operates on view of network
  Input: global network view (graph/database)
  Output: configuration of each network device
Control program is not a distributed system
  Abstraction hides details of distributed state
Source: Nick Mckeown, Stanford

## Slide 19: Forwarding Abstraction
Purpose: Abstract away forwarding hardware
Flexible
  Behavior specified by control plane
  Built from basic set of forwarding primitives
Minimal
  Streamlined for speed and low-power
  Control program not vendor-specific
OpenFlow is an example of such an abstraction
Source: Nick Mckeown, Stanford

## Slide 20
Independent
Software Vendors
BRAS
Firewall
DPI
CDN
Tester/QoE
monitor
WAN
Acceleration
Message
Router
Radio Network
Controller
Carrier Grade NAT
Session Border
Controller
Classical Network Appliance Approach
PE Router
SGSN/GGSN
Generic High Volume
Ethernet Switches
Generic High Volume Servers
Generic High Volume Storage
Orchestrated,
automatic
remote install
Network Functions
Virtualisation Approach
hypervisors
Notes: The Classical network appliance approach uses a proprietary chassis for every new service, some typical examples are shown above left. Although inside the appliances use similar chips they are packaged very differently outside. This creates complexity through the entire life cycle of network services e.g. Design, procurement, test, deployment, configuration, repair, maintenance, replacement, end-of-life, removal. There is no economies of scale (some boxes may only sell in the thousands as opposed to 9 Million IT servers every year). The need for start-ups to develop new hardware, including getting it NEBs and ETSI qualified, is a significant cost and deterrent to enter the telecoms market.
The Network Virtualisation (NV) approach replaces physical network appliances with software virtual appliances running on commodity IT servers. Using open IT techniques allows a competitive and innovative ecosystem to exploit the many x86 and Linux programmers in the world. The Virtual Appliances can be installed on IT servers using orchestration software, this will automatically and remotely install software, driven either by traffic demands or customer orders. To complement the standard high volume IT servers we will also use standard high volume storage and Ethernet switches. The standard high volume Ethernet switches will use merchant silicon which spreads the cost of switching ASICs over the widest possible Enterprise & Carrier market.
20

## Slide 21: Outline
Review of Previous Lecture
Future Direction of Cellular Networks
  Introduction to SDN and NFV
  Software Defined Cellular Networks
    Radio Access Networks
    Cellular Core Networks
    Cellular Wide Area Networks

## Slide 22: A Clean-Slate Design: Software-Defined Radio Access Networks

## Slide 23: Carrier’s Dilemma
Chart: Exabyte
| 2007.0 | 2008.0 | 2009.0 | 2010.0 | 2011.0 | 2012.0 | 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0
Total Mobile Data Traffic | 0.026 | 0.033068 | 0.091 | 0.23668 | 0.54605 | 0.88491 | 1.5772 | 2.797 | 4.7005 | 7.4385 | 11.1555
Chart: 
| -15.0 | -12.5 | -10.0 | -5.0 | -2.5 | 0.0 | 2.5 | 5.0 | 7.5 | 10.0 | 12.5 | 15.0 | 17.5 | 20.0
Shannon | 0.06 | 0.1 | 0.15 | 0.4 | 0.7 | 1 | 1.5 | 2 | 2.7 | 3.5 | 4.2 | 5 | 5.9 | 6.8
Shannon (3dB) | 0.05 | 0.09 | 0.13 | 0.2 | 0.4 | 0.7 | 1 | 1.5 | 2 | 2.6 | 3.3 | 4.1 | 5 | 5.7
4G | 0.05 | 0.09 | 0.125 | 0.19 | 0.39 | 0.68 | 0.96 | 1.45 | 1.92 | 2.45 | 3.12 | 3.8 | 4.6 | 5.1
Exponential Traffic Growth
Limited Capacity Gain
Poor wireless connectivity if left unaddressed

## Slide 24: LTE Radio Access Networks
access
core
Packet Data Network Gateway
Serving Gateway
Internet
Serving Gateway
Base Station (BS)
User Equipment (UE)
Goal: high capacity wide-area wireless network
  Dense deployment of small cells
Notes: This figure shows the architecture of today’s cellular core networks. User equipment connect to base stations via radio channels.
Base stations connect to the Internet via the cellular core network. There are two main components in the cellular core network, serving gateway and packet data network gateway.

## Slide 25: Dense and Chaotic Deployments
Dense: high SNR per user leads to higher capacity
  Small cells, femto cells, repeaters, etc

## Slide 26: Problems
Current LTE distributed control plane is ill-suited
  Hard to manage inter-cell interference
  Hard to optimize for variable load of cells
Dense deployment is costly
  Need to share cost among operators
  Maintain direct control of radio resources
    Lacking in current 3gpp RAN sharing standards
26

## Slide 27: SoftRAN: Big Base Station Abstraction
time
frequency
time
frequency
time
frequency
frequency
radio element
time
controller
Radio Element 1
Radio Element 2
Radio Element 3
Big Base Station
27

## Slide 28: Radio Resource Allocation
frequency
radio element
time
Flows
3D Resource Grid
28

## Slide 29: SoftRAN: SDN Approach to RAN
BS1
BS2
BS3
BS4
BS5
PHY & MAC
Control Algo
Coordination :
X2 Interface
PHY & MAC
Control Algo
PHY & MAC
Control Algo
PHY & MAC
Control Algo
PHY & MAC
Control Algo

## Slide 30: SoftRAN: SDN Approach to RAN
RE1
RE2
RE3
RE4
RE5
Network OS
Control Algo
Operator Inputs
PHY & MAC
RadioVisor
PHY & MAC
PHY & MAC
PHY & MAC
PHY & MAC
Radio Element (RE)

## Slide 31: SoftRAN Architecture Summary
RADIO ELEMENTS
CONTROLLER
Radio
Element API
Controller
API
Interference
Map
Flow
Records
Bytes
Rate
Queue
Size
Network
Operator
Inputs
QoS
Constraints
RAN Information Base
Radio Resource
Management
Algorithm
POWER
FLOW
Time
Frequency
Radio Element
3D Resource Grid
Periodic Updates
31

## Slide 32: SoftRAN Architecture: Updates
Radio element -> controller (updates)
  Flow information (downlink and uplink)
  Channel states (observed by clients)
Network operator -> controller (inputs)
  QoS requirements
  Flow preferences
32

## Slide 33: SoftRAN Architecture: Controller Design
RAN information base (RIB)
  Update and maintain global network view
    Interference map
    Flow records
Radio resource management
  Given global network view: maximize global utility
  Determine RRM at each radio element
33

## Slide 34: SoftRAN Architecture: Radio Element API
Controller -> radio element
  Handovers to be performed
  RF configuration per resource block
    Power allocation and flow allocation
  Relevant information about neighboring radio elements
    Transmit Power being used
34

## Slide 35: Refactoring Control Plane
Controller responsibilities:
  Decisions influencing global network state
    Load balancing
    Interference management
Radio element responsibilities:
  Decisions based on frequently varying local network state
    Flow allocation based on channel states
35

## Slide 36: SoftRAN Advantages
  Logically centralized control plane:
  Global view on interference and load
    Easier coordination of radio resource management
    Efficient use of wireless resources
  Plug-and-play control algorithms
    Simplified network management
  Smoother handovers
    Better user-experience
36

## Slide 37: SoftRAN: Evolving the RAN
Switching off radio elements based on load
  Energy savings
Dynamically splitting the network into Big-BSs
  Handover radio elements between Big-BSs
37

## Slide 38: Implementation: Modifications
SoftRAN is incrementally deployable with current infrastructure
  No modification needed on client-side
  API definitions at base station
    Femto API : Standardized interface between scheduler and L1 (http://www.smallcellforum.org/resources-technical-papers)
    Minimal modifications to FemtoAPI required
38

## Slide 39: RadioVisor Design
Slice manager
  Slice configuration, creation, modification, deletion and multi-slice operations
Traffic to slice mapping at RadioVisor and radio elements
3D resource grid allocation and isolation
  Considers traffic demand, interference graph and policy
RadioVisor
Slice
Manager
3D Resource Grid
Allocation & Isolation
Traffic to Slice
Mapping

## Slide 40: Slice Manager
Slice definition
  Predicates on operator, device, subscriber, app attributes
    A slice can be all M2M traffic of operator 1
Slice configuration at data plane and control plane
  PHY and scheduler: narrow band PHY for M2M slice
  Interference management algorithm
Slice algebra to support flexible slice operations
  Slice merge, split, (un)nest, duplicate

## Slide 41: Resource Grid Allocation and Isolation
Slices present resource demands every time window
Max min fair allocation
Example
  Red slice entitles 2/3 and demands 2/3 RE1 only
  Blue slice entitles 1/3 and demand 1/3 RE2 and 1 RE3
Radio
Element 1
Radio
Element 2
Radio
Element 3
Interference Edge
Time
Radio Element
Frequency

## Slide 42: Conclusion
Dense deployment calls for central control of radio resources
Deployment costs motivate RAN Sharing
We present the design of RadioVisor
  Enables direct control of per slice radio resources
  Configures per slice PHY and MAC, and interference management algorithm
  Supports flexible slice definitions and operations

## Slide 43: A Clean-Slate Design: Software-Defined Cellular Core Networks

## Slide 44: Cellular Core Network Architecture
access
core
Packet Data Network Gateway
Serving Gateway
Internet
Serving Gateway
Base Station (BS)
User Equipment (UE)
Notes: This figure shows the architecture of today’s cellular core networks. User equipment connect to base stations via radio channels.
Base stations connect to the Internet via the cellular core network. There are two main components in the cellular core network, serving gateway and packet data network gateway.

## Slide 45: SoftCell Overview
Internet
Controller
Simple hardware
+ SoftCell software
Notes: To be free from such control bottlenecks, we designed a new cellular network architecture called SoftCell. SoftCell applies the principle of software defined networking. Instead of using specialized data plane equipment, we will just use SDN switches. The SoftCell controller coordinates the data plane functions.
To enable direct control and flexibility, we propose a new architecture. It uses the principle of software defined networking. We will make use of commodity hardware which will be controlled by a controller. We make no changes to user equipment and the Internet.
It makes no change no user equipment, the radio access technology, or the Internet.
It only replaces the core network with commodity switches and middleboxes, controlled by a logically centralized controller.
Data Plane:
Switch: connectivity, traffic steering
Middlebox: various network services
~mix-match, combine functionality from different vendors
~easy to add new functionality
~up-/down-scale
~cheap
Control Plane:
Logically centralized controller, centralized control, rather than distributed protocol (hard to reason, debug, trouble shooting)
~Easy to manage
~Easy to change

## Slide 46: SoftCell Design Goal
Fine-grained service policy for diverse app needs
  Video transcoder, content filtering, firewall
  M2M services: fleet tracking, low latency medical device updates
with diverse needs!
Notes: Due to the diverse needs from subscriber mobile apps and M2M apps, we need to support fine-grained policies such as video transcoder, content filtering, fleet tracking.
We wan three things. First, we want unified control of data plane. Second, we would like to flexibly control routing and Internet exit points. Third,
Given the different needs of subscribers and the many user scenarios of machine type communication (also known as Internet of Things), we would like to design the network for high performance and scalable support of fine-grained policies.

## Slide 47: Characteristics of Cellular Core Networks
“North south” traffic pattern
Asymmetric edge
Traffic initiated from low-bandwidth access edge
Access Edge
Internet
Gateway Edge
~1K Users
~10K flows
~1 – 10 Gbps
~1 million Users
~10 million flows
~400 Gbps – 2 Tbps
Notes: How should we design SoftCell to support fine-grained policies? Can we just apply data center SDN solutions? Before we can answer the question, lets try to understand the characteristics of cellular networks.
First, the dominant traffic in cellular core networks are to or from the Internet, while in data centers, most traffic stays inside the data center. Second, cellular core networks have asymmetric edge. The access edge has lower bandwidth than the gateway edge. At the access, we are talking about 1K users, 10K flows and a few Gbps. At the gateway edge, we are talking about millions of Users, 10s of millions of flows and Tera bits per second. Third, traffic are initiated from low-bandwidth access edge.
First, cellular core networks have fine-grained and sophisticated policies. A cellular core network serves millions of customers with diverse needs.

## Slide 48: Challenge: Scalability
Packet classification: decide which service policy to be applied to a flow
  How to classify millions of flows per second?
Traffic steering: generate switch rules to implement policy paths, e.g. traversing a sequence of middleboxes
  How to implement million of paths?
    Limited switch flow tables: ~1K – 4K TCAM, ~16K – 64K L2/Ethernet
Network dynamics: setup policy paths for new users and new flow?
  How to hand million of control plane events per second?
Notes: SoftCell design faces key scalability challenges. First, we have to do packet classification. Given a flow, we have to decide which service policy to be applied to a flow. The challenge is how to classify millions of flows. Second, we have to generate switch rules to implement policy paths. A policy path needs to go through a sequence of middleboxes. As switches have limited flow table size, how to implement millions of paths in switches is a big challenge. Third, users and M2M devices come and go. They generate millions of control plane events per second. How to scalably handle them is challenging.

## Slide 49: SoftCell: Design-in-the-Large
Scalable system design
  Classifying flows at access edge
  Offloading controller tasks to switch local agent
Intelligent algorithms
  Enforcing policy consistency under mobility
  Multi-dimension aggregation to reduce switch rule entries
~1K Users
~10K flows
~1 – 10 Gbps
Gateway Edge
~1 million Users
~10 million flows
~up to 2 Tbps
Access Edge
Controller
LA
LA
LA
LA
Notes: We will apply the principle of design-in-the-large to address the challenges. We leverage the strength of the numerous access switches. In our system design, we move the packet classification function to the access edge. We offload controller tasks to switch local agent. For example, we can cache service policies. We do not need the controller involvement for flows which matches cached policies.
We use intelligent algorithms to enforce policy consistency under mobility and reduce the number of rules we put in switches.
We would like to move the service functions out of P-GW. To support fine-grained polices, we will need intelligent algorithms to minimizes the number of service routing entries in switch tables.

## Slide 50: Multi-Dimensional Aggregation
Use multi-dimensional tags rather than flat tags
Exploit locality in network topology and traffic pattern
Selectively match on one or multiple dimensions
  Supported by the multiple tables in today’s switch chipset
Policy Tag
BS ID
User ID
Aggregate flows going to the same Users.
Aggregate flows going to the same (group of) base stations
Aggregate flows that share a common policy (even across Users and BSs)
Notes: Let me show you the basic idea of multi-dimensional aggregation. We aggregate in three dimensions, policy tag, BS ID and UE ID. Policy tag aggregate flows that share a common policy, even across devices or base stations. BS ID aggregates flows going to the same base station. UE ID aggregates flows going to the same device. This is especially useful in UE handoff. Multi-dimensional tags allow us to exploit locality in the network. And we can selectively match on one or multiple dimensions in order to further reduce flow table size.

## Slide 51: Conclusion and Future Work
SoftCell uses commodity switches and middelboxes to build flexible and cost-effective cellular core networks
SoftCell cleanly separates fine-grained service policies from traffic management policies
SoftCell achieves scalability with
Data Plane
Control Plane
Asymmetric Edge Design
Multi-dimensional Aggregation
Hierarchical Controller Design
Deploy SoftCell in real test bed
Exploit multi-stage tables in modern switches
  Reduce m×n rules to m+n rules
Notes: In conclusion, CellSDN uses commodity switches and middleboxes to build flexible and cost-effective cellular core networks.
It supports fine-grained service policies and traffic management policies.
It achieves scalability with asymmetric edge design, multi-dimensional aggregation and hierarchical controller.

## Slide 52: A Clean-Slate Design: Software-Defined WAN

## Slide 53: Current Mobile WANs
Organized into rigid and very large regions
Minimal interactions among regions
Centralized policy enforcement at PGWs
Two Regions

## Slide 54: Mobile WANs Problems
Suboptimal routing in large carriers
  Lack of sufficiently close PGW is a major cause of path inflation
Lack of support for seamless inter-region mobility
  Users crossing regions experience service interruption
Scalability and reliability
  The sheer amount of traffic and centralized policy enforcement
Ill-suited to adapt to the rise of new applications
  E.g., machine-to-machine
  All users’ outgoing traffic traverses a PGW to the Internet, even for reaching a user served by a close base station in a neighbor region

## Slide 55: SoftMoW Motivation
Question: How to make the packet core scalable, simple, and flexible for tens of thousands of base stations and millions of mobile users?
Mobile networks should have fully connected core topology, small logical regions, and more egress points
Operators should leverage SDN to manage the whole network with a logically-centralized controller:
  Directs traffic through efficient network paths that might cross region boundaries
  Handles high amount of intra-region signaling load from mobile users
  Supports seamless inter-region mobility and optimizes its performance
  Performs network-wide application-based such as region optimization

## Slide 56: SoftMoW Solution
Hierarchically builds up a network-wide control plane
  Lies in the family of recursive SDN designs (e.g. XBAR, ONS’13)
In each level, abstracts both control and data planes and exposes a set of “dynamically-defined” logical components to the control plane of the level above.
  Virtual Base stations (VBS), Gigantic Switches (GS), and Virtual Middleboxes (VMB)
Core Net
GS
Latency Matrix
Radio Net
VBS
Union of Coverage
Policy
VMB
Sum of capacities

## Slide 57: SoftMoW Solution
New Dynamic Feature: In each level, the control logic can modify its logical components for optimization purposes
  E.g., merge/spilt and move operations
Move and Split
Merge/Split

## Slide 58: First Level-SoftMoW Architecture
Replace inflexible and expensive hardware devices (i.e., PGW, SGW) with SDN switches
Perform distributed policy enforcement using middle-box instances
Partition the network into independent and dynamic logical regions
A child controller manages the data plane of each regions
Bootstrapping phase:
based on location and processing capabilities of child controllers

## Slide 59: Second Level-SoftMoW Architecture
A parent runs a global link discovery protocol
  Inter-region links are not detected by BDDP and LLDP
A parent participates in the inter-domain routing protocol
A parent builds virtual middlebox chains and egress-point policies, and dictates to GSs
Notes: Add inter-domain routing protocol.

## Slide 60: Hierarchical Traffic Engineering
Latency (P1,E2)=300
Latency (P1,E4)=100
Web
Voice
GS Rules
A parent pushes a global label into each traffic group
Child controllers perform label swapping
  Ingress point: pop the global label and push some local labels for intra-region paths
  Egress point: pop the local labels and push back the global label
Push W
Pop W
Push W
Push W
Push W2
Push W1
Pop W2
Pop W
Pop W1

## Slide 61: Time-of-day Handover Optimization
Handover graph
Q: How can an operator reduce inter-region handovers in peak hours?
Abstraction update
GS Rule:
Move Border VBS1
coordination

## Slide 62: Conclusion
SoftMoW:
Brings both simplicity and scalability to the control plane of very large cellular networks
  decouples control and data planes at multiple levels ( focused only on two levels here)
Makes the deployment and design of network-wide applications feasible
  E.g., seamless inter-region mobility, time-of-day handover optimization, region optimization, and traffic engineering

## Slide 63: Summary
Mobile computing depends on cellular networks
Cellular network performance still far from meeting demands of mobile computing
Cellular network architecture is evolving to meet demands of mobile computing
  SDN and NFV
    AT&T’s domain 2.0

## Slide 64: Questions?

## Slide 65
User Equipment (UE)
Serving
Gateway (S-GW)
Mobility Management Entity (MME)
Packet Data
Network Gateway
(P-GW)
Home Subscriber Server (HSS)
Policy Control and Charging Rules Function (PCRF)
Base
Station (eNodeB)