## Slide 1: Software Defined Networking COMS 6998-8, Fall 2013
Instructor: Li Erran Li (lierranli@cs.columbia.edu)
http://www.cs.columbia.edu/~lierranli/coms6998-8SDNFall2013/
11/26/2013: SDN Debugging and Security

## Slide 2: Outline
Review on SDN Wireless Networks
  Data Plane Abstraction
  Controller Design
SDN Debugging
  Data Plane Approach (Breakpoints + Packet Trace): NDB
  Control Plane Approach (Model Checking + Symbolic Execution): NICE
SDN Security
  Defense again Control Plane Attacks
  Security as a Service (Next Lecture)

## Slide 3: Review of Previous Lecture: Data Plane Abstraction
Programmable wireless dataplane using off-the-shelf components
  Single platform capable of LTE, 3G, WiMax, WiFi
  OpenFlow for Layer 3
  Inexpensive ($300-500)
Control
CPU
Forwarding
Dataplane
Baseband &
Layer 2 DSP
RF
RF
RF
Exposes a match/action interface to program how a flow is forwarded, scheduled & encoded
Source: Katti, Stanford

## Slide 4: Review of Previous Lecture: Data Plane Abstraction-Modular Declarable Interface
Inserting RULES
Composing ACTIONS
  Blocks
OFDM Demod
A
Demap (BPSK)
B
Demap (64QAM)
C
Deinterleave
(WiFi)
D
Deinterleave (UEP)
E
Decode
(1/2)
F
Decode
(3/4)
G
Descramble
H
CRC Check
I
Hdr Parse
J
A
B
D
F
H
I
J
A
C
D
G
H
I
J
A
C
E
G
H
I
J
F
H
J
6M
54M
UEP
A
B
D
F
H
I
J
6M
A
B
D
F
H
I
J
C
G
6M, 54M
  Rules: Branching logic
Data
flow
Control
flow
  Actions: DAGs of blocks
Source: Katti, Stanford
Notes: Convenient abstraction level means that declarative description of protocol is possible with blocks as units; hardware is abstracted in the blocks so that the imperative execution plan need not be specified.
Sufficient expressiveness means that most protocol variants of interest can be realized with this API.

## Slide 5: Review of Previous Lecture: Data Plane Abstraction: State machines & deadlines
Rules and actions encode the protocol state machine
  Rules define state transitions
  Each state has an associated action
Deadlines are expressed on state sequences
deadline
A
C
B
D
G
F
H
I
J
Start
decoding
Finish
decoding
5
Source: Katti, Stanford

## Slide 6: Review of Previous Lecture: Controller Abstraction and Architecture
RADIO ELEMENTS
CONTROLLER
Radio
Element API
Controller
API
Interference
Map
Flow
Records
Bytes
Rate
Queue
Size
Network
Operator
Inputs
QoS
Constraints
RAN Information Base
Radio Resource
Management
Algorithm
POWER
FLOW
Time
Frequency
Radio Element
3D Resource Grid
Periodic Updates

## Slide 7: Outline
Review on SDN Wireless Networks
  Data Plane Abstraction
  Controller Design
SDN Debugging
  Data Plane Approach (Breakpoints + Packet Backtrace): ndb
  Control Plane Approach (Model Checking + Symbolic Execution): NICE
SDN Security
  Defense again Control Plane Attacks
  Security as a Service

## Slide 8: Bug story: incomplete handover
A
B
Switch X
WiFi AP Y
WiFi AP Z
Source: Handigol, et al., Stanford

## Slide 9: Debugging SDNs
Bugs can be anywhere in the SDN stack
  Hardware, control plane logic, race conditions
Switch state might change rapidly
Bugs might show up rarely
Source: Handigol, et al., Stanford

## Slide 10: How can we exploit the SDN architecture to systematically track down the root cause of bugs?
Source: Handigol, et al., Stanford

## Slide 11: ndb: Network Debugger
  Goal
  Capture and reconstruct the sequence of events leading to the errant behavior
Allow users to define a Network Breakpoint
  A (header, switch) filter to identify the errant behavior
Produce a Packet Backtrace
  Path taken by the packet
  State of the flow table at each switch

## Slide 12: Debugging software programs
Function A():
i = …; j = …;
u = B(i, j)
Function B(x, y):
k = …;
v = C(x, k)
Function C(x, y):
…
w = abort()
Breakpoint
  “line 25, w = abort()”
Backtrace
  File “A”, line 10, Function A()
  File “B”, line 43, Function B()
  File “C”, line 21, Function C()
Source: Handigol, et al., Stanford

## Slide 13: Debugging networks
Breakpoint
  “ICMP packets A->B, arriving at X,
  but not Z”
Backtrace
  Switch X: {
  inport: p0,
  outports: [p1]
  mods: [...]
  matched flow: 23 [...]
  matched table version: 3
  }
  Switch Y: {
  inport p1,
  outports: [p3]
  mods: ...
  ...
  }
Y
X
A
B
Switch X
WiFi AP Y
WiFi AP Z

## Slide 14: Using ndb to debug common issues
Reachability
  Symptom: A is not able to talk to B
  Breakpoint: “Packet A->B, not reaching B”
Isolation
  Symptom: A is talking to B, but it shouldn’t
  Breakpoint: “Packet A->B, reaching B”
Race conditions
  Symptom: Flow entries not reaching on time
  Breakpoint: “Packet-in at switch S, port P”
Source: Handigol, et al., Stanford

## Slide 15: So, how does ndb work?

## Slide 16
Control Plane
Flow Table State Recorder
Match
ACT
Match
ACT
Postcard
Collector
S
Breakpoint
Switch = S
IP src = A, IP dst = B
TCP Port = 22
B
A
Source: Handigol, et al., Stanford

## Slide 17
Postcard
Collector
Control Plane
Flow Table State Recorder
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
B
A
Source: Handigol, et al., Stanford

## Slide 18
Postcard
Collector
Control Plane
Flow Table State Recorder
<Flow Table State, Version>
<Datapath ID, Packet ID, Version>
Source: Handigol, et al., Stanford

## Slide 19: Who benefits
Network developers
  Programmers debugging control programs
Network operators
  Find policy errors
  Send error report to switch vendor
  Send error report to control program vendor
Source: Handigol, et al., Stanford

## Slide 20: Performance and scalability
Control channel
  Negligible overhead
  No postcards
  Extra flow-mods
Postcards in the datapath
  Single collector server for the entire Stanford backbone
  Selective postcard generation to reduce overhead
  Parallelize postcard collection
Source: Handigol, et al., Stanford

## Slide 21: Summary
  ndb: Network Breakpoint + Packet Backtrace
Systematically track down root cause of bugs
Practical and deployable today
Source: Handigol, et al., Stanford

## Slide 22: Outline
Review on SDN Wireless Networks
  Data Plane Abstraction
  Controller Design
SDN Debugging
  Data Plane Approach (Breakpoints + Packet Backtrace): ndb
  Control Plane Approach (Model Checking + Symbolic Execution): NICE
SDN Security
  Security as a service

## Slide 23: Software Faults
Will make communication unreliable
Major hurdle for success of SDN
We need effective ways to test SDN networks NICE: automatically testing OpenFlow Apps
Source: Canini, et al.

## Slide 24: Quick OpenFlow 101
Host B
Host A
Switch 2
Flow Table
Rule 1
Rule 2
Rule N
Switch 1
Packet
OpenFlow program
Controller
Install rule; forward packet
Default: forward to controller
Match
Actions
Counters
Dst: Host B
Fwd: Switch 2
pkts / bytes
System is distributed and asynchronous  can misbehave under corner cases
Execute packet_in event handler
Source: Canini, et al.

## Slide 25: Bugs in OpenFlow Apps
OpenFlow program
Host B
Host A
Switch 2
Controller
Switch 1
Packet
Install rule
?
Goal: systematically test possible behaviors to detect bugs
Install rule
Delayed!
Drop packet
Inconsistent distributed state!
Source: Canini, et al.

## Slide 26: Systematically Testing OpenFlow Apps
State-space exploration via Model Checking (MC)
Target
system
Unmodified OpenFlow program
Complex environment
Environment model
Switch 1
Switch 2
Host A
Host B
  Carefully-crafted streams of packets
  Many orderings of packet arrivals and events
Source: Canini, et al.

## Slide 27: Scalability Challenges
Huge space of possible packets
Huge space of possible event orderings
Data-plane driven
Complex network behavior
Enumerating all inputs and event orderings is intractable
Equivalence classes of packets
Domain-specific search strategies
Source: Canini, et al.

## Slide 28
Network topology
Correctness properties (e.g., no loops)
Traces of property violations
Input
Output
NICE
State-space search
No bugs In Controller Execution
NICE found 11 bugs in 3 real OpenFlow Apps
Unmodified OpenFlow program

## Slide 29
Network topology
Correctness properties (e.g., no loops)
Traces of property violations
Input
Output
NICE
No bugs In Controller Execution
Unmodified OpenFlow program
State-space search

## Slide 30: State-Space Model
Model Checking
State 0
State 2
State 6
State 7
State 4
State 9
State 1
State 3
State 5
State 8

## Slide 31: System State
State
Controller (global variables)
Environment:
Switches (flow table, OpenFlow agent)
Simplified switch model
End-hosts (network stack)
Simple clients/servers
Communication channels (in-flight pkts)
Source: Canini, et al.

## Slide 32: Transition System
State 0
State 2
State 6
State 7
State 4
State 9
State 1
State 3
ctrl packet_in(pkt A)
host send
switch process_of
switch process_pkt
ctrl packet_in(pkt B)
Run actual packet_in handler
State 5
State 8
Data-dependent transitions!

## Slide 33: Combating Huge Space of Packets
Packet arrival handler
is dst broadcast?
Flood packet
Install rule and forward packet
dst in mactable?
Equivalence classes of packets:
Broadcast destination
Unknown unicast destination
Known unicast destination
yes
no
no
yes
Code itself reveals equivalence classes of packets
pkt
Source: Canini, et al.

## Slide 34: Code Analysis: Symbolic Execution (SE)
Packet arrival handler
is λ.dst broadcast?
yes
no
Symbolic packet λ
Flood packet
λ .dst ∈ {Broadcast}
λ.dst in mactable?
no
yes
λ .dst ∉ {Broadcast}
Install rule and forward packet
λ .dst ∉ {Broadcast} ∧ λ .dst ∉ mactable
λ .dst ∉ {Broadcast}
∧ λ .dst ∈ mactable
1 path =
1 equivalence class of packets =
1 packet to inject
Source: Canini, et al.

## Slide 35: Combining SE with Model Checking
New packets
Enable new transitions: host / send(pkt B) host / send(pkt C)
Symbolic execution of packet_in handler
State 0
State 1
Controller state 1
State 2
host discover_packets
State 3
host send(pkt B)
State 4
host send(pkt C)
discover_packets transition:
Controller state changes
host send(pkt A)
Source: Canini, et al.

## Slide 36: Combating Huge Space of Orderings
MC + SE
PKT-SEQ
FLOW-IR
NO-DELAY
UNUSUAL
OpenFlow-specific search strategies for up to 20x state-space reduction:
Source: Canini, et al.

## Slide 37
Network topology
Traces of property violations
Input
Output
NICE
No bugs In Controller Execution
Unmodified OpenFlow program
State-space search
Correctness properties (e.g., no loops)

## Slide 38: Specifying App Correctness
Library of common properties
  No forwarding loops
  No black holes
  Direct paths (no unnecessary flooding)
  Etc…
Correctness is app-specific in nature
Source: Canini, et al.

## Slide 39: API to Define App-Specific Properties
State 0
State 1
ctrl packet_in(pkt A)
def init(): init local vars register(“packet_in”) def on_packet_in():
check system-wide state
Register callbacks to observe transitions
Execute after transitions
Source: Canini, et al.

## Slide 40: Prototype Implementation
Built a NICE prototype in Python
Target the Python API of NOX
Unmodified OpenFlow program
Stub NOX API
NICE
Controller state & transitions
Source: Canini, et al.

## Slide 41: Experiences
Tested 3 unmodified NOX OpenFlow Apps
  MAC-learning switch
  LB: Web server load balancer [Wang et al., HotICE’11]
  TE: Energy-aware traffic engineering [CoNEXT’11]
Setup
  Iterated with 1, 2 or 3-switch topologies; 1,2,… pkts
  App-specific properties
    LB: All packets of same request go to same server replica
    TE: Use appropriate path based on network load
Source: Canini, et al.

## Slide 42: Results
NICE found 11 property violations  bugs
  Few secs to find 1st violation of each bug (max 30m)
  Few simple mistakes (not freeing buffered packets)
  3 insidious bugs due to network race conditions
    NICE makes corner cases as likely as normal cases
Source: Canini, et al.

## Slide 43: MAC-learning switch (3 bugs)
OpenFlow program
Host A
A->B | port 2
1
2
2
1
A->B | port 1
Host B
BUG-I: Host unreachable after moving
3
Source: Canini, et al.

## Slide 44: MAC-learning switch (3 bugs)
OpenFlow program
Host A
B->A | port 1
1
2
2
1
B->A | port 2
Host B
BUG-I: Host unreachable after moving
3
BUG-II: Delayed direct path
A->B | port 2
A->B | port 1
Source: Canini, et al.

## Slide 45: MAC-learning switch (3 bugs)
OpenFlow program
Host A
1
2
2
1
BUG-I: Host unreachable after moving
3
BUG-II: Delayed direct path
BUG-III: Excess flooding
3
2
1
Source: Canini, et al.

## Slide 46: Web Server Load Balancer (4 bugs)
OpenFlow program
Host A
1
3
Host B
2
4
Server 1
Server 2
BUG-IV: Next TCP packet always dropped after reconfiguration
BUG-V: Some TCP packets dropped after reconfiguration
BUG-VI: ARP packets forgotten during address resolution
BUG-VII: Duplicate SYN packets during transitions
Custom property: all packets of same request go to same server replica
Source: Canini, et al.

## Slide 47: Conclusions
http://code.google.com/p/nice-of/
NICE automates the testing of OpenFlow Apps
Explores state-space efficiently
Tests unmodified NOX applications
Helps to specify correctness
Finds bugs in real applications
SDN: a new role for software tool chains to make networks more dependable.
NICE is a step in this direction!
Source: Canini, et al.

## Slide 48: Outline
Review on SDN Wireless Networks
  Data Plane Abstraction
  Controller Design
SDN Debugging
  Data Plane Approach (Breakpoints + Packet Trace): NDB
  Control Plane Approach (Model Checking + Symbolic Execution): NICE
SDN Security
  Defense against Control Plane Attacks
  Security as a Service
Source: S. Shin, et al.

## Slide 49: Avant-Guard
Security extension to the OpenFlow data plane
  Connection migration
    To address scalability
    issue
  Actuating trigger
    To address responsiveness
    issue
Control Plane Interface
Flow Table (TCAM and SRAM)
Flow Table Lookup
Packet Processing
Control Plane
Data Plane
Connection Migration
Actuating Trigger
Avant-Guard
Source: S. Shin, et al.

## Slide 50: Connection Migration - Idea
Inspired by TCP SYN Cookie
Concept
  TCP connection will stat from a SYN packet, and an initiator will wait for TCP SYN/ACK packet
  TCP-handshake does not issue any kind of data delivery
  Then, how about treating this TCP-handshake at network devices
  instead of target hosts
SYN
SYN/ACK
ACK
SYN
SYN/ACK
ACK
Source: S. Shin, et al.

## Slide 51: Connection Migration – Access Table
List of visiting clients
  Format
    Client IP address: # of TCP connection trials
      # of TCP connection trials include wrong trials (ACK, FIN, and RST)
    Simple data structure : 6 bytes (4 bytes for IP and 2 bytes for
    counter)
Overhead
  1,000,000 client IP addresses  less than 6 MB of memory
A controller application can read this table
10.0.0.1
15
12.2.0.1
1
40.0.0.4
100
IP Address
Counter
Source: S. Shin, et al.

## Slide 52: Connection Migration – State Diagram
4 state
  Classification
    Distinguish useful TCP connections
  Report
    Report to a controller
  Migration
    Migrate a TCP connection
    if it is a useful (or valid) connection
  Relay
    Relay all TCP packets between a
    connection source and a destination
Classification stage
Report
stage
Migration
stage
Replay
stage
TCP sessions
Failed
TCP sessions
Then, Ignore
Established
TCP sessions
Allow
Migration
Success or
Failure
Allow
Relay
Source: S. Shin, et al.

## Slide 53: Connection Migration – Flow Chart
Flow chart
- The case of receiving TCP SYN/RST/FIN packet
Flow chart
- The case of receiving TCP ACK packet

## Slide 54: Connection Migration – Packet Diagram
A
B
Control Plane
(1) TCP SYN
(2) TCP SYN/ACK
(3) TCP ACK
(6) TCP SYN
(7) TCP SYN/ACK
(8) TCP ACK
(11) TCP ACK
TCP Data
(12) TCP ACK
TCP Data
(4)
(5)
(9)
(10)
A-1: A --> B: Migrate
A-2: A --> B: Relay
Data Plane
Classification stage
Relay stage
Migration stage
Relay stage
Report stage
Report stage
Source: S. Shin, et al.

## Slide 55: Delayed Connection Migration
Concept
  Delay Connection Migration until the data plane receives (a) data
  packet(s)
Why?
  Good for reducing the effects of some advanced attacks
    E.g., fake TCP connection setup
A
B
Control Plane
(1) TCP SYN
(2) TCP SYN/ACK
(3) TCP ACK
(7) TCP SYN
(8) TCP SYN/ACK
(9) TCP ACK
(4) TCP ACK
TCP Data
(12) TCP ACK
TCP Data
(5)
(6)
(10)
(11)
A-1: A --> B: Migrate
A-2: A --> B: Relay
Data Plane
Classification stage
Migration stage
Relay stage
Report stage
Report stage

## Slide 56: Actuating Trigger - Idea
Two functions
  Report the following items to the control plane
  asynchronously
    Network status
    Payload information
  Activate flow rules based on some predefined conditions
    Security application can use this feature to turn on security
    policies without delay
Source: S. Shin, et al.

## Slide 57: Activating Trigger – Operations
4 main operations
  In the control plane
    Define a condition
    Register the condition
  In the data plane
    Check the condition
    When the condition is satisfied,
      Report a network
      status or payload
      Activate a flow rule
Flow Rule
Condition
Predefined Flow Rule
Control Plane
Host
(1) Define condition
(2) Register condition
(3) Check condition
(4-2) Activate a flow rule
(4-1) Report status
Data Plane
match
Source: S. Shin, et al.

## Slide 58: Activating Trigger - Example
Example of reporting payload
  1) defined a condition : want to see payloads of packet from 10.0.0.1
  2) register this condition to the data plane
  3) packet is delivered from 10.0.0.1
  4) payload is delivered to the control plane
10.0.0.1 *
1: Condition for payload
Control Plane
10.0.0.1
(1)
Data Plane
10.0.0.2
(2)
(3)
(4)
Source: S. Shin, et al.

## Slide 59: Implementation
Data plane
  Implemented in the Software-based OpenFlow reference switch
    Covers OpenFlow spec. 1.0.0
Control plane
  Implemented in the POX controller
Extend OpenFlow protocols for
  Connection migration
    E.g., OFPFC_MIGRATE, …
  Actuating trigger
    E.g., OFPFC_REG_PAYLOAD, …
  Please refer to our paper for more information (Table 1)
Source: S. Shin, et al.

## Slide 60: Evaluation – Use Case
Network saturation attack case
  A normal client sends HTTP requests to a web server
  An attacker tries a SYN flooding attack to a web server
Test Scenario
Packet delivered rate to a web server
Nearly 0 loss
Normal
Attacker
OF switch
POX Controller
Web Server
Normal
Attacker
OF switch
(Avant-Guard)
Modified
POX Controller
Web Server

## Slide 61: Evaluation – Use Case
Detecting SYN flooding/scanning
  Approach
    SYN flooding packets are automatically rejected
    Network scanning attackers will be confused by our response
    packets
      They may think that all network hosts are alive and all network ports
      are open (a kind of White hole)
SYN
SYN/ACK
(1)
(2)
No packet delivery
SYN
SYN/ACK
(1)
(2)
SYN Flooding
Network Scanner
No packet delivery
Attacker receives SYN/ACK packets even though there are no hosts
 White hole

## Slide 62: Evaluation – Use Case
Intelligent Honeynet
  Approach
    When we try to do connection migration,
      If we can not find a real target host, we may consider this
      connection as suspicious
    Then, a security application can redirect this connection to our honeynet automatically
    Finally, this attacker will perform malicious operations inside a honenet
SYN
SYN/ACK
ACK
SYN
(1)
(2)
(3)
(4)
No host
SYN
(5)
SYN/ACK
(6)
(7)
ACK
attacker
honeynet
Source: S. Shin, et al.

## Slide 63: Evaluation - Overhead
Connection migration
normal | connection migration | overhead
1608.6 us | 1618.74 us | 0,626 %
Actuating trigger
item | time
Traffic-rate based condition check | 0.322 us
Payload based condition check | = 0
Rule activation | 1.697 us
Source: S. Shin, et al.

## Slide 64: Summary
Avant-Guard
  New data plane architecture for addressing the problems of OpenFlow, when devising network security applicatons
    Address the scalability issue with the connection migration scheme
    Address the responsiveness issue with the actuating trigger scheme
  Can be a new candidate architecture of the future data plane for SDN
Source: S. Shin, et al.

## Slide 65: Questions?