## Slide 1: Software Defined Networking COMS 6998-8, Fall 2013
Instructor: Li Erran Li (lierranli@cs.columbia.edu)
http://www.cs.columbia.edu/~lierranli/coms6998-8SDNFall2013/
12/3/2013: SDN Security, End Host Networking Stack and Storage

## Slide 2: Outline
Reminder: Course Evaluation Due on Dec 9
Review on SDN Debugging
  Data Plane Approach (Breakpoints + Packet Trace): NDB
  Control Plane Approach (Model Checking + Symbolic Execution): NICE
SDN Security
  Defense again Control Plane Attacks (Review)
  Security as a Service
SDN End Host Networking Stack
SDN Storage

## Slide 3: Review of Previous Lecture: ndb
  Network Debugger (ndb) Goal
  Capture and reconstruct the sequence of events leading to the errant behavior
Allow users to define a Network Breakpoint
  A (header, switch) filter to identify the errant behavior
Produce a Packet Backtrace
  Path taken by the packet
  State of the flow table at each switch

## Slide 4: Review of Previous Lecture: ndb (Cont’d)
Control Plane
Flow Table State Recorder
Match
ACT
Match
ACT
Postcard
Collector
S
Breakpoint
Switch = S
IP src = A, IP dst = B
TCP Port = 22
B
A

## Slide 5: Review of Previous Lecture: ndb (Cont’d)
Postcard
Collector
Control Plane
Flow Table State Recorder
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
<Match, Action>
…
…
B
A

## Slide 6: Review of Previous Lecture: ndb (Cont’d)
Postcard
Collector
Control Plane
Flow Table State Recorder
<Flow Table State, Version>
<Datapath ID, Packet ID, Version>

## Slide 7
Network topology
Correctness properties (e.g., no loops)
Traces of property violations
Input
Output
NICE
No bugs In Controller Execution
Unmodified OpenFlow program
State-space search
Review of Previous Lecture: NICE

## Slide 8
State
Controller (global variables)
Environment:
Switches (flow table, OpenFlow agent)
Simplified switch model
End-hosts (network stack)
Simple clients/servers
Communication channels (in-flight pkts)
Review of Previous Lecture: NICE (Cont’d)

## Slide 9: Combining Symbolic Execution with Model Checking
New packets
Enable new transitions: host / send(pkt B) host / send(pkt C)
Symbolic execution of packet_in handler
State 0
State 1
Controller state 1
State 2
host discover_packets
State 3
host send(pkt B)
State 4
host send(pkt C)
discover_packets transition:
Controller state changes
host send(pkt A)
Review of Previous Lecture: NICE (Cont’d)

## Slide 10: Review of Previous Lecture: Avant-Guard
Security extension to the OpenFlow data plane
  Connection migration
    To address scalability
    issue
  Actuating trigger
    To address responsiveness
    issue
Control Plane Interface
Flow Table (TCAM and SRAM)
Flow Table Lookup
Packet Processing
Control Plane
Data Plane
Connection Migration
Actuating Trigger
Avant-Guard

## Slide 11: Review of Previous Lecture: Connection Migration
A
B
Control Plane
(1) TCP SYN
(2) TCP SYN/ACK
(3) TCP ACK
(6) TCP SYN
(7) TCP SYN/ACK
(8) TCP ACK
(11) TCP ACK
TCP Data
(12) TCP ACK
TCP Data
(4)
(5)
(9)
(10)
A-1: A --> B: Migrate
A-2: A --> B: Relay
Data Plane
Classification stage
Relay stage
Migration stage
Relay stage
Report stage
Report stage

## Slide 12: Review of Previous Lecture: Delayed Connection Migration
Concept
  Delay Connection Migration until the data plane receives (a) data
  packet(s)
Why?
  Good for reducing the effects of some advanced attacks
    E.g., fake TCP connection setup
A
B
Control Plane
(1) TCP SYN
(2) TCP SYN/ACK
(3) TCP ACK
(7) TCP SYN
(8) TCP SYN/ACK
(9) TCP ACK
(4) TCP ACK
TCP Data
(12) TCP ACK
TCP Data
(5)
(6)
(10)
(11)
A-1: A --> B: Migrate
A-2: A --> B: Relay
Data Plane
Classification stage
Migration stage
Relay stage
Report stage
Report stage

## Slide 13: Outline
Reminder: Course Evaluation Due on Dec 9
Review on SDN Debugging
  Data Plane Approach (Breakpoints + Packet Trace): NDB
  Control Plane Approach (Model Checking + Symbolic Execution): NICE
SDN Security
  Defense again Control Plane Attacks (Review)
  Security as a Service
SDN Storage

## Slide 14: Roadmap
Security in the paradigm of SDN/OpenFlow
Security as an App (SaaA)
  New app development framework: FRESCO
  New security enforcement kernel: FortNOX
Security as a Service (SaaS)
  New security monitoring service for cloud tenants: CloudWatcher
Summary

## Slide 15: Problems of Legacy Network Devices
Too complicated
  Control plane is implemented with complicated S/W and ASIC
Closed platform
  Vendor specific
Hard to modify (nearly impossible)
  Hard to add new functionalities
Source: G. Gu, et al, Texas A&M &SRI

## Slide 16: Software Defined Networking (SDN)
Three layer
  Application layer
    Application part of control layer
    Implement logic for flow control
  Control layer
    Kernel part of control layer
    Run applications to control network flows
  Infrastructure layer
    Data plane
    Network switch or router
SDN architecture from ONF

## Slide 17: OpenFlow Architecture
OpenFlow Switch
Flow
Table
Secure
Channel
PC
OpenFlow
Protocol
SSL
hw
sw
OpenFlow Switch specification
From openflow tutorial
controller
A controller application
can enforce any flow rules
to network switches
application

## Slide 18: Killer Applications of SDN?
Reducing Energy in Data Center Networks (load balancing)
WAN VM Migration
…
How about security?
  We are going to talk about this, more specifically:
  Security as an App (SaaA)
  Security as a Service (SaaS)
Source: G. Gu, et al, Texas A&M &SRI

## Slide 19: Software App Store Today

## Slide 20: Security as an App
SDN naturally has an application layer
Security functions can be apps on top of SDN/ networking OS
  Firewall
  Scan detection
  DDoS detection
  Intrusion detection/prevention
  …
Why SaaA?
  Cost efficiency
  Easy deployment/maintenance
  Rich, flexible network control
Source: G. Gu, et al, Texas A&M &SRI

## Slide 21: Security as a Service
Clouds are large, complicated, and dynamic
How do tenants deploy security devices/functions?
    Tenant can use some pre-installed fixed-location security devices
      Not able to keep up with the high dynamisms in network configurations
    Tenant can Install security devices for themselves
      Difficult
Need a new Security Monitoring as a Service mechanism for a cloud network
Source: G. Gu, et al, Texas A&M &SRI

## Slide 22: Challenges and New Contributions
It is not easy to develop security apps
  FRESCO: a new app development framework for modular, composable security services
It is not secure when running buggy/vulnerable/multiple security apps (e.g., policy conflict/bypass)
  FortNOX: a new security enforcement kernel
It is not convenient to install/use security devices for cloud tenants
  CloudWatcher: a new security monitoring service model based on SDN
Source: G. Gu, et al, Texas A&M &SRI

## Slide 23: FRESCO: Framework for Enabling Security Controls in OpenFlow networks

## Slide 24: What is FRESCO?
A new framework
  Enables to compose diverse network security functions easily (with combining multiple modules)
  Enables to create own network security functions easily (without requiring additional H/Ws)
  Enables to deploy network security functions easily and dynamically (without modifying the underlying network architecture)
  Enable to add more intelligence to current network security functions
Source: G. Gu, et al, Texas A&M &SRI

## Slide 25
Source: G. Gu, et al, Texas A&M &SRI

## Slide 26: FRESCO – Overall Operation
Create
Modules
Load Modules
Notify NOX of loading FRESCO modules
Run
Modules
Monitor OpenFlow switches
Answer from NOX
Source: G. Gu, et al, Texas A&M &SRI

## Slide 27: FRESCO Modular Design
parameter
action
input
output
event
key
values
Module
F-DB instance
Source: G. Gu, et al, Texas A&M &SRI

## Slide 28: FRESCO – Script Language
Goal
  Define interfaces, actions, and parameters
  Connect multiple modules
  Similar to C/C++ function, start with { and end with }
Format
  Instance name (# of input) (# of output)
    denotes the module name and the number of input and output variables
  INPUT: a1,a2,
    denotes input items for a module an may be set of flows, packets or integer values
  OUTPUT: b1,b2,
    denotes output items for a module bn may be set of flows, packets or integer values
  PARAMETER: c1,c2,
    denotes configuration values of a module cn may be real numbers or strings
  EVENT: d1,d2,
    denotes events that will be delivered to a module dn may be any predefined string
  ACTION : condition ; action,
    denotes actions that will be performed based on condition
Source: G. Gu, et al, Texas A&M &SRI

## Slide 29: Simple Working Example: Reflector Net
find_scan (1) (2) {
TYPE: ScanDetector
EVENT:TCP_CONNECTION_FAIL
INPUT: SRC_IP
OUTPUT: SRC_IP, scan_result
PARAMETER: 5
ACTION: -
/* no actions are defined */
}
do_redirect (2) (0) {
TYPE: ActionHandler
EVENT:PUSH
INPUT:SRC_IP, scan_result
OUTPUT: -
PARAMETER: -
ACTION: scan_result == 1? REDIRECT: FORWARD
/* if scan_result equals 1, redirect; otherwise, forward */
}
Module 1
Module 2
Source: G. Gu, et al, Texas A&M &SRI

## Slide 30: Reflector Net
Source: G. Gu, et al, Texas A&M &SRI

## Slide 31: Cooperating with Legacy Security Applications
Source: G. Gu, et al, Texas A&M &SRI

## Slide 32: BotMiner - Overview
How to detect botnet C&C channels
  Find C-plane
    Who is talking to whom?
      Flow: SRC IP, DST IP, DST Port, Protocol
      Features
        BPS (bytes per second), FPH (flows per hour)
        BPP (bytes per packet), PPF (packets per flow)
      Clustering based on features
  Find A-plane
    Who is doing what?
      Clients perform malicious activities
        E.g., scanning, spam activity and etc
      Clustering based on malicious actions
        E.g., scan cluster
  Co-Clustering
    Combine results of two clusters to find botnet C&C channels
    Channels showing similar C-plane patterns and performing malicious actions
Source: G. Gu, et al, Texas A&M &SRI

## Slide 33: BotMiner in FRESCO (Diagram)

## Slide 34: BotMiner in FRESCO (Script)
BM1 (1) (2) {
EVENT:TCP_CONNECTION_FAIL,
TCP_CONNECTION_SUCCESS
INPUT: Source IP
OUTPUT: Result, Input1
PARAMETER: -
ACTION: -
}
BM2 (2) (1) {
EVENT:PUSH
INPUT:BM1-0, BM1-1
OUTPUT: Result
PARAMETER:10
ACTION: -
}
BM4 (2) (2) {
EVENT:PUSH
INPUT:BM2-0, BM3-0
OUTPUT: Result1, Result2
PARAMETER:-
ACTION: -
}
BM3 (0) (1) {
EVENT:TCP_CONNECTION_FAIL,
TCP_CONNECTION_SUCCESS
INPUT: -
OUTPUT: Result
PARAMETER: -
ACTION: -
}
BM5 (2) (0) {
EVENT:PUSH
INPUT:BM4-0, BM4-1
OUTPUT: -
PARAMETER:-
ACTION: BM4-0 == 1 ?Drop
}
A-Plane Clustering
Co-Clustering
C-Plane Clustering
Action
Source: G. Gu, et al, Texas A&M &SRI

## Slide 35: More …
Tarpits
White Holes
Scan detector
P2P detector (P2P Plotter)
Botnet detector (BotMiner)
…
Over 90% reduction in lines of code compared with their standard implementations
Already include more than 16 commonly reusable modules (expending over time)
Source: G. Gu, et al, Texas A&M &SRI

## Slide 36: FortNOX: A Security Enforcement Kernel for OpenFlow
Source: G. Gu, et al, Texas A&M &SRI

## Slide 37: New Threat
SDN apps can compete, contradict, override one another, incorporate vulnerabilities
Worst case: an adversary can use a vulnerable and deterministic SDN app to control the state of all SDN switches in the network
Source: G. Gu, et al, Texas A&M &SRI

## Slide 38
  .
SDN/OpenFlow Evasion Scenario
Dynamic Flow Tunneling
Source: G. Gu, et al, Texas A&M &SRI

## Slide 39: Prerequisites for a Secure OpenFlow Platform
Must be resilient to
  Vulnerabilities in OF applications
  Malicious code in 3rd party OF apps
  Complex interaction that arise between OF app interactions
  State inconsistencies due to switch garbage collection or policy coordination across distributed switches
  Sophisticated OF applications that employ packet modification actions
  Adversaries who might directly target our security services to harm the network
Source: G. Gu, et al, Texas A&M &SRI

## Slide 40: New Contributions
Development of a security enforcement kernel for the NOX OpenFlow controller
Role-based authorization
Rule conflict detection
Security directive translation
Source: G. Gu, et al, Texas A&M &SRI

## Slide 41: Classic NOX Architecture
Native C
OF Apps
PY OF
Apps
NOX
Python SWIG
Send_OpenFlow_Command()
Source: G. Gu, et al, Texas A&M &SRI

## Slide 42
FortNOX Architecture
Security Apps
Native C
OF Apps
PY OF
Apps
FortNOX
Python SWIG
OF IPC Proxy
Separate
Process
Directive Translator
IPC Interface
Actuator
Switch Callback tracking
Aggregate Flow Table
Operator Rules
SECURITY Rules
OF App Rules
FT_Send_OpenFlow_Command
Role-based Source Auth
State Table Manager
Conflict Analyzer
OF Mod Commands
Add (conflict enforced)
Modify (conflict enforced)
Delete (priority enforced)
Switch Callback Tracking
Source: G. Gu, et al, Texas A&M &SRI

## Slide 43
FortNOX – A new security enforcement kernel for OF networks
  Role-based Authorization
  Rule-Authentication
  Conflict Detection and Resolution
  Security Directive Translation
Ongoing Efforts and Future Work
  Prototype implementations for newer controllers (Floodlight, POX)
  Security enforcement in multicontroller environments
  Improving error feedback to OF applications
  Optimizing rule conflict detection
Summary of FortNOX
“A Security Enforcement Kernel for OpenFlow Networks”. HotSDN’12
Source: G. Gu, et al, Texas A&M &SRI

## Slide 44: Some Demonstrations
www.openflowsec.org
  Some technical reports and publications
  DEMO videos
  Demo 1: Constraints Enforcement [high res .mov or Youtube! ]
  Demo 2: Reflector Nets [high res .mov or Youtube! ]
  Demo 3: Automated Quarantine [high res .mov or Youtube! ]
  FRESCO/FortNOX beta to be released soon
Source: G. Gu, et al, Texas A&M &SRI

## Slide 45: CloudWatcher: Network Security Monitoring Using OpenFlow in Dynamic Cloud Networks or: How to Provide Security Monitoring as a Service in Clouds?
Source: G. Gu, et al, Texas A&M &SRI

## Slide 46: Goal
Provide Security Monitoring as a Service for a cloud network
How to Provide
  Routing algorithms
    The algorithms guarantee that specified (static) network security devices can monitor (dynamic) specific network flows
  A script language
    Register security devices easily
    Create security policies easily
Source: G. Gu, et al, Texas A&M &SRI

## Slide 47: CloudWatcher
A new framework
  Provide security monitoring services for large and dynamic cloud networks
  Detour network packets to be inspected by pre-installed network security devices automatically
    OpenFlow
  Provide a script to operate this framework
Source: G. Gu, et al, Texas A&M &SRI

## Slide 48: Operating Scenario
Register Security Devices
Create Security Policies
Parse Security Policies
Create Routing Rules
Enforce Flow Rules into Routers
Translate Routing Rules into OpenFow Rules
Administrator
Router (Device ID = 8)
{ID, TYPE, LOCATION, MODE, Func}
{1, NIDS, 8, PASSIVE, Detect HTTP}
NIDS (ID = 1)
{FLOW CONDITON, DEVICE SET}
{10.0.0.*  *:80, {1}}
Source: G. Gu, et al, Texas A&M &SRI

## Slide 49: How to Control Flows
4 approaches
  Multipath naïve
  Shortest through
  Multipath shortest
  Shortest inline
- Sample network -
S: start node, E: end node
R: router, C: security device

## Slide 50: Shortest Through (algorithm 2)
Find the shortest path passing through R4
  Shortest path between S and R4
  Shortest path between R4 and E
  Path: S  R1  R2  R4  R4  R6  E
It considers the security device without producing redundant paths
However, it may take more time to deliver packets
Source: G. Gu, et al, Texas A&M &SRI

## Slide 51: Summary of CloudWatcher
CloudWatcher provides a new framework to monitor cloud networks
  With the help of the SDN technology
A cloud administrator can select algorithms based on network status
A cloud administrator can monitor his network by writing simple scripts
Work in progress; a position paper in NPSec’12
Source: G. Gu, et al, Texas A&M &SRI

## Slide 52: Summary
SDN is a new technology, and security can be a new killer app
  SDN is impactful to drive a variety of innovations in network security
We investigate the possibilities of security as an app and security as a service
We propose key technologies to enable SaaA and SaaS
  FRESCO
  FortNOX
  CloudWatcher
Let’s contribute together to SDN and Security!
Source: G. Gu, et al, Texas A&M &SRI

## Slide 53: Outline
Reminder: Course Evaluation Due on Dec 9
Review on SDN Debugging
  Data Plane Approach (Breakpoints + Packet Trace): NDB
  Control Plane Approach (Model Checking + Symbolic Execution): NICE
SDN Security
  Defense again Control Plane Attacks (Review)
  Security as a Service
SDN End Host Networking Stack
SDN Storage

## Slide 54: 15 Years Ago
Linux networking stack

## Slide 55: 15 Years of Research
New network architectures (e.g. x-kernel)
Domain specific languages (e.g. Click)
Path abstraction (e.g. Scout)
(Now) Software-Defined Networking
Source: Sapan, et al, Princeton

## Slide 56: 15 Years Later
Linux networking stack

## Slide 57: Click
Source: Sapan, et al, Princeton

## Slide 58: NativeClick
Key mechanisms: OS container and VPP
Source: Sapan, et al, Princeton

## Slide 59: Comparison with Openvswitch
Openvswitch is in linux kernel
  Controls L2 and L3
NativeClick: a holistic view of Linux networking stack
  Much more than L2 and L3, e.g. tc (traffic control)

## Slide 60: Summary
Standard networking tools are here to stay
NativeClick combines benefits of Click (clean modularity) and Linux stack
NativeClick abstractions: NativeClick elements and NativeClick ports
Source: Sapan, et al, Princeton

## Slide 61: Outline
Reminder: Course Evaluation Due on Dec 9
Review on SDN Debugging
  Data Plane Approach (Breakpoints + Packet Trace): NDB
  Control Plane Approach (Model Checking + Symbolic Execution): NICE
SDN Security
  Defense again Control Plane Attacks (Review)
  Security as a Service
SDN End Host Networking Stack
SDN Storage
Source: Thereska, et al, MSR

## Slide 62: Background: Enterprise data centers
General purpose applications
Application runs on several VMs
Separate network for VM-to-VM
traffic and VM-to-Storage traffic
Storage is virtualized
Resources are shared
Hypervisor
Switch
Switch
Switch
Storage server
Storage server
S-NIC
S-NIC
S-NIC
NIC
S-NIC
NIC
VM
VM
VM
Virtual Machine
vDisk
VM
VM
VM
Virtual Machine
vDisk
2
Software Defined Networking (COMS 6998-8)
Source: Thereska, et al, MSR
Notes: -Such DCs comprise compute and storage servers. We can think of each app as a tenant -The storage servers act as front ends for back end storage. Storage is virtualized and VMs are presented with virtual hard disks that are simply large files on storage servers.

## Slide 63: Motivation
It is hard to provide such SLAs today
Want: predictable application behaviour and performance
Need system to provide end-to-end SLAs, e.g.,
Guaranteed storage bandwidth B
Guaranteed high IOPS and priority
Per-application control over decisions along IOs’ path
Source: Thereska, et al, MSR
Notes: -Tenant want predictable behaviour and performance in these shared resource environments, as if they had their own dedicated resources. They want performance guarantees and control over the services processing their data along the IO stack.
- The problem is that data centers today cannot provide those guarantees and control. Let’s understand why through an example.

## Slide 64: Example: guarantee aggregate bandwidth B for Red tenant
Hypervisor
Switch
Switch
Switch
Storage server
Storage server
S-NIC
S-NIC
S-NIC
NIC
S-NIC
NIC
VM
Virtual Machine
vDisk
VM
Virtual Machine
vDisk
App
OS
Hypervisor
Caching
Scheduling
IO Manager
Drivers
App
OS
Malware scan
File system
…
Compression
File system
…
Caching
Scheduling
Storage server
Caching
Scheduling
Drivers
File system
Deduplication
…
Deep IO path with 18+ different layers that are configured and operate independently and do not understand SLAs
Notes: No understanding of application performance requirements. Applications today do not have any way of expressing their SLAs, e.g., you do not open a file specifying how fast you want to read from it. It’s all best effort.
Sharing resources today means living with interference from neighbouring tenants, e.g., blue application can be aggressive and consume most of the storage bandwidth. This interference causes unpredictable performance.
Now, you might be thinking: there are other resources, e.g., network resources are also part of the end-to-end SLA, and we have ways to handle this complexity like software-defined networking. Why is storage different?

## Slide 65: Challenges in enforcing end-to-end SLAs
No storage control plane
No enforcing mechanism along storage data plane
Aggregate performance SLAs
  - Across VMs, files and storage operations
Want non-performance SLAs: control over IOs’ path
Want to support unmodified applications and VMs
Source: Thereska, et al, MSR
Notes: -No storage control plane that can coordinate the layers configuration to enforce an SLA
-Each layer has own configuration and makes own decisions.
- We have set a high bar for the SLAS: Want detailed SLAs. Aggregate is challenging because it adds a further distributed dimension to the config problem: configuration of layers across machines

## Slide 66: IOFlow architecture
…
App
OS
Hypervisor
File system
Scheduling
IO Manager
Drivers
Storage server
Caching
Scheduling
Drivers
File system
Deduplication
App
OS
Malware scan
File system
Scheduling
Compression
Controller
Client-side IO stack
Server-side IO stack
High-level SLA
IOFlow API
Decouples the data plane (enforcement) from the
control plane (policy logic)
Source: Thereska, et al, MSR
Notes: Controller is logically centralized and has global visibility

## Slide 67: Contributions
Defined and built storage control plane
Controllable queues in data plane
Interface between control and data plane (IOFlow API)
Built centralized control applications that demonstrate power of architecture
Source: Thereska, et al, MSR

## Slide 68: Storage flows
Storage “Flow” refers to all IO requests to which an SLA applies
  <{VMs}, {File Operations}, {Files}, {Shares}> ---> SLA
Aggregate, per-operation and per-file SLAs, e.g.,
<{VM 1-100}, write, *, \\share\db-log}>---> high priority
<{VM 1-100}, *, *, \\share\db-data}> ---> min 100,000 IOPS
Non-performance SLAs, e.g., path routing
<VM 1, *, *, \\share\dataset>---> bypass malware scanner
source set
destination sets
Source: Thereska, et al, MSR
Notes: - IOFlow supports a flow abstraction described using four parameters
- Min: system can do more if underutilized
-We make the observation that this high level flow description maps in a straightforward way to low level queues and their functions that we’ve built as we’ll see next.

## Slide 69: IOFlow API: programming data plane queues
  1. Classification [IO Header -> Queue]
  2. Queue servicing [Queue -> <token rate, priority, queue size>]
  3. Routing [Queue -> Next-hop]
…
IO
Header
…
…
Malware
scanner
Source: Thereska, et al, MSR
Notes: 3 key functions that IOFlow provides. -If a queue reaches the queue size threshold, the queue notifies the controller and blocks any further inserts to that queue. There is no support in the IO stack for dropping IO requests like in networking, but there is support for blocking requests and applying
- There are two storage-specific technical challenges: there is no end-to-end classification of storage traffic in the storage stack. Also, rate limiting storage requests is challenging.

## Slide 70: Lack of common IO Header for storage traffic
SLA: <VM 4, *, *, \\share\dataset> --> Bandwidth B
Stage configuration: “All IOs from VM4_sid to //serverX/AB79.vhd should be rate limited to B”
Block device
Z: (/device/scsi1)
Server and VHD
\\serverX\AB79.vhd
Volume and file
H:\AB79.vhd
Block device
/device/ssd5
Source: Thereska, et al, MSR
Notes: -For concreteness, we move to a concrete storage stack inside Windows.
  - Mismatch: SLAs specified using high-level names, but layers observe different low-level identifiers/IO Headers
-VM name is also lost. By the time a request arrives at the storage server its source VM is lost.
-This is not just a problem in Windows. Other OSes have similar stacks.
  - Root cause: layers with diverse functionalities. Virtualization made problem worse. Networks do not have this problem <ip, port, protocol>

## Slide 71: Flow name resolution through controller
SLA: {VM 4, *, *, //share/dataset} --> Bandwidth B
Controller
SMBc exposes IO Header it understands:
<VM_SID, //server/file.vhd>
Queuing rule (per-file handle):
<VM4_SID, //serverX/AB79.vhd> --> Q1
Q1.token rate --> B
Source: Thereska, et al, MSR
Notes: -Layers expose IO headers to controller. Controller maps the SLA to layer-specific IO headers
-SMB is file server protocol inside hypervisor. It understands VM Security descriptors, remote servers and file names. – When do you install this rule? When the file is opened. Queuing rule is maintained as part of the file handle and any subsequent IOs on that handle obey the rule. The controller is not on the IO data path
-Main takeaway is that controller is exposed to previously-private metadata that each layer had.
Controller is not on critical path

## Slide 72: Rate limiting for congestion control
  Queue servicing [Queue -> <token rate, priority, queue size>]
Important for performance SLAs
Today: no storage congestion control
Challenging for storage: e.g., how to rate limit two VMs, one reading, one writing to get equal storage bandwidth?
IOs
tokens
Source: Thereska, et al, MSR
Notes: - If an aggressive tenant sends too many IO requests to the storage node it might prevent it from meeting another tenant’s SLA
-Token buckets are a standard algorithm for rate limiting network packets. The token bucket algorithm outputs incoming packets as long as enough tokens are available. By providing a queue with more or less tokens, one can control the rate at which its requests drain.

## Slide 73: Rate limiting on payload bytes does not work
Storage server
VM
VM
8KB Writes
8KB Reads
Source: Thereska, et al, MSR
Notes: - Note that requests cannot be dropped on the storage stack, unlike in networks. So a key congestion signal is unavailable for storage. Once they enter the storage server, the server is committed to completing them.

## Slide 74: Rate limiting on bytes does not work
Storage server
VM
VM
8KB Writes
8KB Reads
Source: Thereska, et al, MSR
Notes: - Step in the right direction since the hypervisor knows the read io size from the IO header
- For SSDs, writes could be more expensive than reads, by an order of magnitude
- So let’s rate limit on number of requests or IOPS

## Slide 75: Rate limiting on IOPS does not work
Storage server
VM
VM
8KB Writes
64KB Reads
Need to rate limit based on cost
Software Defined Networking (COMS 6998-8)
Source: Thereska, et al, MSR
Notes: Read limiting based on IOPS cannot handle bandwidth changes. Reads would get more bandwidth. Furthermore, storage requests can have arbitrary long sizes (e.g., 1GB)
Clear that need to rate limit based on cost.

## Slide 76: Rate limiting based on cost
Controller constructs empirical cost models based on device type and workload characteristics
    RAM, SSDs, disks: read/write ratio, request size
Cost models assigned to each queue
    ConfigureTokenBucket [Queue -> cost model]
Large request sizes split for pre-emption
Source: Thereska, et al, MSR
Notes: Controller knows when new devices are added and through the discovery component it constructs models for them.
Cost models: E.g., consume 2 tokens for 64KB requests and 1 token for 4K requests.

## Slide 77: Recap: Programmable queues on data plane
  Classification [IO Header -> Queue]
    Per-layer metadata exposed to controller
    Controller out of critical path
  Queue servicing [Queue -> <token rate, priority, queue size>]
    Congestion control based on operation cost
  Routing [Queue -> Next-hop]
How does controller enforce SLA?
Source: Thereska, et al, MSR
Notes: Changes on data plane: Not all layers are expected to implement all 3 calls, they can implement 0 or a subset

## Slide 78: Distributed, dynamic enforcement
SLA needs per-VM enforcement
Need to control the aggregate rate of VMs 1-4 that reside on different physical machines
Static partitioning of bandwidth is sub-optimal
<{Red VMs 1-4}, *, * //share/dataset> --> Bandwidth 40 Gbps
VM
VM
Hypervisor
Storage server
VM
VM
Hypervisor
VM
VM
VM
VM
40Gbps
Source: Thereska, et al, MSR
Notes: In practice they read from multiple servers, but for simplicity here we focus on VM aggregation

## Slide 79: Work-conserving solution
VMs with traffic demand should be able to send it as long as the aggregate rate does not exceed 40 Gbps
Solution: Max-min fair sharing
VM
VM
Hypervisor
Storage server
VM
VM
Hypervisor
VM
VM
VM
VM
Source: Thereska, et al, MSR

## Slide 80: Max-min fair sharing
Well studied problem in networks
  Existing solutions are distributed
    Each VM varies its rate based on congestion
    Converge to max-min sharing
  Drawbacks: complex and requires congestion signal
But we have a centralized controller
  Converts to simple algorithm at controller
Source: Thereska, et al, MSR

## Slide 81: Controller-based max-min fair sharing
What does controller do?
Infers VM demands
Uses centralized max-min within a tenant and across tenants
Sets VM token rates
Chooses best place to enforce
Controller
INPUT:
per-VM demands
OUTPUT:
per-VM allocated token rate
t
s
t = control interval
s = stats sampling interval
Source: Thereska, et al, MSR

## Slide 82: Controller decides where to enforce
SLA constraints
  Queues where resources shared
  Bandwidth enforced close to source
  Priority enforced end-to-end
Efficiency considerations
  Overhead in data plane ~ # queues
  Important at 40+ Gbps
Minimize # times IO is queued and distribute rate limiting load
VM
VM
Hypervisor
Storage server
VM
VM
Hypervisor
VM
VM
VM
VM
Source: Thereska, et al, MSR
Notes: -Based on SLA constraints and efficiency considerations. Can be thought of as an optimization problem. -The enforcement bottleneck tends to be queue locks. In this case this means enforcing at the hypervisors, but there are cases for high IOPS rates (>400000) when both hypervisors and storage servers do enforcement.
- Controller sets up queues and their service rates

## Slide 83: Centralized vs. decentralized control
Centralized controller in SDS allows for simple algorithms that focus on SLA enforcement and not on distributed system challenges
Analogous to benefits of centralized control in software-defined networking (SDN)
Source: Thereska, et al, MSR

## Slide 84: IOFlow implementation
Controller
2 key layers for
VM-to-Storage
performance SLAs
4 other layers
. Scanner driver (routing)
. User-level (routing)
. Network driver
. Guest OS file system
Implemented as filter drivers on top of layers
Source: Thereska, et al, MSR
Notes: - Adding the IOFlow API to all layers I mentioned in the design is ongoing work. So far we have added it to:
- 2 key layers. File server protocol in hypervisor and entrance to the storage server.
- Key strength: no need to change apps
We have also added it to several other layers. For routing we have scanner and the ability to route to a user-space layer.
Controller is a separate service

## Slide 85: Evaluation map
IOFlow’s ability to enforce end-to-end SLAs
Aggregate bandwidth SLAs
Priority SLAs and routing application in paper
Performance of data and control planes
Source: Thereska, et al, MSR

## Slide 86: Evaluation setup
VM
VM
Hypervisor
Storage server
VM
VM
Switch
Hypervisor
VM
VM
VM
VM
…
Clients:10 hypervisor servers, 12 VMs each
4 tenants (Red, Green, Yellow, Blue)
30 VMs/tenant, 3 VMs/tenant/server
Storage network:
Mellanox 40Gbps RDMA RoCE full-duplex
1 storage server:
16 CPUs, 2.4GHz (Dell R720)
SMB 3.0 file server protocol
3 types of backend: RAM, SSDs, Disks
Controller: 1 separate server
1 sec control interval (configurable)
Source: Thereska, et al, MSR
Notes: RoCE: RDMA over Converged Ethernet.
In this evaluation we show RAM for two reasons: it shows IOFlow can enforce high-perf SLAs and it shows worst-case data plane overheads in doing so.

## Slide 87: Workloads
4 Hotmail tenants {Index, Data, Message, Log}
Used for trace replay on SSDs (see paper)
IoMeter is parametrized with Hotmail tenant characteristics (read/write ratio, request size)
Source: Thereska, et al, MSR
Notes: -The “Message” workload stores email content in files; ‘Index” is a background maintenance activity scheduled at night time in the data center; the “Data” and “Log” workloads are database data and transaction logs respectively. Metadata on emails is stored on these databases. So we have a diverse combination of file system, database and log workloads, typical of enterprise data centers.

## Slide 88: Enforcing bandwidth SLAs
  4 tenants with different storage bandwidth SLAs
  Tenants have different workloads
    Red tenant is aggressive: generates more requests/second
Tenant | SLA
Red | {VM1 – 30} -> Min 800 MB/s
Green | {VM31 – 60} -> Min 800 MB/s
Yellow | {VM61 – 90} -> Min 2500 MB/s
Blue | {VM91 – 120} -> Min 1500 MB/s
Notes: Access same storage server

## Slide 89: Things to look for
Distributed enforcement across 4 competing tenants
  Aggressive tenant(s) under control
Dynamic inter-tenant work conservation
  Bandwidth released by idle tenant given to active tenants
Dynamic intra-tenant work conservation
  Bandwidth of tenant’s idle VMs given to its active VMs
Source: Thereska, et al, MSR

## Slide 90: Results
Controller notices red tenant’s performance
Tenants’ SLAs enforced. 120 queues cfg.
Inter-tenant work conservation
Intra-tenant work conservation
Source: Thereska, et al, MSR

## Slide 91: Data plane overheads at 40Gbps RDMA
Negligible in previous experiment. To bring out worst case varied IO sizes from 512Bytes to 64KB
Reasonable overheads for enforcing SLAs
Notes: Metric: total throughput overhead across 120 tenants
Per-op overheads in general dominate per-byte overheads as expected, but overall the overheads are reasonable. The results for SSDs and disks are qualitatively similar.
At 512B: ~500K IOPS
Details: IoMeter with random-access requests, read:write 1:1
120 tenants with an SLA of 1/120th of storage capacity
Enforcement at hypervisors SMBc layer

## Slide 92: Control plane overheads: network and CPU
Overheads (MB)
<0.3% CPU overhead at controller
Controller configures queue rules, receives statistics and updates token rates every interval
Source: Thereska, et al, MSR

## Slide 93: Summary of contributions
Defined and built storage control plane
Controllable queues in data plane
Interface between control and data plane (IOFlow API)
Built centralized control applications that demonstrate power of architecture
Ongoing work: applying to public cloud scenarios
Source: Thereska, et al, MSR

## Slide 94: Questions?