## Slide 1: Software Defined Networking COMS 6998-8, Fall 2013
Instructor: Li Erran Li (lierranli@cs.columbia.edu)
http://www.cs.columbia.edu/~lierranli/coms6998-8SDNFall2013/
9/17/2013: SDN Scalability

## Slide 2: Outline
Juniper & Comcast SDN competition
Homework 1
Review of previous lecture
SDN scalability
  Scale controller
    Flat structure multiple controllers [ONIX, OSDI’10]
    Recursive controller design [Xbar, ONS,13]
    Hierarchical controller design [Kandoo, HotSDN’12]
  Offload to switch
    Offload to switch control plane [Diffane, SIGCOMM’10]
    Offload of switch data plane [DevoFlow, SIGCOMM’11]

## Slide 3: Home Work 1
Switch
Switch
vSwitch
IFloodlight-Module
External Application
REST
Floodlight Controller
There is a learning switch module and a firewall module in Floodlight
Implement IFloodlightModule, IOFMessageListener
Need to process OpenFlow messages
  PacketIn: switch generates PacketIn message for first packet of a flow
  PacketOut: used by controller to send a packet through data plane
  FlowMod: used by controller to modify flow table entries (add/delete/modify)
  FlowRemoved: used by switch to notify controller about flow entry time out

## Slide 4: Review of Previous Lecture
What is the definition of SDN?
  The separation of control plane from data plane
  A specific SDN: configuration, distribution and forwarding abstraction
What is the API between control plane and data plane?
  OpenFlow protocol

## Slide 5: Review of Previous Lecture (Cont’d)
Which is the configuration and management protocol?
  OF-CONFIG
Why does OF-CONFIG do?
  Bootstrap OpenFlow network, e.g. configure switches to connect to controllers
  Allocate resources within switches, e.g. ports, queues

## Slide 6: Outline
SDN scalability
  Scale controller
    Flat structure multiple controllers [ONIX, OSDI’10]
    Recursive controller design [Xbar, ONS,13]
    Hierarchical controller design [Kandoo, HotSDN’12]
  Offload to switch
    Offload to switch control plane [Diffane, SIGCOMM’10]
    Offload of switch data plane [DevoFlow, SIGCOMM’11]

## Slide 7: Scalability issues
Control Plane
Data Plane
Frequent events stress the control plane.
Stress the control channels.
Stress controller’s resources.
Source: Soheil Hassas Yeganeh
Notes: Highly frequent events consume a lot from the control channel and computing resources.
For example, if we collect network-wide state with high frequency
LOAD ON THE NETWORK

## Slide 8: Solution Space
Distributed Controllers:
Data Plane Extensions:
Control Plane
Control Plane
Consider this as an intrinsic limitation.
Onix, Devolved Controllers, ...
Delegate more responsibilities to the data plane.
DIFANE, DevoFlow, ...
Control Plane
Data Plane
Control Plane
Data Plane
Source: Soheil Hassas Yeganeh
Notes: There are two categories of solutions for this problem: 1. ... and 2....

## Slide 9: Solution Space (Cont’d)
Control Plane
Control Plane
Control Plane
Data Plane
Control Plane
Data Plane
Still, high control channel consumption.
Need to modify the data plane.
Comes at the cost of visibility.
Source: Soheil Hassas Yeganeh
Notes: The problem with ... is that ...
On the other hand, dataplane extensions result into less visibility
More importantly you need to modify OpenFlow, more optional features, fragmentation, ...

## Slide 10: Overheads: Flow Setup
Switch w/ finite BW between data / control plane, i.e. overheads between ASIC and CPU
Setup capability: 275~300 flows/sec
In data center: mean interarrival 30 ms
Rack w/ 40 servers  1300 flows/sec

## Slide 11: Overheads: Flow Setup
Experiment: a single switch

## Slide 12: Overheads: Flow Setup
ASIC switching rate
Latency: 5 s

## Slide 13: Overheads: Flow Setup
ASIC  CPU
Latency: 0.5 ms

## Slide 14: Overheads: Flow Setup
CPU  Controller
Latency: 2 ms
A huge waste
of resources!

## Slide 15: Overheads: Gathering Statistics
[30] most longest-lived flows: only a few sec
Counters: (pkts, bytes, duration)
Push-based: to controller when flow ends
Pull-based: fetch actively by controller
88F bytes for F flows
In 5406zl switch: Entries:1.5K wildcard match/13K exact match  total 1.3 MB, 2 fetches/sec, 17 Mbps  Not fast enough! Consumes a lot of BW!
[30] S. Kandula, S. Sengupta, A. Greenberg, and P. Patel. The
Nature of Datacenter Trac: Measurements & Analysis. In
Proc. IMC , 2009.

## Slide 16: Overheads: Gathering Statistics
2.5 sec to pull 13K entries
1 sec to pull 5,600 entries
0.5 sec to pull 3,200 entries

## Slide 17: Overheads: Gathering Statistics
Per-flow setup generates too many entries
More the controller fetch  longer
Longer to fetch  longer the control loop
In Hedera: control loop 5 secs BUT workload too ideal, Pareto distribution
Workload in VL2, 5 sec only improves 1~5% over ECMP
[41], must be less than 0.5 sec to be better
[41] C. Raiciu, C. Pluntke, S. Barre, A. Greenhalgh, D. Wischik,
and M. Handley. Data center networking with multipath TCP.
In HotNets , 2010.

## Slide 18: ONIX: Distributed Controller
Abstractions: It provides general API for management applications.
Basic functionalities:
  State distribution primitives between controllers and network elements.
  Virtualized network elements

## Slide 19: Design Requirements
Generality: Support a wide range of network management applications
Scalability: No inherent limitations due to the platform
Reliability: Graceful failure handling
Simplicity: Network management applications should become simpler
Performance: Sufficient performance

## Slide 20: Onix Architecture

## Slide 21: Four components of Onix
Physical infrastructure: switches, routers, and other things.
Connectivity infrastructure: Channels for control messages.
Onix: A distributed system running the controller.
Control logic: Network management applications on top of Onix.

## Slide 22: Onix Abstractions
Global View: Observe and control a centralized network view which contains all physical network elements.
Flows: The packet and subsequent packets with the same header are treated in the same way.
Switch: <header: counters, actions>
Event-based operation: The controller operations are triggered by routers or applications.
Do you like these abstractions for networking management? Why?

## Slide 23: Onix API
Developers program against a network graph
Nodes represent physical network entities
Write flow entry
List ports
Register for updates
……

## Slide 24: Network Information Base
The NIB is the focal point of the system
  State for applications to access
  External state changes imported into it
  Local state changes exported from it

## Slide 25: Scalability and Reliability
A single physical controller will become the bottlenecks:
  Memory: to keep NIB
  CPU and bandwidth: to process events
Solutions: Partitioning and aggregation
Now, either performance or consistency will suffer.

## Slide 26: Scalability/Reliability Requirements
Lets the applications decide the preference for durability and consistency.
Onix provides two built-in storage options
  Replicated transactions (SQL) storage
  One-hop memory-based DHT
What if there are conflicts? The applications should detect and resolve conflicts.

## Slide 27: Discussion: Consistency
Do we need strong consistency for forwarding state between the controller and routers?
Do we need strong consistency for NIB stored in controllers?
Can Onix do better than asking applications for consistency preference and resolving conflicts?

## Slide 28: Scaling: Partitioning
Multiple dimensions available to applications:
  Onix instances with different computations tasks
  Onix instances have only subsets of the NIB
  Switches connect to a subset of Onix instances

## Slide 29: Scaling: aggregation
Reduce fidelity of information before disseminating within the cluster

## Slide 30: Scaling: aggregation
Reduce fidelity of information before disseminating within the cluster

## Slide 31: Reliability
Network Element & Link Failures: Applications' responsibility
Connectivity Infrastructure Failures: Assumed reliable
Onix Failures: Onix provides distributed coordination facilities provided for app failover

## Slide 32: Summary
Onix solves state distribution for developers
The designers of management applications still have to understand the scalability implications of their design

## Slide 33: Outline
SDN scalability
  Scale controller
    Flat structure multiple controllers [ONIX, OSDI’10]
    Recursive controller design [Xbar, ONS,13]
    Hierarchical controller design [Kandoo, HotSDN’12]
  Offload to switch
    Offload to switch control plane [Diffane, SIGCOMM’10]
    Offload of switch data plane [DevoFlow, SIGCOMM’11]

## Slide 34: Incorporate Recursion into SDN
Aggregation/hierarchy/recursion are the proven method for scaling networks
Recursive hierarchy is the midway point between centralized and distributed
  Looks centralized at any particular level
  But introduces points for aggregation, failure domains, etc.
Source: Murphy Mccauley

## Slide 35: Implementing RSDN Control Logic
Controller knows its children and its parent
Keeps necessary local state
Logic broken up into:
  Aggregation functions – transform info from children to local state
  Fan-out functions – transform local state to info for children
Not a strict requirement
Source: Murphy Mccauley

## Slide 36: Example: Logical xBars (LXBs)
Specific RSDN control logic that supports a recursive programmable switch abstraction
Each controller looks like switch to its parent
  Transforms table entries from parent to children (more abstract → more specific)
  Uses label versioning to support transactional changes at each level
Source: Murphy Mccauley

## Slide 37: LXBs: Handling Failures
Source: Murphy Mccauley

## Slide 38: LXBs: Handling Failures
Source: Murphy Mccauley
Notes: Link handled by…

## Slide 39: LXBs: Handling Failures
Source: Murphy Mccauley
Notes: Link handled by…

## Slide 40: LXBs: Handling Failures
State
Config
Source: Murphy Mccauley
Notes: Link handled by…
State up, config down

## Slide 41: LXBs: Some Questions
How good is LXB-based failure localization?
How optimal are LXB-based paths?
How do you optimally divide network into hierarchical subgraphs (e.g., LXBs)?
  We don’t!
  Not even for evaluation (we use naïve clustering)
Source: Murphy Mccauley
Notes: Assumption is that in general, clustering is dictated by technology, organization, geography

## Slide 42: Summary
Single mechanism for entire control plane:
  Hopefully true even across technologies (we have mostly been thinking about copper)
Standard benefits of hierarchy:
  Failures localized, churn is contained
  Maps to organizational boundaries
  Stacks arbitrarily high to meet needs
Source: Murphy Mccauley

## Slide 43: Next Steps
Mapping to provider network topologies
Addressing regulatory boundaries
Multitechnology issues (e.g., copper, fiber, wireless)
… ?
Source: Murphy Mccauley

## Slide 44: Outline
SDN scalability
  Scale controller
    Flat structure multiple controllers [ONIX, OSDI’10]
    Recursive controller design [Xbar, ONS,13]
    Hierarchical controller design [Kandoo, HotSDN’12]
  Offload to switch
    Offload to switch control plane [Diffane, SIGCOMM’10]
    Offload of switch data plane [DevoFlow, SIGCOMM’11]

## Slide 45: Kandoo: The IDEA
OFFLOADING
LOCAL CONTROL APPS
TO
LOCAL RESOURCES.
Applications that do not need the network-wide state.
Resources close to switches.
Source: Soheil Hassas Yeganeh
Notes: Our answer to this question is based on offloading control applications that ... to resources close to switches.
In the next couple of slides I will explain ...

## Slide 46: Local Apps
But, there are many apps that are local in scope:
  Applications that require only local switch state.
An assumption in distributed controllers:
  All control apps require the network-wide state.
Controller
Controller
Controller
App
App
App
Switch
Switch
Switches
Local App
Switch
Local App
Switch
Source: Soheil Hassas Yeganeh

## Slide 47: Local apps.
Local applications:
Learning Switch
Local Policy Enforcer
Link Discovery
Local components in control applications:
Elephant Flow Detection in an Elephant Flow Rerouting application.
Local apps have implicit parallelism.
Local App
Switch
Local App
Switch
Local App
Switch
Local App
Switch
Source: Soheil Hassas Yeganeh
Notes: are either local in nature such as ....
are local components in a larger non-local app! for example

## Slide 48: Local Resources
End-Host
Switch
Programmable
Switch
On the same hosts running software switches.
Inside programmable switches.
We can offload local apps to computing resources next to switches.
Local App
Soft. Switch
End-Host
Hosts close to switches.
Local App
Switch
Local App
Source: Soheil Hassas Yeganeh

## Slide 49: Kandoo
Two layers of controllers:
  A logically centralized Root Controller.
  Local Controllers.
Local controllers run local apps.
The root controller runs non-local apps.
Local controllers shield the root controller.
Lightweight and easy to implement.
Source: Soheil Hassas Yeganeh

## Slide 50: An Example: Elephant flow rerouteing.
Source: Soheil Hassas Yeganeh

## Slide 51: An Example: Elephant flow rerouteing.
Application-specific events.
Kandoo’s event channels.
Scales linearly with the number of switches.
Source: Soheil Hassas Yeganeh

## Slide 52: Future directions
A Generalized Hierarchy
  Filling the gap between local and non-local apps
  Finding the right scope is quite challenging
  Finding the right scope is quite challenging
Source: Soheil Hassas Yeganeh

## Slide 53: Outline
SDN scalability
  Scale controller
    Flat structure multiple controllers [ONIX, OSDI’10]
    Recursive controller design [Xbar, ONS,13]
    Hierarchical controller design [Kandoo, HotSDN’12]
  Offload to switch
    Offload to switch control plane [Diffane, SIGCOMM’10]
    Offload of switch data plane [DevoFlow, SIGCOMM’11]

## Slide 54: What’s DIFANE?
Traditional enterprise
  Hard to manage
  Limited policies
  Distributed
Flow-based networking
  Easy to manage
  Support fine-grained policy
  Scalability remains a challenge
DIFANE:
A scalable way to apply fine-grained policies in enterprises
Source: Minlan Yu

## Slide 55: Flexible Policies in Enterprises
HTTP
Access control
  Drop packets from
  malicious hosts
Customized routing
  Direct Skype calls on
  a low-latency path
Measurement
  Collect detailed HTTP traffic statistics
HTTP
Source: Minlan Yu

## Slide 56: Flow-based Switches
Install rules in flow-based switches
  Store rules in high speed memory (TCAM)
Perform simple actions based on rules
  Rules: Match on bits in the packet header
  Actions: Drop, forward, count
drop
forward via link 1
Flow space
src.
dst.
Source: Minlan Yu

## Slide 57: Challenges of Policy-Based Management
Policy-based network management
  Specify high-level policies in a management system
  Enforce low-level rules in the switches
Challenges
  Large number of hosts, switches and policies
  Limited TCAM space in switches
  Support host mobility
  No hardware changes to commodity switches
Source: Minlan Yu

## Slide 58: Pre-install Rules in Switches
Packets hit
the rules
Forward
Problems:
  No host mobility support
  Switches do not have enough memory
Pre-install
rules
Controller
Source: Minlan Yu

## Slide 59: Install Rules on Demand (Ethane, NOX)
First packet
misses the rules
Buffer and send
packet header
to the controller
Install
rules
Forward
Controller
Problems:
  Delay of going through the controller
  Switch complexity
  Misbehaving hosts
Source: Minlan Yu

## Slide 60: DIFANE Architecture (two stages)
DIstributed Flow Architecture
for Networked Enterprises

## Slide 61: Stage 1
The controller proactively generates the rules and distributes them to authority switches.
Source: Minlan Yu

## Slide 62: Partition and Distribute the Flow Rules
Ingress Switch
Egress Switch
Distribute partition information
Authority Switch A
AuthoritySwitch B
Authority Switch C
reject
accept
Flow space
Controller
Authority
Switch A
Authority
Switch B
Authority
Switch C
Source: Minlan Yu

## Slide 63: Stage 2
The authority switches keep packets always in the data plane and reactively cache rules.
Source: Minlan Yu

## Slide 64: Packet Redirection and Rule Caching
Following packets
Ingress Switch
Authority Switch
Egress Switch
First packet
Redirect
Forward
Feedback:
Cache rules
Hit cached rules and forward
A slightly longer path in the data plane is faster than going through the control plane
Source: Minlan Yu

## Slide 65: Locate Authority Switches
Partition information in ingress switches
  Using a small set of coarse-grained wildcard rules
  … to locate the authority switch for each packet
Distributed directory service but not DHT
  Hashing does not work for wildcards
  Keys can have wildcards in arbitrary bit positions
Authority Switch A
AuthoritySwitch B
Authority Switch C
X:0-1 Y:0-3  A
X:2-5 Y: 0-1B
X:2-5 Y:2-3  C
Source: Minlan Yu

## Slide 66: Packet Redirection and Rule Caching
Following packets
Ingress Switch
Authority Switch
Egress Switch
First packet
Redirect
Forward
Feedback:
Cache rules
Hit cached rules and forward
Cache Rules
Partition Rules
Auth. Rules
Source: Minlan Yu

## Slide 67: Three Sets of Rules in TCAM
Type | Priority | Field 1 | Field 2 | Action | Timeout
Cache Rules | 210 | 00** | 111* | Forward to Switch B | 10 sec
 | 209 | 1110 | 11** | Drop | 10 sec
 | … | … | … | … | …
Authority Rules | 110 | 00** | 001* | Forward Trigger cache manager | Infinity
 | 109 | 0001 | 0*** | Drop, Trigger cache manager | 
 | … | … | … | … | …
Partition Rules | 15 | 0*** | 000* | Redirect to auth. switch | 
 | 14 |  |  | … | 
 | … | … | … | … | …
In ingress switches
reactively installed by authority switches
In authority switches
proactively installed by controller
In every switch
proactively installed by controller
Source: Minlan Yu

## Slide 68: DIFANE Switch Prototype Built with OpenFlow switch
Cache Rules
Data
Plane
Control Plane
Cache
Manager
Send Cache
Updates
Recv Cache
Updates
Only in Auth. Switches
Authority Rules
Partition Rules
Just software modification for authority switches
Notification
Cache rules
Source: Minlan Yu

## Slide 69: Caching Wildcard Rules
Overlapping wildcard rules
  Cannot simply cache matching rules
Source: Minlan Yu

## Slide 70: Caching Wildcard Rules
Multiple authority switches
  Contain independent sets of rules
  Avoid cache conflicts in ingress switch
Authorityswitch 1
Authorityswitch 2
Source: Minlan Yu

## Slide 71: Partition Wildcard Rules
Partition rules
  Minimize the TCAM entries in switches
  Decision-tree based rule partition algorithm
Cut A
Cut B
Cut B is better than Cut A
Source: Minlan Yu

## Slide 72: Handling Network Dynamics
Network dynamics | Cache rules | Authority Rules | Partition Rules
Policy changes at controller | Timeout | Change | Mostly no change
Topology changes at switches | No change | No change | Change
Host mobility | Timeout | No change | No change
Source: Minlan Yu

## Slide 73: Summary
Controller proactively generates the rules and distributes them to authority switches
Authority switches keep packets always in the data plane and ingress switches reactively cache rules
Can the switch control plane handle all the events?
What if high level policy changes often?
What about monitoring overhead?

## Slide 74: Outline
SDN scalability
  Scale controller
    Flat structure multiple controllers [ONIX, OSDI’10]
    Recursive controller design [Xbar, ONS,13]
    Hierarchical controller design [Kandoo, HotSDN’12]
  Offload to switch
    Offload to switch control plane [Diffane, SIGCOMM’10]
    Offload of switch data plane [DevoFlow, SIGCOMM’11]

## Slide 75: Dilemma
Control dilemma:
  Role of controller: visibility and mgmt capability however, per-flow setup too costly
  Flow-match wildcard, hash-based: much less load, but no effective control
Statistics-gathering dilemma:
  Pull-based mechanism: counters of all flows full visibility but demand high BW
  Wildcard counter aggregation: much less entries but lose trace of elephant flows
Aim to strike in between

## Slide 76: Main Concept of DevoFlow
Devolving most flow controls to switches
Maintain partial visibility
Keep trace of significant flows
Default v.s. special actions:
  Security-sensitive flows: categorically inspect
  Normal flows: may evolve or cover other flows become security-sensitive or significant
  Significant flows: special attention
Collect statistics by sampling, triggering, and approximating

## Slide 77: Design Principles of DevoFlow
Try to stay in data-plane, by default
Provide enough visibility:
  Esp. for significant flows & sec-sensitive flows
  Otherwise, aggregate or approximate statistics
Maintain simplicity of switches

## Slide 78: Mechanisms
Control
  Rule cloning
  Local actions
Statistics-gathering
  Sampling
  Triggers and reports
  Approximate counters

## Slide 79: Rule Cloning
ASIC clones a wildcard rule as an exact match rule for new microflows
Timeout or output port by probability

## Slide 80: Rule Cloning
ASIC clones a wildcard rule as an exact match rule for new microflows
Timeout or output port by probability

## Slide 81: Rule Cloning
ASIC clones a wildcard rule as an exact match rule for new microflows
Timeout or output port by probability

## Slide 82: Local Actions
Rapid re-routing: fallback paths predefined Recover almost immediately
Multipath support: based on probability dist. Adjusted by link capacity or loads

## Slide 83: Statistics-Gathering
Sampling
  Pkts headers send to controller with1/1000 prob.
Triggers and reports
  Set a threshold per rule
  When exceeds, enable flow setup at controller
Approximate counters
  Maintain list of top-k largest flows

## Slide 84: DevoFlow Summary
Per-flow control imposes too many overheads
Balance between
  Overheads and network visibility
  Effective traffic engineering / network management
Switches with limited resources
  Flow entries / control-plane BW
  Hardware capability / power consumption

## Slide 85: Questions?