## Slide 1: Software Defined Networking COMS 6998-8, Fall 2013
Instructor: Li Erran Li (lierranli@cs.columbia.edu)
http://www.cs.columbia.edu/~lierranli/coms6998-8SDNFall2013/
10/22/2013: SDN Virtualization

## Slide 2: Outline
Announcements
  Prof. Jen Rexford’s Talk on August 28, 11:00 am, Davis Auditorium, CEPSR
  Juniper/Comcast SDN Competition: participate as a 3rd team if interested
  Reminder: midterm next Tuesday!
Review of Previous Lecture: Forwarding Abstraction
SDN Virtualization
  OpenvSwitch
  Network Function Virtualization (NFV)
  FlowVisor

## Slide 3: Review of Previous Lecture
What are the different platforms for forwarding?
  Dedicated hardware
  Network processors
  NetFPGA
  General purpose software on commodity servers

## Slide 4: Review of Previous Lecture (Cont’d)
What are performance and programmability tradeoffs?
  Software:
    Flexible and easy to program
    Slow forwarding speed
  Programmable hardware:
    Flexible and fast
    Hard to program, costly and power hungry
  Custom hardware:
    Fast, cheap and power efficient
    Long development cycle and not flexible

## Slide 5: Review of Previous Lecture (Cont’d)
What are the forwarding abstractions?
  Fixed match action table (today’s switch chipset)
  Reconfigurable match table (OpenFlow++)
    Flexible header fields, flexible actions, flexible memory allocation in multi-stages of match and actions
  Programmable pipeline with modular hardware building blocks on NetFPGA (SwitchBlade)
  Modular router (Click)

## Slide 6: Fixed function switch
Deparser
In
Queues
Data
Out
ACL Stage
L3 Stage
L2 Stage
Action: set L2D
Stage 1
L2 Table
L2: 128k x 48
Exact match
Action: set L2D, dec TTL
Stage 2
L3 Table
L3: 16k x 32
Longest prefix
match
Action: permit/deny
Stage 3
ACL Table
ACL: 4k
Ternary match
?????????
PBB Stage
Parser
X
X
X
X
X
Source: P. Bosshart, TI
Review of Previous Lecture (Cont’d)

## Slide 7: Review of Previous Lecture (Cont’d)
CPU
Memory
NetFPGA
Hard Disk
PCI
Software
VE1
VE2
VE3
VE3
VE1
VE2
VE3
VE4
VDP1
VDP2
VDP3
VDP4
SwitchBlade
Click
Click
Click
Click
Software
Hardware
Virtual Env.
VDP = Virtual Data Plane
Click = Click Software Router
VE = Virtual Environment
Source: B. Anwer, Gatech
NetFPGA
Notes: Switchblade is simply a server with an FPGA card installed in it, in this case its NetFPGA.
[Click] As you can see this is a simple server with software running on CPU utilizing memory and harddsik. There is a NetFPGA card that is connected through the PCI slot.
[Click]
So what SwitchBlade does is that it extends the software virtual environments to hardware and each virtual environment has a corresponding virtualized data plane in hardware.
So what happens in switchblade is that the pipeline changes according the virtualized data plane. So for each incoming packet the pipeline changes according to individual dataplane user selection. For an OpenFlow VDP pipeline is different than IPv4 VDP etc.
Switchblade is a forwarding device that can be used as a switch or router or at any layer which user wants.

## Slide 8: Review of Previous Lecture (Cont’d)
Parallel custom data planes
  Ability to demultiplex into existing data planes and maintain isolation on common hardware platform
Rapid development and deployment
  Pluggable preprocessor (e.g. packet parser) modules enable a range of customizable functions at hardware rates
Customizability and programmability
  Dynamic selection of modules, and ability to operate in several different forwarding modes (IPv4, IPv6, OpenFlow).
Source: B. Anwer, Gatech
Virtual Data Plane Selection
Preprocessing
Shaping
Forwarding
Postprocessing
SwitchBlade

## Slide 9: Review of Previous Lecture (Cont’d)
User-level
routing daemons
Control plane
Forwarding plane
  Elements
    Small building blocks, performing simple operations
    Instances of C++ classes
  Packets traverse a directed graph of elements
FromDevice(eth0)->CheckIPHeader(14)
->IPPrint->Discard;
Linux kernel
Click
Click modular router

## Slide 10: Review of Previous Lecture (Cont’d)
10/22/13
PATS Research Group
10
Push connection
  Source pushes packets downstream
  Triggered by event, such as packet arrival
  Denoted by filled square or triangle
Agnostic connection
  Becomes push or pull depending on peer
  Denoted by double outline
Pull connection
  Destination pulls packets from upstream
  Packet transmission or scheduling
  Denoted by empty square or triangle
Notes: 10

## Slide 11: Review of Previous Lecture (Cont’d)
Ethernet
IPV4
TCP
UDP
Done
ACL
L2S
L2D
IPV4-DA
ETHERTYPE
Table Graph
VLAN
VLAN
IPV6-DA
IPV6
RCP
RCP
Parse Graph
MY-TABLE
Source: P. Bosshart, TI
RMT

## Slide 12: Review of Previous Lecture (Cont’d)
TCAM
640b
640b
Physical
Stage n
Physical
Stage 2
Logical Table 1
Ethertype
Logical Table 6
L2D
8 UDP
2
VLAN
3
IPV4
5
IPV6
4
L2S
7 TCP
SRAM
HASH
Physical
Stage 1
ACL
UDP
TCP
L2S
L2D
IPV4
ETH
VLAN
IPV6
9 ACL
Table Graph
Action
Match Table
Action
Match Table
Action
Match Table
RMT logical to physical mapping
Notes: To make it possible to efficiently use multiple stages of match tables, it is assumed that the RMT Model can be configured to map Logical Tables to the Physical Tables.
To create bigger tables, one table may traverse multiple stages.
To create many smaller tables, several tables can be packed into one stage.
To make the allocation even more flexible, the Action instructions and the Statistic could share the same table space.
This slide gives a crude representation of how the the Logical Tables could be mapped to the Physical Tables.
In practice, the control plane would need to create a Table Flow Graph (to accompany the Parse Graph) to decide how the Logical Tables are mapped.
The control plane is assumed to know the number and size of the physical stages available.
There could be as few as 1 stage. A given switch might only allow Logical Tables to directly correspond to Physical Tables.

## Slide 13: Outline
Announcements
Review of Previous Lecture: Forwarding Abstraction
SDN Virtualization
  OpenvSwitch
  Network Function Virtualization (NFV)
  FlowVisor

## Slide 14
Networking in Virtual Environments is Important
One cloud is planning to run 128 VMs per host. That's 2+ full racks in one machine.

## Slide 15
Networking in Virtual Environments is Different
Challenges
● Scalability (105 VMs) ● Isolation
● Mobility
● ...
Conveniences ● Hypervisor info ● Introspection ● Leaf nodes
● ...
Source: B. Pfaff, Nicira

## Slide 16
Networking in Virtual Environments is Different
Challenges
● Scalability (105 VMs)
● Isolation ● Mobility
● ...
Conveniences ● Hypervisor info ● Introspection ● Leaf nodes
● ...
Open vSwitch
Distribute the Switch Centralized Control Take Advantage
Source: B. Pfaff, Nicira

## Slide 17
Basic Design (Xen)
Xen host (physical machine)
Virtual machines (DomUs)
Control domain (Dom0)
...other Xen hosts...
VM 1 VM 2
VNIC VNIC VNIC
ovs-vswitchd
NIC
Controller
VM 3
VNIC VNIC
XAPI
NIC
Adminstrative CLI/GUI
Source: B. Pfaff, Nicira

## Slide 18: Open vSwitch
Controller
  Configuration: read/write config. states, setup triggers for asynchronous events
  OpenFlow
Features
  VLAN
  Port mirroring
  ACLs
  NetFlow logging for VMs
  QoS
Source: B. Pfaff, Nicira

## Slide 19
Open vSwitch Application: Single Distributed Switch
VM host 1
VM host n
Web UI
Controller
Source: B. Pfaff, Nicira

## Slide 20
Open vSwitch Application: Multiple Distributed Switches
Physical
VM host 1
Physical vSwitch
Logical
VM 1 VM n
GRE
VM host n
Tenant #1 (switched)
VM 1
VM n
Web UI
Controller
Web UI
Tenant #2 (routed)
Source: B. Pfaff, Nicira

## Slide 21
Open vSwitch Application:
Extending Data Center into Cloud
Managed Cloud
VM host 1
GRE/
IPSEC/
GRE
VM host n
SSL
“Cloud access server”
Controller
Customer Data Center
Source: B. Pfaff, Nicira

## Slide 22
Implementation (Xen)
Physical machine
Virtual machines (DomUs)
VM 1 VM 2
VNIC VNIC VNIC
VM 3
VNIC VNIC
Control domain (Dom0)
XAPI ovs-vswitchd
user
Fast Path
kernel
Xen hypervisor
NIC
NIC
Controller
Source: B. Pfaff, Nicira

## Slide 23
Open vSwitch is Fast
As fast as Linux bridge with same CPU usage
Bandwidth
Latency
Fast Path: > 1 Gbps
Fast Path: < 1 µs
ovs-vswitchd: 100 Mbps
ovs-vswitchd: < 1 ms
Controller: 10 Mbps
Controller: ms
Source: B. Pfaff, Nicira

## Slide 24
Open vSwitch is Fast
vswitch
Linux bridge
Source: B. Pfaff, Nicira

## Slide 25: Open vSwitch Source Code and Commands
Install in OpenFlow VirtualBox VM
  git clone git://git.openvswitch.org/openvswitch
  make install
Run
  /etc/init.d/openvswitch-switch start
ovs-vsctl: Configures ovs-vswitchd, a high-level interface for database
  Create a bridge:
    ovs-vsctl -- --may-exist add-br br0
  Add port to a bridge:
    ovs-vsctl -- --may-exist add-port br0 eth0

## Slide 26: Open vSwitch Source Code and Commands (Cont’d)
  List all bridges:
    ovs-vsctl list-br
  List all ports:
    ovs-vsctl list-ports br0
  Find uuid of port s1-eth1:
    Ovs-vsctl list port s1-eth1
ovsdb-tool: Command-line tool for managing database file
  ovsdb-tool show-log [-mmm] <file>

## Slide 27: Open vSwitch Source Code and Commands (Cont’d)
ovs-ofctl speaks to OpenFlow module
  ovs-ofctl dump-flows <bridge>
  ovs-ofctl snoop <bridge>
ovs-dpctl speaks to kernel module
  See datapaths and their ahached interfaces:
    ovs-dpctl show <bridge>
  Exact match flows cached in datapath:
    ovs-dpctl dump-flows <bridge>

## Slide 28: Outline
Announcements
Review of Previous Lecture: Forwarding Abstraction
SDN Virtualization
  OpenvSwitch
  Network Function Virtualization (NFV)
  FlowVisor

## Slide 29: Network Functions Virtualization
Many network equipment: switches, routers, NATs, firewalls, can be replaced by software running on VM
Advantage
  use standard COTS hardware (e.g., high volume servers, storage)
    reduces CAPEX and OPEX
  fully implement functionality in software
    reducing development and deployment cycle times, opening up the R&D market
  consolidate equipment types
    reducing power consumption
  optionally concentrate network functions in datacenters
    obtaining further economies of scale and enabling rapid scale-up and scale-down

## Slide 30: Is NFV a new idea?
VLAN and VRF: virtualized L2/L3 infrastructure
Linux router (e.g. Click): virtualized router on Linux platform
Open vSwitch
  Open Source (Apache 2.0 license) production quality virtual switch
  extensively deployed in datacenters, cloud applications, …
  switching can be performed in SW or HW
  now part of Linux kernel (from version 3.3)
  runs in many VMs
  broad functionality (traffic queuing/shaping, VLAN isolation, filtering, …)
  supports many standard protocols (STP, IP, GRE, NetFlow, LACP, 802.1ag)

## Slide 31: Potential VNFs
Potential Virtualized Network Functions (from NFV ISG whitepaper)
switching elements: Ethernet switch, Broadband Network Gateway, CG-NAT, router
mobile network nodes: HLR/HSS, MME, SGSN, GGSN/PDN-GW, RNC, NodeB, eNodeB
residential nodes: home router and set-top box functions
tunnelling gateway elements: IPSec/SSL VPN gateways
traffic analysis: DPI, QoE measurement
QoS: service assurance, SLA monitoring, test and diagnostics
NGN signalling: SBCs, IMS
converged and network-wide functions: AAA servers, policy control, charging platforms
application-level optimization: CDN, cache server, load balancer, application accelerator
security functions: firewall, virus scanner, IDS/IPS, spam protection

## Slide 32: NFV Industry Specifications Group
An Industry Specifications Group (ISG) has been formed under ETSI to study NFV
  ETSI is the European Telecommunications Standards Institute with >700 members
NFV Members
  Acme Packet, Allot, Amdocs, AT&T, ALU, Benu Networks, Broadcom, BT, Cablelabs, Ceragon, Cisco, Citrix, DT, DOCOMO, ETRI, FT, Fraunhofer FOKUS, Freescale, Fujitsu Labs, HP, Hitachi, Huawei, IBM, Intel, Iskratel, Italtel, JDSU, Juniper, KT, MetraTech, NEC, NSN, NTT, Oracle, PT, RadiSys, Samsung, Seven Principles, Spirent, Sprint, Swisscom, Tektronix, TI, Telefon Ericsson, Telefonica, TA, Telenor, Tellabs, UPRC, Verizon UK, Virtela, Virtual Open Systems, Vodafone Group, ZTE
Working and expert groups
  Architecture of the Virtualisation Infrastructure (INF)
  Management & Orchestration (MANO)
  Performance & Portability Expert Group (PER)
  Reliability & Availability (REL)
  Security Expert Group (SEC)
  Software Architecture (SWA)

## Slide 33: NFV architecture
The NFV architecture is still being debated
VNF
VNF
VNF
NFV infrastructure
NFV Orchestrator
hypervisor
VM
VM
VM
NFV hardware
compute
storage
networking
special purpose
net partitioner
VNP
VNP
VNP
NFV OS
VM
image

## Slide 34: Outline
Announcements
Review of Previous Lecture: Forwarding Abstraction
SDN Virtualization
  OpenvSwitch
  Network Function Virtualization (NFV)
  FlowVisor

## Slide 35: Flowvisor Overview
Windows
(OS)
Windows
(OS)
Linux
Mac
OS
x86
(Computer)
Windows
(OS)
App
App
Linux
Linux
Mac
OS
Mac
OS
Virtualization
App
Simple, common, stable, hardware substrate below
+ Programmability + Strong isolation model
+ Competition above
 Faster innovation
Controller 1
App
App
Controller
2
Virtualization (FlowVisor)
App
OpenFlow
Controller 1
Controller 1
Controller
2
Controller
2

## Slide 36
Flowvisor Overview (Cont’d)
• Divide the production network into logical slices
o each slice/service controls its own packet forwarding o users pick which slice controls their traffic: opt-in o existing production services run in their own slice e.g., Spanning tree, OSPF/BGP
• Enforce strong isolation between slices
o actions in one slice do not affect another
• Allows the (logical) slice to mirror the production network o real hardware, performance, topologies, scale, users
Source: R. Sherwood

## Slide 37
Current Network Devices
Switch/Router
• Computes forwarding rules
Control
• “128.8.128/16 --> port 6”
Plane
• Pushes rules down to data
plane
General-purpose CPU
Control/Data
Rules
Excepts
Protocol
• Enforces forwarding rules
Data
Plane
• Exceptions pushed back to control plane
• e.g., unmatched packets
Custom
ASIC

## Slide 38
Add a Slicing Layer Between Planes
Slice 2
Control
Plane
Slice 1
Control
Plane
Slice 3
Control
Plane
Slice
Policies
Rules
Control/Data Protocol
Excepts
Data
Plane
Source: R. Sherwood

## Slide 39
Network Slicing Architecture
A network slice is a collection of sliced switches/routers
• Data plane is unmodified
- Packets forwarded with no performance penalty
- Slicing with existing ASIC
• Transparent slicing layer
- each slice believes it owns the data path
- enforces isolation between slices
• i.e., rewrites, drops rules to adhere to slice police
- forwards exceptions to correct slice(s)
Source: R. Sherwood

## Slide 40
Slicing Policies
The policy specifies resource limits for each slice:
- Link bandwidth
- Maximum number of forwarding rules
- Topology
- Fraction of switch/router CPU
- FlowSpace: which packets does the slice control?
Source: R. Sherwood

## Slide 41: Substrate: “Flowspace”
Payload
Ethernet
DA, SA, etc
IP
DA, SA, etc
TCP
DP, SP, etc
Collection of bits to plumb flows
(of different granularities)
between end points
Payload
Header
User-defined flowspace
“OpenFlow++”
Source: N. Mckeown

## Slide 42: Flowspace: Simple example
IP SA
IP DA
Single flow
All flows from A
A
All flows between two subnets
Source: N. Mckeown

## Slide 43: Flowspace: Generalization
Field 2
Field 1
Single flow
Set of flows
Field n
Source: N. Mckeown

## Slide 44: Properties of Flowspace
Backwards compatible
  Current layers are a special case
  No end points need to change
Easily implemented in hardware
  e.g. TCAM flow-table in each switch
Strong isolation of flows
  Simple geometric construction
  Can prove which flows can/cannot communicate
Source: N. Mckeown

## Slide 45
FlowSpace: Maps Packets to Slices
Source: R. Sherwood

## Slide 46
Real User Traffic: Opt-In
• Allow users to Opt-In to services in real-time
o Users can delegate control of individual flows to Slices
o Add new FlowSpace to each slice's policy
• Example:
o "Slice 1 will handle my HTTP traffic" o "Slice 2 will handle my VoIP traffic" o "Slice 3 will handle everything else"
• Creates incentives for building high-quality services
Source: R. Sherwood

## Slide 47
OpenFlow
Switch
OpenFlow
Protocol
FlowVisor
Bob’s
Controller
Alice’s
Controller
OpenFlow
Protocol
FlowVisor Slicing Example
OpenFlow
Switch
OpenFlow
Switch
Source: N. Mckeown

## Slide 48
OpenFlow
Protocol
FlowVisor
Broadcast
Multicast
OpenFlow
Protocol
http
Load-balancer
FlowVisor Slicing Example (Cont’d)
OpenFlow
Switch
OpenFlow
Switch
OpenFlow
Switch
Source: N. Mckeown

## Slide 49
OpenFlow Protocol
FlowVisor Slicing Example (Cont’d)
OpenFlow
Switch
OpenFlow
Switch
OpenFlow
Switch
Network Administrator’s
FlowVisor
OpenFlow Protocol
Production
Network
Controller
Alices’s
FlowVisor
GENI’s
FlowVisor
Bob’s
FlowVisor
Learning
switch
Mobile VMs
New BGP
LTE-WiFi
Handover
Tricast Lossless
Handover
Source: N. Mckeown

## Slide 50
FlowVisor Implemented on OpenFlow
Custom
Control
Plane
Network
Stub
Control
Plane
Data
Plane
Server
OpenFlow Controller
OpenFlow
Protocol
OpenFlow
Firmware
Data Path
Switch/
Router
Servers
OpenFlow OpenFlow OpenFlow
Controller Controller Controller
OpenFlow
FlowVisor
OpenFlow
OpenFlow
Firmware
Data Path
Switch/
Router

## Slide 51
FlowVisor Message Handling
Alice Bob
Controller Controller
OpenFlow
Rule
Cathy
Controller
Policy Check:
Is this rule allowed?
Full Line Rate Forwarding
Packet
FlowVisor
OpenFlow
Exception
OpenFlow
Firmware
Data Path
Policy Check:
Who controls this packet?
Source: R. Sherwood

## Slide 52
FlowVisor Implementation
●Custom handlers for each of OpenFlow's 20 message types
● Transparent OpenFlow proxy ● 8261 LOC in C
● New version with extra API for GENI
●Code: git clone git://openflow.org/flowvisor.git`
Source: R. Sherwood

## Slide 53
Isolation Techniques
Isolation is critical for slicing
Link bandwidth: per-slice queue on each port of a switch
Forwarding rules: pre-set limit of number of flow entries of a given slice
Topology: limit to per-slice view
Flow space: rewrite flow definition and actions to prevent violation of slice definition
Device CPU

## Slide 54
Device CPU Isolation
• Ensure that no slice monopolizes device CPU
• CPU exhaustion
• prevent rule updates
• drop LLDPs ---> Causes link flapping
• Techniques
• Limiting rule insertion rate from controller
• Use periodic drop-rules to throttle exceptions
Source: R. Sherwood

## Slide 55: Flowvisor Commands
fvconfig generate config.xml
Run: flowvisor config.xml
fvctl is the cli used to control a running instance of flowvisor (over XMLRPC)
fvctl --passwd-file=/etc/flowvisor/fvpasswd command [args…]
fvctl command [args…]

## Slide 56
Conclusion and Future Work
• Network slicing can help perform more realistic evaluations and support multiple tenants
• FlowVisor allows experiments to run concurrently but safely on the production network
• Currently limited to subsets of actual topology
  - Add virtual links, nodes support

## Slide 57: Questions?